Documentation for MUSPAT.HEX
	Written by: Tom Digate
	Version 1.0 - Dec., 1979

     MUSPAT.HEX is a file that is to be used with Software
Technology Music System and SOL-20 machines. It adds the
ability to SAVE and GET programs from files on a CP/M
disk as well as still being able to go to SOLOS to read
and save files from tape. To install the HEX file you must
boot up your CP/M system and then RESTART to SOLOS.
Then using the SOLOS GET command, load MUSIC from tape
like this:	GET MUSIC/1 100 <cr>

    After the tape is read in, EXEC 0 and your CP/M system
should warm boot.  Now save 18 pages using the CP/M SAVE
command.  You now have a copy of the MUSIC program on the
disk which needs to be modified with the HEX file. To do this,
type DDT MUSIC.COM <cr>
     IMUSIC.HEX
     R
    -^C
   A>SAVE 18 MUSIC.COM <cr>

The installation is now complete. To run, just type MUSIC and
hit return. The title will list the additional commands
that have been added to MUSIC.
	R	Returns to SOLOS
	RS	Will ask for name and then save file on disk
	RG	Will ask for name and then get file from disk
	RC	Will warm boot back to CP/M
The filename is entered like SOLOS tape file names.
Example: RG
	 Enter name of Song?
	 CHORA/2
This will get a file called CHORA from drive B:. Once a drive
has been specified, it will be a default drive on future
disk accesses for reads or writes. On startup, the default is
always drive B:. MUSIC does an INIT command on BDOS before
printing the title block at startup so that you can change
disks on drive B:.

Note-This file will only work for systems that use SOLOS or
CUTER at C000H and have RAM at C800H for storage of
the file header block.

The file format is as follows: The first 16 bytes are an
exact duplicate of the SOLOS Header block used for TAPE
storage. Then the rest of the file is a byte for byte copy
of what is in the file (Just like SOLOS block file).
The last sector is filled with 1AH for end of file
detection. A disk error will print a message on the console.
All Console I/O is done using SOLOS and does not call CP/M.

I hope that you find this program as useful as I have and
that you enjoy using your new MUSIC System!

			Regards,
			Tom Digate