DSZ - a ZMODEM, True YMODEM(TM), XMODEM File Transfer Program

                                  Chuck Forsberg

                               Omen Technology Inc


                           Omen Technology Incorporated
                          The High Reliability Software

                       17505-V Northwest Sauvie Island Road
                              Portland Oregon 97231
              Modem: 503-621-3746 Speed 1200,2400,19200(Telebit PEP)
                         Compuserve:70007,2304  GEnie:CAF
                        UUCP: ...!tektronix!reed!omen!caf











































    Chapter 0             Rev 10-19-88  Typeset 10-19-88                     1







    Chapter 0                  DSZ Quick Reference                           2



    1.  IN CASE OF DIFFICULTY

    If you have difficulty getting DSZ to work, start with the following
    command to DSZ directly from the DOS prompt, without running any TSR or
    other COMM program:
            dsz port 1 speed 2400 d t
    (Change the port number and speed as necessary.) This connects you to the
    modem.  Dial a bulletin board by typing AT commands to the modem
    ("ATDP621-3746").  Log in as usual.  Then, request a ZMODEM download of a
    file you don't already have.  The file will download automatically, you
    don't have to do anything.  This procedure verifies the correct operation
    of DSZ.

    The "sb" and "sz" commands exploit DOS's tree structured file system.  An
    "sz" command with no file specified sends all the files in the current
    directory.  A directory or disk specifier expands to all files in that
    directory.


    1.1  Incorrect Batch Files

    Incorrect batch files are the number one source of problems using DSZ for
    downloads.  DSZ's command line echo was added to assist in correcting
    defective batch files.  Try running DSZ by itself, without any batch files
    or TSR programs, calling it directly from DOS as described above.


    1.2  No Carrier Detect

    If you see a No Carrier Detect message, you really need to give the d
    command:
            dsz port 1 speed 2400 d t

    Better yet, correct your modem cable to allow proper operation of the
    Carrier Detect signal (CD)!

    Some BBS and/or "door" programs hang when the program (such as DSZ) they
    call returns with a non 0 exit status.  Please refer to the "EXIT STATUS"
    chapter of the document for more information.

    1.3  PKARC 3.6

    It has been reported that PK36 grabs some interrupts and doesn't restore
    them on exit in an attempt to prevent hacks of the program.  Since
    eliminating that newer version and cleaning up memory, highspeed xfers
    even with 8250 UARTS work properly again.

    The problem with PK 3.6 appears to be most severe if a BBS operator has
    doorware, etc that accesses the PK programs from a shell of some sort.
    This info may be helpful to users who are having otherwise inexplicable
    file xfer problams.



    Chapter 1             Rev 10-19-88  Typeset 10-19-88                     2







    Chapter 1                  DSZ Quick Reference                           3



    1.4  COMMAND NOT FOUND

    If you see this message, make sure DSZ is in the DOS PATH.  Sometimes this
    error is caused by having too many environment variable strings.


    1.5  DOS 3.x

    DOS 3.x systems may need to have a "STACKS = 8,256" line in CONFIG.SYS to
    prevent antisocial behavior. This is required on the NEC Multispeed, or if
    certain TSR's are used.


    1.6  Lockups

    DSZ is fastidious about which interrupt vectors it takes over.  Unlike
    some COMM programs, DSZ grabs only the correct interrupt vector for its
    interrupt service routine.  This allows multi line operation under
    DESQview and other multitasking systems.

    Incorrectly configured serial ports that work with programs that pig out
    both IRQ3 and IRQ4, will lock up with DSZ.  If DSZ locks up the machine as
    soon as it tries to send or receive data, this is usually the fault.  Make
    sure the comm port is strapped correctly; COM1 uses IRQ4, COM2 uses IRQ3.
    DSZ will lock up if the comm port is not properly set up.

    In addition, DSZ will not work properly if two devices are connected to
    the same IRQ line, even when some other programs (that don't use
    interrupts as intensively) do work normally on the same machine.


    1.7  IBM PS/2 Model 50Z

    Early samples of this machine have a design error on the motherboard that
    causes comms programs to lock up the machine.  Replacing the motherboard
    with a correctly functioning unit from current production corrects the
    problem.


    1.8  Brain Damaged UARTS

    Omen Technology has received reports of problems with defective 8250 type
    UART integrated circuits in Leading Edge modem boards, serial port
    interfaces, and computers.  The defective chip logic affects high
    performance software.  Replacing the buggy chip with a newer chip (16450
    or NS16550AN) corrects the problem.  The NS16550AN is a plug in
    replacement for 8250 and 16450 serial chips.  386 and fast 286 machines
    should use the NS16550AN for best results.) Arrow Electronics 1-800-932-
    7769 sells National NS16550AN chips mail order (credit card) for about $22
    each in small quantities.




    Chapter 1             Rev 10-19-88  Typeset 10-19-88                     3







    Chapter 1                  DSZ Quick Reference                           4



    1.8.1  Everex Internal Modems
    Numerous reports have been received concerning difficulties with Everex
    modem cards.  Some of these cards contain buggy 8250 chips which are not
    up to the demands of full duplex streaming protocols such as ZMODEM.
    Replacing the buggy 8250 chip with a 16450 (or better yet NS16550AN) chip
    corrects these problems.


    1.9  Weird Iron

    A few machines, some with V20 CPUs, don't like DSZ.COM.  We have not been
    able to repeat this; TeleGodzilla (using a V20) runs DSZ.COM without a
    hitch.  Switching to DSZ.EXE has cleared up the problems on other
    machines.


    1.10  Will the real YMODEM please stand up?

    Some XMODEM programs claiming to support YMODEM do not send or accept the
    YMODEM pathname block.  1024 byte XMODEM is XMODEM-1k, not YMODEM as
    defined by Ward Christensen in 1985 when he coined the word.  1987 and
    later versions of YMODEM.DOC remind the reader of the official YMODEM
    definition, which has not changed since YMODEM's coinage in 1985.


    1.11  286 and 386 Extended Memory

    Virtual memory disk caches and ramdisks using 80286 or 80386 extended
    memory require a kluge hardware reset of the CPU chip to return to the
    normal "real mode" after accessing extended memory.  This interference to
    the interrupt response time causes lost characters on comm ports, and may
    be minimized by specifying shorter memory transfers.

    Switching to a National NS16550AN UART chip helps tremendously, allowing
    transfers at 115200 bps instead of 9600 bps with a standard 8250.  The
    NS16550AN is a plug in replacement for 8250 and 16450 serial chips.  Arrow
    Electronics 1-800-932-7769 sells National NS16550AN chips mail order
    (credit card) for about $22 each in small quantities.
















    Chapter 1             Rev 10-19-88  Typeset 10-19-88                     4







    Chapter 2                  DSZ Quick Reference                           5



    2.  FAIR PLAY

    Unlike snazzy menu interfaces, reliable high speed transfer protocols take
    many hours of testing, often over expensive phone connections, to develop.
    Two decades of communications experience and protocol testing are
    distilled in DSZ.

    DSZ is a user supported program developed and supported by Chuck Forsberg,
    owner of Omen Technology.  Countless hours of work and expen$ive resources
    went to develop and support DSZ for the myriad environments users use it
    in.  The fact that most of the problems people encounter with DSZ are
    caused by other software, hardware problems, failure to read the supplied
    documentation, or pirating has not kept users from seeking and getting
    help, even if it means calling the author in the middle of his sleep.

    Beyond this, the world of communications is constantly evolving, and it
    requires a significant ongoing effort to keep DSZ and its documentation up
    to date with the current state of the art.  Individuals with little
    knowledge of the dynamic nature of telecommunications (or hidden agendas)
    have misrepresented the frequency of enhancements to DSZ as a sign that
    DSZ is "unstable" and unworthy of "serious consideration".  If you think
    such sniping is fair play, you are more than welcome to use one of the
    many other protocol programs available, each of which claim to offer speed
    and reliability comparable to DSZ.

    Non registered users are welcome to use DSZ for a reasonable evaluation
    period.  "Reasonable" means "until you've decided whether the program is
    worth $20.00".  It does not mean "until some competing program gets around
    to adding ZMODEM or True Ymodem(TM)".  Afterwards, ethical use of DSZ
    requires registering the copy.

    DSZ is not and never has been Public Domain.  Every version of DSZ has
    included a Copyright Notice and a prohibition against sale or
    modification.  There is no usage counter or other Trojan Horse in DSZ, but
    if you use this program, you have a moral and ethical obligation to
    register it.

    Registration enables OverThruster(TM), YMODEM-g, and other advanced
    features.  The registration package serializes all past and future
    versions of DSZ.COM and DSZ.EXE.

    2.1  Sharing DSZ Files

    You are welcome to share unmodified copies of DSZ.ARC with your friends
    and associates for their evaluation.  This documentation file and the
    MAILER file must be provided with all copies of DSZ except by prior
    written permission from Omen Technology Inc.  Because of piracy problems,
    Omen Technology must INSIST that DSZ be distributed only as part of the
    DSZ.ARC file EXACTLY as provided by Omen Technology Inc or Dynamis
    Software.




    Chapter 2             Rev 10-19-88  Typeset 10-19-88                     5







    Chapter 2                  DSZ Quick Reference                           6



    PLEASE!!! Do NOT repack the Omen supplied DSZ.ARC file with Pkarc!!!

    The few bytes saved by PKARC are more than offset by confusion and
    increased difficulty identifying virus infection and unauthorized patches.

    The only approved exceptions to this rule are:

     [1]  Dissemination the contents of the DSZ.DOC file (part of DSZ.ARC) in
          a convenient machine readable or human readable form, providing the
          editorial content is unchanged.

     [2]  Encoding the DSZ.ARC file into printable characters for transmission
          over text based networks and/or message/news distribution systems.
          The "uuencode" program used with Usenet comp.binaries is an instance
          of such encoding.

    If you distribute DSZEXE.ZOO, DSZ.ARC must be included in the same
    directory since DSZEXE.ZOO references files in DSZ.ARC.  The DSZEXE.ZOO
    file may not be modified in any way, including repacking with another
    archive program.  I ask this favor because Rahul's ZOO is a superior
    archiving format, and I want to help it along.

    If you see an unpacked, repacked, or otherwise modified DSZ archive or
    parts thereof in a bulletin board, please ask the board's operator to
    replace such files with DSZ.ARC exactly as provided by Omen Technology
    Inc.  Flame them until they behave responsibly.

    No version of DSZ may be sold without the prior written permission of Omen
    Technology Inc.

    Distribution of programs that modify, patch, disassemble, decompile, or
    otherwise reverse engineer DSZ without prior written permission by Omen
    Technology Inc is a bloody theft of services and a violation of federal
    copyright law.  The same applies to debug scripts and documentation
    written for the same purposes.  When possible, such piracy will be
    referred to the FBI for investigation and prosecution under federal
    conspiracy statutes.  Applicable "RICO" law provides for treble damages
    and recovery of attorney's fees.  So far, none of the cretins producing
    such bilge have seen fit to sign their real name and address to their
    attempts at ego gratification.

    Distribution of DSZ in any medium without this documentation file is an
    unauthorized modification to DSZ that deprives the rightful author of
    registration revenues.  That is a theft of intellectual property.  Such
    distribution also damages the author also obliges the user and author to
    waste time and phone bills scrounging for the documentation, and answering
    questions that are fully covered in the documentation.

    If any version of DSZ is distributed with any other product, software or
    hardware, the product documentation must clearly and prominently state
    that the customer's continued use of DSZ requires registration directly



    Chapter 2             Rev 10-19-88  Typeset 10-19-88                     6







    Chapter 2                  DSZ Quick Reference                           7



    with Omen Technology or its duly authorized agent(s).  When DSZ is
    distributed on disk, a contemporary copy of ZCOMMDOC.ARC should be
    included on the same disk.

    Thank you for your support.

    2.2  REGISTRATION

    After a short evaluation period, ethical users must register their copy of
    DSZ with a check for $20.00 in U.S. funds sent to:

           Omen Technology Inc.
           P.O. Box 4681
           Portland, OR 97208
           For VISA/MC Registrations, call 503-621-3406

    Canadians should remit to:

           Dynamis Productivity Software LTD
           P. O. Box 5008, Station B
           Victoria BC V8R 6N3

    The address on your check is sufficient, no need to fill out forms.

    Don't bother scrounging for an envelope, just print the INSTANT MAILER
    included in this archive!

    Users, especially those overseas, may choose to register their copy of DSZ
    for $25.00 U.S.  by providing their VISA or Mastercard card number with
    expiration date and their name as it appears on their credit card.
    Overseas registrations are sent out Air Mail.

    Please contact Omen Technology before issuing unfunded purchase orders.

    *************************************************************************
    The user registration package includes a printed serial number card,
    latest versions of the DSZ programs, the installation program which
    enables features and bypasses the opening advertisement, and additional
    documentation.

    The registration package serializes all past and future versions of
    DSZ.COM and DSZ.EXE.
    *************************************************************************

    The unique serial number on the registration card is registered to the
    user, and is acceptable proof of registration to corporate auditors.

    The putsnp program inserts your unique DSZ Serial Number Password (SNP)
    into you copy of DSZ with the following command:
           putsnp dsz.com
    Putsnp accepts your SNP and asks appropriate questions before inserting



    Chapter 2             Rev 10-19-88  Typeset 10-19-88                     7







    Chapter 2                  DSZ Quick Reference                           8



    the SNP.

    Some TSR programs have been known to interfere with putsnp.  If you have a
    lockup running putsnp, run it without any TSR programs.


    The only legitimate way to disable the opening advertisement in DSZ is to
    insert an authorized SNP obtained from Omen Technology into DSZ with the
    putsnp program.  Any other suppression or modification of the opening
    screen is an illegal, unethical theft of services.

    Piracy is stealing.


    2.3  Files on Registration Disk

    The following files are currently included on the Registration Disk sent
    to paid registrants.

    DSZEXE.ZOO     Contains DSZ.EXE.


    DSZ.ARC        Contains DSZ.COM, this document, DESQview description
                   files, and an instant no-effort registration mailer.


    YZMODEM.ZOO    Contains Official YMODEM and ZMODEM protocol descriptions.


    LOOZ.DOC       Documentation on running the LOOZ program


    LOOZ.EXE       Program to unpack .ZOO archives


    RZSZ.ZOO       ZMODEM C source code, porting base for several dozen ZMODEM
                   implementations


    PUTSNP.EXE     Installs your unique registered serial number into DSZ.


    DSZBG.DOC (in DSZBG.ZOO) Background information for DSZ, part of the ZCOMM
                   User's Manual.  DSZBG.DOC is for paid registered users
                   only; registered bulletin boards and unregistered users are
                   welcome to read the ZCOMM manual contained in ZCOMMDOC.ARC.








    Chapter 2             Rev 10-19-88  Typeset 10-19-88                     8







    Chapter 2                  DSZ Quick Reference                           9



    2.4  Bulletin Board Registration

    DSZ may be freely used and copied by public bulletin board systems which
    agree to the conditions stated in the accompanying bbs_reg.txt file.
    Those not abiding to these conditions must obtain a paid registration for
    each node.

    Free bulletin board registrations are processed in batches.














































    Chapter 2             Rev 10-19-88  Typeset 10-19-88                     9







    Chapter 3                  DSZ Quick Reference                          10



    3.  DESCRIPTION

    DSZ is a "protocol driver" that uses the ZMODEM, True YMODEM(TM), or
    XMODEM protocol to transfer files over a serial port with a variety of
    programs.

    ZMODEM Transfers feature 32 bit CRC, crash recovery, and advanced file
    management.

    When calling bulletin boards to download files with ZMODEM you can avoid
    the bother of starting DSZ for each transfer by calling DSZ first, before
    asking the BBS for the download.          dsz t The "t" command allows you
    to keyboard the file request to the BBS.  DSZ's ZMODEM AutoDownload(TM)
    then receives the file automatically, without any wasted keystrokes or
    delay.  Try it, you'll like it!  (The "t" command is described below.)

    YMODEM downloads are almost as easy.  Use the "t" command as shown above,
    and hit the F3 key after telling the board to download a file with YMODEM.

    ZMODEM and True YMODEM(TM) transfers preserve exact file length and
    modification time.

    DSZ supports XMODEM-1k (XMODEM with 1024 byte blocks, sometimes mislabeled
    YMODEM) and CRC-16 with the sx -k and rc commands.

    DSZ is derived from Omen Technology's "Professional-YAM" high reliability
    communications tools, (also known as PowerCom(TM)), and supports a subset
    of Pro-YAM's file transfer related commands.  This documentation makes
    extensive references to contemporary editions of the ZCOMM or Pro-YAM
    manual, and is incomplete without it.

    DSZ is designed to be called from a communications bulletin board program.
    DSZ may also be called from other communications programs, but the
    combination lacks much of the enjoyable user friendliness of a program
    with integrated ZMODEM.

    DSZ uses its own modem I/O.  The original interrupt vector, UART parity,
    and interrupt configuration are restored on exit.  The original state of
    the 8259 interrupt mask bit for this vector is also restored on exit.

    DSZ uses DOS standard output (stdout) for messages.  It never writes
    directly to the screen.  DSZ expects its standard output to point to the
    console, a logging file, or NUL, not the modem port.  If dsz's standard
    output is redirected to the modem (as with ProComm's Host mode DOS shell),
    the combination may lock up the computer.  If necessary, dsz's standard
    output may be redirected back to the console device with the CON command.








    Chapter 3             Rev 10-19-88  Typeset 10-19-88                    10







    Chapter 4                  DSZ Quick Reference                          11



    4.  EXIT STATUS

    DSZ exits with 0 status for successful transfers, or the value of the Q
    parameter (default 1) if a file transfer failed.  Some languages and
    "door" programs do not return this information to the calling program.
    Some languages and "door" programs freak out (hang) on certain non-zero
    exit values.

    A batch file that calls DSZ directly may be used to detect the DSZ exit
    status with the DOS "errorlevel" construct.  Please refer to the Q numeric
    parameter below for more information.

    DSZ's log file entries may also be examined to determine the success or
    failure of a file transfer.








































    Chapter 4             Rev 10-19-88  Typeset 10-19-88                    11







    Chapter 5                  DSZ Quick Reference                          12



    5.  COMMANDS

    dsz [CON] [port N] [speed S] [handshake XX] [D] [d] command

    DSZ commands are an improper subset of Pro-YAM/PowerCom/ZCOMM commands.
    They are fully described in the ZCOMM User's Manual, contained in
    ZCOMMDOC.ARC.  Portions of that document are included with the DSZ
    registration disk.  Please refer to that document for details on the
    following commands.

           ***********************************************************
                                    NOTE WELL
    Except as noted, all commands must be in entered lower case.  (Case is
    significant!)
           ***********************************************************

    When used (in any combination), the CON, port, speed, handshake, and d
    commands must be given in the order shown.


    CON   Redirect message output to the DOS "CON" (console) device,
          overriding any previous redirections.  This is necessary to avoid
          lockups caused by Procomm host mode.  Most programs do not require
          this hack.  This command is unique to DSZ.

    estimate length [speed] Use the specified length and optional specified
          effective speed for the next receive file to be created.  Please
          refer to the ZCOMM manual for details.

    handshake XX Enable one of several choices of hardware handshake.  (The
          default is XOFF/XON software handshake).  This command is documented
          in the ZCOMM or Pro-YAM manual, and in DSZBG.DOC.  (The ZCOMM manual
          is available on all bulletin boards registered for DSZ as
          ZCOMMDOC.ARC.) On DSZ the "handshake" command may be abbreviated to
          "ha".

    port N select port N (n = 1,2,3,4,5,6,7,8, 10,11,12,13,14,15,16,17,18)
          Default is port 1 (COM1) or read from the DSZPORT dos environment
          variable.  COM10 to COM18 refer to the COM1 to COM8 ports on the
          PS/2.

          In multitasking operation, accessing a port used by another running
          program may hang the machine.
          EXAMPLE: to use COM2:
          dsz port 2 rz

    portx ... Select arbitrary port address and interrupt vector.  Please
          refer to the ZCOMM or Professional-YAM manual for information on
          this command.





    Chapter 5             Rev 10-19-88  Typeset 10-19-88                    12







    Chapter 5                  DSZ Quick Reference                          13



    speed S Set the specified speed.  This command is rarely needed because
          DSZ reads the port's current speed by default.  Please refer to the
          FLOW CONTROL, MAIN COMMANDS and SOFTWARE COEXISTENCE chapters in the
          ZCOMM or Pro-YAM manual for important information about the speed
          command.

    D     Disables the modem (drops Data Terminal Ready, DTR) if carrier is
          lost.  This may be used to prevent spurious events (phone ringing)
          from interfering with the calling bulletin board's recovery from
          carrier loss.

    d     Disables carrier dropout monitoring, for modems that do not properly
          drive the "Carrier Detect" input on the PC.  If you see a No Carrier
          Detect message, you need to give the d command.

    LARG  Convert ARG to lower case, then parse arg.

    pxN   Set a numeric parameter x to N.  These parameters are mostly a
          subset of the Pro-YAM/ZCOMM numeric parameters, and are listed
          below.  They assume their defaults each time DSZ is called.  Without
          an argument, p displays the numeric parameters and their values.

          EXAMPLE: C>dsz p

          z pxN Set zmodem numeric parameter x to N.  These parameters
          correspond to the Pro-YAM or ZCOMM "zmodem" parameters and rarely
          need changing.  These parameters assume their defaults each time DSZ
          is called.  Without an argument, z p displays the zmodem numeric
          parameters and their values.

    restrict Restrict pathnames to the current disk and directory tree, and
          disallow overwriting of existing files.  When DSZ is restricted, it
          will refuse to transfer files containing the string autoexec.bat and
          command.com in upper or lower case.  This provides some defense from
          malicious uploaded files.

    t     [-8g] Talk with ZMODEM AutoDownload(TM).  The optional -8g
          (available on registered copies only) allows "BBS (ANSI) graphics".
          (A video device driver such as ANSI.SYS must be loaded to suppport
          some types of graphics.) A small subset of ZCOMM/Pro-YAM term
          function subcommands are recognized.  Keyboard F1 or ALT-X to exit.
          F3 receives file(s) with True YMODEM(TM), ALT-P toggles parity
          between the 8n default and 8g (enables ANSI "graphics").  ALT-H
          toggles two local echo ("Half Duplex") modes; the second displays a
          newline (CR/LF) when Enter is keyboarded.  Keyboarded ASCII
          characters are sent to the modem.

          Modem characters print on the screen.  A device driver such as
          ANSI.SYS may be used to recognize escape sequences.

          DSZ's ZMODEM AutoDownload(TM) detects the start of a ZMODEM file



    Chapter 5             Rev 10-19-88  Typeset 10-19-88                    13







    Chapter 5                  DSZ Quick Reference                          14



          download and accepts the file(s) without operator intervention.

    rz    [-abenprt+Yy] [dir] [file ...]          (ZMODEM receive)

    rb    [-abt+y] [dir] [file ...]     (YMODEM receive)

    rb -g [-abt+y] [dir] [file ...]     (YMODEM-g receive)

    rc    [-abt+y] file1                (XMODEM/CRC receive)

    ro    [-abt+y] file1                (XMODEM OverThruster receive)

    rx    [-abt+y] file1                (XMODEM receive)

    rx    -g [-abt+y] file1             (Qmodem-G receive)


    sz    [-abefnprtY+y] [-w[N]]  file ...        (ZMODEM send)

    sb    [-ft] [PREFIX=p | ONAME=n] file ...     (YMODEM, YMODEM-g send)

    sb -k [-ft] [PREFIX=p | ONAME=n] file ...     (YMODEM-1k send)

    sx    [-t] file1                    (XMODEM, XMODEM/CRC, Qmodem-G send)

    sx -k [-t] file1                    (XMODEM-1k send)
    The meanings of the optional arguments are described in the ZCOMM manual.

    Send files may be specified indirectly:
                               dsz sz @C:files.lst
    sends the files in C:files.lst.  This provides another means of bypassing
    the DOS command line limit.  The first letter must be "@" and the third
    letter must be ":" to distinguish this from an ordinary pathname.
    Pathnames in the indirect may be separated with any combination of
    space(s), tab(s), CR and/or LF.  No spaces may appear inside a pathname;
    "FOO     .BAR" won't work.

    5.1  Interrupt Keys

    Ctrl-Break Terminates the transfer in progress.

    ALT-N Abruptly terminates (NUKES) the transfer in progress.

    Ctrl-X Typing a dozen Ctrl-X characters to another ZMODEM program
         terminates ZMODEM operations.

    ALT-F Skips the current file in ZMODEM transfers.

    ALT-B Cancels the current ZMODEM session.





    Chapter 5             Rev 10-19-88  Typeset 10-19-88                    14







    Chapter 6                  DSZ Quick Reference                          15



    6.  NUMERIC PARAMETERS

    DSZ uses the following main numeric parameters, settable with the pxN
    command.

    EXAMPLE: C>dsz pQ0


    In addition, DSZ uses the Pro-YAM/ZCOMM zmodem numeric parameters
    described in the Pro-YAM/ZCOMM reference manual.


    B   Set the size of buffer used for disk reads and writes.  The default is
        1024, 8192 maximum.  If your copy of DSZ is running on a floppy disk
        system or a very slow turkey hard disk, a larger value may give better
        results.  Too large a value may exhaust memory, induce receiver
        timeouts, cause disconnects(!), or generate spurious CRC errors.  If
        performance logging doesn't work, this parameter is too big.  This
        parameter is supported on versions compiled with TurboC.

        EXAMPLE: C>dsz pB4096 sz A:floppy.fil

        Setting the buffer size larger may lock out the performance log,
        DSZFILES, and/or indirect pathname list in the "tiny model" DSZ
        flavor.  If you aren't bloody sure you need a bigger buffer, don't use
        one.

    O   This parameter controls XMODEM OverThruster(TM).  It is described in
        dszbg.doc.  This file is part of the software package sent to paid
        registrants.

    Q   Error code returned to DOS (default 1).  (Success always returns 0.)
        Some programs toss cookies when confronted with certain exit codes.

        EXAMPLE: C>dsz pQ-1 sz foo.bar


    S   Timeout in seconds (default 15) waiting for restraint release (XON
        and/or handshake).

    W   Wait for Enter key before exiting after an error.  Effective on
        registered copies.  Useful when calling DSZ from DESQview, allows the
        window to close unless there is an error message that should remain
        visible.

    a   Calibrates certain protocol timeouts used with XMODEM and YMODEM
        transfers (Cybernetic Data Recovery(TM)).  This parameter does not
        affect ZMODEM transfers.

        The a numeric parameter is automatically set to 2000 for a 4.77 mHz PC
        or XT, 4000 for a PS2/30, 6000 for an 8 mHz 1ws AT, and 12000 for a



    Chapter 6             Rev 10-19-88  Typeset 10-19-88                    15







    Chapter 6                  DSZ Quick Reference                          16



        PS2/80.  If your computer has a speedup card or otherwise runs
        unusually fast (or slow!) for its type, you may set the a numeric
        parameter to a value that reflects its speed.

        EXAMPLE: dsz port 2 pa4000 rb


        NOTE: Setting this parameter does not suppress the "Unknown Machine
        Type" message which is displayed before the command line is scanned.

    d   A non zero value (the default) causes incoming files received with
        ZMODEM and full YMODEM transfers to have their Date set to that sent
        in the file header.  ZMODEM's file management features depend on the
        transmission of each file's modification date.  Files will have the
        same creation date, even if the two machines are in different time
        zones.  When transferring files to/from a Unix system, creation dates
        are interpreted according to GMT or Universal Coordinated Time.  File
        dating may be disabled with a pd0 command.
        NOTE: Backdating file creation times may confuse some backup programs.

    v   Verbose level (debugging output) Negative values inhibit some routine
        messages.  Setting v to 1 or greater causes serialized copies to ring
        the bell when a transfer is done.

    z   Timezone in minutes behind GMT, used for ZMODEM and True YMODEM file
        transfers to coordinate the actual date of the file with computers in
        other time zones.  Effective on registered copies.  PDT or MST
        corresponds to 420.  This may be preset with the ZONE DOS environment
        variable.

























    Chapter 6             Rev 10-19-88  Typeset 10-19-88                    16







    Chapter 7                  DSZ Quick Reference                          17



    7.  ENVIRONMENT VARIABLES

    The following DOS environment variables may be set to modify DSZ
    operation.

    DIRRX (Registered copies only.) Specifies the directory to receive
        (download) files.  If the sting in DIRRX ends with "/", directory
        and/or disk designators in the incoming pathname are stripped, and
        only the stem (name and extension) is used.  Otherwise, if an incoming
        file has an absolute pathname, the incoming pathname is used.

        EXAMPLE: C>set DIRRX=C:/rxdirect/
        C>dsz rz -r


    DSZFILES May contain a list of up to 9999 pathnames to transmit, with
        entries separated by spaces.  If present, DSZFILES is used in place of
        a normal command line list of files to send with the sb and sz
        commands.

        EXAMPLE: C>set DSZFILES=file1 file2 file3 *.c
        C>dsz port 2 handshake on sz -r

        In practice, this string would be built up by a calling program and
        passed to DSZ with a "spawnvpe", "execvpe", or similar subroutine
        call.

        SEE ALSO: Pathname list specification @C:files.lst

    DSZLOG log file to receive entries for files sent and received.  (Default
        null).  Sample entries:

    Z  46532 38400 bps 3324 cps   0 errors    66 1024 DSZ.COM 1177
    Z 124087 19200 bps 1880 cps   0 errors     6 1024 MXY.TMP 1177

        Transfer times are based on the DOS time of day clock and have one
        second jitter.  As with all protocol throughput reports generated by
        Omen Technology programs (and contrary to the false claims of some
        critics), DSZ's throughput figures for ZMODEM, Kermit, and True
        YMODEM(TM) transfers do not take "credit" for pathname and/or protocol
        overhead characters.  DSZ's throughput reports do not include the time
        required to send the pathname.  This understates the true time
        required to transfer files, but the time required to send the pathname
        often depends on the alacrity of the operator, and thus does not
        always reflect the performance of the protocol itself.

        Transfers measuring less than one second are reported as having 9999
        characters per second throughput.

        The unlabeled numeric field after the error (retry) count is the
        number of flow control stoppages encountered sending the file.  This



    Chapter 7             Rev 10-19-88  Typeset 10-19-88                    17







    Chapter 7                  DSZ Quick Reference                          18



        number gives an indication of flow control restrictions (overloaded
        networks, etc.) encountered during the transfer.

        The last numeric field before the file name is the block or subpacket
        length used for the last block in the file.

        The last field is the serial number of the other program, or -1 if
        this information is not available.

        The code letter indicates the type of transfer, Z (ZMODEM), S
        (X/YMODEM), R (X/YMODEM), E (error), or L (transfer terminated by loss
        of data carrier).

        WARNING: If DSZ encounters a loss of carrier or other fatal error
        condition before a file commences transmission, a log entry will not
        be made.

        EXAMPLE: C>set DSZLOG=C:/yam/dszlog


    DSZOPT (Registered copies only) String containing default options for DSZ
        file transfers.  Options are optional modifiers to the DSZ sz, rz, sx,
        rx, sb, rb commands.

        An 8n may be appended to the string to make BBS (ANSI) graphics the
        default for DSZ's t command.  The ability to preset these options is
        especially helpful for controlling ZMODEM automatic downloads from
        DSZ's t command.

        EXAMPLE: C>set DSZOPT=r
        Enables DSZ's Intelligent Crash Recovery(TM) as a default.

        Let's say you wish ZMODEM crash recovery, and BBS "graphics" for the
        DSZ term function:
        C>set DSZOPT=r8g


        WARNING: Do NOT include "ena" or any other commands in the DSZOPT
        string.  With the exception of the "8g" mode, only **options** may be
        placed in the DSZOPT string!  (Options are the letters that modify the
        sz, rz, sb, etc. commands.  In "rz -r", "r" is an option.)

    MAXBYTES Maximum number of bytes allowed for transfer.  If this number is
        exceeded, DSZ skips the offending files (ZMODEM) or aborts remaining
        files in the batch (YMODEM).

    DSZPORT Default communications port override, default 1.
        EXAMPLE:
        C>set DSZPORT=2





    Chapter 7             Rev 10-19-88  Typeset 10-19-88                    18







    Chapter 7                  DSZ Quick Reference                          19



    ZONE sets the z numeric parameter to the number of minutes the current
        local time lags GMT time.  PDT or MST corresponds to 420.  (Registered
        copies only)
        EXAMPLE:
        C>set ZONE=420

















































    Chapter 7             Rev 10-19-88  Typeset 10-19-88                    19







    Chapter 8                  DSZ Quick Reference                          20



    8.  EXAMPLES

    dsz sz c:foo.* b:*.c          (send files)

    dsz sz -r yzmodem.arc         (CRASH RECOVERY: resume interrupted
    transfer)

    dsz rz -r                     (CRASH RECOVERY: resume interrupted
    transfer)

    dsz handshake both sz yzmodem.arc       (Hardware+Software handshake)

    dsz sz -n *.*                 (send files that are newer or rx has no
    copy)

    dsz sz -Yn *.*                (Only send files that are newer than
    receiver's copy)
                                  (Do not send files that do not exist on
    receiver's disk)

    dsz rz C:/UPLOADS             (receive files to specified directory)

    dsz port 2 speed 38400 restrict rz

    dsz rz  -y prog.arc           (ZMODEM, single file pathname override)

    dsz z pr1 rx foo.dat          (XMODEM receive, remove file if error)

    dsz pO60 ro foo.dat           (XMODEM/OverThruster receive, GEnie MNP)

    DSZ LRC L-Y NEWPROG.ARC       (generate lower case "rc -y" command)

    dsz pv2 sz foo >debug.dmp     (Debugging data dump)

    dsz sz @C:/bbs/files.lst      (Indirect file list)



















    Chapter 8             Rev 10-19-88  Typeset 10-19-88                    20







    Chapter 9                  DSZ Quick Reference                          21



    9.  BACKGROUND OPERATION

    Three DESQview description files are provided to demonstrate background
    operation with modest (66 kb window) memory requirements.  DSZ uses tight
    C/ASM code, table driven CRC generators, and buffered receive and transmit
    for good performance in the background without hogging CPU cycles.  On a
    QIC Labs PC-AT clone, DSZ can download files in the background (3
    background clock ticks, 9 foreground clock ticks) with a throughput better
    than 9600 bps.

    2S   Prompts for file name(s) and sends them with ZMODEM protocol.  File:
         2S-PIF.DVP

    2T   Talks to the modem and allows manual YMODEM (F3) or automatic ZMODEM
         downloads.  File: 2T-PIF.DVP

    2A   Like 2T, but using Quarterdeck's dvansi.com memory resident ANSI CRT
         device driver to process ANSI screen codes.  File: 2A-PIF.DVP DS.BAT
         is the batch file used by 2A.

    These files are written for a port 2 local connection and \TMP directory,
    but may be modified to suit your requirements using the DESQview CP
    command.  The W numeric allows DESQview to close the window after DSZ
    finishes, providing a pleasant user interface.

    Operation at high speed (above 9600 bps) requires the DESQview "Optimize
    communications" performance Advanced Setup option.

           ***********************************************************
                                     WARNING
    When running DSZ under a multi tasking system such as DESQview, do not
    allow two programs to access the same comm port at the same time.  At
    best, such actions will disrupt communications.  At worst, your computer
    will attempt to open a subspace channel to V'ger.
           ***********************************************************



















    Chapter 9             Rev 10-19-88  Typeset 10-19-88                    21







    Chapter 10                 DSZ Quick Reference                          22



    10.  CALLING DSZ FROM COMM PROGRAMS

    It may be necessary to give a

    SET COMSPEC=A:\COMMAND.COM

    (change as needed) in your AUTOEXEC.BAT file to allow programs to call
    DSZ.

    10.1  GT POWER 13.00/14.00

    GT Power version 13/14 includes a YMRX.BAT (YMODEM-g receive) file with an
    "rz" command.  You guessed it, "rz" is for ZMODEM protocol (the z means
    ZMODEM!).  Please change the file to use the correct "rb -g" for YMODEM-g.

    The files ZMTX.ARC and GT1300.NOT available on many bulletin boards
    contain useful information for GT Power users.

    10.2  PROCOMM

    DSZ may not operate properly when called from Procomm if Procomm has files
    open at the time.

    When running under ProComm's Host mode, failure to use the CON command may
    cause Procomm to lock up the computer.

    The POE, PCALL, DSZ_ZAP, and PROZ programs have been popular in
    interfacing DSZ to Procomm's editor gateway.

    Hint: the DOS PATH environment variable must include Procomm's directory
    to allow POE to locate all the POE files,.  The POE files should be stored
    in the Procomm directory.  Setting the "PROCOMM" environment variable is
    insufficient.

    10.3  PROCOMM PLUS

    DSZ may not operate properly when called from Procomm if Procomm has files
    open at the time.

    Here are some handy settings for Procomm Plus.

    First, set the DOS environment as necessary before running Procomm:
    SET DSZPORT=2                           (Only needed for COM2)
    SET DSZLOG=DSZ.LOG            (If you wish a log file)

    Then set Procomm's external protocol strings:
    A- External protocol 1 upload filename  ...ZMODEMU
    B- External protocol 1 download filename ... ZMODEMD

    And then some short batch files:
    ZMODEMU.BAT:                  DSZ sz %1 %2 %3 %4 %5 %6 %7 %8 %9



    Chapter 10            Rev 10-19-88  Typeset 10-19-88                    22







    Chapter 10                 DSZ Quick Reference                          23



    ZMODEMD.BAT:    DSZ rz

    To make downloads easier, use the "dsz t" command described above.
    ZMODEMT.BAT:                  DSZ t

    10.4  Qmodem

    The following is based on a message from Mike Cody, sysop of HomePlate
    313-385-9969 3/12/24/96 HST

    Go into Qinstall and go to frame 3 Directories. Then select External
    protocols #3 I think. Now you will see a definition area to tell Qmodem
    the Letter,batchfile combo to use.

    Now put Z in the letter definition, Zup.bat in the u/l batch zdown.bat in
    the d/l batch, and Y in the btch protocol. Now save it at the menu with
    f10 and S.

    Then go to DOS and create the following batch files in your Qmodem
    directory...

    Zdown.bat: DSZ port %2 speed %1 rz -w %3

    Zup.bat: DSZ port %2 speed %1 sz %3

    These are the batch files that will be called by Qmodem.  If uou did
    everthing right when uoy hit PGDN or PGUP you will see an external
    protocol called Z) Zmodem in the box. For an easier time do a serch for
    either External.arc or maybe the string "Qmodem" in the file database as
    there is a file with several external prootcols and batch files available
    in the Mahoney file section (EXEC BBS).

    10.5  BULLETIN BOARDS

    When installing DSZ on a bulletin board or host system, be sure to check
    for proper operation when the caller hangs up while a file is being sent
    or received.

    Currently, Only the TurboC version supports file sharing (shared read
    access on files sent by  dsz).

    Some bulletin board interface routines do not call DSZ to send a file
    until they have verified the file's presence by opening the file.  If this
    checking is done in DOS's default exclusive open mode, dsz's file sharing
    will be defeated.









    Chapter 10            Rev 10-19-88  Typeset 10-19-88                    23







    Chapter 11                 DSZ Quick Reference                          24



    11.  FLOW CONTROL

    If you plan to send files over Telenet (PC-Pursuit), you must refer to the
    Pro-YAM or ZCOMM Reference manual (in ZCOMMDOC.ARC) FLOW CONTROL chapter
    for vital information on flow control considerations necessary for proper
    operation of ZMODEM and other streaming protocols.
















































    Chapter 11            Rev 10-19-88  Typeset 10-19-88                    24







    Chapter 12                 DSZ Quick Reference                          25



    12.  ERROR MESSAGES

    COM2 1200 bps Carrier Detect enabled Handshake slow
    Command line = (commands)
    This is a normal message displayed to help resolve problems with incorrect
    batch files.  The port number, speed, carrier detect ("enabled" or
    "DISABLED") and "handshake" indicate the selected mode of operation.

    Unknown Machine Type XX, 'a' parameter preset to 6000 indicates a ROM BIOS
    that does not follow the IBM specification for identifying the machine
    type.  If your computer causes DSZ to display this message, you may set
    the a numeric parameter described elsewhere in this document.  This
    message is generated before any commands are read, so do not be alarmed
    when setting the a parameter doesn't make this message go away.  The a
    parameter does not affect ZMODEM transfers.

    Need more memory to run DSZ or Abnormal program termination is displayed
    by the TurboC startup routine if DSZ is run in too small a memory
    partition.  If you see this message, use a larger memory partition for DSZ
    or remove some memory resident programs.  This message may also appear if
    the calling program fails to free memory before calling DSZ.

    No Carrier Detect is displayed when DSZ recognizes a loss or lack or
    carrier detect signal from the modem.  This is caused by a line
    disconnect, defective cable, or incorrect modem strapping.  It may be
    disabled with the d command.  Sometimes this is caused by setting the B
    parameter to too large a value.

    Garbage Count Exceeded Indicates ZMODEM has not detected a valid start of
    header in a reasonable number of characters.

    If DSZ becomes "stuck" on emitting this messages, it is possible the
    sending program may not be able to recognize and act upon transmission
    requests (ZROPS headers).  The sending program should be corrected.  In
    the meantime, setting a ZMODEM packet length with the "zmodem pl4096"
    command forces the sender to wait for the receivers' progress reports.

    Permission denied comes from the Microsoft C Library.  This may be caused
    by attempts to modify a read only file or directory, or create a file in a
    nonexistient directory.

    A furtive flashing appearance of XOFF or FLOW during ZMODEM or YMODEM-g
    file sending signifies DSZ is responding to flow control restraint.  This
    is normal operation when buffered modems or packet switched networks are
    used.  ZMODEM's robustness and reliability allow creative users to
    transfer files over unusual multiple computer lash-ups, causing modem data
    lights and computer status displays to dance in unfamiliar rhythms.  Got
    ZRPOS indicates the receiving program has detected a transmission error
    and has requested retransmission.  In other words, ZMODEM is doing its job
    of detecting and correcting missing and garbled data.  If this happens
    more often than observed line errors would indicate is reasonable, there



    Chapter 12            Rev 10-19-88  Typeset 10-19-88                    25







    Chapter 12                 DSZ Quick Reference                          26



    may be a flow control problem in one of four areas:

      + Between the sending program and its modem.  If using an interface
        speed higher than the transmission speed, or modem to modem error
        correction (MNP, LAPB, PEP, etc.), check that the modem and the
        sending program are configured for the same flow control methods.  DSZ
        is faster than most other programs, and may expose flow control
        problems not seen with slower software.

      + Between the sending modem and the network.  Correcting this requires
        "handshake both" to allow the sending program to honor both hardware
        (CTS) flow control from the modem and software flow control (XON/XOFF)
        from the network.

      + Between parts of the network.

      + Between the receiving modem and the receiving program.  This can
        happen at high transmission speeds when the receiver has specified a
        large I/O buffer size with the B numeric parameter.

        Excessive interrupt latency from extended memory ramdisks or disk
        caches, and poorly written hard disk drivers also wreak havoc on
        streaming protocols but do not affect start-stop protocols (XMODEM,
        etc.).

        To correct these problems, give the "handshake slow" command to the
        receiver.

    Byte NNNN retry M: <error message> These messages appear when the protocol
    has detected an error and is attempting to retransmit the garbled data.
    These are normal messages.

    Serial Input Error: Line Status Register HH indicates a slow device
    driver, TSR program, or other software is disabling interrupts too long
    for DSZ to accept incoming data, and some characters are lost.  A slow
    response to folow control also triggers this message.

    The value of the line status register is displayed in HEX.  The following
    error conditions when present OR into the Line Status Register.


    01   Interrupt level circular buffer overrun.  The remote did not respond
         to 's XOFF or hardware flow control.


    02   Data Overrun generally caused by formware or other software locking
         out interrupts for excessive periods.  Other chapters in this
         document give suggestions on decreasing excessive interrupt latency.






    Chapter 12            Rev 10-19-88  Typeset 10-19-88                    26







    Chapter 12                 DSZ Quick Reference                          27



    08   Framing Error generally caused by line noise or an incorrect
         transmission speed or format (number of bits).  Most protocols
         require 8 bits no parity for proper operation.  This is set
         automatically by Omen Technology programs, but other programs may not
         be so smart.


    10   Break Interrupt generally caused by line noise or an incorrect
         transmission speed or format (number of bits).

    Please refer to the In Case of Difficulty chapter of this document for
    solutions.

    Less commonly encountered DSZ error messages are explained in the Pro-YAM
    manual.







































    Chapter 12            Rev 10-19-88  Typeset 10-19-88                    27







    Chapter 13                 DSZ Quick Reference                          28



    13.  ASSOCIATED DOCUMENTS

    Consult the Professional-YAM, PowerCom, or ZCOMM manual chapter "OPTIONS
    FOR FILE TRANSFERS" for descriptions of the file transfer options.  The
    "FILE TRANSFER BASICS" chapter explains the relative merits of XMODEM,
    YMODEM, ZMODEM, and other protocols and gives tips on their use.  The
    "MAIN COMMANDS" chapter describes the rb, rx, rc, rz, sb, and sz commands.
    The "MODEM INTERFACING" and "FLOW CONTROL" chapters contain important
    information on the use of buffered modems with DSZ.

    Information on the ZMODEM Inter Application File Transfer Protocol may be
    found in ZMODEM.DOC, part of YZMODEM.ZOO (yzmodem.arc).

    C Source code for XMODEM, YMODEM, and ZMODEM transfers is included in
    RZSZ.ZOO.  This file includes a Pro-YAM/ZCOMM script to upload a bootstrap
    file to a Unix system, force its compilation, and (if the compilation is
    successful) upload the rz/sz source files.

    The C source code now includes VAX/VMS support.



































    Chapter 13            Rev 10-19-88  Typeset 10-19-88                    28







    Chapter 14                 DSZ Quick Reference                          29



    14.  FILES

    2S-PIF.DVP, 2A-PIF.DVP, DS.BAT, 2T-PIF.DVP DSZ.COM, and DSZ.DOC constitute
    Omen Technology's DSZ.ARC.

    2S-PIF.DVP, 2A-PIF.DVP, DS.BAT, and 2T-PIF.DVP are used with the DESQview
    multitasking executive for background operation.

    ZCOMMDOC.ARC (manual), ZCOMMEXE.ARC (programs), ZCOMMHLP.ARC (help
    processor and database), ZCOMM communications tools.  The ZCOMM files
    should be available on the BBS you downloaded DSZ.ARC from.  If these
    files are not available, the BBS is not fulfilling the concractual
    requirements of free BBS registration of DSZ.

    YZMODEM.ARC contains XMODEM, YMODEM, and ZMODEM Protocol Descriptions.

    RZSZ.ZOO contains ZMODEM "C" source code.  (COMPLETE VAX VMS and
    Unix/Xenix programs).

    DSZ.EXE compiled with the Xenix to DOS XC provides moderately higher
    maximum throughput (1700 vs 1300 cps downloading to a 4.77 mHz XT).  The
    speed difference is a function of the compiler, the source code is the
    same.  The Xenix XC version requires more memory, and does not support
    file sharing or a large I/O buffer.  This version is available in
    DSZEXE.ZOO.

    ZCOMM and Pro-YAM also run at a higher speed than DSZ.COM.

    DSZBG.ZOO contains DSZBG.DOC.  Part of the DSZ registration disk (and not
    for public distribution), this file provides background information on the
    ZCOMM/Pro-YAM commands provided in DSZ.

    LOOZ.EXE unpacks .ZOO archives.  LOOZ.DOC describes LOOZ.EXE.  The ZOO
    archive format is a machine independent improvement on the PC-DOS specific
    .ARC format.



















    Chapter 14            Rev 10-19-88  Typeset 10-19-88                    29







    Chapter 15                 DSZ Quick Reference                          30



    15.  CHANGES

    Be sure to save your serial number/password (SNP) card and the putsnp
    program you received from Omen to use with future versions of DSZ you may
    download!

    10-19-88  ZMODEM crash recovery of files where the source is shorter than
    the destination is now (properly) inhibited.

    The "z" parameters may now be set in the context of an XMODEM or YMODEM
    transfer.

    8-30-88 Bloated file transfer times when spanning midnight have been
    corrected.  Some of the error messages have been made more understandable,
    and are explained in this document.

    8-10-88, 7-19-88 Further Documentation enhancements.

    7-11-88  Documentation enhancements.  Putsnp program now compiled under
    TurboC, resets console raw mode to avoid lockup with off the wall device
    drivers.

    Portx command allows selection of comm port with specified base address
    and interrupt vector.

    YMODEM-g modified for better compatibility with non standard programs such
    as EXEC-BBS.

    6-07-88 Minor changes which do not affect normal file transfers.  The
    speed/handshake status readout now reflects the conditions used for the
    actual transfer instead of the first speed or handshake command
    encountered.

    With the sz command, the k option forces an initial 1024 byte subpacket
    length.  This is for you folks that just can't wait until Dsz's adaptive
    optimizations get up to 1k subpackets.

    EXAMPLE: sz -k *.c *.h


    REMEMBER: ZMODEM subpacket length isn't the same as the difference between
    128 and 1024 byte XMODEM blocks!!!

    DSZ.COM is now compiled with TurboC under SCO 386 Xenix+VP/ix to reduce
    the possibility of virus infection.

    5-7-88  A spurious message about Crash Recovery when the -r option is used
    and no old file is present has been suppressed.  "Handshake slow" is more
    effective than previously.

    4-23-88  Good news for tired frog stompers!  The ZMODEM rz/sz programs are



    Chapter 15            Rev 10-19-88  Typeset 10-19-88                    30







    Chapter 15                 DSZ Quick Reference                          31



    now available in a VMS C flavor.  The VAX/VMS source files are contained
    in the RZSZ.ARC (RZSZ.ZOO) archive file.

    Support for CP/M format (0x1A EOF character) log files has been restored.
    (Previously, it had been removed to save memory).

    The value of the DSZOPT string (if set) is now displayed to aid debugging.

    A coding error that caused excruciatingly slow throughput if a
    transmission error or common section mismatch was detected *after* the
    sending program had reached EOF was fixed.

    "Handshake slow" has been added to disable the RTS signal to the modem
    while writing to disk, even if the interrupt buffer is not chock full of
    bytes.  This should help systems with excessive interrupt latency on disk
    writes.

    4-14-88 The DSZOPT=8g feature (for the t command term function) now works
    as documented.

    Bogus file count displays seen on YMODEM and ZMODEM downloads have been
    fixed.  (They were caused by the serial number being sent in decimal
    instead of octal.)

    4-6-88 Send pathnames may be specified indirectly:
                               dsz sz @C:files.lst
    sends the files in C:files.lst.  This provides another means of bypassing
    the DOS command line limit.  The first letter must be "@" and the third
    letter must be ":" to distinguish this from an ordinary pathname.

    Obligations of Bulletin Boards requesting free BBS registrations have been
    amended.  Unethical behavior on the part of a small minority prompted
    these clarifications.

    3-29-88 There never was a 3-26-88 version, except for use by the
    Sandinista troops in Honduras.

    3-26-88 First general release compiled with TurboC version 1.5.
    Outstanding meganit: on certain networked systems, the reported number of
    files on batch send is ridiculous.

    This version no longer needs or accepts the "memory allocation patch".

    This version has a number of changes to ease interfacing and problem
    resolution.  The command line and acive com port are displayed to aid
    debugging of batch files that call DSZ.

    The DIRRX environment variable may be used to specify a directory for
    receiving files.  If the DIRRX environment variable ends with a slash, any
    drive designators and/or directory names in the incoming file are
    stripped.



    Chapter 15            Rev 10-19-88  Typeset 10-19-88                    31







    Chapter 15                 DSZ Quick Reference                          32



    The DSZFILES environment variable may be used to specify an alternate list
    of pathnames to transmit whose length is not limited by the DOS command
    line.  It is typically used by calling programs using one of the C library
    "spawn" functions.

    Setting the v (verbose) parameter to 1 or greater causes serialized copies
    to ring the bell when a transfer is done.

    2-28-88 More changes in DSZ.DOC, no changes to the software.

    2-8-88 DSZ.DOC has been extensively rewritten and reorganized.  DSZ now
    supports the advanced buffering of the National NS16550AN and Intel 82510
    serial interface devices.  Arrow Electronics 1-800-932-7769 sells National
    NS16550AN chips mail order (credit card) for about $22 each in small
    quantities.

    ZMODEM subpacket length adjustment has been improved to deal with Telenet
    congestion.

    Pirated/hacked versions of DSZ have cost users and DSZ's developer
    thousands of dollars in lost time and other expenses, in addition to
    injuring the reputation of Omen Technology and its products.  Regrettably,
    Omen Technology cannot support prior versions of DSZ because of this
    piracy.

    Name             Length                           Date        Time   CRC

    dsz.com          50582  Squeezed   10%     45772   7 Jun 88   3:57a  5fa8
    dsz.com          50704  Squeezed   10%     45870  11 Jul 88   7:51a  1036
    dsz.com          50736  Squeezed   10%     45863  30 Aug 88   4:04a  aae1
    dsz.com          50784  Squeezed   10%     45968  19 Oct 88  12:07a  f0fe

    Your copy of DSZ should show this information as provided by

           arc v dsz.arc
    or
          pkxarc -v dsz.arc

    If your copy shows a different CRC or file length, insist on a legitimate
    copy and report the source of the bogus/pirated copy to Omen Technology
    Inc.













    Chapter 15            Rev 10-19-88  Typeset 10-19-88                    32







    Chapter 16                 DSZ Quick Reference                          33



    16.  Other Omen Technology Products

    Omen Technolgy makes Professional-YAM, a comphrensive comms program with
    unmatched power.  Flavors are available for PC-DOS, Unix, Xenix, and OS/2
    Protected mode.

    ZCOMM is a full featured shareware version with a $40.00 basic
    registration.














































    Chapter 16            Rev 10-19-88  Typeset 10-19-88                    33







    Chapter 17                 DSZ Quick Reference                          34



    17.  ACKNOWLEDGEMENTS

    32 bit CRC code courtesy Gary S. Brown.

    The High Reliability Software(TM), TurboLearn Script Writer(TM),
    Cybernetic Data Recovery(TM), AutoDownload(TM), Intelligent Crash
    Recovery(TM), Error Containment(TM), Full Time Capture(TM), True
    YMODEM(TM), OverThruster(TM), Password Guardian(TM), CryptoScript(TM), and
    TurboDial(TM) are Omen Technology trademarks.

    PowerCom was trademarked in 1985 by POLYTRON Corporation, Hillsboro
    Oregon.

    DSZ and this documentation are Copyright 1988 by Omen Technology Inc, all
    rights reserved.  True YMODEM(TM) is an Omen Technology Trademark
    signifying YMODEM protocol support that meets the full YMODEM
    specification.

                           Omen Technology Incorporated
                          The High Reliability Software

                       17505-V Northwest Sauvie Island Road
                              Portland Oregon 97231
                  Modem: 503-621-3746 Speed 1200,2400,19200 PEP
                         Compuserve:70007,2304  GEnie:CAF





























    Chapter 17            Rev 10-19-88  Typeset 10-19-88                    34











                                     CONTENTS


     1.  IN CASE OF DIFFICULTY............................................   2
         1.1   Incorrect Batch Files......................................   2
         1.2   No Carrier Detect..........................................   2
         1.3   PKARC 3.6..................................................   2
         1.4   COMMAND NOT FOUND..........................................   3
         1.5   DOS 3.x....................................................   3
         1.6   Lockups....................................................   3
         1.7   IBM PS/2 Model 50Z.........................................   3
         1.8   Brain Damaged UARTS........................................   3
         1.9   Weird Iron.................................................   4
         1.10  Will the real YMODEM please stand up?......................   4
         1.11  286 and 386 Extended Memory................................   4

     2.  FAIR PLAY........................................................   5
         2.1   Sharing DSZ Files..........................................   5
         2.2   REGISTRATION...............................................   7
         2.3   Files on Registration Disk.................................   8
         2.4   Bulletin Board Registration................................   9

     3.  DESCRIPTION......................................................  10

     4.  EXIT STATUS......................................................  11

     5.  COMMANDS.........................................................  12
         5.1   Interrupt Keys.............................................  14

     6.  NUMERIC PARAMETERS...............................................  15

     7.  ENVIRONMENT VARIABLES............................................  17

     8.  EXAMPLES.........................................................  20

     9.  BACKGROUND OPERATION.............................................  21

    10.  CALLING DSZ FROM COMM PROGRAMS...................................  22
         10.1  GT POWER 13.00/14.00.......................................  22
         10.2  PROCOMM....................................................  22
         10.3  PROCOMM PLUS...............................................  22
         10.4  Qmodem.....................................................  23
         10.5  BULLETIN BOARDS............................................  23

    11.  FLOW CONTROL.....................................................  24

    12.  ERROR MESSAGES...................................................  25

    13.  ASSOCIATED DOCUMENTS.............................................  28

    14.  FILES............................................................  29



                                      - i -











    15.  CHANGES..........................................................  30

    16.  Other Omen Technology Products...................................  33

    17.  ACKNOWLEDGEMENTS.................................................  34

















































                                      - ii -









          DSZ - a ZMODEM, True YMODEM(TM), XMODEM File Transfer Program


                                  Chuck Forsberg

                               Omen Technology Inc


                                     ABSTRACT



                      ZMODEM - Not just another XMODEM hack

    The ZMODEM file transfer protocol provides reliable file and command
    transfers with complete END-TO-END data integrity between application
    programs.  ZMODEM's 32 bit CRC protects against errors that continue to
    sneak into even the most advanced networks.

    Unlike traditional and many recently introduced protocols, ZMODEM
    safeguards all data and supervisory information with effective error
    detection.

    ZMODEM rapidly transfers files, particularly with buffered (error
    correcting) modems, timesharing systems, satellite relays, and wide area
    packet switched networks.

    User Friendliness is an important ZMODEM feature.  ZMODEM AutoDownload(TM)
    (Automatic file Download initiated without user intervention) greatly
    simplifies file transfers compared to traditional protocols.

    DSZ's ZMODEM provides advanced file management features including
    Intelligent Crash Recovery, flexible control of selective file transfers,
    and security verified command downloading.

    DSZ is one of many available programs that implement the ZMODEM file
    transfer protocol.