DSZ(Shareware)           Omen Technology           DSZ(Shareware)



     NAME
          dsz - ZMODEM, True YMODEM(TM), XMODEM file transfer
          subprogram

     SYNOPSIS
          dsz [CON] [port N] [speed S] [handshake XX] [d] [d] command

     DESCRIPTION
          Dsz is a "protocol driver" that uses the ZMODEM, True
          YMODEM(TM), or XMODEM protocol to transfer files over a
          serial port with a variety of programs.

          Non registered users are granted a license to use dsz for a
          limited evaluation period.  Otherwise, use of dsz requires
          registering the copy.  Registration enables some advanced
          features.

          If you received this copy of DSZ with another progam, even
          if your copy of the other program is registered, this copy
          of DSZ has not been registered.  Please refer to the
          licensing information below, and support the continued
          development of high quality shareware.

          ZMODEM Transfers feature 32 bit CRC, crash recovery, and
          advanced file management.  When calling bulletin boards to
          download files with ZMODEM or True YMODEM(TM), you can avoid
          the bother of starting DSZ for each transfer by calling dsz
          first, before asking the BBS for the download (dsz t).  The
          "t" command allows you to keyboard the file request to the
          BBS, and then DSZ's ZMODEM AutoDownload receives the file
          automatically, without any wasted keystrokes or delay.  Try
          it, you'll like it!  (The "t" command is described below.)

          True YMODEM(TM) transfers preserve exact file length and
          modification time.

          Dsz supports XMODEM-1k (XMODEM with 1024 byte blocks,
          sometimes mislabeled YMODEM) and CRC-16 with the sx -k and
          rc commands.

          Dsz is derived from Omen Technology's Professional-YAM
          communications software, (also published by POLYTRON Corp of
          Hillsboro Oregon as PowerCom(TM)), and supports a subset of
          Pro-YAM's file transfer related commands.  This
          documentation makes extensive references to contemporary
          editions of the ZCOMM or Pro-YAM manual, and is incomplete
          without it.

          Dsz is designed to be called from a communications bulletin
          board program.  Dsz may also be called from other
          communications programs, but the combination lacks much of
          the power of a communications program with integrated



     Page 1                                         (printed 10/26/87)






     DSZ(Shareware)           Omen Technology           DSZ(Shareware)



          ZMODEM.

          Dsz uses its own modem I/O.  The original interrupt vector,
          UART parity, interrupt configuration, and 8259 interrupt
          mask are restored on exit.

          Dsz uses DOS standard output (stdout) for messages, it does
          not write directly to the screen.  Dsz expects its standard
          output to point to the console, a logging file, or NUL, not
          the modem port.  If necessary, dsz's standard output may be
          redirected to the console device with the CON command.  If
          dsz's standard output has been redirected to the modem (as
          with ProComm's Host mode DOS shell), failure to use the CON
          command may lock up the computer.

          Dsz exits with 0 status for successful transfers, or the
          value of the Q parameter (default 1) if a file transfer
          failed.  Some languages do not return this information to
          the calling program.  A batch file that calls dsz directly
          may be used to detect the dsz exit status, or dsz's log file
          entries may be examined.

     ENVIRONMENT VARIABLES
          DSZLOG
               log file to receive entries for files sent and
               received.  (Default null).  Sample entries:

           Z  46532 38400 bps 3324 cps   0 errors    66 1024 DSZ.COM
           Z 124087 19200 bps 1880 cps   0 errors     6 1024 MXY.TMP

               Transfer times are based on the DOS time of day clock
               and have one second jitter.  As with all protocol
               throughput reports generated by Omen Technology
               programs (and contrary to the false claims of some
               critics), dsz's throughput figures for ZMODEM, Kermit,
               and True YMODEM(TM) transfers do not take "credit" for
               pathname and/or protocol overhead characters.  Dsz's
               throughput reports do not include the time required to
               send the pathname.  This understates the true time
               required to transfer files, but the time required to
               send the pathname often depends on the alacrity of the
               operator, and thus does not always reflect the
               performance of the protocol itself.

               Transfers measuring less than one second are reported
               as having 9999 characters per second throughput.

               The unlabeled numeric field after the error (retry)
               count is the number of flow control stoppages
               encountered sending the file.  This number gives an
               indication of flow control restrictions (overloaded
               networks, etc.) encountered during the transfer.



     Page 2                                         (printed 10/26/87)






     DSZ(Shareware)           Omen Technology           DSZ(Shareware)



               The last numeric field is the block or subpacket length
               used for the last block in the file.

               The code letter indicates the type of transfer, Z
               (ZMODEM), S (X/YMODEM), R (X/YMODEM), E (error), or L
               (transfer terminated by loss of data carrier).
          DSZOPT
               String containing default options for DSZ file
               transfers.  (Registered copies only) An 8n may be
               appended to the string to make BBS (ANSI) graphics the
               default for dsz's t command.  The ability to preset
               these options is especially helpful with dsz's t
               command.  EXAMPLE:
               C>set DSZOPT=r
               Enables dsz's intelligent Crash Recovery as a default.
          DSZPORT
               Default communications port override, default 1.
          ZONE sets the z numeric parameter to the number of minutes
               the current local time lags GMT time.  PDT or MST
               corresponds to 420.  (Registered copies only) EXAMPLE:
               C>set ZONE=420

     COMMANDS
          Dsz commands are an improper subset of Pro-
          YAM/PowerCom/ZCOMM commands.  Except as noted, all commands
          must be in lower case.

          Unlike ZCOMM, PowerCom, and Pro-YAM, dsz does not support
          ZMODEM AutoDownload with ZMODEM security challenge.
          (AutoDownload is a pleasant user interface that recognizes
          the start of a file download and automatically starts the
          correct file transfer protocol. Please refer to the
          ZCOMM/PowerCom/Pro-YAM user manual for details on this
          powerful and convenient feature.) Unregistered copies of dsz
          do not support OverThruster(TM).  Dsz does not support
          Kermit, Kermit AutoDownload, Super Kermit, B Protocol, the
          traditional XMODEM variants MODEM7 batch, Telink, WXMODEM,
          and Clink/SEAlink supported by Pro-YAM/PowerCom/ZCOMM.

          Interrupt keys:

          Ctrl-Break
               Terminates the transfer in progress.
          ALT-N
               Abruptly terminates (NUKES) the transfer in progress.


          When used, the CON, port, speed, handshake, and d commands
          must be given in the order shown.

          CON  Redirect message output to the DOS "CON" (console)
               device, overriding any previous redirections.



     Page 3                                         (printed 10/26/87)






     DSZ(Shareware)           Omen Technology           DSZ(Shareware)



          handshake XX
               Enable one of several choices of hardware handshake.
               (The default is XOFF/XON software handshake).  This
               command is documented in the ZCOMM or Pro-YAM manual.
          port N
               select port N (n = 1,2,3,4 ... 8) Default is port 1
               (COM1) or read from the DSZPORT dos environment
               variable.  In multitasking operation, accessing a port
               used by another running program will hang the machine.
          speed S
               Set the specified speed.  This command is rarely needed
               because dsk reads the port's current speed by default.
               Please refer to to the FLOW CONTROL, MAIN COMMANDS and
               SOFTWARE COEXISTENCE chapters in the ZCOMM or Pro-YAM
               manual for important information about the speed
               command.
          d    Disables carrier dropout monitoring, for modems that do
               not properly drive the "Data Carrier Detect" input on
               the PC.
          LARG Convert ARG to lower case, then parse arg.
          pxN  Set a numeric parameter x to N.  These parameters are a
               subset of the Pro-YAM or ZCOMM numeric parameters, and
               are listed below.  They assume their defaults each time
               dsz is called.  Without an argument, p displays the
               numeric parameters and their values.
          z pxN
               Set zmodem numeric parameter x to N.  These parameters
               correspond to the Pro-YAM or ZCOMM "zmodem" parameters
               and rarely need changing.  These parameters assume
               their defaults each time dsz is called.  Without an
               argument, z p displays the zmodem numeric parameters
               and their values.
          restrict
               Restrict pathnames to the current disk and directory
               tree, and disallows overwriting of existing files.
               When dsz is restricted, it will refuse to transfer
               files containing the string autoexec.bat and
               command.com in either case.  This provides some defense
               from malicious uploaded files.
          t    [-8g] Talk with ZMODEM AutoDownload.  The optional -8g
               (available on registered copies only) allows "BBS
               (ANSI) graphics".  A small subset of ZCOMM/Pro-YAM term
               function subcommands are recognized.  Keyboard F1 or
               ALT-X to exit.  F3 receives file(s) with True YMODEMTm,
               ALT-P toggles parity between the 8n default and 8g
               (enables ANSI "graphics").  ALT-H toggles two local
               echo ("Half Duplex") modes; the second displays a
               newline on Enter.  Keyboarded ASCII characters are sent
               to the modem.  Modem characters print on the screen.  A
               device driver such as ANSI.SYS may be used to recognize
               escape sequences.  ZMODEM AutoDownload detects the
               start of a ZMODEM file download and accepts the file(s)



     Page 4                                         (printed 10/26/87)






     DSZ(Shareware)           Omen Technology           DSZ(Shareware)



               without operator intervention.
          sz   [-abefnprtY+y] [-w[N]] [PREFIX=p | ONAME=n] file
               ...(ZMODEM)
          sb   [-ft] [PREFIX=p | ONAME=n] file ...     (YMODEM)
          sb -k
               [-ft] [PREFIX=p | ONAME=n] file ...     (YMODEM-1k)
          sx   [-t] file1                    (XMODEM or XMODEM/CRC)
          sx -k
               [-t] file1                    (XMODEM-1k)
          rz   [-abenprt+Yy] [dir] [file ...]          (ZMODEM)
          rb   [-abt+y] [dir] [file ...]     (YMODEM)
          rb -g
               [-abt+y] [dir] [file ...]     (YMODEM-g)
          rc   [-abt+y] file1                (XMODEM/CRC)
          ro   [-abt+y] file1                (XMODEM OverThruster)
          rx   [-abt+y] file1                (XMODEM)

     PARAMETERS
          Dsz uses the following main numeric parameters, settable
          with the pxN command.  In addition, dsz uses the Pro-
          YAM/ZCOMM zmodem numeric parameters described in the Pro-
          YAM/ZCOMM manual.

          B    Set the size of buffer used for disk reads and writes.
               The default is 1024, 8192 maximum.  A larger value may
               give better results when sending files to or from from
               sluggish floppy disk systems.  Too large a value will
               exhaust memory or induce receiver timeouts.  This
               parameter is supported on versions compiled with
               TurboC.
          Q    Error code returned to DOS (default 1).  (Success
               returns 0.) Some programs toss cookies when confronted
               with certain exit codes.
          O    Controls OverThruster(TM) operation with XMODEM,
               XMODEM-1k, and YMODEM downloads.  This parameter should
               be set as follows:

               CompuServe XMODEM Negative numbers control the number
               of bytes added to the window on XMODEM downloads from
               the CompuServe Information Service.  Larger numbers
               increase throughput, but cause improperly interfaced
               MNP modems on CIS nodes to drop characters under
               stress, disrupting the file transfer.  EXAMPLE:
               pO-512; ro file1.ext

               Other XMODEM Positive numbers up to a system dependent
               value less than the protocol block size increase
               throughput.  Larger values induce timeouts and/or
               retransmitted blocks.  The optimum value must be
               determined by experiment.  60 usually give best results
               with MNP modems at 2400 bps.  The optimum value varies
               depending on the remote computer, modem(s), system



     Page 5                                         (printed 10/26/87)






     DSZ(Shareware)           Omen Technology           DSZ(Shareware)



               traffic, and the network node.  EXAMPLE:
               pO60; ro file1.ext
          S    Timeout in seconds (default 15) waiting for restraint
               release (XON and/or handshake).
          W    Wait for Enter key before exiting after an error.
               Useful when calling dsz from DESQview, allows the
               window to close unless there is an error message that
               should remain visible.
          a    Calibrates certain protocol timeouts used with XMODEM
               and YMODEM transfers (Cybernetic Data Recovery(TM)).
               The a numeric parameter is automatically set to 2000
               for a 4.77 mHz PC or XT, 4000 for a PS2/30, 6000 for an
               8 mHz 1ws AT, and 12000 for a PS2/80.  If your computer
               has a speedup card or otherwise runs unusually fast (or
               slow!) for its type, you should set the a numeric
               parameter to a value that reflects its speed.
          v    Verbose level (debugging output) Negative values
               inhibit some routine messages
          z    Timezone in minutes behind GMT, used for ZMODEM and
               True YMODEM file transfers to coordinate the actual
               date of the file with computers in other time zones.
               Effective on registered copies.  PDT or MST corresponds
               to 420.  This may be preset with the ZONE DOS
               environment variable.

     BACKGROUND OPERATION
          Three DESQview description files are provided to demonstrate
          background operation with modest (66 kb window) memory
          requirements.  Dsz uses tight C/ASM code, table driven CRC
          generators, and buffered receive and transmit for good
          performance in the background without hogging CPU cycles.
          On a QIC Labs PC-AT clone, dsz can download files in the
          background (3 background clock ticks, 9 foreground clock
          ticks) with a throughput better than 9600 bps.

          2S   Prompts for file name(s) and sends them with ZMODEM
               protocol.
          2T   Talks to the modem and allows manual YMODEM (F3) or
               automatic ZMODEM downloads.
          2A   Like 2T, but using Quarterdeck's dvansi.com memory
               resident ANSI CRT device driver to process ANSI screen
               codes.  DS.BAT is the batch file used by 2A.

               These files are written for a port 2 local connection
               and \TMP directory, but may be modified to suit your
               requirements using the DESQview CP command.  The W
               numeric allows DESQview to close the window after dsz
               finishes, providing a pleasant user interface.

               Operation at high speed (above 9600 bps) requires the
               DESQview "Optimize communications" performance Advanced
               Setup option.



     Page 6                                         (printed 10/26/87)






     DSZ(Shareware)           Omen Technology           DSZ(Shareware)



               ***********************************************************
                                       WARNING
               When running dsz under a multi tasking system such as
               DESQview, do not allow two programs to access the same
               comm port at the same time.  At best, such actions will
               disrupt communications.  At worst, your computer will
               attempt to open a subspace channel to V'ger.
               ***********************************************************

     FLOW CONTROL
          Please refer to the Pro-YAM, PowerCom, or ZCOMM manual FLOW
          CONTROL chapter for important information on flow control
          considerations necessary for proper operation of ZMODEM and
          other streaming protocols with buffered (error correcting)
          modems and/or networks.

     EXAMPLES
          dsz sz c:foo.* b:*.c          (send files)

          dsz sz -r yzmodem.arc         (CRASH RECOVERY: resume
          interrupted transfer)

          dsz handshake both sz yzmodem.arc       (Hardware+Software
          handshake)

          dsz sz -n *.*                 (send files that are newer or
          rx has no copy)

          dsz sz -Yn *.*                (Only send files that are
          newer than receiver's copy)
                                        (Do not send files that do not
          exist on receiver's disk)

          dsz rz C:/UPLOADS             (receive files to specified
          directory)

          dsz port 2 speed 38400 restrict rz

          dsz rz  -y prog.arc           (ZMODEM, single file pathname
          override)

          dsz z pr1 rx foo.dat          (XMODEM receive, remove file
          if error)

          dsz pO60 ro foo.dat           (XMODEM/OverThruster receive,
          GEnie MNP)

          DSZ LRC L-Y NEWPROG.ARC       (generate lower case "rc -y"
          command)

          dsz pv2 sz foo >debug.dmp     (Debugging data dump)




     Page 7                                         (printed 10/26/87)






     DSZ(Shareware)           Omen Technology           DSZ(Shareware)



     ERROR MESSAGES
          The message Abnormal program termination is printed by the
          TurboC startup routine if dsz is run in too small a memory
          partition.  If you see this message, use a larger memory
          partition for dsz or remove some memory resident programs.
          This message may also appear if the calling program fails to
          free memory before calling dsz.

          The message Unknown Machine Type XX, Assuming AT indicates a
          ROM BIOS that does not follow the IBM specification for
          identifying the machine type.  If your computer causes dsz
          to display this message, you must set the a numeric
          parameter described elsewhere in this document.

          A perplexing, cryptic message comes from the Microsoft C
          Library: "Permission denied".  This may be caused by
          attempts to modify a read only file or directory, or create
          a file in a nonexistient directory.

          A furtive flashing appearance of "XOFF" or "FLOW" during
          ZMODEM or YMODEM-g file sending signifies dsz is responding
          to flow control restraint.  This is normal operation when
          buffered modems or packet switched networks are used.
          ZMODEM's robustness and reliability allow creative users to
          transfer files over unusual multiple computer lash-ups,
          causing modem data lights and computer status displays to
          dance in unfamiliar rhythms.

          Other Dsz error messages are listed in the Pro-YAM manual.

     SEE ALSO
          Consult the Professional-YAM, PowerCom, or ZCOMM manual
          chapter "OPTIONS FOR FILE TRANSFERS" for option meanings.
          The "FILE TRANSFER BASICS" chapter explains the relative
          merits of XMODEM, YMODEM, ZMODEM, and other protocols and
          gives tips on their use.  The "MAIN COMMANDS" chapter
          describes the rb, rx, rc, rz, sb, and sz commands.  The
          "MODEM INTERFACING" and "FLOW CONTROL" chapters contain
          important information on the use of buffered modems with
          dsz.

          Information on the ZMODEM Inter Application File Transfer
          Protocol may be found in ZMODEM.DOC, part of YZMODEM.ZOO
          (yzmodem.arc).

          C Source code for XMODEM, YMODEM, and ZMODEM transfers is
          included in RZSZ.ZOO.  This file includes a Pro-YAM/ZCOMM
          script to upload a bootstrap file to a Unix system, force
          its compilation, and (if the compilation is successful)
          upload the rz/sz source files.

     GT POWER 13.00



     Page 8                                         (printed 10/26/87)






     DSZ(Shareware)           Omen Technology           DSZ(Shareware)



          GT Power version 13.00 includes a YMRX.BAT (YMODEM-g
          receive) file with an "rz" command.  You guessed it, "rz" is
          for ZMODEM protocol (the z means ZMODEM!).  Please change
          the file to use the correct "rb -g" for YMODEM-g.

     PROCOMM
          When running under ProComm's Host mode, failure to use the
          CON command may cause Procomm to lock up the computer.

     BULLETIN BOARDS
          When installing dsz on a bulletin board or host system, be
          sure to check for proper operation when the caller hangs up
          while a file is being sent or recieved.

          Currently, Only the TurboC version supports file sharing
          (shared read access on files sent by  dsz).

          Some bulletin board interface routines do not call dsz to
          send a file until they have verified the file's existience
          by opening the file.  If this checking is done in MS-DOS's
          default exclusive open mode, dsz's file sharing will be
          defeated.

     NOTES
          DOS 3.x systems may need to have a "STACKS = 8,256" line in
          CONFIG.SYS to prevent antisocial behavior, especially on the
          NEC Multispeed, or if certain TSR's are used.

          A few machines, some with V20 CPUs, don't like DSZ.COM.  We
          have not been able to repeat this; TeleGodzilla (using a
          V20) runs DSZ.COM without a hitch.  Switching to DSZ.EXE has
          cleared up the problems on other machines.

          Some XMODEM programs claiming to support YMODEM do not send
          or accept the YMODEM pathname block.  1024 byte XMODEM is
          XMODEM-1k, not YMODEM as defined by Ward Christensen in 1985
          when he coined the word.  1987 versions of YMODEM.DOC remind
          the reader of the official YMODEM definition.

          32 bit CRC code courtesy Gary S. Brown.

          Cybernetic Data Recovery(TM), Error Containment(TM),
          OverThruster(TM), Password Guardian(TM), CryptoScript(TM),
          and TurboDial(TM) are Omen Technology trademarks.

          PowerCom was trademarked in 1985 by POLYTRON Corporation,
          Hillsboro Oregon.

          Dsz and this documentation are Copyright 1987 by Omen
          Technology Inc, all rights reserved.  True YMODEM(TM) is an
          Omen Technology Trademark signifying YMODEM protocol support
          that meets the full YMODEM specification.



     Page 9                                         (printed 10/26/87)






     DSZ(Shareware)           Omen Technology           DSZ(Shareware)



     FILES
          ZCOMMDOC.ARC, ZCOMMEXE.ARC, ZCOMMHLP.ARC, YZMODEM.ZOO
          (yzmodem.arc) (Official XMODEM, YMODEM, and ZMODEM Protocol
          Description), RZSZ.ZOO (rzsz.arc) (Unix/Xenix source code),
          2S-PIF.DVP, 2A-PIF.DVP, DS.BAT, 2T-PIF.DVP DSZ.COM, DSZ.DOC
          (this file).

          DSZ.EXE compiled with the Xenix to DOS XC provides
          moderately higher maximum throughput (1700 vs 1300 cps
          downloading to a 4.77 mHz XT).  The speed difference is a
          function of the compiler, the source code is the same.  The
          Xenix XC version requires more memory, and does not support
          file sharing or a large I/O buffer.  This version is
          available in DSZEXE.ZOO.

          ZCOMM and Pro-YAM also run at a higher speed than DSZ.COM.

          Incompatible batch files may cause dsz to fail.

     LICENSING INFORMATION
          Dsz is a user supported program developed and supported by
          Chuck Forsberg.  It has taken countless hours of work and
          considerable resources to develop and support dsz in the
          myriad environments users use it.  Unlike snazzy menu
          interfaces, developing high performance transfer protocols
          takes many hours of testing.  Help fight the high cost of
          software by supporting high quality shareware.  Thank you
          for your support.

          Dsz is not and never has been public domain, nor has it been
          free software.  If you use this program, you ought to
          register it.

          This documentation file and the MAILER file must be provided
          with all copies of DSZ except by written permission from
          Omen Technology Inc.  Dsz may not be modified, patched,
          hacked, disassembled, decompiled, or otherwise reverse
          engineered, or sold, without prior written permission by
          Omen Technology Inc.

          Distribution of dsz in any medium without this documentation
          file constitutes an unauthorized modification.

          If dsz is distributed with any other product, software or
          hardware, the product documentation must clearly and
          promimently state that the customer's continued use of dsz
          requires registration directly with Omen Technology or its
          duly authorized agent(s).  When dsz is distributed on disk,
          a contemporary copy of ZCOMMDOC.ARC must be included on the
          same disk.

          After an initial short evaluation period, users should



     Page 10                                        (printed 10/26/87)






     DSZ(Shareware)           Omen Technology           DSZ(Shareware)



          register their copy of dsz with a check for $20.00 in U.S.
          funds sent to:

                 Omen Technology Inc.
                 P.O. Box 4681
                 Portland, OR 97208

          Don't bother scrounging for an envelope, use the INSTANT
          MAILER included in this archive!

          Users, especially those overseas, may choose to register
          their copy of dsz for $25.00 U.S.  by providing their VISA
          or Mastercard card number with expiration date and their
          name as it appears on their card.

          ***********************************************************
          The USER registration package includes a serial number, the
          latest DSZ programs, the installation program which enables
          features and bypasses the opening advertisement, and
          additional documentation.

          The registration package serializes all past and future
          versions of DSZ.COM and DSZ.EXE.
          ***********************************************************

          The putsnp program inserts YOUR DSZ, ZCOMM, PowerCom, or
          Pro-YAM Serial Number Password (SNP) into you copy of DSZ:
                 putsnp dsz.com
          Putsnp accepts your SNP and asks appropriate questions
          before inserting the SNP.

          The only legitimate way to disable the opening advertisement
          in dsz is to insert an authorized SNP obtained from Omen
          Technology into dsz with the putsnp program.  Any other
          suppression or modification of the opening screen is
          illegal, unethical, and prohibited.

          Distribution of programs and/or instructions on how to
          modify, patch, disassemble, decompile, or otherwise reverse
          engineer dsz without prior written permission by Omen
          Technology Inc is a theft of services and a violation of
          federal copyright law, and will be referred to the FBI for
          investigation and prosecution under federal conspiricy
          statutes.  Applicable RICO law provides for treble damages
          and recovery of attorney's fees.

          Dsz may be used and copied by bulletin board systems which
          feature the ZCOMM files (ZCOMMEXE.ARC, ZCOMMDOC.ARC,
          ZCOMMHLP.ARC) for downloading.  A Dsz registration and a
          diskette with current versions of the ZCOMM files (for
          bulletin board downloading) will be mailed upon validation.
          Dsz may be registered without charge by sending your



     Page 11                                        (printed 10/26/87)






     DSZ(Shareware)           Omen Technology           DSZ(Shareware)



          bulletin board's address, telephone number and a valid
          login.

     CHANGES
          10-25-87 A bug fix for the distributed Demo of GT Power
          13.00 is included.

          The ZCOMM/Pro-YAM "ro" command and O parameter been added
          for XMODEM OverThruster(TM) downloads.  With clean lines,
          OverThruster can speed up network XMODEM downloads
          considerably, enough to pay for registration quickly.
          Typical values for the "O" parameter are 35 for regular
          modems, 60 for MNP modems, but vary widely on different
          systems and even between ports on the same network.  For
          XMODEM downloads from Compuserve, the "O" parameter should
          be set to 0.
          EXAMPLE: "dsz pO35 ro speedy.fil"

          The "w[N]" option was added to allow an easier way to
          specify a window size for the "sz" command over PC Pursuit.
          A missing N gives a window size of 4096.  This option allows
          the DSZOPT environmet string to set the window size.

          The ZCOMM/Pro-YAM "t" option (term talk after transfer) has
          been added.  This allows you to enter a description after
          uploading a file to a bulletin board.
          EXAMPLE: "dsz sz -t stealth.zoo"

          Memory requirements have been reduced by eliminating unused
          routines.  The DIRSIZE environment variable is not used;
          files are sent in directory order.

          10-15-87 Disables file sharing calls on DOS levels less than
          3.x.  Registered copies recognize "t -8g" as well as a
          trailing "8g" in DSZOPT.  10-6-87 English command error
          explanations have been reinstated.  For registered programs
          only, the ZONE and DSZOPT environment variables were added.
          The z parameter now works.  The -r option (Crash Recovery)
          is now intelligent, checking for discrepeancies between the
          old file and the new file.

          Acquisition and release of the modem port was enhanced for
          smoother operation in computers multitasking multiple
          communications programs on different ports.

          Pirated/hacked versions of DSZ have cost users and dsz's
          developer thousands of dollars in lost time and other
          expenses, in addition to injuring the reputation of Omen
          Technology and its products.  Regrettably, Omen Technology
          cannot support prior versions of dsz because of this piracy.

          Name    Length  Date       Time   CRC



     Page 12                                        (printed 10/26/87)






     DSZ(Shareware)           Omen Technology           DSZ(Shareware)



          dsz.com 45446  25 Oct 87   4:46a  7244

          Your copy of dsz show show this information as provided by

                                        arc v dsz.arc
          (Reg.)or
                                        pkxarc -v dsz.arc (Reg.) If
          your copy shows a different CRC or file length, insist on a
          legitimate copy and report the source of the pirated copy to
          Omen Technology Inc.

                          Omen Technology Incorporated


                         The High Reliability Software

                      17505-V Northwest Sauvie Island Road
                             Portland Oregon 97231
                           VOICE: 503-621-3406 :VOICE
                 Modem: 503-621-3746 Speed 1200,2400,19200 PEP
                        Compuserve:70007,2304  GEnie:CAF
                       UUCP: ...!tektronix!reed!omen!caf

































     Page 13                                        (printed 10/26/87)