PROBLEMS WHEN RUNNING DSZ UNDER A MULTITASKING ENVIRONMENT

The following stats were generated using a program called COMSTAT which resides
in the public domain.  It's function is to return UART and interupt
information for programming and debugging purposes.

Extracted from the NOVAC RBBS, these tests show the results of port
and UART conflicts when running DSZ within DesqView windows.  The active
communications port which runs the BBS is COM1.  COM2 is used by other
communictions programs but is primarily used by a mouse driver which drives
a Logitech C7 mouse.

Speculation has mounted as to DSZ's stability and functionality when
running under DesqView.  Numerous reports have been made which claim
DSZ locks all COM tasks in other windows and on other ports until the DSZ
task has been completed.  This is in fact the case as my Logitech mouse
and other concurrent COM sessions lock solid when a BBS user intitiates a 
DSZ transfer.


The following screen is the status of the dormant COM2 port and UART before
a DSZ transfer.  Nothing has accessed this port since a cold hardware reset
and serves to show the UART's default start up parmaters:

           MODEM PORT 2 (BASE = 02F8H, BAUDRATE = 2400)

BIT  7 6 5 4 3 2 1 0  (HEX)  MEANING
-------------------------------------------------------------------
DAT: 0 0 0 0 0 0 0 1  (01H)  (BYTE FROM DATA REGISTER)
IER: 0 0 0 0 0 0 0 0  (00H)  Ints enabled: NONE
IIR: 0 0 0 0 0 0 0 1  (01H)  Int pending: NONE
LCR: 0 0 0 0 0 0 1 1  (03H)  8 bits, 1 stop bit(s), parity DISABLED
MCR: 0 0 0 0 0 0 0 0  (00H)  Bits set: NONE
LSR: 0 1 1 0 0 0 0 0  (60H)  Bits set: THRE TSRE
MSR: 0 0 0 0 0 0 0 0  (00H)  Bits set: NONE

           HARDWARE INTERRUPT STATUS FROM PORT 21H
                     (1 = MASKED OFF)

IRQ #:    7 6 5 4 3 2 1 0  (HEX)  MEANING
-------------------------------------------------------------------
STATUS:   1 0 1 0 1 0 0 0  (A8H)  IRQ's enabled:  6 4 2 1 0

VECTOR FOR INTERRUPT 0BH AT 0000:002C = F000:EF6F


This is the status of the COM2 just after loading the Logitech mouse driver.


           MODEM PORT 2 (BASE = 02F8H, BAUDRATE = 2400)

BIT  7 6 5 4 3 2 1 0  (HEX)  MEANING
-------------------------------------------------------------------
DAT: 0 0 0 1 1 0 1 0  (1AH)  (BYTE FROM DATA REGISTER)
IER: 0 0 0 0 0 0 0 1  (01H)  Ints enabled: RDA
IIR: 0 0 0 0 0 0 0 1  (01H)  Int pending: NONE
LCR: 0 0 0 0 1 1 1 1  (0FH)  8 bits, 2 stop bit(s), parity ODD
MCR: 0 0 0 0 1 0 1 1  (0BH)  Bits set: DTR RTS OUT2
LSR: 0 1 1 0 0 0 0 0  (60H)  Bits set: THRE TSRE
MSR: 0 0 1 1 1 0 1 1  (3BH)  Bits set: DCTS DDSR DRLSD CTS DSR

           HARDWARE INTERRUPT STATUS FROM PORT 21H
                     (1 = MASKED OFF)

IRQ #:    7 6 5 4 3 2 1 0  (HEX)  MEANING
-------------------------------------------------------------------
STATUS:   1 0 1 0 1 0 0 0  (A8H)  IRQ's enabled:  6 4 2 1 0

VECTOR FOR INTERRUPT 0BH AT 0000:002C = 22F3:0D4E


The following is the status of COM2 during the DSZ session.


           MODEM PORT 2 (BASE = 02F8H, BAUDRATE = 2400)

BIT  7 6 5 4 3 2 1 0  (HEX)  MEANING
-------------------------------------------------------------------
DAT: 0 0 0 0 1 1 1 1  (0FH)  (BYTE FROM DATA REGISTER)
IER: 0 0 0 0 0 0 0 1  (01H)  Ints enabled: RDA
IIR: 0 0 0 0 0 0 0 1  (01H)  Int pending: NONE
LCR: 0 0 0 0 1 1 1 1  (0FH)  8 bits, 2 stop bit(s), parity ODD
MCR: 0 0 0 0 1 0 1 1  (0BH)  Bits set: DTR RTS OUT2
LSR: 0 1 1 0 0 0 0 0  (60H)  Bits set: THRE TSRE
MSR: 0 0 1 1 0 0 0 0  (30H)  Bits set: CTS DSR

           HARDWARE INTERRUPT STATUS FROM PORT 21H
                     (1 = MASKED OFF)

IRQ #:    7 6 5 4 3 2 1 0  (HEX)  MEANING
-------------------------------------------------------------------
STATUS:   1 0 1 0 1 0 0 0  (A8H)  IRQ's enabled:  6 4 2 1 0

VECTOR FOR INTERRUPT 0BH AT 0000:002C = 22F3:0D4E


This is the status of COM2 after the DSZ session:


           MODEM PORT 2 (BASE = 02F8H, BAUDRATE = 2400)

BIT  7 6 5 4 3 2 1 0  (HEX)  MEANING
-------------------------------------------------------------------
DAT: 0 0 0 0 0 0 0 1  (01H)  (BYTE FROM DATA REGISTER)
IER: 0 0 0 0 0 0 0 1  (01H)  Ints enabled: RDA
IIR: 0 0 0 0 0 0 0 1  (01H)  Int pending: NONE
LCR: 0 0 0 0 1 1 1 1  (0FH)  8 bits, 2 stop bit(s), parity ODD
MCR: 0 0 0 0 1 0 1 1  (0BH)  Bits set: DTR RTS OUT2
LSR: 0 1 1 0 0 0 0 0  (60H)  Bits set: THRE TSRE
MSR: 0 0 1 1 0 0 0 0  (30H)  Bits set: CTS DSR

           HARDWARE INTERRUPT STATUS FROM PORT 21H
                     (1 = MASKED OFF)

IRQ #:    7 6 5 4 3 2 1 0  (HEX)  MEANING
-------------------------------------------------------------------
STATUS:   1 0 1 0 0 0 0 0  (A0H)  IRQ's enabled:  6 4 3 2 1 0

VECTOR FOR INTERRUPT 0BH AT 0000:002C = 22F3:0D4E

From this quick test, it is evident that DSZ is changing the MSR register
in the UART and not properly restoring it when exiting.  It also points out
that DSZ is masking the COM2 interupt IRQ3 upon exit when when it shouldn't be!
In fact DSZ should not even touch COM2 unless it is told to do so.  In 
these tests it was told only to utilize COM1.
  
It appears that a bug still resides in DSZ which plays some kind of 
non-standard game with the UART and confuses DesqView's ability to 
handle multiple COM tasks. The problem hasn't occured when running under 
straight DOS.  Since DOS cannot multitask COM or any other tasks, it would
never surface!

A quick solution to this problem may be forthcoming if users force Forsberg
to address the issue.  Thus far he has remained unresponsive to numerous
requests and complaints.

Here is his address and phone number:

	Chuck Forsberg
	Omen Technology Inc
	17505-V Northwest Sauvie Island Road
	Portland, Oregon  97231

	Modem: (503)-621-3746 (Better have credit card in hand!)
	Voice: (503)-621-3406

I would also be interested in hearing of similar problems others are having
when running DSZ under DesqView or other multitasking operating systems.
I can be reached through any one of the following sources:

	NOVAC RBBS - 703-256-4777 - Springfield VA
	FIDOnet 109/118
	RBBSnet 935/102
	and the DESQVIEW National Echo Conference carried by most 
		FIDOnet Echohubs.

Blaine Korcel
AAC Associates, Inc.