PC-TALK III    1/19/85

            DOCUMENTATION FOR THE IBM 3101 EMULATION INCORPORATED
                 IN THE PROGRAM PC-TALK Version: EXECPCT 2.0

         -> by Kyle Cummings, 5507 North 36th St., Arlington VA 22207 <-



        GENERAL

        The changes in the updated PC-TALK program Version EXECPCT correct
        some problems in the 3101 protocol section. The escape characters
        were corrected and a few new ones were added.



        REFERENCE

        The subroutine was cleaned up a bit and refined using the protocol 
        for 3101 communication as defined in the IBM manual:
                  "IBM 3101 Display Terminal Description"
                             Page A-4 & A-5
                     (IBM manual number GA18-2033-2)



        COMMENTS

        The subroutine works well for full screen support with the Alanthus
        Protocol Converter we use for communication to a IBM 3083 running VM.
        Appendix A-11B is for users of the Alanthus Protocol Converter.

        To use the emulation while running PC-TALK, hold down the Alt key
        and press "O". This will result in a message saying:

                    "=== I.B.M. 3101 Operation On"

        You are now in 3101 mode. Place the call to the other computer and
        the program will emulate an IBM 3101.



        We have defined some of the keys for use under 3101
        emulation. They are as follows:

        IBM PC KEYS           IBM 3101 KEYS           IBM 3270 KEYS
        -----------------------------------------------------------
   Program Attention Keys:
        Enter.................New Line................ENTER
        Esc 1 Enter...........PF1.....................PF1
        Esc 2 Enter...........PF2.....................PF2
        Esc 3 Enter...........PF3.....................PF3
        Esc 4 Enter...........PF4.....................PF4
        Esc 5 Enter...........PF5.....................PF5
        Esc 6 Enter...........PF6.....................PF6
        Esc 7 Enter...........PF7.....................PF7
        Esc 8 Enter...........PF8.....................PF8
        Esc 9 Enter...........ESC 9 New Line..........PF9
        Esc 1 0 Enter.........ESC 1 0 New Line........PF10
        Esc 1 1 Enter.........ESC 1 1 New Line........PF11
        Esc 1 2 Enter.........ESC 1 2 New Line........PF12
        Esc 1 3 Enter.........ESC 1 3 New Line........PF13
        Esc 1 4 Enter.........ESC 1 4 New Line........PF14
        Esc 1 5 Enter.........ESC 1 5 New Line........PF15
        Esc 1 6 Enter.........ESC 1 6 New Line........PF16
        Esc 1 7 Enter.........ESC 1 7 New Line........PF17
        Esc 1 8 Enter.........ESC 1 8 New Line........PF18
        Esc 1 9 Enter.........ESC 1 9 New Line........PF19
        Esc 2 0 Enter.........ESC 2 0 New Line........PF20
        Esc 2 1 Enter.........ESC 2 1 New Line........PF21
        Esc 2 2 Enter.........ESC 2 2 New Line........PF22
        Esc 2 3 Enter.........ESC 2 3 New Line........PF23
        Esc 2 4 Enter.........ESC 2 4 New Line........PF24
        Home..................CLEAR...................CLEAR
   Cursor Control Keys:
        Left Arrow............Left Arrow..............Left
        Right Arrow...........Right Arrow.............Right
        Up Arrow..............Up Arrow................Up
        Down Arrow............Down Arrow..............Down
        Pg Dn.................NEW LINE................NEW LINE
        Tab Right.............TAB RIGHT...............TAB RIGHT
        Tab Left..............TAB LEFT................TAB LEFT
        Ctrl-Home.............Home....................Home
   Editing Control Keys:
        Ctrl-Pg up............ERASE INPUT.............ERASE INPUT
        End...................ERASE EOF...............ERASE EOF
        Ins...................ALT-V...................INSERT MODE
        Del...................DEL.....................DELETE
   Miscellaneous Functions:
        Pg Up.................CANCEL..................RESET
        Ctrl-F................ALT-F...................FIELD MARK
        Ctrl-D................ALT-D...................DUP
   **   ")"(Right ............")"(Right ..............Initial Sign On
        Parenthesis),         Parenthesis),
        repeatedly until      repeatedly until
        MDS-8070 responds.    MDS-8070 responds.

** (For Alanthus Protocol Converter Only)

Note: IBM 3270 KEYS are as the Alanthus Protocol Converter would recognize
      them.


                              APPENDIX A-11B

                  Special Function Keys - IBM PC (IBM 3101)

    The following table lists IBM 3270 special function keys in the left
 column, and in the right column the corresponding key (or multiple-key
 sequence) on the IBM PC terminal keyboard which will cause the MDS-8070
 to simulate the function performed by the respective 3270 key.
    Display fields which the host computer has defined as "intensified"
 are indicated by an exclamation point (!) in the display position
 preceding each field.


 IBM 3270                  IBM PC         IBM 3270                  IBM PC
Key Function             Equivalent      Key Function             Equivalent
***********************************      ***********************************
Program Attention Keys:                  Cursor Control Keys:
   ENTER.................Enter             Left...................Left Arrow
   PA1...................Ctrl-A A          Right..................Right Arrow
   PA2...................Ctrl-A B          Up.....................Up Arrow
   PA3...................Ctrl-A C          Down...................Down Arrow
   PF1...................Esc 1 Enter       NEW LINE...............Pg Dn
   PF2...................Esc 2 Enter       TAB RIGHT..............Tab Right
   PF3...................Esc 3 Enter       TAB LEFT...............Tab Left
   PF4...................Esc 4 Enter       Home...................Ctrl-Home
   PF5...................Esc 5 Enter     Editing Control Keys:
   PF6...................Esc 6 Enter       ERASE INPUT............Ctrl-Pg up
   PF7...................Esc 7 Enter       ERASE EOF..............End
   PF8...................Esc 8 Enter       INSERT MODE............Ins
   PF9...................Esc 9 Enter       DELETE.................Del
   PF10..................Esc 1 0 Enter   Miscellaneous Functions:
   PF11..................Esc 1 1 Enter     RESET..................Pg Up
   PF12..................Esc 1 2 Enter     FIELD MARK.............Ctrl-F
   PF13..................Esc 1 3 Enter     DUP....................Ctrl-D
   PF14..................Esc 1 4 Enter   s Print..................Ctrl-P
   PF15..................Esc 1 5 Enter   s IDENT..................Ctrl-T
   PF16..................Esc 1 6 Enter   s DEV CNCL...............Pg Up
   PF17..................Esc 1 7 Enter   * Refresh Screen.........Ctrl-Z
   PF18..................Esc 1 8 Enter   * Display Status Line....Ctrl-E
   PF19..................Esc 1 9 Enter   * Remove Status Line.....Ctrl-X
   PF20..................Esc 2 0 Enter   * Supervisor Req.........Ctrl-Y
   PF21..................Esc 2 1 Enter b#* Copy...................Ctrl-P
   PF22..................Esc 2 2 Enter  #* Printer Not Available..Ctrl-N
   PF23..................Esc 2 3 Enter  #* Printer Online.........Ctrl-O
   PF24..................Esc 2 4 Enter   * Remote Loopback........
 b TEST REQ..............Ctrl-A T        * Initial Sign On........")"(Right
 s SYS REQ...............Ctrl-A T                            Parenthesis), 
   CLEAR.................Home                                repeatedly until
 s ATTN..................Ctrl-A S                            MDS-8070 responds.



* These functions are not 3270-compatible, but are unique to the MDS-8070.
  Their functions are described in the MDS-8070 documentation.
# Shared Printer not fully supported - See Appendix-B.
b BSC protocol only.
s SNA protocol only.


Explanations of ESCape codes for 3101 EMULATION in PC-TALK
 
In this document the word ESCAPE refers to CHR$(27)
All characters in uppercase are included in the code.
All characters in LOWERcase are reference and NOT included in the code.
Plus signs are used to show that charcters are used together.
They are NOT part of the code unless specified.
(Ex. ESCAPE+A is equal to the BASIC code CHR$(27)+"A")




-> Move cursor to a position on the screen (LOCATE):

Format:  ESCAPE+Y+row+col

Remarks:  row  REFERS TO A CHARACTER FROM CHR$(32) TO CHR$(55) 
               CHR$(32) is equal to row 1 on the screen. 
               CHR$(55) is equal to row 24 on the screen. 
    
          col  REFERS TO A CHARACTER FROM CHR$(32) TO CHR$(111) 
               CHR$(32) is equal to col 1 on the screen. 
               CHR$(111) is equal to col 80 on the screen. 





-> Move cursor UP one location:

Format:  ESCAPE+A

Remarks:       This ESCape code moves the cursor UP one row.
               It is the same as pressing the UP ARROW key
               on the keyboard.




-> Move cursor DOWN one location:

Format:  ESCAPE+B

Remarks:       This ESCape code moves the cursor DOWN one row.
               It is the same as pressing the DOWN ARROW key
               on the keyboard.





-> Move cursor RIGHT one location:

Format:  ESCAPE+C

Remarks:       This ESCape code moves the cursor RIGHT one col.
               It is the same as pressing the RIGHT ARROW key
               on the keyboard.


-> Move cursor LEFT one location:

Format:  ESCAPE+D

Remarks:       This ESCape code moves the cursor LEFT one col.
               It is the same as pressing the LEFT ARROW key
               on the keyboard.




-> Erase until end of page:

Format:  ESCAPE+J

Remarks:       This erases from the current cursor position until
               the end of the page. On 3270 type terminals it performs
               as a Erase EOF key. 
               (Ex. If you are on col 3, everything from col 3 to col 80
                is erased.)




-> Clear the screen:

Format:  ESCAPE+L

Remarks:       This clears the screen and sets col and row to 1.





-> Goto Home address:

Format:  ESCAPE+H

Remarks:       This sets col and row to 1 without clearing the screen.





-> Turn 3101 emulation ON/OFF:   (NOT standard 3101 protocol)

Format:  ESCAPE+O+action

Remarks:       This turns the 3101 emulator off and on inside PC-TALK.
               If action is equal to "-" then 3101 is off. If action
               is equal to "+" then 3101 is on.