Lynx 1.3 - Full Streaming/Compression/CRC-32 Batch
                             File Transfer Protocol


          By Matthew Thomas - Copyright (c)1988 - All Rights Reserved



     What is Lynx?

     Lynx is a brand new high-speed data transfer protocol. I have
     designed it to be easy to use, memory efficient, and effective for
     transfers of any type of data, regardless of content.

     Lynx is based on the assumption that the connection between the two
     sites is capable of full-duplex transmission. Lynx will send a stream
     of data while simultaneously polling the receive buffer for any
     interruptions from the other end. On half duplex links, this will not
     work. But since almost all modems in use today are capable of full-
     duplex operation, this specification should not be a problem.

     The reason that Lynx makes full use of full-duplex operations is to
     insure optimum transfer speed. When transmitting information, Lynx
     spends very little time waiting for the other end to respond.  On
     certain occasions (after the file header is transmitted or after
     recovering from a line error) Lynx will wait for the other end to
     resynchronize. This handshaking is in the best interest all parties
     because when errors occur, loss of sync is quite possible if the
     proper hand is not shaken.




     What makes Lynx so 'optimal'?

     Well...it's free!  Actually, there are more important reasons.

        * Baud rates from 300 - 38400 bps

        * Support  of   COM1,  COM2,   and  COM3/4   under  the Everex
          Configuration.

        * Full line error protection with CRC-32 techniques.

        * Full streaming (full-duplex) transmissions.

        * Dynamic packet size from 128  to 1024 bytes. (Actually, for the
          technically inquisitive  users out there,  Lynx will drop to a
          64-byte packet if an error-prone situation becomes apparent.)

        * Run-Length-Limited  (is that what RLL  stands for?) compression
          of transmitted data.  Obviously, if a packet's size  can not be
          reduced  by  RLL  encoding,  it  will  be transmitted in it's
          original form, however inefficient it may be.

        * Resuming  aborted/crashed/hung-up   file  transfers.  This is
          similar to DSZ's resume feature.









     Now that I know what Lynx does, how do I use it?

     Since this is a public domain protocol, and I've already spent
     countless hours developing the actual code, I will allow you to find
     out for yourself the best ways to make use of Lynx.  A good 'hint
     sheet' is available by invoking Lynx without any parameters.

     A few things I should mention, though:

       Lynx resumes - The /R parameter MUST be used by the receiver in
                      order for a resume to take place.  The transmitter
                      will always respond to a resume request from the
                      receiver.  But the receiver will only send the
                      request if the /R switch has been used.


       Receiving    - When attempting to receive a batch of files using
         Files        Lynx, the user may only specify a path name in the
                      command line to tell Lynx where to place the
                      received files. For example:

                      LYNX r /1 /2400 c:\download\

                      will receive a batch of files using COM1 at 2400
                      baud, placing the received files in the sub
                      directory C:\DOWNLOAD.


      Sending       - The user may specify up to 9 filespecs (wildcards
       Files          are fully supported) when sending files.  A total of
                      35 files may be sent in one batch.


      Environment   - Lynx supports two environment variables for
       Variables      parameters:

                       DSZPORT - This may be 1, 2, 3, or 4
                                 Lynx will use the corresponding serial
                                 port if this variable is set.

                       DSZLOG  - If this contains a legal dos filespec,
                                 Lynx will maintain a DSZ compatible log
                                 file under the specified filename.

                      These variables are so named to allow some
                      compatibility with DSZ environment variables.



     Well, that's about it, I think.  I hope this protocol proves useful
     to many, as it results from hours of labor and headaches. (As do most
     programming projects!)

     I wish no remuneration for this code, but I ask that it remain
     unmodified in any way.  If you have any questions, feel free to leave
     me (Matt Thomas) mail on either PC ACCESS (414) 634-5776 or AIMS User
     Service (414) 634-5294 BBS's.  I'll attempt to answer all questions,
     but I offer no guarantees.