-----------------------------------------------------------------
     This  program  is made available free of cost  to  all  non-
commercial users. It is not to be sold or traded in any form. 


     Please  leave any questions,  suggestions and problems at my 
BBS:
          Fido (415)-864-1418

     MINITEL  is  a  stripped version of  TELINK.  The  following 
functions  have  been  removed:   text  download,   auto-dialing, 
telephone  directory  support,  SmartModem  modes  and  controls, 
console  control  character  processing,  configurable  keyboard, 
file transmission/reception statistics.
-----------------------------------------------------------------

MINITEL is an asynchronous communications program for any 
MSDOS  or  PCDOS machine.  (A version must be  configured  for  a 
particular machine.) 

MINITEL  can receive or transmit files in XMODEM,  MODEM7 
(batch)  or  TELINK modes.  TELINK mode is  described  in  detail 
later,  but  basically  it is a MODEM7 compatible  protocol  that 
supports DOS exact file sizes and dates.

This manual is divided into a number of sections:

Section 1  Operating TELINK
Section 2  Quick Command Summary
Section 3  Command Descriptions
Appendix A File Transmission Format
Appendix B File and Path names
Appendix C Command prompt Line Editing
Appendix D TELINK console details
Index

The  first  section walks you through operating  MINITEL,  
and gives you a feel of how it works.   Section 2 is a  one  page  
list  of MINITEL's  commands,    followed  in section  3  with  a  
complete description of each.  You will find all commands in the  
index. You do not need to read any appendixes to operate MINITEL;   
they  are provided  for more detailed  operating  and   technical  
information.

To   run  MINITEL,   you need (besides the computer)  64K   
of memory,   a  disk of some sort,  a serial port,  and a  modem.   
You  will  have  to refer to your modem  manual  for  details  on  
dialing and making connections.
1.00            O P E R A T I N G   M I N I T E L

MINITEL  is menu driven,   with all  commands  accessible  
with  two   keystrokes.   You   do  not need to  enter  and  exit  
"modes"  or levels to get where you want.  Most command keys  are 
mnemonic. 

Error  handling  is  simple,    straightforward  and  non-
dangerous,   especially in entering keyboard commands.  (Like all 
programs,    you  can  bash  diskfiles if you try hard   enough.)  
Error recovery usually consists of some default action;  entering   
a non-existent command results in a list of available   commands;   
entering  a  blank line at a prompt quits that command;   illegal   
baud rate  selections  result in  no  change,    etc.  All  error  
messages are  in plain English,   so you don't have  to  memorize  
secret codes.

Running MINITEL is easy: at the system prompt, type:

A: MINITEL <cr>

MINITEL  clears the screen,  displays it's signon on  the  
top two lines,  and waits for commands.  At this point,  anything  
you type goes directly to your modem;  for a SmartModem,  you can  
dial and make your connection.
Entering Commands:

MINITEL   provides  fancy line editing whenever you  need   
to enter filenames or whatever; see Appendix C for details. 

MINITEL  is always in communication mode;  if  the  modem 
were  to receive data,  it would be displayed on the screen  now,  
and you could type directly back to it. 

With  the  cursor still in the lower  left  corner,  type 
ESCape. The cursor now moves to the upper left corner, and types:

Command: _

If you wait a second or so, the menu is displayed.

Entering  one  of the command letters from the  menu  now 
executes  that  command.  (How to send an  ESCape?  Type  another 
ESCape.)  If  you type a key that's not a command,  MINITEL  will 
type  the menu again (if it's not already there),   display  your 
screen,  and return the cursor to where it came from. You can get  
the menu  at  any time by typing the ESCape key,    and   waiting   
about one  second.

If  you type the ESCape key,  followed by a  command  key 
within  one  second,  the  command will be  executed  immediately 
without  displaying the menu.  This provides an expert mode  once  
you remember the command keys.

2.00              C O M M A N D   S U M M A R Y

Here is a quick list of command available in MINITEL.

Text and character oriented commands.

ESC C Save all console conversation.
ESC S Stops the 'C' command.
ESC L Auto linefeeds on.
ESC M Disable Auto line feed (default)
ESC F Full duplex. (default)
ESC H Half duplex.
ESC ESC Send an ESCape.
ESC V Parity selection. (none, default)

File oriented commands.

ESC R Receive file(s) in selected mode
ESC T Transmit file(s) in selected mode
ESC N   Select a file transfer protocol

System and miscellaneous commands.

ESC ? List current MINITEL settings.
ESC Q Quit. Closes any text collection file.
ESC B Select a baud rate for the modem. Default is 300.
ESC Y List disk files, sizes and transmission times.

            C O M M A N D    D E S C R I P T I O N S 

All  of  the following commands act somehow on the  disk. 
Some  create files and write on the disk;  with these you can  do 
things like delete files or change their contents,  so some  care   
is required.

ESC Y List disk file information

The   'Y'  command is similar to a DIR command  from  the  
operating  system,   but   gives you more information.   You  are 
asked for  the name of files to look for;  entering an empty line  
is the same as *.*, like the DIR command.

Under  MSDOS  version 2.00,  you can  enter  a  path name, 
specifying the directory you want to look at. If you do not, only 
files  within the current directory are listed.  Wildcards cannot   
be used in the directory portion of the path name.

In  addition to the file names,   MINITEL gives  you  the 
file  size,   in  bytes,   and the time it would take to send it,   
at the current baud rate.(See the 'T' and 'R' file   transmission  
commands.)

The transmission times are of course approximate, because 
errors sometimes occur,  requiring blocks to be resent, and other 
variables in both computers. The guesses are a little on the safe 
side for that reason.  It also takes time for the person  running 
each  each  computer to type whatever is necessary to start  file 
transmission,   and  of  course  this cannot  be  accounted  for.  
Transmission  times are most accurate when sending more than  one 
file, using the automatic batch mode.

After all the files are listed, the total file count, and  
the total  size and transmission times for all of the  files   is  
listed.
ESC C Collect text

This  asks you for a file name,  then starts putting  all 
text  you  see  on the screen into  it.   Everything  the  remote 
computer   sends you is saved as is.   (Control-Z characters  are  
NOT  put  in the file if they appear from the modem  or  console;   
this prevents "lost" data.    Though one is put at the end of the  
file when it is closed.)

The  text  file  can be closed  by  the  S  command,   or 
automatically   by  the  ESC Q command.   You will get  an  error 
message  if you try an ESC C when one is already in effect.

Text  is  temporarily stored in memory;  every once in  a 
while it must be written out to disk to make room for more.  When 
MINITEL  is  almost out of room,  it sends  a  control-S  to  the 
remote  computer,   to tell it to pause sending data.   Up to  82 
characters after the control-S are collected,  to give the remote  
a chance to stop.  Then, the text is written out to the disk, and  
a control-Q  is sent to tell it that it may continue.    This  is  
done automatically by MINITEL. 

Most  remote  computers will pause when  a  control-S  is 
received;   if   it  does  not,   you will probably  lose  a  few 
characters.  On systems with hard disks, you won't lose more that   
10 or so; with mini-floppies, you may lose up to 40 or so.

If  the  disk fills up while collecting  text,  an  error 
message  will  appear at the top of the  screen.  If  the  screen 
happens  to  scroll while you're not looking,  you won't see  the 
message. Oh well.

When   MINITEL is first run,   it gets as much memory  as   
it can  (up to 64K) to use as the text buffer.   You can see  the  
amount available using the ESC ? command.   The only  thing  this  
affects  is  how  often  MINITEL must write saved  text  to   the   
disk;  the  more memory, the less often it must write it out.






ESC S Stop text collection

Stops the collection of text.  (The 'C' command.) You get   
an error  message if you're not  collecting  text.     Appends  a  
control-Z  to  the file,   flushes it and closes the disk   file,  
where  you  can type,  print or edit it.  If you forget  to  stop 
collecting,   MINITEL  will  do  it  when you exit  via  the  'Q' 
command.
ESC T Transmit file(s) 
ESC R Receive file(s) 

     The  T  (transmit)  and  R (receive) commands  are  used  to 
transfer files,  to a similar program running on another machine. 
Either   binary  or  text  files  can  be   transmitted.    Error  
detection  and recovery are done automatically.

There  are  a  number  of  ways in  which  files  can  be 
transferred; see ESC N for details. Selecting the right method is 
important, as transfers sometimes will not work. MINITEL tries to 
automatically  choose  the right transfer mode,  but  it  is  not 
always possible.

     Invoking  either command prompts you for files to be sent or 
received.  Except in XMODEM mode (again, see ESC N) you can enter  
any number  of  filenames,    where  each  can  contain  wildcard 
characters.  Separate each name with spaces commas or plus signs.  
The filenames can contain drive letters,  and pathnames on  MSDOS  
v2.00.

     The  default  mode on CP/M is MODEM7,  and on MSDOS  is  the 
TELINK mode.   The TELINK mode is identical to MODEM7,  except it 
"sneaks in"  information on exact file size and creation date. If 
you  use this  mode  with  MODEM7 running on the other  computer,  
that  computer   will  get four or six errors on the  first  data  
block,   by which  time  MINITEL will figure out that it will not 
accept   the  extra   information,  and finish the  transfers  in 
MODEM7 mode.

     All  display transmission status continually on the top  two 
lines.   The   current  block  number   being   sent,   estimated 
transmission  time  left,  name,  etc is displayed.  The time  is 
constantly  recalculated,  and may be blank if:  (1) less than  1 
second,  or (2) receiving a file where the file size is  unknown. 
EXAMPLES:

     The  following  are valid filenames that can be entered  for 
transmitting files. (XMODEM can only accept a single filename.)

     FOO.COM                            send one file
     B:FOO.COM                          send one file
     FOO.*                              one or more files
     B:FOO.*,XYZ.ASM                    one or more files
     FOO.COM,\BIN\*.COM,/WORK/*.ASM     many files
     AFILE.EXE,BFILE.DOC ANOTHER.FIL    many files

     These  are  valid entries for  receiving  files.  Note  that 
filenames  themselves  are ignored,  since the actual  names  are 
received along with the files.

     B:                                 put files on drive B:
     ?                                  files to default drive
     *                                  same as above
     \bin\                              put files in \BIN\
     foo                                in default drive 
     ESC N          Select file transmission mode


MINITEL  now  supports all popular  file  transfer  modes 
currently in use. These are:

        XMODEM One file at a time, popular on remote systems,
MODEM7 Similar to XMODEM, one or more at a time,
TELINK Similar to MODEM7, but sends DOS info.

In  addition,  transfers  can  be  done  with  the  older 
CHECKSUM  method,  or the newer,  more  reliable,  CRC  (Cyclical 
Redundancy Check). This of course makes for six different ways to 
handle files, but it's not really that bad.

When receiving file(s) (ESC R) you must select either CRC 
or  CHECKSUM properly.  Most systems that support CRC say so  when 
you  start the transfer.  If you get it wrong,  then you'll get a 
"timeout" or other error; change to CHECKSUM and it should work.

The  methods  and how to select one is  described  below; 
first, some suggestions on how to choose the right one.

BULLETIN BOARDS AND OTHER REMOTE SYSTEMS:

Most of these support only XMODEM, so there is usually no 
choice!  (Fido  supports all methods.) More and more systems  are 
supporting CRC mode;  MINITEL defaults to CRC mode. Try selecting 
XMODEM and CRC; if that does not work, try XMODEM and CHECKSUM.

TO ANOTHER COMPUTER OR SYSTEM USING MINITEL, TELINK, OR MODEM7:

Using  the TELINK method,  CRC vs.  CHECKSUM  is  handled 
automatically;  this  is  the  best way to  transfer  files  from 
machine to machine.  It handles multiple files,  etc so you don't 
need to do ESC T and ESC R for each file. If both have MINITEL or 
TELINK,  then use TELINK and CRC;  if either machine has an older 
MINITEL  or TELINK that does no support CRC,  it will  switch  to 
CHECKSUM automatically.

If  MODEM7 is used on one or the other,  you may have  to 
select CHECKSUM.  TELINK mode will switch to MODEM7 automatically 
if necessary.

SELECTING THE TRANSFER METHOD:

After  entering  ESC N,  you will see a small  menu.  You 
select a type by typing the first letter of a selection.  At  the 
left edge,  you will see the current setting;  just type the right 
letter until you see what you want,  then type [CR]. This setting 
is  also displayed by ESC ?  and also when actually  transferring 
files.

MODEM7:
     This is the most popular method used to transfer files,  and   
is available on almost all CP/M and MSDOS machines.   The  MODEM7 
compatible  programs  can transfer one or more files at  a  time, 
with  full  error detection and correction.  The  limitations  on 
MSDOS  are  that the original file creation time and  exact  file 
size are lost.  For text files this does not matter, but for data 
base and spreadsheet files, it can cause great problems.

XMODEM:
     Most frequently used on bulletin boards and the like,  it is  
the original MODEM transfer protocol.   It can transfer only  one  
file  at  a  time,    and  the  user  must  enter  the   filename 
specifically.  (No  wild card characters.) It is included  mostly  
for completeness,   and should only need to be used for computers  
that do not support MODEM7 or TELINK modes.

TELINK:
     The TELINK mode is an extension of the MODEM7 protocol,  but 
includes extra information on each file sent.  After the filename   
is sent,  the file size,  creation time and date are sent  before   
the first data block.    If MINITEL receives this block,   it  is  
used  to exactly duplicate the file on the receiving end.

     This mode is still compatible with the MODEM7 mode. However, 
MODEM7  will get four or six errors while transferring the  first 
file,   while   MINITEL  figures out that it cannot  accept  this 
data.   If  it   cannot  be accepted,   then  MINITEL  will  stop  
sending   this  info,  and will operate for the rest of the files  
in MODEM7 mode.

CRC / CHECKSUM:

Entering  C  at  the prompt will toggle between  CRC  and 
CHECKSUM.   The   CRC  method  is  a  very  reliable  method   of 
transferring files; the worst error rate is 99.9969% reliability! 
CHECKSUM is probably about 95% or more accurate. Use CRC whenever 
possible,  CHECKSUM  only  if CRC isn't supported  by  the  other 
computer.
The  following commands control the way MINITEL  acts  to  
the remote computer,   and you. All of these are "not dangerous",  
i.e. you cannot wreck anything with them.

ESC ?List MINITEL status

The  current  settings  of the commands  in  MINITEL  are 
listed  on the screen, like so:

<Full, half> duplex(ESC F, H)
Auto linefeed <on, off>(ESC L, M)
The cursor is at line 10 column 23
Either:
*Collecting text in file TEXT.FIL,(ESC C, S)
* 4022 saved so far, room for 18101 more 
Or:Not collecting text
Currently <300, 1200, 9600> baud(ESC B)
<TELINK,  MODEM7,  XMODEM> file transmission(ESC N,J)
<no, odd, even> parity selected(ESC V)

Most   of  these can be changed via a  MINITEL   command.  
The command  is listed to the right of each,   above.  Others are 
just internal status: they are:

The cursor is at line <n> column <n>

This  just tells you where the cursor is.  Some  bulletin 
boards  and  editors  require  you to fit  typed  lines  in  some  
arbitrary  line length;   with this you can see how close to  the  
end you are. It is updated every time you type a key.

Either:Collecting text in file TEXT.FIL,
 4022 saved so far, room for 48101 more in memory
-or-Not collecting text

If  you  have not started text collection with the ESC  C 
command,  you  will get "Not collecting text",  which means  just 
what it says.

If  you  are collecting text,  MINITEL will tell you  the 
name  of the file being used,  and some simple statistics on  it.  
The "...  saved so far" is the number of characters saved in  the 
disk   file.  The  "room  ..." message tells you about  how  many 
characters   will   be  saved in memory before they  need  to  be 
written   out  to  disk.   You do  not ever need to  worry  about  
the   numbers  here;   MINITEL automatically takes care of saving 
text in the disk file.  (See the ESC C command description) 
ESC ESCape

Not  really  a command,  it just sends an ESCape  to  the 
remote. The cursor will still go up to the command area, but will   
go right back down.


ESC F Full duplex
ESC H Half duplex

Changes  the  line operating mode.  The default is  Full. 
Half  duplex caused keyboard characters to be displayed  as  they  
are typed.

ESC L Enable Auto linefeed
ESC M Disable auto linefeed

When enabled, causes a line feed character (control-J) to   
be typed after each carriage return typed. This is independent of   
half duplex. The linefeed is sent to the remote.


ESC V Parity selection

The  default  is no parity.  Parity is  generated  within 
MINITEL, and  is  either none,  even or odd.  If even or  odd  is 
selected,   the   parity  bit replaces bit 7 of  the  data  byte.  
(Obviously   only  7  bit  data can be  sent.)  Parity  will   be  
suspended when file transmission or reception is used.

ESC Q Exit to DOS

The  'Q' command exits MINITEL,  and returns  control  to 
DOS.   If  text  collection  is on (via the 'C' command) text  is  
saved  before exiting.

CAUTION:
You must remember to disconnect from the remote computer. 
MINITEL cannot do it when you Quit.  You will still  be connected  
to the remote computer.

Of you do quit,  (to change diskettes,  or whatever) then  
run MINITEL again,  do not forget to set the baud rate again,  as  
MINITEL cannot remember what it was set to when you  exited,  and   
it always selects 300 baud when started.

ESC B Baud rate

Tells you the current baud rate,  and lets you change it. 
Only 300,  1200 and 9600 are implemented.  A blank line or a  bad 
selection results in no change.  Once you type CR, it changes the 
rate, and displays the rate now in effect. 

     MINITEL  supports all popular file transfer  modes:  XMODEM, 
MODEM7, TELINK, in CRC or Checksum modes.

All  use  an identical technique to  transmit   the  data   
in   the   file;    the  difference is that   batch   mode   also  
transmits  the  file  name,   and there is a method to  tell  the  
receiver "no more files".

Batch mode operates in the following manner:

Send filename,
Send data,
Send end of file,
Send filename,
Send data,
Send end of file,

....

Send "no more files".

Single file mode is simply:

Send data,
Send end of file.


BATCH MODE FILENAMES:

In  batch  mode,  the file name is sent before the  data. 
When  the  receiver is ready,  it sends a NAK  character  to  the 
transmitter,  telling it that it's ready to receive the file. The 
transmitter then sends an ACK to acknowledge that.

The  11 filename characters are sent one at a  time,  and  
the  receiver  acknowledges  each by sending an  ACK  after  each 
character. After the last one has been sent, the transmitter then 
sends an ___,  indicating end of name, at which time the receiver 
sends  a checksum of all the characters it's received so far.  If  
the checksum matches the transmitter's checksum,  the transmitter  
sends an ___,  indicating filename sent and received properly. If   
at any point during this something goes wrong,   the  transmitter   
sends an ___,  indicating a bad transmission,  and both computers   
abort.

If the first filename character is an EOT,  it  indicates 
that  there  are no more files,   i.e.  end of batch  mode.  Both 
computers are then finished with the file transmissions.
SINGLE FILE TRANSFER and BATCH MODE DATA TRANSFER

File  data  is sent 128 bytes at a time,   in a  132 byte 
block. After a block is sent to the receiver, the receiver either 
acknowledges  good or bad reception of the block.  If  good,  the 
next  block is sent,  otherwise the block is retransmitted up  to 
some predetermined number of times. Once the entire file has been 
transmitted,  an  end  of transmission character  is  sent.  This 
should be also acknowledged by the remote.

The   first  character  sent  by  the  file   transmitter  
determines  what  kind of block it is;  an ASCII SOH (01 hex)  or 
Start  Of Header,   indicates an upcoming block,  and an EOT  (04 
hex), or End Of Transmission, means no more blocks. 

If  the first byte of the block is an SYN,  it  indicates 
it's a TELINK extended information block.  The 128 byte data area 
then  contains extended system information.  The first four  byte   
are  the file size,   in bytes,   and the next four bytes contain 
the  MSDOS creation date and time.   This block is only sent once  
per   file,  just be fore the first data block.  If the  receiver 
does  not  properly acknowledge this block (i.e.    MODEM7  thinks 
it's   a   bad  block) TELINK will not make further  attempts  at 
sending  it.    In  this  case,   TELINK will write all  received 
data  blocks as is  to  the disk,  which will cause the file size 
to  be  rounded off to the  next highest multiple  of  128  bytes 
(like MODEM7).   If the file size is received  properly, the file 
size will be exact.

The receiver uses one of two ASCII characters to indicate  
the success  of  the block just  transmitted:   ACK  (06  hex)  to 
acknowledge  correct  reception,   or  NAK  (15  hex),   Negative 
Acknowledgement, to indicate the block was received incorrectly.

Each   block   contains  a  block  number,   which   (not 
coincidentally)  corresponds to a CP/M file record number.  There  
are 128 data bytes per block,    and all other bytes in the block  
are overhead.

The data block format is like so:

 SOH SEC /SEC data0 data1 ... data126 data127 CHKSUM
or      SOH SEC /SEC data0 data1 ... data126 data127 CRCH CRCL

Where:

SOH is the ASCII Start Of Header character,

SEC is the 8 bit disk record number,

/SEC  is  the  ones complement of SEC,  the  disk  record 
number, used for error checking. (later...)

data0 ...  data127 are the 128 bytes of data.  These  are  
all 8 bit quantities, with no constraints as to the contents.

CHKSUM  is an 8 bit checksum of the 128 data  bytes.  The 
idea  is that the receiver makes it's own check sum of the  data, 
adds it to the CHKSUM, and the result should become zero. This is  
one  of  the  criteria  used  in selecting  ACK  or  NAK  as  the  
acknowledgement.

        CRCH is the upper 8 bits of the CRC, and
        CRCL is the lower 8 bits.
     Like  the  checksum  method,  CRC is used  to  validate  the 
contents of the data block. The CRC is a polynomial that the data 
gets passed though. The CCITT method is used, which is:

               X^16 + X^12 + X^5 + 1

     Each  data  byte is passed through this,  and the result  is 
sent to the receiving computer, which makes the same calculation. 
if both match, then the block was good. 

     CRC  vs.  CHECKSUM method is selected just before  the  file 
transfer  starts;  when the receiving end is ready,  it sends  an 
initial character to tell the sender it is ready.  This character 
(sent  by the receiver) determines the transfer mode:  NAK  means 
CHECKSUM, C (capital C) means CRC. (Older systems don't recognize 
the  C  character;  it  waits for the  NAK,  which  never  comes; 
therefore  it  is  important  to select the  right  mode  on  the 
receiving end.

     The  accuracy  of the CRC method is:  detects  100%  of  all 
single  and double bit errors,  all errors with an odd number  of 
error  bits,  all burst errors of length 16 or less,  99.9969% of 
all  17 bit error bursts,  99.984% of all possible  longer  error 
bursts.

     The  original XMODEM CRC method and polynomial algorithm was 
done  by Paul Hanksknecht,  of Carpenter  Associates,  Bloomfield 
Hills, MI.

MINITEL   can   be used on any version of  MSDOS  or   PC  
DOS.  Version  2 or higher of either DOS,   however,   has a more 
complex file structure. MINITEL supports both.

Under older DOS's,  (before version 2) only "normal" file 
names can be used: The format is:

d:filename.ext

Where:

d:is an optional drive specifier,
file name is an 8 character maximum name,
* or ? being allowed for certain
commands,
.ext is an optional filename extension,
wildcards * and ? the same as in
'filename'.

FRUMP.ASM, *.COM are typical examples.

Under later DOS's,  however,  full path names can be used 
wherever a filename is asked for. This takes the form:

pathname\filespec

Where:

path name is a valid path name specifier. It
may contain one or more directory
specifiers, separated by a \, and also / if the 
switch character has been set to - in CONFIG.SYS.

filespec is a "normal" filename, described 
above.
/BIN/*.COM
/MARCH/DOG/BARF are typical examples.

You  can  of course enter a "simple"  filename  in  newer 
DOS's, as long as the file is in the current directory.

Any  filename  typed  in  to  MINITEL can  be  up  to  80 
characters long.   In any case,   see the appropriate DOS  manuals 
for filename  and path name restrictions and operation.

Obviously some commands will require more input than just  
the  ESC/command  key;    filenames and baud rates are  the  most  
common. MINITEL prompts you for these as necessary. When ever you  
are prompted for a filename or whatever,   you enter it by typing   
the name,    and  a <cr> when done.  Up until you type the  <cr>,  
however, you can do some simple editing of the line.

Control keys are used to edit the line. Control keys that 
aren't    used   by MINITEL are ignored.     The following   are  
the control keys used:

^C Delete the entire line
^X Same as ^C
^U Same as ^C
^Y Same as ^C
^H Delete the last character typed
^G Same as ^H
^S Same as ^H
DEL or RUBOUT
Same as ^H

Carriage return (CR),  linefeed (LF) and ESCape (ESC) are 
used to enter the line, executing it.

Two more special keys are:

^R Retype the previous line
^D Retype the last deleted character

These  can be useful if you want to enter the same  thing  
as last time.  If you delete the line (using ^C, ^X, etc) you can  
get it all back ("undelete" the line) by typing a  ^R,   and  the  
last character by typing a ^D.   Also,  you can get back the line  
you used for the last command by typing ^R before anything  else.  
After  you type any other key,  (except an editing key) you lose  
the old contents.

All  commands  can be aborted by entering a  blank  line. 
Either enter <cr> at the prompt,  or delete the line,  then  type 
<cr>.

MINITEL   does   some processing of the  characters   you  
see displayed  on  the console.   None of this processing affects  
the text collected in a disk file using the ESC C command.

This processing is done to ensure a "clean"  screen,  and  
to make sure that MINITEL can keep track of where the cursor is.

All  characters  have bit 8 stripped off,  to  make  sure 
they're 7 bit ASCII.  Some terminals respond differently to 8 bit 
characters,  and some strip them internally. In particular, files 
created by popular editors such as WordStar set bit 8 on carriage 
returns   (CR  ) to make "soft paragraphs",   and  MINITEL  would  
not otherwise know it was a carriage return.

Certain   code  sequences  make a mess  of  the  terminal  
display;   these  characters can be filtered out using the ESC  I  
command,   and  not sent to the display.   Mainly this  is  the 
control-Z character,   which  clears  the screen on many  popular  
terminals, such  as the ADM-3A,  most Televideo models,  and  the  
Hazeltine Esprit. 

Tabs  are  expanded within MINITEL to space over  to  the 
next  tab column,   which are fixed at every eight columns.  Tabs 
are put  as is into any ESC C disk file. 

None  of this filtering ever affects characters put  into  
the text collection file, if one is used.

        Auto linefeed........................... 4,10,11
        Auto-dialing............................ 1
        Baud rate............................... 4,11
        Binary.................................. 7
        Collect text............................ 6
        Collecting text......................... 6
        Command key............................. 3
        Command letter.......................... 3
        Commands................................ 2
        Control-J............................... 11
        Control-Q............................... 6
        Control-S............................... 6
        Control-Z............................... 6,6,17
        CP/M.................................... 8
        CR...................................... 17
        Cursor.................................. 3,3
        DEL..................................... 16
        DIR command............................. 5
        Disk.................................... 1,6
        Error detection......................... 7
        Error handling.......................... 2
        Error messages.......................... 2
        Error recovery.......................... 2
        ESC ?................................... 4,6,10
        ESC B................................... 4,11
        ESC C................................... 4,6,6,10,17
        ESC ESC................................. 4,11
        ESC F................................... 4,11
        ESC H................................... 4,11
        ESC I................................... 17
        ESC L................................... 4,11
        ESC M................................... 4,11
        ESC N................................... 4,7,8
        ESC Q................................... 4,6,11
        ESC R................................... 4,7
        ESC S................................... 4,6
        ESC T................................... 4,7
        ESC V................................... 4,11
        ESC Y................................... 4,5
        ESCape)................................. 3
        Exit to DOS............................. 11
        Expert mode............................. 3
        File count.............................. 5
        File size............................... 5
        File transfer protocol.................. 4
        File transmission mode.................. 8
        Filenames............................... 7
        Files................................... 5
        Full duplex............................. 4,11
        Half duplex............................. 4,11
        Memory.................................. 1,6,6
        Menu.................................... 2,3,3
        MINITEL................................. 1
        Modem................................... 1,3
        MODEM7.................................. 1,7
        MODEM7:................................. 8
        Parity.................................. 4,11
        Pathname................................ 5
        Quit.................................... 4
        Receive file(s)......................... 4,7
        RUBOUT.................................. 16
        SmartModem.............................. 1
        TELINK.................................. 1,7
        TELINK:................................. 9
        Text.................................... 6
        Text collection......................... 6
        Text download........................... 1
        Text file............................... 6
        Transmission status..................... 7
        Transmission time....................... 5
        Transmission times...................... 5
        Transmit file(s)........................ 4,7
        Wildcards............................... 5
        XMODEM.................................. 1,7
        XMODEM:................................. 8
        ^C...................................... 16
        ^D...................................... 16
        ^G...................................... 16
        ^H...................................... 16
        ^R...................................... 16
        ^S...................................... 16
        ^U...................................... 16
        ^X...................................... 16
        ^Y...................................... 16