KERMIT

Larry Jordan

The first time I heard the term KERMIT used in association with data
communications I couldn't help but think of the funny green frog. I had
difficulty taking a file transfer utility seriously that reminded me of the
amphibian. The more I learned about KERMIT, however, the more I liked it.

KERMIT is a file transfer protocol similar to XMODEM. Like XMODEM, KERMIT
transfers files between computers in blocks or packets and each packet is
checked for communication errors. The transmitting computer calculates a
checksum based on the contents of each packet and sends the checksum along with
the packet. Like XMODEM, the receiving computer calculates its own checksum
based on its contents of each received packet and compares the value to the
received checksum. The receiving computer requests a retransfer of a packet
when the received checksum does not match the calculated checksum. Like XMODEM,
KERMIT repeats this process packet-by-packet until an entire file is
transferred or until the file transfer is abnormally aborted.

For XMODEM users, this KERMIT block mode transfer sounds all too familiar. The
users of PC-TALK.III and CROSSTALK XVI have watched block counts methodically
increment as utility and other assorted software moved from a distant TCOMM or
RBBS-PC to a local floppy disk. These communications users have confidence in
files transferred using XMODEM because they know Ward Christensen designed the
protocol to ensure better than 99.6% error-free transmission. Many XMODEM
enthusiasts will question the need for yet another public domain protocol, but
there is a legitimate need for KERMIT.

The XMODEM protocol requires a full 8 data bits to properly transfer a file.
The communications software and hardware on both ends of a communications link
must be set for no parity error- checking and 8 data bits. When these
parameters are properly set, XMODEM simply divides a file into 128 byte (each
byte contains 8 bits) blocks and moves the file one block at a time.  There is
no conversion or translation of the data.  The file may contain text, data or
binary program execution code. WordStar files and compiled source code are
transferred "as is" and can be used in the receiving computer just as they were
used in the transmitting computer, assuming the computers are compatible.

Unfortunately, the ubiquitous XMODEM cannot perform its majestic work with some
computer systems. Some computer front-end processors can only operate using 7
data bits. Other computers that can operate at 8 data bits cough and choke when
they receive bit patterns that match control characters (characters with ASCII
values between 0 and 31 and the DEL character--ASCII 127). And finally, some
modems lock up when they receive bit patterns that appear to be command mode
signals. To accommodate these cranky but useful devices (that are already paid
for) it is necessary to use an asynchronous file transfer protocol that ensures
"error- free" transfer while overcoming the equipment limitations. Columbia
University has developed and released a public domain protocol called KERMIT
that accomplishes all these objectives.

KERMIT can handle any kind of file and can be used with just about every kind
of computer. The protocol is capable of converting all data into the equivalent
of printable 7-bit ASCII characters and numbers when necessary. When KERMIT is
forced to communicate 8-bit binary files, it simply sends the extra bit by
itself. This "prefixing" or "8-bit quoting" process overcomes the 7-bit
limitation of some old mainframe front-end processors. When Kermit is asked to
transmit a control character, it encodes the character in a process which
produces a printable character that can pass through control character
sensitive devices without a hitch.  In both of these cases, the KERMIT on the
receiving end of the file transfer has to work hard to decode each block of
data before it is transferred from the KERMIT program to disk.

Because of the relatively slow speed of microprocessors (yes the IBM PC is
slower than the VAX 11/780) most microcomputer KERMIT implementations are
written in assembly language. Implementations on faster machines are often
written in PL/1 or some other high-level language with good string handling
capabilities.  The original KERMIT was written in C to operate under the UNIX
operating system, but other more recent implementations are generally written
in the most powerful and productive language available on a specific computer. 
A partial listing of KERMIT implementations are shown in Figure 1.

KERMIT has four other advantages over XMODEM.  First, it allows wildcard file
transfers.  An asterisk can be used in place of several file name letters in
order to sequentially and automatically transmit many files with common
filenames or extensions.  XMODEM has to be manually restarted at the end of
each file transfer.  Second, minicomputer and mainframe versions of KERMIT
often include a SERVER mode.  After the host KERMIT is placed in the SERVER
mode, the local KERMIT performs all handshaking necessary to both send and
receive files--the remote host KERMIT is taken over by the local KERMIT and is
slave to the local KERMIT's wishes.  Both the KERMIT wildcard and SERVER
feature are time savers when several files have to be transferred. Third,
Kermit saves time during ASCII file transfers by supporting data compression.
Characters that are repeated in a file are only sent once for each repeat
sequence. This often results in a 30 percent faster file transfer for Kermit
compared to Xmodem for the same file. Finally, Kermit avoids the "deadly
embrace" that can abnormally abort XMODEM transfers when handshake character
synchronization are thrown off by bad telephone connections.

Will KERMIT displace XMODEM for error-checked file transfers? Not in the near
future, but perhaps it will eventually win out as the public domain protocol of
choice. It is already in use in many universities, and several major federal
government organizations have standardized on the protocol. The National
Institute of Health in Bethesda has standardized on KERMIT for file transfers.
THE SOURCE has also implemented KERMIT and supports the protocol for their
subscribers. Both the BLAST and the Microcom Networking Protocol file transfer
techniques that are being widely touted as the future national standard for
asynchronous communications have characteristics that prevent their use with
certain computers without special add-on equipment. Kermit does not suffer this
limitation.

It is often vitally important to move data from one computer to another with
assurance that errors are not introduced in the data as a result of the
transfer process.  When such a transfer has to be done using the asynchronous
method of communications, KERMIT is a good candidate for the job.  It is
available at reasonable cost, and it is a proven protocol.  If it has not
already been implemented for a specific hardware configuration, it can be
implemented quickly because the protocol is well documented. The protocol
documentation manual comes complete with a full source code listing of a UNIX
KERMIT written in C.

Ordering Information

The KERMIT software is free and is distributed by Columbia University. The
university is not, however, set up to distribute free software on the scale
required for KERMIT. Therefore, to defray costs for media, printing, postage,
labor, and computing resources, the university requests a moderate donation
from sites that request KERMIT directly. The schedule is as follows:

       Complete KERMIT Distribution   $100.00
         (Tape, Users Guide, and Protocol Manual)

       Printed Documents      $5.00 each
         (Users Guide, Protocol Manual, or Any Source Listing)

Other sites are free to redistribute KERMIT on their own terms, and are
encouraged to do so, with the following stipulations: KERMIT should not be sold
for profit; credit should be given where it is due; and new material should be
sent back to Columbia University at the address below so that we can maintain a
definitive and comprehensive set of KERMIT implementations for further
distribution.

To order KERMIT from Columbia University, send a letter requesting either:

   (a) The manuals or source listings you desire (specify each one), or
   (b) A 9-track magnetic tape in one of the following formats:

      System    Tape Format              Densities
      TOPS-10   BACKUP/Interchange,      Unlabeled 800, 1600
      TOPS-20   DUMPER, Unlabeled        800, 1600
      IBM VM/CMS  EBCDIC, CMS Format     1600, 6250
           or EBCDIC, OS Standard Label  1600, 6250
      Other    ASCII, ANSI Label, Format ``D'' 800, 1600

      Specify system, format, and density. One copy of each
      manual is included with the tape. The University supplies
      the tape, packaging, and postage.

Columbia University can only make tapes in the formats listed above. They
cannot produce floppy disks; bootstrapping procedures are provided to allow the
microcomputer versions to be downloaded from the mainframe for which the tape
is produced. The tape includes all source programs, documentation, and, when
practical, binaries or hex.

Send your letter to:

       KERMIT Distribution
       Columbia University Center for Computing Activities
       7th Floor, Watson Laboratory
       612 West 115th Street
       New York, N.Y. 10025

Please list the machines and operating systems you expect to run KERMIT on. You
should also specify the tape format or the listings desired. Make checks
payable to Columbia University Center for Computing Activities.


Another Alternative

You may also obtain a working version of KERMIT and the complete KERMIT users
manual and protocol documentation from the CAPITAL PC Public Domain Software
Software Library. To get the two KERMIT diskettes by mail send a $10 check made
out to CAPITAL PC to the following address:

                CAPITAL PC
                Public Domain Software Library
                P.O.BOX 6128
                Silver Spring, MD 20906

Be sure to ask for the "KERMIT" diskettes and include a return mailing label.
CAPITAL PC provides the diskettes and the mailers at no extra cost. These
diskettes will be available by mail order only because of the limited demand
expected for them.


---------------------------------------------------------------
<<Larry Jordan is a freelance writer and a communications and data base
management system consultant with NUS Corporation. He coauthored the book
>>COMMUNICATIONS and NETWORKING for the IBM PC,<< published by the Robert J.
Brady Company and has just completed another book titled >>IBM PCjr
COMMUNICATIONS<< which will also be published by the Brady Company.>>





-------------------------------------------------------------------------

                 Operating  Source
Machine          System     Language    Done By    Service   Capabilities
---------------  --------   ---------   ---------  -------   ------------
DECSYSTEM-20     TOPS-20    MACRO-20    Columbia   R L U S   T F I W D E
DECsystem-10     TOPS-10    MACRO-10    Stevens    R L       T F     D E
IBM 370 series   VM/CMS     370 ASM     Columbia   R           F   W   E
(various)        UNIX       C           Columbia   R L       T     W D
VAX-11           VMS        Bliss-32    Stevens    R     S   T F   W D E
PDP-11           RT-11      OMSI Pascal Toronto/CU R L             W D E
IBM PC           PC DOS     8086 ASM    Columbia     L U       F I W D E
Heath/Zenith 100 MS DOS     8086 ASM    CU/Stevens   L U       F I W D E
DEC VT180 Robin  CP/M       8080 ASM    CU/DEC       L U       F I W   E
DEC Rainbow 100  CP/M-86/80 8080 ASM    CU/DEC       L U       F I W   E
DEC DECmate II   CP/M       8080 ASM    CU/DEC       L U       F I W   E
Heath/Zenith 89  CP/M       8080 ASM    CU/DEC       L U       F I W   E
Heath/Zenith 100 CP/M-85    8080 ASM    CU/Stevens   L U       F I W   E
Apple II/Z80     CP/M       8080 ASM    CU/DEC       L U       F I W   E
TRS-80 II        CP/M       8080 ASM    CU/Cerritos  L U       F I W   E
Osborne 1        CP/M       8080 ASM    CU/NIH       L U       F I W   E
Superbrain       CP/M       8080 ASM    Columbia     L U       F I W   E
Vector Graphics  CP/M       8080 ASM    Columbia     L U       F I W   E
Telcon Zorba     CP/M       8080 ASM    CU/Stevens   L U       F I W   E
Ohio Scientific  CP/M       8080 ASM    Columbia     L U       F I W   E
"Generic"        CP/M       8080 ASM    CU/DEC       L U       F I W   E
Apple II         Apple DOS  CROSS       Stevens      L         F       E

Legend:

CU -- Columbia University
DEC -- Digital Equipment Corporation
Stevens -- the Stevens Institute of Technology
R -- it can act  as  a  Remote  Kermit  (the  object  of  a connection)
L -- it can act as a Local Kermit (initiate a connection to a
     Remote Kermit via a CONNECT command)
U -- it can be the User of a remote Kermit server
S -- it can act as a Server
T -- it can time out
F -- it can take evasive action to avoid filename conflicts
I -- it can communicate with an IBM mainframe
W -- it can do "wildcard" sends
D -- it has a Debug mode that can display the packet traffic on the screen
E -- it can exchange Error messages with another Kermit
---------------------------------------------------------------------------
Figure 1. KERMIT Implementations.