1
:
$**$ MARGIN=.6
 
 
                 RUNNING MTS GRAPHICS PROGRAMS ON THE IBM PC
 
  1. Introduction
 
     This  document  describes how graphics programs (e.g. *PLOTSEE)
  that produce graphics on a TEKTRONIX 4010 series terminal  may  be
  run on an IBM PC with output on an attached graphics monitor. This
  is achieved by use of TEKTRONIX 4010 terminal  emulation  software
  (TEKEMUL)  running  on  the PC. This program communicates with MTS
  and causes the TEKTRONIX ASCII codes from MTS  to  be  interpreted
  and displayed on the monitor. Thus a user needs a graphics monitor
  in order to use the system. TEKEMUL is written in complied  BASIC.
  The structured nature (as much as BASIC permits) of the program is
  intended to allow it to be adapted to other micro-computers in the
  future.
 
  2. Using TEKEMUL to Output MTS Graphics on the PC
 
     Here  we  assume  that  the  user  has  some  familiarity  with
  operating the IBM PC. The  emulation  program  displays  graphical
  information  in the high resolution mode of the computer. Thus the
  IBM colour/graphics monitor card and a graphics  monitor  must  be
  attached  to  the  IBM  PC  in order that the facility can work as
  intended.
 
     Upon inserting the disk containing TEKEMUL into the disk  drive
  one  merely  types  in  "TEKEMUL".  This  command loads and begins
  executing the emulator program.
 
     The program is of an interactive nature making it quite easy to
  use. The following describes the use of the TEKEMUL program:
 
     a)  A general instruction menu is displayed. This explains some
     of the operational details on how the program is  to  be  used.
     Pressing any key allows one to continue on.
 
     b)  A  communication set-up menu is then displayed. The default
     parameter values for baud rate, parity, data size,  and  number
     of stop bits is displayed in bold face. It is up to the user to
     ensure that the communication  parameters  are  correct  before
     continuing.  For  example,  he should insure that the baud rate
     given to the program is the same as the baud rate of  the  line
     that communicates with MTS.
 
     Changing  the  communication  parameters  is a simple matter of
     entering the new value of the parameter in  place  of  the  old
     value.  If  all of the parameters are correct the user enters a
     "Y" to indicate that the parameters displayed are correct.  The
     message  "Time  to  flick  your  data  set now..." is displayed
     momentarily and then the screen is cleared. It is at this point
     that the user initiates the connection with MTS.
1
 
 
 
     c)  The  standard  MTS header should be displayed at this time.
     When prompted for terminal-id, you should respond with "T4010".
     This  signifies  to  MTS  that you have a Tektronix 4010 series
     terminal. You can now sign onto MTS in the usual manner.
 
     d) TEKEMUL at this point in time is emulating a  simple  "dumb"
     terminal;  it  is  not  emulating  the Tektronix 4010. Thus any
     attempt to run a graphics program will yield erroneous results.
 
     The Tektronix emulation phase is initiated by  pressing  F9  on
     the keyboard.
 
     e)  Pressing F9 yields another menu which asks you what type of
     display monitor(s) you have. Enter "a", "b", or "c".  And  asks
     whether  you want to use *IG or *PLOTSEE. Enter "c" or "d". And
     finally it prompts you fßr the object module that will generate
š     the  graphics.  You  may press the enter key if you are running
     *PLOTSEE.
 
     f) The program then switches to the color monitor (if  you  are
     not already on it) and issues the MTS RUN command in the form:
 
           $RUN -LOAD#+*IG
 
               or
 
           $RUN *PLOTSEE
 
     depending  on  which  of  the two facilities you selected. When
     your  graphics  program  has  completed  running  you  will  be
     returned to MTS.
 
  3. Running More Than One Graphics Program
 
     Once  you  have  been<eke>  returned to MTS you can run another
  graphics program in one of two ways. You can (a) issue an MTS $RUN
  command directly or (b) press F9 once again.
 
     The  MTS  $RUN  command will work directly since you previously
  pressed F9. Remember that F9 places  you  in  Tektronix  emulation
  mode  and onto the color monitor. Thus any graphics codes intended
  for a Tektronix 4010 will be interpreted and executed by TEKEMUL.
 
  You may also press F9 again to continue having graphical  programs
  run.
 
  4. Exiting the Emulator and the Color Monitor
 
     Pressing  F8  on  the  keyboard  will  transfer you back to the
  monochrome monitor ( if your system has one ). It will  also  take
  you out of Tektronix emulation mode but will leave you on MTS.
 
1
 
 
 
 
  5. Exit to DOS
 
     Pressing  the  F10  function  key  will  cause  the  program to
  transfer control back to the monochrome monitor ( if  your  system
  has  one  )  and will end the TEKEMUL program, leaving you back in
  DOS. It will not explictly sign you off MTS. You must either  sign
  off yourself or disconnect the line.
 
  6. System Overview
 
     TEKEMUL  accepts  Tektronix  4010 codes and plots the graphical
  information represented by these on the color  monitor.  Figure  1
  illustrates how the system works.
 
 
 
        --------------------
        | Graphics Program |
   MTS  |        |         |
        |  Tektronix 4010  |
        |       codes      |
        --------------------
                 |
           Communication
                line
                 |
        ------------------------------
        |           TEKEMUL          |
        |              |             |          -----------
   IBM  |   ----------------------   |          |  Color  |
   PC   |   |                     |  |----------| Monitor |
        |  Communication  Tektronix  |          -----------
        |     Program        Code    |
        |                Interpreter |
        ------------------------------
 
  Figure 1 - System Diagram
 
     To get MTS graphics on the PC color monitor, we  have  to  have
  two  programs running; one is the graphics program on the MTS side
  and the other is TEKEMUL in the PC. The latter allows the user  to
  connect  and sign on to MTS. At this stage no graphics is done yet
  and the PC simply acts as a regular  terminal  with  the  help  of
  TEKEMUL.  Once  signed on the user can run the graphics program on
  MTS (such as *IG or *PLOTSEE) that generates  the  Tektronix  4010
  codes.
 
     As MTS sends out the Tektronix 4010 codes, the emulator program
  on the IBM PC interprets the information and produces a picture on
  the monitor.
 
1
 
 
  6.1 General System Information
 
     The  information  passed  to the Tektronix emulation program is
  the same as that which would be passed to a Tektronix 4010  series
  terminal.
 
     Plotting  of graphical information on the IBM PC is done in the
  high resolution mode of the BASIC compiler. Thus a  color  monitor
  hooked up to the IBM color monitor adapter must be used.
 
     The  resolution  of  high  resolution mode on the IBM PC is 640
  horizontal pixels by 200 vertical. Thus TEKEMUL performs a mapping
  from  the  Tektronix  coordinate  space (1024 x 780) to the IBM PC
  coordinate space.
 
  7. TEKEMUL Details
 
     The code for this  program  has  been  largely  separated  into
  subroutines  and  function  key  and  communication trap routines.
  Figure 2 shows the program flow.
 
 
 
            Define and initialize
            global variables
                     |
            Go to subroutine
            Set up screen  border
                     |
            Print out general
            instruction menu
                     |
            Wait for keyboard input
                     |
            Go to subroutine:
            clear out body of menu
                     |
            Print out communication
            parameter  menu
                     |
            Set  up  communications.
            Initialize communications
            and F8 F9 and F10  trap  routines.
                     |
                     |
   ------>-----------|
   |                 |
   |                 |
   |                 |
   ------<--------Keyboard input ?
   |                 |
   |     No          |    Yes
   |                 |
   -------<------- Send input to MTS
 
  Figure 2 - TEKEMUL program flow
 
1
 
 
     The program follows the sequence of events outlined  in  Figure
  2.  The last loop is one that the program constantly executes when
  it has nothing to do: reading input from the keyboard and  if  any
  input exists, transmitting it to the host.
 
     All  other  functions  of  the program are accomplished through
  trap  (interrupt)  routines.  When  a  trap  routine  is  finished
  executing,  control is once again returned to the keyboard reading
  loop.
 
  7.1 Subroutine and Trap Routines
 
     There are three trap routines in this program. One of  them  is
  for  the  communications buffer; the other three for function keys
  F8, F9 and F10.
 
     Any information received from  the  host  causes  an  interrupt
  situation and control is passed to the communication trap routine.
  The structure diagram for this routine is in Figure 3.
 
 
                     Communication        YES
    ---------------> buffer empty? ----------------> Return
    |                      |
    |                      |
    |                      |  NO
    |                      |
    |               Get a character
    |                      |
    |               Are we in Tektronix
    |               emulation mode?
    |                   |  |
    |                   |  |
    |       -----<---------------->-------
    |       |                            |
    |       |                            |
    |   Go to Tektronix            perform ordinary
    |   simulation                 terminal functions based
    |   subroutines                on characters received
    |       |                            |
    |       ----->-----------------<------
    |                      |
    |                      |
    -----------<------------
 
  Figure 3 - Communication Trap Routine
 
1
 
 
     The communication trap routine  processes  characters  received
  from  MTS one at a time until the IBM PC's communication buffer is
  empty. If the program is in  Tektronix  emulation  mode  then  the
  character is passed to the subroutines that actually simulates the
  Tektronix 4010.
 
     If the program is not in  Tektronix  emulation  mode  then  the
  character  is  merely  printed  on  the  screen.  The routine then
  carries on to deal with the next character.
 
     The other three trap routines are executed depending on whether
  F8  F9  or  F10  is  pressed  on the keyboard. The F8 trap routine
  allows the user to stay signed onto MTS, with the  output  of  the
  screen  going to the monochrome screen ( if one is attached ). The
  advantage is that most people prefer to use the monochrome monitor
  for  viewing  text  as  opposed to the colour monitor. The F9 trap
  routine begins the Tektronix emulation mode, switches the user  to
  the  color  monitor and issues various instruction menus. Figure 4
  shows the program flow for this routine.
 
 
           Set up instruction menu
                       |
           Prompt for monitor types
                       |
                       |                       NO
           Does user have  colour  monitor  -------->stop
                       |
                      YES
                       |
           Prompt for graphics software
           to use (*IG or  *PLOTSEE)
                       |
           Prompt  for  user's  object module
                       |
           Switch  to  colour monitor
                       |
           Enable Tektronix emulation mode
                       |
           Send $RUN command to MTS
                       |
                     Return
 
 
           Figure 4 - F9 Trap Routine
 
1
 
 
     The F10 trap routine ends Tektronix emulation mode and switches
  the  user  back  to  the monochrome monitor (if there is one). The
  diagram for this routine is in Figure 5.
 
           Disable Tektronix emulation mode
                           |
           Switch to monochrome monitor if
                     there is one
                           |
                      Exit to DOS
 
 
               Figure 5 - F10 Trap Routine
 
 
     The  subroutines  that actually simulate the Tektronix 4010 are
  comprised of TEKSIM, ESCAPE-TRUE and ESCAPE-FALSE.
 
     TEKSIM is called from the communications trap routine. Here the
  current character from the communications buffer is placed in BYTE
  as an ASCII decimal value. If the previous charactor was an escape
  character ESCAPE-TRUE is called; else, ESCAPE-FALSE is called.
 
     ESCAPE-TRUE  simulates  the  various  functions  of  the escape
  sequences for the Tektronix 4010.
 
     ESCAPE-FALSE checks to  see  if  the  current  character  is  a
  control  character  or  not. If it is a control character then the
  appropriate control function for the Tektronix 4010 is simulated.
 
     Characters other than control characters are decoded  into  X,Y
  coordinates.  When a complete (X,Y) address is decoded then a move
  or  a  draw  is  made  to  that  coordinate  address.  A  draw  is
  accomplished  by using the BASIC subroutine LINE to draw a line on
  the screen.
 
  7.2 Global Variables
 
     Global variables  important  to  the  simulation  part  of  the
  program are described below.
 
  TEKAMUL:  a  flag  indicating  whether the program is in Tektronix
  emulation mode (TEKEMUL=1) or isn't (TEKEMUL=0).
 
  MODE: indicates if we are in graph mode  (MODE=0)  or  alpha  mode
  (MODE=1) of the Tektronix 4010 terminal.
 
  DARK:  this flag, when set to TRUE, indicates that the next vector
  drawn is to be a dark vector. DARK  is  set  to  TRUE  when  a  GS
  control character is encountered.
1
 
  7.3 Adaptability to other Micros
 
     TEKEMUL has been structured so that it may easily be adapted to
  other micro  computers.  Should  the  communications  facility  on
  another  micro  be different than the IBM PC's then one can merely
  use the simulator routines TEKSIM, ESCAPE-TRUE,  and  ESCAPE-FALSE
  from the TEKEMUL program.
 
     All  that  these routines require to function by themselves are
  the global variables defined in the start of  the  program  and  a
  character given to the subroutine TEKSIM.
 
  8. History of the Emulator Program
 
     The original Tektronix emulation project began with a desire to
  preview an MTS graphic Plot Description File (PDF) on the IBM  PC.
  We  decided  to write a program for the IBM PC which would be much
  like *PLOTSEE on MTS, except it would run in the PC.  However,  we
  encountered  some  practical  problems  with this scheme. The most
  serious of these problems was the amount of time required to  plot
  a PDF.
 
     This  time  factor  was  due to the fact that the PDF had to be
  transferred over to the IBM PC in order to be plotted. A  PDF  can
  be  on  the  order  of  800,000  bytes.  Given  this  size  it was
  calculated that many plot files would require several  minutes  to
  be transferred using the file transfer programs.
 
     Another  problem complicating the design approach was that Plot
  description files are in binary format. The file transfer programs
  transfer   binary   information   much   slower   than   character
  information.
 
     One solution to this was to represent vector coordinates  in  a
  more  compact form. This solution led to the Tektronix 4010 method
  of transferring coordinates as efficiently as possible.
 
     We considered  converting  a  plot  description  file's  vector
  coordinates  into  Tektronix  format vector coordinates. This much
  smaller file could then be transferred over  to  the  IBM  PC  (as
  character data) and then plotted.
 
     But  there  was  no  sense  writing  a  conversion  program  to
  translate a PDF into Tektronix  format  vector  coordinates  since
  Integrated  Graphics already has a device driver for the Tektronix
  4010 that generated what was needed. It was desirable to eliminate
  the  file  transfer  step  and have the Tektronix emulator work in
  real time as MTS delivered Tektronix 4010 graphics commands.
 
     The regular Tektronix 4010 device driver can be  used  on  MTS,
  and,  it would be easy for the user to operate. In fact the IBM PC
  would operate just like a Tektronix 4010 from a logical  point  of
  view.
1
 


 to operate. In fact the IBM PC
  would operate just like a Tektronix 4010 from a logical  point