T I N Y   T A L K

                      Version 1.3, May 5th, 1986

               THE World's Smallest IBM PC Comm Program
                    (Jaxtalk, eat your heart out!) 
                                 

   Tiny Talk is a TINY communications program, designed with basic modem
   communications and testing in mind.  At 392 bytes in size....it remains
   a very usable program.

 
-Versions---Size-------Notes-------------------------------------------------

   1.0      198 bytes  Experimental vers. w/ unbuffered input.  Poor
                       performance at high speeds.

   1.1      227 bytes  The original Tiny Talk with buffered input.  Baud rate
                       changes required program modification using DEBUG.
  
   1.2      392 bytes  Allowed for baud rate setting by a passed parameter.
                       Better performance.

   1.3      402 bytes  Latest version.  Now supports ANSI graphics!

--------------
   Tiny Talk Operation

   There are two different copies of Tiny Talk included:

        TTALK1.COM    -   supports use of COM1: port
        TTALK2.COM    -   supports use of COM2: port


   Use the version which corresponds to your communications setup.

   To load Tiny Talk, type as follows:

   (example assumes use of COM1: port)

        TTALK1.COM x

   The parameter x must be one of the following baud rate codes:

        0  -  for  300 baud
        1  -  for 1200 baud
        2  -  for 2400 baud
 

   Once Tiny Talk is loaded, you may quit to DOS, at any time, by pressing
   the [Esc] key.


   Tiny Talk is a very basic communication program, and requires the use
   of YOUR modem commands to operate.  For example, if you use a modem
   supporting Hayes compatible AT commands, you may enter the following:

      ATZ                         <-  initialize your modem

      ATDT 1-402-449-1015         <-  dial a BBS.

      ATE1                        <-  enable 'echo' of modem commands entered.

      ATM0                        <-  disable the modem speaker.

   You should consult your modem manual for more command descriptions.


--------------
   ANSI Graphics

   With Tiny Talk release 1.3 came ANSI graphics support.  In order for
   this feature to work correctly, you must install the ANSI.SYS driver
   into your CONFIG.SYS file.  If you already have a CONFIG.SYS file on
   your boot disk, then edit it with your wordprocessor or EDLIN and
   add the statement:

                  DEVICE=ANSI.SYS

   If you do not have a CONFIG.SYS file then you can create one by
   typing from the DOS prompt (on your DOS boot disk):

                  COPY CON CONFIG.SYS <return>
                  DEVICE=ANSI.SYS <return>
                  <F6> (function key F6)  <return>

   Be sure to re-boot your system if you just installed ANSI.SYS.


--------------
   What does the future hold in store for Tiny Talk?

      * Memory resident option
      * Auto-dialing
      * Text capture capabilities
      * more....

      
   If you would like to obtain a listing of the latest Tiny Talk source
   code, send $5.00 along with a return address to:

                  Jeff Huston
                  9724 Brentwood Circle
                  Omaha, NE  68114