---  W A M --- 
		       Wow Another Modem Program.

	      Copyright(c) N. Franks & Associates P/L 1985.
		     All rights reserved worldwide.

























	Neville Franks.
	3 Pullman Crt,
	East St.Kilda
	Victoria, 3183
	Australia 
	Ph. (03)528 2516















    WAM Vers 2.00 Documentation.  4/May/85  (c) N. Franks & Assoc P/L 1985




    **********************************************************************
    ***   THIS RELEASE OF WAM IS PLACED INTO THE PUBLIC DOMAIN, NO     ***
    ***   WARRANTY INTENDED OR IMPLIED. 			       ***
    ***   This program may be copied and used for NON-COMMERCIAL       ***
    ***   purposes only.  Any commercial use conflicts with copyright  ***
    ***   and the offenders may be liable for criminal prosecution.    ***
    **********************************************************************


    WAM is a portable, easy to use communications package.  It has a	
    command  structure similar to the users operating system, with 
    the addition of communications commands and a powerful 
    programable shell.	WAM provides Dumb Terminal communications 
    with  automatic buffering, as well as File transfer facilities 
    using Christensen protocols.  CP/M and MSDOS operating systems 
    are currently supported.  WAM is well behaved and does not 
    interfere with the users operating system.

    WAM has two basic modes of operation Local and Remote.  In Local 
    mode WAM works in a similar manner to most communications 
    programs, ie. commands are issued from the local terminal to 
    control the program.  However when in remote mode WAM is 
    controlled from the system communicating with WAM.	The local 
    console (host) still has a limited number of commands available 
    such as returning WAM to local mode.  By adding autoanswer 
    facilities to WAM a simple remote access system becomes possible.

    WAM makes use of a simple general purpose shell and command 
    processor.	The shell allows multiple commands per line, and 
    provides `if then else' and `while' constructs.  All commands 
    return values back to the shell, which can then be used in `if' 
    and `while' tests.	The shell is extensible, allowing new 
    commands to be added easily.  Command aliases and variable 
    substitution are also available.  Input to the shell can come 
    from a file or the console.  This enables startup conditions to 
    be set, or automated communications sessions to be held.

    WAM is written in C and adheres to Unix V7 standards.  The Aztec 
    C compiler, assembler and linker have been used.   This compiler 
    is available for a number of 8 and 16 bit Cpu's and also a 
    variety of operating systems.  The current version of WAM is 
    available for Cp/m-80, Cp/m-86 and MS-DOS 2 operating systems.  
    DOS directories and Cp/m user areas are supported.	All operating 
    system specific routines are contained in one source file, and 
    hardware specific functions in another.

      This document briefly describes WAM Version 2.0.	This version 
    of WAM is being placed in the public domain to illicit comment 
    and suggestions.  WAM is an evolutionary product which is still 
    under development and testing. The source code and documentation 
    will probably be available at a later date for a nominal fee. 




				    2





    WAM Vers 2.00 Documentation.  4/May/85  (c) N. Franks & Assoc P/L 1985


    WAM COMMAND PROCESSOR USAGE.

	cmd ; cmd	    where ; is the command separator.
	IF   cmd	    Start if block
	ELSE [cmd]	    else clause for if
	FI		    end if [else] block
	WHILE cmd	    Start while block
	BREAK		    Break out of while block
	END		    End while block
	!cmd		    Not operator - used with if & while

    eg. 
    C>>while !test -m dcd ; echo -n waiting for carrier\r ; end

    C>>if yn run logon script y/n ? ; script logon ; fi

    C>>if del fred.c ; echo file deleted ; else echo file not found ; fi

    C>>if sb wam5.doc ; term ; rb ; else ; echo couldn't send file ;
       sleep 5 ; fi

    The if/else constructs can be nested and blocks can span any 
    number of lines.  You must be carefull to match if/else/fi pairs.  
    If nothing happens when you enter a command it is probably 
    because you are in an IF or ELSE block which is not being 
    executed.  To get back to if level 0 enter FI until the message 
    "No matching if" appears. 

    While loops must be contained on a single line and cannot be 
    nested, they can however be within an if block, or have if blocks 
    within them.  Break would normally be used with an if and will 
    skip all commands until the matching end is encountered.  You can 
    break out of an infinite loop by pressing any key on the keyboard 
    (a few times).  This has the same effect as break.

    The not operator "!" is used to negate the result of commands. It 
    is most useful with the while construct as in the example above.


    WAM command line editing.

    WAM has provides some simple editing commands. 
      ^R repeats the previous command line from the current position 
	 on the new cmd line up to the end of the previous one.
      ^X deletes the command line.  ^R will restore it.
      Delete & Backspace perform a destructive backspace.











				    3





    WAM Vers 2.00 Documentation.  4/May/85  (c) N. Franks & Assoc P/L 1985


    WAM STARTUP OPTIONS AND SCRIPT FILES.

      WAM [-p] [filename [arg1...argn]]
    -p enables priviledged mode.  This allows some normally 
    restricted remote commands to be used.

    filename is an input command file (script).  This file will be     
    processed when WAM starts, after which WAM will go into 
    interactive mode.  If the cmd `bye' is in the file then WAM will 
    return to the operating system.  If filename is not in the current 
    directory then the directories specified in the dos path command 
    will be searched. 
    An example startup file might contain the following:-

      rem  this is a sample startup file
      echo loading startup file
      rem  connect to line and set baud rate
      mdm on ; baud 300 	  
      rem see if user wants to open a capture file
      if yn open capture file y/n? 
       cap open bbs ; cap xon ; cap on
      fi
      rem if carrier detected go into terminal mode else command mode
      if test -m dcd ; term ; else echo no carrier detected ; fi

    The startup file would also be used for defining aliases and 
    performing other initialization.  By using the rxwait commands 
    etc; it is possible to automate a complete communications 
    session with a script file.


    The SCRIPT command provides the ability to load and run input 
    files.  Scripts can be nested and can contain while loops, even 
    if there is a while loop running in an outer level.  This 
    provides a rudimentry method for running nested while loops, as 
    do aliases. Script commands return the value of the last command 
    executed back to the shell.  This enables scripts to determine 
    the next action be taken by the caller.  Variable substitution is 
    also provided.

      if script logon ; term ; else sb *.c ; fi

      where the logon script may be as follows:-
	while !test -m dcd ; echo -n waiting for carrier\r ; end
	if yn terminal mode y/n ?

    See also the script file `logon.wam' and the examples on page 11.










				    4





    WAM Vers 2.00 Documentation.  4/May/85  (c) N. Franks & Assoc P/L 1985


    WAM COMMAND SUMMARY:-

    WAM commands can be entered in upper or lower case.

    `dpfe' means [d:][path][filename[.ext]] where filename & ext can 
    be ambiguous in most cases.
    Under Cp/m path can be `nn/x:' where nn is the cp/m user number 
    and x: the drive specification. 

    `message' can include the following:-
    \r	  specifies a carriage return char
    \n	  specifies a new line char (line feed)
    \b	  specifies a back space char
    \t	  specifies a tab char
    \f	  specifies a form feed char
    \"    specifies a double quote char
    \\    specifies the '\' char
    \nnn  where <nnn> is 1, 2 or 3 decimal digits which specify the 
          value of the desired character.

    A message or string can also be enclosed in double quotes.  This 
    allows whitespace or command separator characters to be included 
    in strings.  ie, echo "	a space & cmd sep ;;; example"

    Multiple commands can be passed as whole by including them within 
    single quotes.  This is mainly for use with the alias command.
    ie, alias r 'rn $1 ; term'

    If a command has an alias with the same name the alias will be 
    run in place of the command.  If this occurs, recursion is 
    prevented by temporarily disabling aliasing.  An example would be 
    `alias dir dir $1 -wdr'.  Entering `dir *.h' will alias into `dir 
    *.h -wdr' with the built-in dir command being executed.  Aliases 
    can be nested and used within script files.  An alias can use any 
    built-in command, construct, other alias or script file and 
    multiple commands can be used by entering them within single 
    quotes as discussed above.  Aliases provide a powerful way to 
    create new commands or just change the names of existing commands.

    Scripts and aliases provide variable substitution by matching 
    parameters with $number strings, where number is between 0 and 9. 
    `$0' is the script filename or alias command itself, and `$1-$9' 
    are the corresponding variables in the command line.
    eg.
    Enter `alias e 'echo $2 ; term $1 ; dir $3 '' then 
          `e hello john *.wam'  would be parsed into 
          `echo john ; term hello ; dir *.wam'.

    To setup aliases in a script, which require variable 
    substitution, preceed the `$' with a `\' ie. \$1.  This prevents 
    substitution occuring.  See the script file `alias.wam' for 
    examples.





                                    5





    WAM Vers 2.00 Documentation.  4/May/85  (c) N. Franks & Assoc P/L 1985


    WAM COMMAND SUMMARY:-

    D - means dos only.   C - means cp/m only.
    L - means valid in local mode only.
    R - means valid in remote mode only.
    P - means valid in remote mode if priviledged startup option was 
         used.


     Local/Remote commands.

        Name                Meaning
        -------             -----------
    DL  CLS                 Clear screen

        DF [d:]             Display free disk space.

        DIR [dpfe..] -dwpr  Directory display.  -d date order (dos),
                             -w wide,  -p page, -r reverse order

     LP DEL dpfe [dpfe..] -a
                            Delete file(s).     -a Ask first

     LP ERASE               See DEL

     LP ERA                 See DEL

        TYPE dpfe [dpfe..] -p
                            Type file(s).      -p page mode


        x:                  change default drive to `x:'

    D   CD [[d:]path]       Display current dos path or change to 
                             new path.

    C   USER [nn]           Display/Change Cp/m user number.

     L  TERM [message]      If message is present send message, else
                             go into terminal mode.

     L  RXWAIT [char]       Go into terminal mode.  When "char" is 
                            received return to command mode.  If no 
                            argument use char set by "set rxwait 
			    char".  Returns true if `char' received 
                            else false if terminal mode abandoned. 

     L  CAP [OPEN dpfe[-a]] [CLOSE] [ON OFF] [SAVE ZAP] [XON NONE] 
                  [nnnn]

     L      OPEN [-a]       Open the file dpfe for capture buffer use.
                            If the file exists, it will by default be
                             opened in append mode. If the -a option 
                             is used you will instead be given a choice.



                                    6





    WAM Vers 2.00 Documentation.  4/May/85  (c) N. Franks & Assoc P/L 1985


     L      CLOSE           Closes the currently open capture file and 
                            turns capture off.  Also closed when 
                            leaving WAM.

     L      ON OFF          Sets capture mode Off/On.

     L      SAVE            Save the capture buffer to the currently 
                             open file.

     L      ZAP             Zap the capture buffer.

     L      XON             Enables Xon/Xoff handshaking with auto 
                             disk saves if capture file open.

     L      NONE            Disables Xon/Xoff handshaking

     L      nnnn            Sets the capture buffer size. 
                            Default size is 16K


        S [A B N]  dpfe [dpfe..]
                            Send file(s) in Ascii, Batch or Normal 
                            mode.  Batch and Normal mode use 
                            Christensen protocol.  Batch mode is 
                            compatible with YAM and Normal with 
                            XMODEM and YAM.

        R [A B N] [path]    Receive file in Ascii, Batch or Normal 
                            mode. If path is present files will be       
                            placed in that path.

     L  BAUD [nnnn]         Display baud rate, or set new baud rate.

     L  MDM [ON OFF]        Display status or Enable/Disable Modem. 
                            On sets DTR & RTS, while off resets them.

     L  SET                 Display current set parameters.

     L      STOP key        Set the stop key value.  The default stop 
                             key is ^_

     L      RXWAIT char     Set the default rxwait character.  This 
                            is used by the "rxwait" command with no 
                            argument.

     L      PAUSE nnn       Set .1 sec timer variable.  This is 
                            machine dependant and comes initialized 
                            for the harware in use.  If you wish to 
                            change it use the sleep command to 
                            establish the best value.

     L      PACE nnn        Set pace variable.  This is used to slow 
                            down WAM output when in remote mode.




                                    7





    WAM Vers 2.00 Documentation.  4/May/85  (c) N. Franks & Assoc P/L 1985


     L      VIEW [ON OFF]   sets View mode off/on.  (Used in file
                             transfers)

     L      VIEW [ASCII HEX] sets View mode to Ascii/Hex

     L  SLEEP [nnnn]        Sleep for nnn seconds.


     L  REMOTE              Switch to remote mode.

     L  LISTEN              Listen for a call and answer it.  This is 
                             currently only being used for testing.

     R  MSG [message]       Send message to host.  If no message 
                             prompt for one.

        ECHO [on off] [[-n] message]        
                            turn console echo on/off or echo message 
                            to console.  if -n is specified then don't 
                            send a NL sequence at end of message. If 
                            no arguments display echo status.

        REM  [message]      message is just a remark.  Useful for 
                            putting remarks in input files. this 
                            function always returns true.

     L  TEST [-m [cts dsr ri dcd]] 
                            returns rs-232 input status where:-
                             cts is clear to send
                             dsr is data set ready
                             ri  is ring indicator
                             dcd is data carrier detect

             [-f filename]  returns true if file `filename' exists.

     L  YN [message]        display message and wait for Y or N 
                            response from console.  returns true if Y 
                            pressed, else false.

     L  BYE                 Return to operating system.  Modem stays 
                            connected.  If there is an open capture 
                            file it will be closed. If the capture 
                            buffer isn't empty you will be prompted 
                            to save it first.

     L  QUIT                See BYE.  Modem is disconnected.











                                    8





    WAM Vers 2.00 Documentation.  4/May/85  (c) N. Franks & Assoc P/L 1985


    DL  DOS [prog [params]] Temporary Exit to DOS or Run prog.  WAM 
                            remains resident and the modem stays 
                            connected.  This lets you use any dos 
                            commands or run any programs and then 
                            return to WAM.  If prog isn't specified 
                            then WAM invokes another copy of the dos 
                            command processor. When you want to 
                            return to WAM type "exit" at the DOS 
                            prompt.  If prog is specified then it 
                            will be run using params.  When it is 
                            finished, control will be returned to WAM.  
                            If prog is not found in the current 
                            directory or along PATH then return 
                            false. If prog contains a path spec then 
                            that will be searched instead of the 
                            current directory.


     L  SCRIPT name [arg1...argn] 
                            process script file "name" as input to       
                            WAM. Script files can use all WAM 
                            commands. There is no limit to the size 
                            of a script and scripts can call other 
                            scripts. A script returns the value of 
                            the last command executed in the script 
                            to the caller.  When a script returns 
                            execution continues at the command 
                            following the script command.  Scripts 
                            can also use the while construct even if 
                            there is one executing outside of it. The 
                            arguments, if any are used for variable 
                            substitution.

        ALIAS name [wordlist] 
                            With no parameters displays all current 
                            aliases, with just name displays the 
                            alias for name if present.  Otherwise 
                            wordlist is associated with name as a new 
                            alias.  Wordlist is a single command, or 
                            multiple commands enclosed in single 
                            quotes.  When an alias is run it returns 
                            the value of the last command executed to 
                            the shell.

        ALIAS [off on]      Turns off/on all current aliases.

        UNALIAS name        Removes name from aliases.


        HELP                Display brief help information.







                                    9





    WAM Vers 2.00 Documentation.  4/May/85  (c) N. Franks & Assoc P/L 1985


      HOST commands:-   These commands are initiated by pressing a single 
                              key only on the host console.

        R or STOP KEY       Remote OFF.

        E                   Toggle host Echo Off/On.

        M                   Send message to remote.  You are prompted 
                            for the message.

        B                   Bye - Return to operating system.  This 
                             will be removed at a later date.

        H or ?              Help 


      TERM commands:-   These commands are initiated by pressing the STOP KEY
                         followed by the cmd key rapidly.

        C                   Toggle capture buffer off/on.  When on 
                            text received in terminal mode is placed 
                            into the capture buffer.

        Z                   Zap capture buffer

        S                   Save capture buffer.  A capture file must 
                            already be open.

        STOP KEY            Exit term mode.  Returns true to command 
                            processor if were using "term" or false 
                            if using "rxchar".


























                                   10





    WAM Vers 2.00 Documentation.  4/May/85  (c) N. Franks & Assoc P/L 1985


    COMMAND SCRIPT EXAMPLES:

    rem a sample script to download files from an rcpm system and 
    rem disconnect when finished.
    mdm on ; baud 300
    while !test -m dcd ; echo -n waiting for carrier\r ; end
    if test -m dcd
      sleep 1 ; term \n\n\n            ; tell'm were here 
      set rxwait ^G                   ; rem bell means ready for name
      rxwait ; term John ; rxwait ; term Citizen 
      rxwait >                              ; rem wait for cp/m prompt
      term xyam                             ; rem fire up xyam etc;
      set rxwait ?
      rxwait ; term b1:                     ; rem tell it what to do
      term b1:                              ; rem log to B0:
      rxwait ; term sb *.c *.h              ; rem send some files
      rb                                    ; rem receive in batch mode
      rxwait ; term quit                    ; rem back to cp/m
      rxwait ; term bye ; rxwait ; term n   ; rem all done disconnect
      bye
    else
      echo logon \7abandoned
    fi


    rem a sample ibbs logon script
    rem usage: wam5 logon firstname lastname password
    rem   given script filename is `logon'
    rem
    echo \nlogon to ibbs
    mdm on ; baud 300
    cap open ibbs ; cap xon ; cap on
    while !test -m dcd ; echo -n waiting for carrier\r                   \r ; end
    if test -m dcd
      sleep 1 ; term \n\n\n                 ; rem let'm no were here
      if rxwait ? 
        term $1                             ; rem send firstname
        rxwait ? ; term $2                  ; rem then lastname
        set rxwait >                                ; rem used from now on
        rxwait   ; term $3                  ; rem password
        rem whatever
        rxwait   ; term m                   ; rem message subsystem
        term 
        rxwait   ; term g                   ; rem goodbye
        rxwait   ; term y                   ; rem Yes i'm sure
        term
      else
        echo logon failed $1
      fi
    else
      echo logon abandoned $1
    fi





                                   11





    WAM Vers 2.00 Documentation.  4/May/85  (c) N. Franks & Assoc P/L 1985


    TYPICAL MODEM RS-232 CONNECTION

       MODEM       PC
         1   ----   1          PG.  Protective ground
         2   <--    2          TD.  Transmit Data
         3    -->   3          RD.  Receive  Data
         4   <--    4          RTS. Request to send
         5    -->   5          CTS. Clear to send 
         6    -->   6          DSR. Data set ready
         7   ----   7          SG.  Signal ground
         8    -->   8          DCD. Data carrier detect
        20   <--   20          DTR. Data terminal ready
        22    -->  22          RI.  Ring indicator

    Handshake Lines.
    RTS - Indicates the pc is ready to transmit data. The modem then 
          enables it's transmit carrier and sets DSR.
    DSR - Indicates the modem is ready to establish communications

    DCD - Indicates the modem is detecting carrier.

    RI  - Indicates that a telephone ringing signal has been received 
          by the modem.

    DTR - Informs the modem the pc is ready to communicate.  The 
          modem then connects to the phone line, and normally 
          acknowledges by setting CTS.
    CTS - Indicates the modem is ready to establish communications.


    NOTES:
    Ascii Send and Receive are not currently implemented.
    Viewing of received data has been temporarily removed.
    The stop key is used to abandon terminal mode and also to abort 
    Send/Recv commands.  The current version of WAM does not make use 
    of any RS-232 input lines, but has a complete set of functions 
    for monitoring their status.  The ouput lines DTR and RTS are 
    set/reset by mdm on/off commands respectively.  Setting DTR 
    normally enables the modem to connect to the line. The mdm 
    command with no options displays the status of the RS-232 lines.  
    The test -m command permits testing of individual input lines.  
    WAM will happily send and receive files at 4800 baud on the PC 
    and faster on some other machines.  In Terminal mode WAM has 
    trouble keeping up at 4800 baud without the send system slowing 
    down it's output by using line pacing or some equivalent 
    system.  WAM itself slows down output when in remote mode. The 
    amount being determined by the value set in the pace variable. 

     ** Unix is a trademark of Bell Labs.
     ** CP/M is a trademark of Digital Research.
     ** DOS  is a trademark of Microsoft.
     ** AZTEC C II is copyright(c) Manx Software Systems.

    /**--  The End  --**/ 



                                   12