<<<===  X F E R - DOS FILE TRANSFER UTILITY  ===>>>
 
                          Version 1.40, May 3, 1986
 
         (C) 1985, 1986 J.C. Kilday Associates, Peaks Island, ME 04108
 
 
     XFER is a  standalone utility supporting  XMODEM/CRC, XMODEM/Checksum,
     and YMODEM file transfer operations at the DOS level.  It is installed
     on a host system and may be accessed by the caller after dropping into
     DOS (through CTTY, etc.).  This release, v1.40, incorporates a  faster
     implementation  of  the  YMODEM  file  transfer protocol.  The receive
     routine appears to be significantly  faster than that used by  PCBoard
     and DBBS during YMODEM uploads.
 
     File transfer occurs to/from the default directory on the host  system
     or the drive/directory included in  the filespec entered for the  file
     to  be  uploaded/downloaded.   XFER.EXE  should  be  located  in   any
     directory included in  the current PATH  on the host  system.  Command
     syntax is simply:
                                  XFER [Y]
 
     where the optional parm ("Y"  or "y") if included specifies  that XFER
     is to be initialized for  conducting YMODEM transfers only.  If  the Y
     parm is omitted,  XFER is initialized  to conduct XMODEM  (Checksum or
     CRC) transfers only.
 
     On start-up, XFER searches  for an "active" communications  port (COM1
     or COM2).  If the status of COM1, is DATA SET READY and CARRIER DETECT
     and  a  speed  of  300,  1200,  or  2400  bps,  then  XFER  takes over
     communications at N, 8, and 1.   If COM1 is not active, it  checks for
     an active COM2 meeting the  same criteria.  If neither port  is active
     (meaning it  was started  while in  local mode  and no  communications
     active), XFER exits after printing on the would-be "host" console  "NO
     COMM PORT ACTIVE."
 
     If  XFER  is  started  without  the  Y  parm, downloads use the XMODEM
     variation the remote system  is set for.  XFER  adjusts automatically.
     XMODEM/CRC  uploads,  however,  are  specified  by  entering  "U"; and
     Checksum uploads by "C".  Any combination of uploads and downloads may
     be performed  before quitting  to DOS.  Return to  DOS is accomplished
     without loss of carrier.
 
     This package is intended for use by SYSOPS or others who have need for
     operating a "host system" remotely and working at the DOS level on the
     host.   It  facilitates  file  transfers  directly to/from directories
     which are not accessible by the host software.  XFER also may be  used
     with simpler host  software packages which  allow a caller  to drop to
     DOS (e.g., JAXHOST2).  XFER will not work in local mode.
 
     You are free to use  this package (privately or commercially)  so long
     as  it  is  not  included  in  any  product or system that is sold for
     profit.  Feedback regarding problems  (and successes, of course)  with
     the use of XFER are welcomed.
                                         Jack Kilday
                                         Northern Lights BBS
                                         207-766-2467 (2400/1200)
 
                                         CIS ID: 72307,2156