==============================================================================
FMONITOR  --  FontMonitor Documentation   Version 1.01   October 31, 1988
==============================================================================

PURPOSE.
--------

FMONITOR is designed to work with DESQview, WordPerfect 5.0, and the
Hercules Graphics Card Plus when using the RamFont feature.  As you switch
back and forth between DESQview windows with WordPerfect running in one of
them with the RamFont option selected, FMONITOR keeps track of the mode
required for the HGC+ card and changes it accordingly.  This way most
screens are in the proper mode.

INSTALLATION.
-------------

FMONITOR must be installed.  The file FMONITOR.ARC contains the following
files:
         FMONITOR.COM ...... the executeable code
         FM-PIF.DVP ........ the DESQview PIF for FMONITOR
         W5-SCRIP.DVS ...... the script file for your WordPerfect 5.0 window
         FMONITOR.DOC ...... this file

Un-arc the files and copy FM-PIF.DVP and W5-SCRIP.DVS to your DESQview
sub-directory.  CAUTION: if you already have a W5-SCRIP.DVS file for DV
scripts in your WordPerfect window, DO NOT copy W5-SCRIP.DVS.  Copy
FMONITOR.COM to whichever sub-directory you want. Suggest you put it in
your DV, WP, or HERC sub-directory.

With DESQview loaded open an 'Add Program' window, select 'Other', enter
your DV sub-directory and select FMONITOR from the resulting list.  Then
open a 'Change Program' window and enter FM for FMONITOR.  On the
'Program' line either delete the path preceding FMONITOR.COM or put in the
correct sub-directory.  You will need to edit the 'Parameter' line to
correctly reflect the name and location of your PIF for WordPerfect 5.0.
Make sure to leave the second parameter, '5' on that line.  The second
parameter must be separated by one and only one space from the WP PIF
name.  The 'Directory' entry may be blanked if you included the path in
the 'Program' line.  Otherwise put in the correct sub-directory for the
location of FMONITOR.COM.  If you want to change the name of the FMONITOR
window from FM to something else, you may do that.  Don't change any of
the other settings.

Next you must establish a DV script for the WordPerfect 5.0 window for the
{Alt-F} key.  Follow the directions in one of the two paragraphs below.

NOT USING DV SCRIPTS FOR WORDPERFECT.
-------------------------------------

If you are not using any DV scripts for the WordPerfect 5.0 window
already, then all you have to do is to rename W5-SCRIP.DVS changing the
first two letters to match up with whatever you call your WordPerfect
window.  Then be sure you have copied the .DVS file to your DV
sub-directory.

USING DV SCRIPTS FOR WORDPERFECT.
---------------------------------

If you already have a script file for your WordPerfect window, then you
need to add one script for {Alt-F}.  If you are already using {Alt-F} for
something else, then you must change the other script key to another
combination.  To add the script the easiest way is to open the WordPerfect
window and use the normal learn procedure to learn a script for {Alt-F}.
The keys you must record are:

         {Shift-F1}DC2{Enter}{Enter}{Enter}

This {Alt-F}, Load RamFonts, script executes the WordPerfect commands to
select the '12 fonts, 256 characters' option for the display fonts.
FMONITOR uses this script, but you may also manually execute {Alt-F} to
load those RamFonts.  If you are using the '6 fonts, 512 characters'
option, change the '2' to '3' in the script above.

WORDPERFECT PIF.
----------------

Recommend you set the 'Starting Height' to 25 and 'Starting Width' to 80
in your WordPerfect PIF.  FMONITOR works best when WordPerfect is using
the full screen.  If you are using the graphics capability within
WordPerfect (e.g. View Document, or importing graphics), then don't forget
to set the 'Display Graphics Information' to 'yes'.  Otherwise the
graphics information will not be saved when you switch away from
WordPerfect.

USAGE.
------

With DESQview loaded and WordPerfect not loaded, open FM (or whatever you
have changed the name).  FM will load in a very small window (3k) and
automatically load WordPerfect.  Now when you switch away from WordPerfect
to a window using normal text, the HGC+ mode will change if the current
window covers the upper left corner of the screen.  When you switch back
to WordPerfect, the mode will change to RamFont.  This also works if you
switch to a window using a graphics mode and back.

After you have exited from WordPerfect, don't forget to close the FM
window.  No harm will be done if you don't, but you could wind up with
several copies of FMONITOR loaded.  Only the most recent one will be
active.

HOW DOES IT WORK?
-----------------

The Hercules Graphics Card Plus has some pseudo-modes for the various
RamFont text modes.  Normally DESQview detects the mode for each window
and saves this parameter before it switches away.  Unfortunately, the HGC+
has registers that are involved with the RamFont modes that can not be
read to determine its state.  Therefore DESQview by itself can not make
automatic mode changes to and from RamFont modes.

Through the use of the DESQview Applications Program Interface (API) which
is built into DESQview, FMONITOR keeps track of which window covers the
upper left corner of the screen (0,0).  FMONITOR assumes WordPerfect is
using RamFont mode 5 which is the '48k RamFont text, 9 dot wide, 48k
RamFont text attribute' mode of the HGC+.  (The other RamFont modes will
be found on page 70 of the HGC+ manual.  They are numbered 0..7.)  If the
window at 0,0 is WordPerfect, FMONITOR sends the appropriate commands to
the HGC+.  If the window at 0,0 is in normal text mode, FMONITOR changes
HGC+ to normal text, which is RamFont mode 0.  If the window at 0,0 is in
a graphics mode, FMONITOR doesn't do anything since DESQview automatically
changes the mode.

If you are in a graphics window and switch back to WordPerfect, then the
mode of the HGC+ is changed as before and the script {Alt-F} is executed
unless WordPerfect is in the graphics mode. The reason for this is that
the RamFonts use the same video buffer space to store the fonts as the
graphics mode uses for its pixels.  Since DESQview does not know about
RamFonts, DV does not save this video buffer space (even if you have
WordPerfect PIF set to 'Displays Graphic Information').  Therefore when
you switch from a graphics window to WordPerfect the RamFonts must be
reloaded.  The {Alt-F} script does this by re-selecting the 12x256 font
mode.

Don't forget FMONITOR will put the HGC+ in whatever mode is appropriate
for the window that covers the 0,0 location on the screen.

APPLICATIONS OTHER THAN WORDPERFECT.
------------------------------------

Although FMONITOR is set up specifically for working with WordPerfect,
there is no reason you can not use FMONITOR with any program that uses
RamFont text mode in DESQview.  The syntax for FMONITOR is:

         FMONITOR d:\path\pif_filename hgc_mode
                                      ^only one space here

The pif_filename is whatever xx-PIF.DVP is for the application using
RamFonts and hgc_mode is the appropriate mode from page 70 of the HGC+
manual (in the range 0..7).  Then you will have to create the appropriate
{Alt-F} script for the application which will re-load the RamFonts for the
application if you are going to be switching to windows using graphics
modes in the same DESQview session.

xMONITOR SERIES.
----------------

The author intends to write other xMONITOR programs for non-DV
applications that are running in DESQview.  These xMONITOR programs will
provide DESQview capabilities to applications that were not written
specifically to operate in DESQview.  For example the next one will be
CMONITOR for use with RBBS and other BBS systems.  It will monitor the
carrier.  If there is a loss of carrier, the RBBS window will be closed
and reopened to restart RBBS without having to re-boot the entire system.


COPYRIGHT.
----------

FMONITOR and the xMONITOR series are copyrighted by John Poindexter 1988.

John Poindexter
SIG004 The SOURCE
October 31, 1988