======================= FORMGEN.EXE   -   Version 1.2 =======================


1. This version will determine if a database was created by PC-FILE III -
   version 3.0 or by an earlier version of PC-FILE. It will process the
   data accordingly.

2. You can specify screen colors and printer setup strings. These parameters
   are specified in the file FORMGSET.FRM. A sample FORMGSET.FRM file
   follows:
                          7,0
                          27,69
                          27,70
   If the program finds FORMGSET.FRM on the default drive upon startup, then
   it will read the screen's foreground and background colors from line 1. In
   the sample, the 7 specifies a foreground color of white and the 0 specifies
   a background color of black. Lines 2 and 3 are optional. Line 2 contains
   the ASCII codes of the string the program will send to the printer before
   printing. Line 3 contains the ASCII codes of the string the program will
   send to the printer after printing. In the sample, the 27 and 69 represents
   the characters   ESC  and   "E". This string sets the emphasized mode on
   EPSON printers. The 27 and 70 on line 3 represents the characters  ESC  and
   "F". This string turns off the emphasized mode on EPSON printers. The
   entries on each line must be separated by commas.

   The following sample FORMGSET.FRM file will set the screen colors to yellow
   foreground and black background. It will send the EPSON printer code for
   condensed print before printing, and it will send the code to return to
   normal print after printing:
                          14,0
                          15
                          18

   The following FORMGSET.FRM file will set the screen colors to white
   foreground and blue background. No printer setup codes will be sent:
                          7,1

3. The HOME key is now active, when you are inserting or modifying lines. It
   will position the cursor at the beginning of a line.

4. The INSERT and MODIFY options no longer request the number of lines to
   insert or modify. When in the INSERT or MODIFY mode, you now press ESC
   on the last line you wish to insert or modify. In other words, pressing
   ENTER when you are finished with a line will move you to the next line,
   whereas pressing ESC will return you to the option menu.

5. This version will accept a file created externally, as long as each line
   is terminated with a carriage return-line feed or a carriage return.
   However the CREATE portion of the program will chop each line longer than
   76 characters. This 76 character limitation does not apply to the OUTPUT
   portion of the program.