---RELOC.DOC---

A86 allows you to produce either .COM files, which can be run 
immediately as standalone programs, or .OBJ files, to be fed to 
the MS-DOS LINK program.  In this chapter I'll discuss .OBJ mode 
of A86.  


.OBJ Production Made Easy 

I'll start by giving you the minimum amount of information you 
need to know to produce .OBJ files.  If you are writing short 
interface routines, and do not want to concern yourself with the 
esoterica of OBJ files (segments, groups, publics, etc.), you can 
survive quite nicely by reading only this section.  

There are two ways you can cause A86 to produce a .OBJ file as 
its object output.  One way is to explicitly give .OBJ as the 
output file name: for example, you can assemble the source file 
FOO.8 by giving the command "A86 FOO.8 FOO.OBJ".  The other way 
is to specify the switch +O (letter O not digit 0).  This is 
illustrated by the invocation "A86 +O FOO.8", which will have the 
same effect as the first invocation.  

My design philosophy for .OBJ production is to accommodate two 
types of user.  The first type of user is writing new code, to 
link to other (usually high-level language) modules.  That person 
should be able to write the module with a minimum of red tape, 
and have A86 do the right thing.  The second type of user has 
existing modules written for Intel/IBM assemblers, and wants to 
port them to A86.  A86 should recognize and act upon all the 
relocation directives (SEGMENT, GROUP, PUBLIC, EXTRN, NAME, END) 
given.  The assembly should work even if several files, assembled 
separately under the Intel/IBM assembler, are fed to a single A86 
assembly.  You'll see if you read on through this entire chapter 
that the multiple-files requirement causes A86 to interpret some 
of the relocation directives a little differently (while 
achieving compatible results).  

Let's suppose you're writing new code: for example, an interface 
routine to the "C" language, that multiplies a 16-bit number by 
10.  "C" pushes the input number onto the stack, before calling 
your routine.  Your code needs to get the number, multiply it by 
10, and return the answer in the AX register.  You can code it as 
follows: 

_MUL10:          ; "C" expects all public names to start with "_"
  PUSH BP        ; "C" expects BP to be preserved
  MOV BP,SP      ; we use BP to address the stack
  MOV AX,[BP+4]  ; fetch the number N, beyond BP and the ret addr
  ADD AX,AX      ; 2N
  MOV BX,AX      ; 2N is saved in BX
  ADD AX,AX      ; 4N
  ADD AX,AX      ; 8N
  ADD AX,BX      ; 8N + 2N = 10N
  POP BP         ; BP is restored
  RET            ; go back to caller 

These 11 lines can be your entire source file!  If you name the 
file MUL10.8, A86 will create an object file MUL10.OBJ, that 
conforms to the standard SMALL model of computation for high-
level languages.  If you use RETF instead of RET (thus, by the 
way, getting the operand from BP+6 instead of BP+4), the object 
module will conform to the standard LARGE model of computation.  
All the red-tape information required by the high-level language 
is provided implicitly by A86.  I'll go through this information 
in detail later, but you should need to read about it only if 
you're curious.  

What happens if you need to access symbols outside the module 
you're assembling?  If the type of the symbol is correctly 
guessed from the instruction that refers to it, then you can 
simply refer to it, and leave it undefined within the module.  
For example, if A86 sees the instruction CALL PRINT with PRINT 
undefined, it will assume that PRINT is a NEAR procedure.  If 
PRINT is never defined within the module, A86 will act as if you 
declared PRINT via the directive EXTRN PRINT:NEAR.  The address 
of PRINT will be plugged into your instruction by LINK when it 
combines A86's .OBJ file with the high-level language's .OBJ 
files, to make the final program.  

In general, the undefined operand to any CALL or JMP instruction 
is assumed to be NEAR.  The second (source) operand to a MOV or 
arithmetic instruction is assumed to be ABS (i.e., an immediate 
constant).  An undefined first (destination) operand is assumed 
to be a simple memory variable, of the same size (BYTE or WORD) 
as the register given in the second operand.  If your external 
symbol does not comply with these guidelines, you need to declare 
it with an EXTRN before you use it.  (You can also use EXTRN to 
declare types of non-complying forward-references within your 
module, as you'll see later.) 

At this point, if you're a casual user, I think you've read 
enough to get going!  Read further only if you wish; or if you 
get stuck, and need to master the esoterica.  


Overview of Relocation and Linkage

When you assemble a program directly into a .COM file, the 
program has just two forms: the source program, that you can 
understand, and the .COM file, that the computer can "understand" 
(i.e., execute).  A .OBJ file is an intermediate format: neither 
you nor the (executing) computer can make sense out a .OBJ file; 
only programs like LINK interpret .OBJ files.  The purpose of a 
.OBJ file is to allow you to assemble or compile just a part of a 
program.  The other parts (also in the form of .OBJ files) can be 
produced at a different time; often by a different assembler or 
compiler, whose source files are in a different language.  It's 
easy to see where the word "linkage" comes from: the LINK program 
puts the pieces of a program together.  The "relocation" comes 
because the assembler or compiler that makes a given program 
piece doesn't know how many other pieces will come before it, or 
how big the other pieces will be.  Each piece is constructed as 
if it started at location 0 within the program; then LINK 
"relocates" the piece to its true location.  
                                     
Many of the relocation features of 86 assembly language are 
couched in terms of LINK's point of view, so we must look at the 
way LINK sees things.  LINK calls a .OBJ file an "object module", 

or just "module".  Each module has a NAME, that can be referred 
to when LINK issues diagnostic messages, such as error messages 
and symbol maps.  If a program symbol is used only within a 
single module, it does not need to be given to LINK, except 
possibly to pass along to a symbolic debugger.  On the other 
hand, if a program symbol is defined in one module and referenced 
in other modules, then LINK needs to know the name of the symbol, 
so it can resolve the references.  Such a symbol is PUBLIC in the 
module in which it is defined; it is "external" in the other 
modules, containing references to it.  Finally, exactly one 
module in a program must contain the starting location for the 
program; that module is called the "main module", and it must 
supply the starting address (which is not necessarily at the 
beginning of the module).  

In the 86 family of microprocessors, the LINK system also does 
much to manage the memory segments that a program will fit into, 
and get its data from.  The (grotesquely ornate) level of support 
for segmentation was dictated by Intel when it specified (and IBM 
and the compiler-makers accepted) the format that .OBJ files will 
have.  I attended the fateful meeting at Intel, in which the 
crucial design decisions were made.  I regret to say that I sat 
quietly, while engineers more senior than I applied their fertile 
imaginations to construct fanciful scenarios which they felt had 
to be supported by LINK.  Let's now review the resulting 
segmentation model.  

The parts of a program, as viewed by LINK, come in three 
different sizes: they can be (1) pieces of a single segment, (2) 
an entire single segment, or (3) a sequence of consecutive 
segments in 86 memory.  Size (1) should have been called 
something like FRAGMENT, but is instead called SEGMENT.  Size (2) 
should have been called SEGMENT, but is instead called GROUP.  
Size (3) should have been called "group", but is instead called 
"class".  Let me cling to the sensible terminology for one more 
paragraph, while I describe the worst scenario Intel wanted to 
support; then when I discuss individual directives, I'll 
regretfully revert to the official terminology.  

The scenario is as follows: suppose you have a program that 
occupies about 100K bytes of memory.  The program contains a core 
of 20K bytes of utility routines that every part of the program 
calls.  You'd like every part of the program to be able to call 
these routines, using the NEAR form to save memory.  By gum, you 
can do it!  You simply(!) slice the program into three fragments: 
the utility routines will go into fragment U, and the rest of the 
program will be split into equal-sized 40K-byte fragments A and 
B.  Now you arrange the fragments in 8086 memory in the order 
A,U,B.  The fragments A and U form a 60K-byte block, addressed by 
a segment-register value G1, that points to the beginning of A.  
The fragments U and B form another 60K-byte block addressed by a 
segment-register value G2, that points to the beginning of U.  If 
you set the CS register to G1 when A is executing, and G2 when B 
is executing, the U fragment is accessible at all times.  Since 
all direct JMPs and CALLs are encoded as relative offsets, the U-
code will execute direct jumps correctly whether addressed by G1 
with a huge offset, or G2 with a small offset.  Of course, if U 
contains any absolute pointers referring to itself (such as an 
indirect near JMP or CALL), you're in trouble.  


It's now been nine years since the fateful design meeting took 
place, and I can report that the above scenario has never taken 
place in the real world.  And I can state with some authority 
that it never will.  The reason is that the only programs that 
exceed 64K bytes in size are coded in high-level language, not 
assembly language.  High-level language compilers follow a very, 
very restricted segmentation model-- no existing model comes 
remotely close to supporting the scheme suggested by the 
scenario.  But the 86 assembly language can support it-- the 
directives "G1 GROUP A,U" and "G2 GROUP B,U", followed by chunks 
of code of the appropriate object size, headed by directives "A 
SEGMENT", "B SEGMENT", and "U SEGMENT".  The LINK program is 
supposed to sort things out according to the scenario; but I 
can't say (and I have my doubts) if it actually succeeds in doing 
so.  

The concept of "class" was added as an afterthought, to implement 
the more sensible and usable features that outsiders thought 
GROUPs were implementing;  namely, the ability to specify that 
different (and disjoint!) segments occur consecutively in memory.  
This allows programs to be arranged in a consistent manner-- for 
example, with all program code followed by all static data 
segments followed by all dynamically-allocated memory.  



The NAME Directive

Syntax:   NAME module_name

The NAME directive specifies that "module_name" be given to LINK 
as the name of the module produced by this assembly.  The symbol 
"module_name" can be used elsewhere in your program without 
conflict: it can even, if you like, be a built-in assembler 
mnemonic (e.g. "NAME MOV" is acceptable)!  

If you do not provide a NAME directive, A86 will use the name of 
the output object file, without the .OBJ extension.   If you 
provide more than one NAME directive, A86 will use the last one 
given, with no error reported.  



The PUBLIC Directive

Syntax:   PUBLIC  sym1, sym2, sym3, ...
          PUBLIC

The PUBLIC directive allows you to explicitly list the symbols 
defined in this assembly, that can be used by other modules.  If 
you do not give any PUBLIC directives in your program, A86 will 
use every relocatable label and variable name in your program, 
except local labels (the redefinable labels consisting of a 
letter followed by digits: L7, M1, Q234, etc.).  Symbols EQUated 
to constants, and symbols defined within structures and DATA 
SEGMENTs, are not implicitly declared PUBLIC: you have to 
explicitly include them in a PUBLIC directive.  

A86 maintains an internal flag, telling it whether to figure out 
for itself which symbols are PUBLIC, or to let the program 

explicitly declare them.  The flag starts out "implicit", and is 
set to "explicit" only if A86 sees a PUBLIC directive with no 
names at all, or a PUBLIC directive containing at least one name 
that would have been implicitly made PUBLIC.  

If you are writing new code, you'll probably want to keep the 
flag "implicit".  You use the PUBLIC directive only for those 
symbols which have the form of local labels, but aren't (e.g., a 
memory variable I1987 for 1987 income); and for absolute values 
that are globally accessed -- e.g. specify "PUBLIC 
OPEN_FILES_LIMIT" for a symbol defined as "OPEN_FILES_LIMIT EQU 
20".  

If you are porting existing code, that code will already have 
PUBLIC directives in it, and A86 will go to "explicit" mode, 
duplicating the functionality of other assemblers.  

The PUBLIC directive with no names is used to force "explicit" 
mode, thus causing (if there are no further PUBLICs with names) 
the .OBJ file to declare no symbols PUBLIC.  

There is another side effect to the PUBLIC directive: if a symbol 
is declared PUBLIC in a module, it had better be defined in that 
module.  If it isn't then A86 includes it in the .ERR listing of 
undefined symbols in the module, and suppresses output of the 
object file.


The EXTRN Directive 

Syntax:  EXTRN  sym1:type, sym2:type, ...

     where "type" is one of:  BYTE WORD DWORD QWORD TBYTE FAR 
            or synonymously:  B    W    D     Q     T     F
                         or:  NEAR  ABS

The EXTRN directive allows you to attach a type to a symbol that 
may not yet be defined (and may never be defined) within your 
program.  This is often necessary for the assembler to generate 
the correct instruction form when the symbol is used as an 
operand.  All the possible types except ABS are defined elsewhere 
in the A86 language, but I list them again here for convenience: 

   B or BYTE:  byte-sized memory variable
   W or WORD:  word (2 byte) sized memory variable
   D or DWORD: doubleword (4-byte) sized memory variable
   Q or QWORD: quadword (8-byte) sized memory variable
   T or TWORD: 10-byte-sized memory variable
   NEAR:       program label accessed within a segment
   FAR:        program label accessed from outside this segment
   ABS:        an absolute number (i.e., an immediate constant)

An example of EXTRN usage is as follows: suppose there is a word 
memory variable IFARK in your program.  The variable might be 
declared at the end of the program; or it might be defined in a 
module completely outside of this program.  Without an EXTRN 
directive, A86 will assemble an instruction such as "MOV 
AX,IFARK" as the loading of an immediate constant IFARK into the 
AX register.  If you place the directive "EXTRN IFARK:W" at the 
top of your program, you'll get the correct instruction form for 

MOV AX,IFARK-- moving a word memory variable into the AX 
register.  

A86 will allow more than one EXTRN directive for a given symbol, 
as long as the same type is given every time.  A86 will even 
allow an EXTRN directive for a symbol that has already been 
defined, as long as the type declared is consistent with the 
symbol's definition.  These allowances exist so that you can 
assemble multiple files written for another assembler, that had 
been fed separately to that assembler.  

Note that EXTRN is viewed by A86 quite differently by A86 than by 
other assemblers.  In fact, if it weren't for those other 
assemblers, I'd use the mnemonic DECLARE instead of EXTRN.  A86 
doesn't really use EXTRN to determine which symbols are external-
- it uses those symbols that are undefined at the end of 
assembly.  As I stated earlier in the chapter, an undefined 
symbol can be referenced without being declared via EXTRN.  
Conversely, a defined symbol can be declared (and redeclared) via 
EXTRN; being defined, such a symbol will not be specified 
"external" in the .OBJ file.  

Because EXTRN is useful in forward-reference situations, it is 
now recognized even when A86 is assembling a .COM file.  

For those of you who are accustomed to the more traditional use 
of EXTRN, and who do not like external records to be created 
"behind your back", A86 offers the "+x" option.  If you include 
"+x" in the program invocation, A86 will require that all 
undefined symbols be explicitly declared via an EXTRN.  Any 
undefined, undeclared symbols will be included in the .ERR 
listing of undefined symbols, and object file output will be 
suppressed.


MAIN: The Starting Location for a Program

I've already stated that exactly one module in a program is the 
"main" module, containing the starting address of the entire 
program.  In A86 when assembling .OBJ files, the starting address 
is given by the label MAIN.  You simply provide the label "MAIN:" 
where you want the program to start.  The module containing MAIN 
is the main module.  


The END Directive

Syntax:  END
         END start_addr

The END directive is used by other assemblers for two purposes, 
both of which are now a little silly.  The first purpose is to 
signal the end of assembly.  This was necessary back in the days 
when source files were input on media such as paper tape: you had 
to tell the assembler explicitly that the contents of the tape 
has ended.  Today the operating system can tell you when you've 
reached the end of the file, so this function is an anachronism.  

The second purpose of END is, nonsensically, to allow you to 
specify the starting location of the program.  I suppose the 

person who wrote the first assembler back in the 1950's was too 
short on memory to implement a separate START directive, or a 
MAIN label like A86 has, and decided to let END do double-duty.  
I've always considered the example "END START" to have an Alice-
in-Wonderland quality; it is fuel for the high-level-language 
snobs who like to attack assembly language.  Please defeat the 
snobs, and use "MAIN:" if you are writing new code.  

For compatibility, A86 treats "END start_addr" exactly the same as 
if you had coded "MAIN EQU start_addr".  Note that if you want 
your program to assemble under both A86 and that other assembler, 
you can specify "END MAIN"-- A86 treats MAIN EQU MAIN as a legal 
redefinition of the symbol MAIN.  

A86 ignores END when there is no starting-address operand, thus 
allowing assembly of multiple files written for other assemblers.  


The SEGMENT Directive

Syntax:  seg_name SEGMENT [align] [combine] ['class_name']

where "align" is one of:  BYTE   WORD   PARA   PAGE
    "combine" is one of:  PUBLIC  STACK  COMMON  MEMORY  AT number

The SEGMENT directive says that assembled object code will 
henceforth go to a block of code whose name is "seg_name".  
"seg_name" is a symbol that represents a value that can be loaded 
into a segment register.  If "seg_name" is not declared in a 
GROUP directive, then its value should in fact be loaded into a 
segment register, in order to address the code.  If "seg_name" is 
declared in a GROUP directive, then the code is a a part of the 
segment addressed by the name of the group.  

A program can consist of any number of named segments, to be 
combined in numerous exotic ways to produce the final program.  
You can redirect your object output from one segment to another 
in your assembly, by providing a SEGMENT directive before each 
piece of code.  You can even return to a segment you started 
earlier, by repeating a SEGMENT with the same name-- the 
assembler just picks up where it left off, subject to some 
possible skipping for memory-alignment, that I'll describe 
shortly.  

The specifications following the word SEGMENT help to describe 
how the code in this module's part of the segment will be 
combined with code for the same segment name given in other 
modules; and also how this named segment will be grouped with 
other named segments.  Other assemblers require the 
specifications to be given in the order indicated.  A86 will 
accept any order, and will accept commas between the 
specifications if you want to provide them.  The only restriction 
is that "AT number" must be followed by a comma if it is not the 
last specification on the line.  


The "align" specification tells if each piece of code within the 
segment should be aligned so that its starting address is an even 
multiple of some number.  BYTE alignment means there is no 
requirement; WORD alignment requires each piece to start at a 

multiple of 2; PARA alignment, at a multiple of 16; PAGE 
alignment, at a multiple of 256.  For example, suppose you have a 
segment containing memory variables.  You can declare the segment 
with the statement "VAR_DATA SEGMENT WORD", which insures that 
the segment is aligned to an even memory address.  That way you 
can insure that all 16-bit and bigger memory quantities in the 
segment are aligned to even addresses, for faster access on the 
16-bit machines of the 86 family.  

There are special rules governing alignment for multiple pieces 
of the same named segment within the same program module.  Other 
assemblers outlaw conflicting alignment specifications in this 
situation; A86 accepts them, and uses the strictest specification 
given.  Furthermore, the alignment given for any specification 
beyond the first will control the alignment for that piece of 
code within this module's chunk.  For example, if a program 
contains two pieces of code headed by "VAR_DATA SEGMENT WORD", 
A86 will insert a byte between the pieces if the first piece has 
an odd number of bytes.  This insures correct assembly for 
multiple files written for another assembler.  

If no "align" type is given for any of the pieces of a named 
segment, an alignment of PARA is assumed.  


The "combine" specification tells how the chunk of code from this 
module will be combined with the chunks of the same named 
segment, that come from other modules.  Yes, I know, that sounds 
like what "align" does; but "combine" takes a different, more 
major point of view: 

* PUBLIC is the kind of combination we've been talking about all 
  along: each piece of the segment is located off the end of the 
  previously linked piece, subject to possible gaps for 
  alignment.  The size of the segment is the sum of the sizes of 
  the pieces, plus the sizes of the gaps.  

* STACK is a combination-type reserved for the system's stack 
  segment.  To illustrate how STACK segment chunks are combined, 
  let's describe the only way a stack segment should ever be 
  used.  We'll call the segment PROG_STACK; and we declare it as 
  follows: 

    PROG_STACK SEGMENT WORD STACK
       DW 100 DUP (?)
    TOP_OF_STACK:

  The code just given declares a stack area of 200 bytes (100 
  words) for this module.  If identical code occurs in each of 
  three modules which are then linked together, the resulting 
  PROG_STACK segment will have 600 bytes (the sizes are added), 
  but TOP_OF_STACK will be the same address (600) for each module 
  (each piece is overlayed at the top of the segment).  That way, 
  every module can declare and access the top of the stack, which 
  is the only static part of the stack that any code should ever 
  refer to.  
 
* COMMON is a type of memory area supported by FORTRAN.  Each 
  module's chunk of a COMMON segment starts at location 0, and 
  overlaps (usually duplicates) the pieces from all the other 

  modules.  The size of a COMMON segment is the size of the 
  largest chunk.  

* MEMORY is supposed to be another kind of COMMON segment, that 
  is distinguished by automatically being located beyond all 
  other segments in memory.  The MS_DOS LINK program, however, 
  does not implement MEMORY segments, and instead treats them 
  identically to PUBLIC (not COMMON!) segments.  I can see no 
  useful purpose to the MEMORY combine-type, since the 
  functionality can be achieved by putting a COMMON segment into 
  a 'class' by itself, that goes above all the other classes.  So 
  don't use MEMORY.  

  Sorry, I don't support the assembly of multiple files written 
  for other assemblers, that contain STACK, COMMON, or MEMORY 
  segments.  If I did, I would have to detect the file breaks, 
  and duplicate the overlapping functionality of these segment 
  types.  Since I don't think anybody out there is using these 
  esoteric types, I didn't bother to support them to that extent.  
  Objections, anyone?  

* "AT number" defines a non-combinable segment at the absolute 
  memory location whose segment register value is "number".  This 
  form is useful for initializing data in fixed locations, such 
  as the 86 interrupt vector (IVECTOR SEGMENT AT 0 followed by 
  ORG 4 * INT_NUMBER), or for reading fixed memory locations, 
  such as the BIOS variables area (BIOS_DATA SEGMENT AT 040).  

The combine-type specification can be repeated in subsequent 
pieces of a given segment, but if it is, it must be the same in 
all pieces.  

Finally, if no combine-type is ever given for a named segment in 
a module, that segment is non-combinable-- no other modules may 
define that segment; the code given in the one module constitutes 
the entire segment.  


The last specification available on a SEGMENT line is the class 
name, which is identified by being enclosed in single quotes.  
Unlike a segment name, which can be used as an instruction 
operand an hence cannot conflict with other assembler symbols, a 
class name can be assigned without regard to its usage elsewhere 
in the program.  It can even be a built-in A86 mnemonic.  In 
fact, both the SMALL and LARGE high-level-language models specify 
the class name 'CODE' for code segments, and the SMALL model 
specifies the class name 'DATA'.  

If no class name is given for a segment, A86 specifies the null 
(zero-length) string as the class name.  



DATA SEGMENT, STRUC and CODE SEGMENT Directives

The DATA SEGMENT and STRUC directives work in .OBJ mode exactly 
as they do in .COM mode-- they define a special assembly mode, in 
which declarations are made, but no object code is output.  
Offsets within DATA segments and structures are absolute, as in 
.COM mode.  Assembly resumes as before when an ENDS or CODE 

SEGMENT directive is encountered.  



The ENDS Directive

Syntax:  [seg_name] ENDS

The ENDS directive closes out the segment currently being 
assembled, and returns assembly to the segment being assembled 
before the last SEGMENT directive.  The "seg_name", if given, 
must match the name in that last SEGMENT directive.  ENDS allows 
you to "nest" segments inside one another.  For example, you can 
declare some static data variables that are specific to a certain 
section of code at the top of that section: 

  _DATA SEGMENT BYTE PUBLIC 'DATA'
    VAR1  DB ?
    VAR2  DB ?
  _DATA ENDS

These four lines can be inserted inside any other segment being 
assembled.  They will cause the two variable allocations to be 
tacked onto the segment _DATA; and assembly will then continue in 
whatever segment surrounded the four lines.  Observe that the 
"nesting" does not occur in the final program; only the 
presentation of the source code is nested.  

If you are not nesting segments inside one another, then the ENDS 
directive serves only to lend a clean, "block-structured" 
appearance to your source code.  It does not assist A86 in any 
particular way; in fact, it consumes a bit more object output 
memory (slightly reducing object output capacity) if you have 
ENDSs, rather than just starting up new segments with SEGMENT 
directives.  



Default Outer SEGMENT

Other assemblers outlaw any code outside of a SEGMENT 
declaration, forcing you to give a SEGMENT declaration before you 
can assemble anything.  A86 lets you assemble just your code; you 
don't have to worry about SEGMENTs if you don't want to.  

If you do provide code outside of all SEGMENT declarations, A86 
performs the following steps, to find a reasonable place to put 
the code: 

1. If there are any segments explicitly declared whose name is or 
   ends with "_TEXT", then the first such segment declared is 
   used.  It is as if the SEGMENT declaration appeared at the top 
   of, rather than within, the program.  

2. If there is no such explicit segment, A86 creates a BYTE 
   PUBLIC segment of class 'CODE', and proceeds to construct a 
   name for the segment.  If there are no RETF instructions in 
   the outer segment, the name chosen is "_TEXT", conforming to 
   the SMALL model of computation.  If there is a RETF 
   instruction, the name chosen is "modulename_TEXT", where 

   "modulename" is the name of this module.  Recall that 
   "modulename" comes from the NAME directive if there is one; 
   from the name of the .OBJ file if there isn't.  



The GROUP Directive

Syntax:  group_name GROUP seg_name1, seg_name2, ...


The GROUP directive causes A86 to tell LINK that all the listed 
segments can fit into a single 64K-byte block of memory, and 
instruct LINK to make that fit.  (If they won't fit, LINK will 
issue an error message.)  Having declared the group, you can then 
use "group_name" as the segment register value that will allow 
simultaneous access to all the named segments.  The order of 
names given in the list does not necessarily determine the order 
the segments will finally appear within the group.  

The most useful application of the GROUP directive is to allow 
you to structure the pieces of a program, all of whose code and 
data will fit into a single 64K segment.  You organize the pieces 
into SEGMENTs, and declare all the SEGMENTs to be within the same 
GROUP.  When the program starts, all segment registers are set to 
point to the GROUP, and you never have to worry about segment 
registers again in the program.  

WARNING: If your segments will be GROUPed in the final program, 
you should have the appropriate GROUP directive in every module 
assembled.  If you don't, then any memory pointers generated will 
be relative to the beginning of the individual named segments, 
not to the beginning of the whole group.  

Because of the obscure scenario I described in the Overview 
section, Intel does not prohibit more than one GROUP from 
containing some of the same segments; so neither does A86.  Any 
pointers within a segment will be calculated from the beginning 
of the last GROUP that the segment was declared within.  But 
again, I have my doubts as to whether LINK will handle this 
correctly.