CHAPTER 7   THE FLOATING-POINT PROCESSOR                  7-1


In this chapter, we'll refer to the various Central Processing 
Units (CPUs) as the "86".  Thus "86" refers to either the 8088, 
8086, 80186, 80286, etc.  We'll refer to the various coprocessors 
as the "87".  Thus "87" refers to either the 8087 or the 287.  


The 8087 and 287 Coprocessors

All IBM-PC's, and most clones, contain a socket for a floating-
point coprocessor.  If you shell out between $80 and $300, and 
plug the appropriate chip into that socket, then a host of 
floating-point instructions is added to the assembly-language 
instruction set.  

The original IBM-PC, and the XT, accept the original floating-
point chip, the 8087.  The AT accepts a later update, the 287.  
From a programming standpoint, the two chips are nearly 
identical: the 287 adds the instructions FSETPM and FSTSW AX, and 
ignores the instructions FENI and FDISI.  There is, however, a 
rather nasty design flaw in the 8087, that was corrected in the 
287.  

To understand the flaw, you must understand how the 86 and 87 
work as coprocessors. Whenever the 86 sees a floating-point 
instruction, it communicates the instruction, and any associated 
memory operands, to the 87.  Then the 86 goes on to its next 
instruction, operating in parallel with the 87.  That's OK, so 
long as the following instructions don't do one of the following: 

  1. Execute another floating point instruction; or
  2. Try to read the results of the still-executing floating 
     point instruction.  

If they do, then you must provide an instruction called WAIT (or 
synonymously FWAIT), which halts the 86 until the 87 is finished. 
For almost all floating-point instructions, it should not be 
necessary to provide an explicit FWAIT; the 86 ought to know that 
it should wait.  For the 8087, it IS necessary to give an 
explicit FWAIT before each floating-point instruction: that is 
the flaw.  

Because of the flaw, all assemblers supporting the 8087 will 
silently insert an FWAIT code (hex 9B) before all 87 
instructions, except those few (the FN-instructions other than 
FNOP) not requiring the FWAIT.  A86 provides the switch +F (the F 
must be capitalized), to signal that the 287 is the target 
processor.  A86 also provides the directive ".287", compatible 
with Microsoft's assembler, that you can insert into your 
programs to accomplish the same thing as +F. However, the actions 
taken by A86 and Microsoft when seeing .287 are completely 
disjoint!  To wit: 

* A86 ceases outputting FWAIT directives that are unnecessary for 
  the 287.  For reasons beyond my comprehension, Microsoft 
  continues to put them out.  Can someone enlighten me as to why 
  Microsoft is putting out those codes?  

                                                          7-2
* A86 ignores the instructions FENI, FDISI, FNENI, and FNDISI 
  after it sees a .287 directive.  Microsoft continues to 
  assemble these instructions.  

* Microsoft recognizes the new 287 instructions, if and only if 
  it sees the .287 directive.  A86 recognizes them even if .287 
  is not given.  In general, I don't attempt to police your 
  instruction usage-- if you use an instruction available on a 
  limited number of processors, I trust that you are programming 
  for one of those processors.  

In summary, if your program will be running only on machines with 
a 287, you can give ".287" directive. Your programs will be 
significantly shorter than if they were assembled by Microsoft.  
If you want your programs to run on all machines containing a 
floating-point chip, you should refrain from specifying .287. 

WARNING: The most common mistake 87 programmers make is to try to 
read the results of an 87 operation in 86 memory, before the 
results are ready.  At least on my AT, the system often crashes 
when you do this!  If your program runs correctly when single-
stepped, but crashes when set loose, then chances are you need an 
extra explicit FWAIT somewhere. 


Emulating the 8087 by Software

There is a software package provided with many compilers 
(Borland's Turbo C and most Microsoft compilers, for example) 
that emulates the 8087 instruction set.  The emulator is very 
cleverly implemented so that the programmer need not know whether 
a floating-point chip will be available, or whether emulation 
will be necessary.  This is done by having the linker replace all 
floating-point machine instructions with INT calls to certain 
interrupts, dedciated to emulation.  The interrupt handlers 
interpret the operands to the instructions, and emulate the 
8087. 

You can tell A86 that the emulator might be used, by providing a 
+f switch in the invocation line, or in the A86 environment 
variable (make sure the f is lower-case).  Since your program 
will be linked to the emulator, you must be producing an OBJ 
file, not a COM file,  for emulation support to take effect.  
Whenever a floating-point instruction is assembled, A86 will 
generate an external reference at the opcode for the instruction.  
Then, if the emulation package is linked with your program, the 
opcodes will be replaced by the INT calls. If a special non-
emulation module is linked, the opcodes will be left alone, and 
the floating-point instructions will be executed directly. 

                                                          7-3

The Floating Point Stack

The 87 has its own register set, of 8 floating-point numbers 
occupying 10 bytes each, plus 14 bytes of status and control 
information.  Many of the 87's instructions cause the numbers to 
act like a stack, much like a Hewlett-Packard calculator.  For 
this reason, the numbers are called the floating-point stack.  

The standard name for the top element of the floating-point stack 
is either ST or ST(0); the others are named ST(1) through ST(7).  
Thus, for example, the instruction to add stack element number 3 
into the top stack element is usually coded FADD ST,ST(3).  

I find this notation painfully verbose.  Especially bad are the 
parentheses, which are hard to type, and which add visual clutter 
to the program.  To alleviate this problem while retaining 
language compatibility, I name my stack elements simply 0 through 
7.  I recognize ST as a synonym for 0.  I allow expression 
elements to be concatenated; concatenation is the same as 
addition.  Thus, when A86 sees ST(3), it computes 0+3 = 3.  So 
you can code the old way, FADD ST,ST(3), or you can code the 
concise way, FADD 0,3 or simply FADD 3.  


Floating Point Initializations

In general, you use the 87 by loading numbers from 86 memory to 
the 87 stack (using FLD instructions), calculating on the 87 
stack, and storing the results back to 86 memory (using FST and 
FSTP instructions).  There are seven constant numbers built into 
the 87 instruction set: zero, one, Pi, and four logarithmic 
conversion constants.  These can be loaded using the FLD0, FLD1, 
FLDPI, FLDL2T, FLDL2E, FLDLG2, and FLDLN2 instructions.  All 
other constants must be declared in, then loaded from, 86 memory.
Integer constant words and doublewords can be loaded via FILD.
Non-integer constant doubleword, quadwords, and ten-byte numbers 
can be loaded via FLD.

A86 allows you to declare constants loaded via FLD as floating-
point numbers, using scientific notation if you like.  As an 
exclusive feature, A86 allows you to use any of the 4 arithmetic 
functions +, -, *, / in expressions involving floating-point 
numbers.  A86 will even do type conversion if one of the two 
operands is given as an integer; though for clarity I recommend 
that you always give floating-point constants with their decimal 
point.


Built-In Constant Names

A86 offers another exclusive feature: the built-in symbols

    PI   ratio of circumference to diameter of a circle
    L2T  log base 2 of 10
    L2E  log base 2 of the calculus constant e = 2.71828...
    LG2  log base 10 of 2 
    LN2  natural log (base e) of 2

                                                          7-4

You can use these symbols in expressions, to declare useful 
constants.  For example, you can declare the degrees-to-radians 
conversion constant:

    DEG_TO_RAD  DT  PI/180.


Special Immediate FLD Form

Yet another exclusive A86 feature is the instruction form
FLD constant.  This form is intended primarily to facilitate 
"fooling around" with the 87 when using D86; but it is also 
useful for quick-and-dirty programs.  For example, the 
instruction FLD 12.3 generates the following sequence of code 
bytes (without explicitly using the local labels given):

    CS FLD T[M1]
    JMP >M2
  M1  DT 12.3
  M2:

Obviously, this form is not terrifically efficient: you can 
always save the JMP by placing the constant outside of the 
instruction stream; and the CS-override might not be needed.  But 
the form is very, very convenient!

NOTE that the preceding 2 sections imply that you can get 
careless and code, for example, FLD PI when you intended FLDPI.  
Though the two are functionally equivalent, the first form takes 
a whopping 17 bytes; and second, only 2 bytes.  Be careful!



Floating Point Operand Types

The list of floating point instructions contains a variety of 
operand types.  Here is a brief explanation of those types: 

0  stands for the top element of the floating-point stack.  A 
   synonym for 0 is ST or ST(0).  

i  stands for element number i of the floating-point stack.  i 
   can range from 0 through 7.  A synonym for i is ST(i).  

mem10r is a 10-byte memory quantity (typically declared with a DT 
   directive) containing a full-precision floating point number.  
   Intel recommends that you NOT store your numbers in full 
   precision; that you use the following double precision format 
   instead.  Full-precision numbers are intended for storage of 
   intermediate results (on the stack); they exist to insure 
   maximum accuracy for calculations on double-precision numbers, 
   which is the official external format of 87 numbers.  

                                                          7-5

mem8r is an 8-byte memory quantity (typically declared with a DQ 
   directive) containing a double-precision floating-point 
   number.  This is the best format for floating-point numbers on 
   the 87.  The 87 takes the same amount of time on double-
   precision calculations as it does on single-precision.  The 
   only extra time is the memory access of 4 more bytes; 
   negligible in comparison to the calculation time.  

mem4r is a 4-byte quantity (typically defined with a DD 
   directive) containing a single-precision floating-point 
   number.  

mem10d is a 10-byte quantity (also defined via DT) containing a 
   special Binary Coded Decimal format recognized by the FBLD and 
   FBSTP instructions.  This format is useful for input and 
   output of floating-point numbers.  

mem4i is a 4-byte quantity representing a signed integer in 
   two's-complement notation.  

mem2i is a 2-byte quantity representing a signed integer in 
   two's-complement notation.  

mem14 and mem94 are 14- and 94-byte buffers containing the 87 
    machine state.  


Operand Choices in A86

The choice of operands for floating-point instructions seems 
inconsistent to me.  For example, to subtract stack i from 0, you 
must provide two operands; to do the equivalent comparison, you 
must provide only one operand.  A86 smooths out these 
inconsistencies by allowing more choices for operands: FADD i is 
equivalent to FADD 0,i.  FCOM 0,i is equivalent to FCOM i.  The 
same holds for the other main arithmetic instructions.  FXCH 0,i 
and FXCH i,0 are allowed.  So if you wish to retain compatibility 
with other assemblers, you should use their more restrictive 
instruction list, not the following one.  


The 87 Instruction Set

Following is the 87 instruction set.  The "w" in the opcode field 
is the FWAIT opcode, hex 9B, which is suppressed if .287 is 
selected.  Again, "0", "1", and "i" stand for the associated 
floating point stack registers, not constant numbers!  Constant 
numbers in the descriptions are given with decimal points: 0.0, 
1.0, 2.0, 10.0.  

                                                          7-6

 w D9 F0     F2XM1           0 := (2.0 ** 0) - 1.0
 w D9 E1     FABS            0 := |0|
 w DE C1     FADD            1 := 1 + 0, pop
 w D8 C0+i   FADD i          0 := i + 0
 w DC C0+i   FADD i,0        i := i + 0
 w D8 C0+i   FADD 0,i        0 := i + 0
 w D8 /0     FADD mem4r      0 := 0 + mem4r
 w DC /0     FADD mem8r      0 := 0 + mem8r
 w DE C0+i   FADDP i,0       i := i + 0, pop
 w DF /4     FBLD mem10d     push, 0 := mem10d
 w DF /6     FBSTP mem10d    mem10d := 0, pop
 w D9 E0     FCHS            0 := -0
9B DB E2     FCLEX           clear exceptions
 w D8 D1     FCOM            compare 0 - 1
 w D8 D0+i   FCOM 0,i        compare 0 - i
 w D8 D0+i   FCOM i          compare 0 - i
 w D8 /2     FCOM mem4r      compare 0 - mem4r
 w DC /2     FCOM mem8r      compare 0 - mem8r
 w D8 D9     FCOMP           compare 0 - 1, pop
 w D8 D8+i   FCOMP 0,i       compare 0 - i, pop
 w D8 D8+i   FCOMP i         compare 0 - i, pop
 w D8 /3     FCOMP mem4r     compare 0 - mem4r, pop
 w DC /3     FCOMP mem8r     compare 0 - mem8r, pop
 w DE D9     FCOMPP          compare 0 - 1, pop both
 w D9 F6     FDECSTP         decrement stack pointer
 w DB E1     FDISI           disable interrupts (.287 ignore)
 w DE F9     FDIV            1 := 1 / 0, pop
 w D8 F0+i   FDIV i          0 := 0 / i
 w DC F8+i   FDIV i,0        i := i / 0
 w D8 F0+i   FDIV 0,i        0 := 0 / i
 w D8 /6     FDIV mem4r      0 := 0 / mem4r
 w DC /6     FDIV mem8r      0 := 0 / mem8r
 w DE F8+i   FDIVP i,0       i := i / 0, pop
 w DE F1     FDIVR           1 := 0 / 1, pop
 w D8 F8+i   FDIVR i         0 := i / 0
 w DC F0+i   FDIVR i,0       i := 0 / i
 w D8 F8+i   FDIVR 0,i       0 := i / 0
 w D8 /7     FDIVR mem4r     0 := mem4r / 0
 w DC /7     FDIVR mem8r     0 := mem8r / 0
 w DE F0+i   FDIVRP i,0      i := 0 / i, pop
 w DB E0     FENI            enable interrupts (.287 ignore)
 w DD C0+i   FFREE i         empty i
 w DE /0     FIADD mem2i     0 := 0 + mem4i
 w DA /0     FIADD mem4i     0 := 0 + mem2i
 w DE /2     FICOM mem2i     compare 0 - mem2i
 w DA /2     FICOM mem4i     compare 0 - mem4i
 w DE /3     FICOMP mem2i    compare 0 - mem2i, pop
 w DA /3     FICOMP mem4i    compare 0 - mem4i, pop
 w DE /6     FIDIV mem2i     0 := 0 / mem2i
 w DA /6     FIDIV mem4i     0 := 0 / mem4i
 w DE /7     FIDIVR mem2i    0 := mem2i / 0
 w DA /7     FIDIVR mem4i    0 := mem4i / 0
 w DF /0     FILD mem2i      push, 0 := mem2i
 w DB /0     FILD mem4i      push, 0 := mem4i
 w DF /5     FILD mem8i      push, 0 := mem8i
 w DE /1     FIMUL mem2i     0 := 0 * mem2i
 w DA /1     FIMUL mem4i     0 := 0 * mem4i

                                                          7-7

 w D9 F7     FINCSTP         increment stack pointer
9B DB E3     FINIT           initialize 80287
 w DF /2     FIST mem2i      mem2i := 0
 w DB /2     FIST mem4i      mem4i := 0
 w DF /3     FISTP mem2i     mem2i := 0, pop
 w DB /3     FISTP mem4i     mem4i := 0, pop
 w DF /7     FISTP mem8i     mem8i := 0, pop
 w DE /4     FISUB mem2i     0 := 0 - mem2i
 w DA /4     FISUB mem4i     0 := 0 - mem4i
 w DE /5     FISUBR mem2i    0 := mem2i - 0
 w DA /5     FISUBR mem4i    0 := mem4i - 0
 w D9 C0+i   FLD i           push, 0 := old i
 w DB /5     FLD mem10r      push, 0 := mem10r
 w D9 /0     FLD mem4r       push, 0 := mem4r
 w DD /0     FLD mem8r       push, 0 := mem8r
 w D9 E8     FLD1            push, 0 := 1.0
 w D9 /5     FLDCW mem2i     control word := mem2i
 w D9 /4     FLDENV mem14    environment := mem14
 w D9 EA     FLDL2E          push, 0 := log base 2.0 of e
 w D9 E9     FLDL2T          push, 0 := log base 2.0 of 10.0
 w D9 EC     FLDLG2          push, 0 := log base 10.0 of 2.0
 w D9 ED     FLDLN2          push, 0 := log base e of 2.0
 w D9 EB     FLDPI           push, 0 := Pi
 w D9 EE     FLDZ            push, 0 := +0.0
 w DE C9     FMUL            1 := 1 * 0, pop
 w D8 C8+i   FMUL i          0 := 0 * i
 w DC C8+i   FMUL i,0        i := i * 0
 w D8 C8+i   FMUL 0,i        0 := 0 * i
 w D8 /1     FMUL mem4r      0 := 0 * mem4r
 w DC /1     FMUL mem8r      0 := 0 * mem8r
 w DE C8+i   FMULP i,0       i := i * 0, pop
   DB E2     FNCLEX          nowait clear exceptions
   DB E1     FNDISI          disable interrupts (.287 ignore)
   DB E0     FNENI           enable interrupts (.287 ignore)
   DB E3     FNINIT          nowait initialize 80287
 w D9 D0     FNOP            no operation
   DD /6     FNSAVE mem94    mem94 := 80287 state
   D9 /7     FNSTCW mem2i    mem2i := control word
   D9 /6     FNSTENV mem14   mem14 := environment
   DF E0     FNSTSW AX       AX := status word
   DD /7     FNSTSW mem2i    mem2i := status word
 w D9 F3     FPATAN          0 := arctan(1/0), pop
 w D9 F8     FPREM           0 := REPEAT(0 - 1)
 w D9 F2     FPTAN           push, 1/0 := tan(old 0)
 w D9 FC     FRNDINT         0 := round(0)
 w DD /4     FRSTOR mem94    80287 state := mem94
 w DD /6     FSAVE mem94     mem94 := 80287 state
 w D9 FD     FSCALE          0 := 0 * 2.0 ** 1
9B DB E4     FSETPM          set protection mode
 w D9 FA     FSQRT           0 := square root of 0

                                                          7-8

 w DD D0+i   FST i           i := 0
 w D9 /2     FST mem4r       mem4r := 0
 w DD /2     FST mem8r       mem8r := 0
 w D9 /7     FSTCW mem2i     mem2i := control word
 w D9 /6     FSTENV mem14    mem14 := environment
 w DD D8+i   FSTP i          i := 0, pop
 w DB /7     FSTP mem10r     mem10r := 0, pop
 w D9 /3     FSTP mem4r      mem4r := 0, pop
 w DD /3     FSTP mem8r      mem8r := 0, pop
 w DF E0     FSTSW AX        AX := status word
 w DD /7     FSTSW mem2i     mem2i := status word
 w DE E9     FSUB            1 := 1 - 0, pop
 w D8 E0+i   FSUB i          0 := 0 - i
 w DC E8+i   FSUB i,0        i := i - 0
 w D8 E0+i   FSUB 0,i        0 := 0 - i
 w D8 /4     FSUB mem4r      0 := 0 - mem4r
 w DC /4     FSUB mem8r      0 := 0 - mem8r
 w DE E8+i   FSUBP i,0       i := i - 0
 w DE E1     FSUBR           1 := 0 - 1, pop
 w D8 E8+i   FSUBR i         0 := i - 0
 w DC E0+i   FSUBR i,0       i := 0 - i
 w D8 E8+i   FSUBR 0,i       0 := i - 0
 w D8 /5     FSUBR mem4r     0 := mem4r - 0
 w DC /5     FSUBR mem8r     0 := mem8r - 0
 w DE E0+i   FSUBRP i,0      i := 0 - i, pop
 w D9 E4     FTST            compare 0 - 0.0
9B           FWAIT           wait for 80287 ready
 w D9 E5     FXAM            C3 -- C0 := type of 0
 w D9 C9     FXCH            exchange 0 and 1
 w D9 C8+i   FXCH 0,i        exchange 0 and i
 w D9 C8+i   FXCH i          exchange 0 and i
 w D9 C8+i   FXCH i,0        exchange 0 and i
 w D9 F4     FXTRACT         push, 1 := expo, 0 := sig
 w D9 F1     FYL2X           0 := 1 * log base 2.0 of 0, pop
 w D9 F9     FYL2XP1         0 := 1 * log base 2.0 of (0+1.0), pop