CHAPTER 6    THE 86 INSTRUCTION SET                       6-1

Effective Addresses

Most memory data accessing in the 86 family is accomplished via
the mechanism of the effective address.  Wherever an effective
address specifier "eb", "ew" or "ed" appears in the list of 8086
instructions, you may use a wide variety of actual operands in
that instruction.  These include general registers, memory
variables, and a variety of indexed memory quantities.

GENERAL REGISTERS: Wherever an "ew" appears, you can use any of
   the 16-bit registers AX,BX,CX,DX,SI,DI,SP, or BP.  Wherever an
   "eb" appears, you can use any of the 8-bit registers
   AL,BL,CL,DL,AH,BH,CH, or DH.  For example, the "ADD ew,rw"
   form subsumes the 16-bit register-to-register adds; for
   example, ADD AX,BX; ADD SI,BP; ADD SP,AX.

MEMORY VARIABLES: Wherever an "ew" appears, you can use a word-
   memory-variable.  Wherever an "eb" appears, you can use a
   byte-memory-variable.  Variables are typically declared in the
   DATA segment, using a DW declaration for a word-variable, or a
   DB declaration for a byte-variable.  For example, you can
   declare variables:

     DATA_PTR  DW ?
     ESC_CHAR  DB ?

   Later, you can load or store these variables:

     MOV SI,DATA_PTR    ; load DATA_PTR into SI for use
     LODSW              ; fetch the word pointed to by DATA_PTR
     MOV DATA_PTR,SI    ; store the value incremented by the LODSW
     MOV BL,ESC_CHAR    ; load the byte-variable ESC_CHAR

   Alternatively, you can address specific unnamed memory
   locations by enclosing the location value in square brackets;
   for example,

     MOV AL,[02000]     ; load contents of location 02000 into AL

   Note that A86 discerned from context (loading into AL) that a
   BYTE at 02000 was intended.  Sometimes this is impossible, and
   you must specify byte or word:

     INC B[02000]       ; increment the byte at location 02000
     MOV W[02000],0     ; set the WORD at location 02000 to zero

                                                          6-2
INDEXED MEMORY: The 86 supports the use of certain registers as
   base pointers and index registers into memory.  BX and BP are
   the base registers; SI and DI are the index registers.  You
   may combine at most one base register, at most one index
   register, and a constant number into a run-time pointer that
   determines the location of the effective address memory to be
   used in the instruction.  These can be given explicitly, by
   enclosing the index registers in brackets:

        MOV AX,[BX]
        MOV CX,W[SI+17]
        MOV AX,[BX+SI+5]
        MOV AX,[BX][SI]5 ; another way to write the same instr.

   Or, indexing can be accomplished by declaring variables in a
   based structure:

        STRUC [BP]         ; NOTE based structures are unique to A86!
          BP_SAVE   DW ?
          RET_ADDR  DW ?
          PARM1     DW ?
          PARM2     DW ?
        ENDS
        INC PARM1         ; equivalent to INC W[BP+4]

    Finally, indexing can be done by mixing explicit components
    with declared ones:

        TABLE    DB  4,2,1,3,5
        MOV AL,TABLE[BX]


Segmentation and Effective Addresses

The 86 family has four segment registers, CS, DS, ES, and SS,
used to address memory.  Each segment register points to 64K
bytes of memory within the 1-megabyte memory space of the 86.
(The start of the 64K is calculated by multiplying the segment
register value by 16; i.e., by shifting the value left by one hex
digit.)  If your program's code, data and stack areas can all fit
in the same 64K bytes, you can leave all the segment registers
set to the same value.  In that case, you won't have to think
about segment registers--no matter which one is used to address
memory, you'll still get the same 64K.  If your program needs
more than 64K, you must point one or more segment registers to
other parts of the memory space.  In this case, you must take
care that your memory references use the segment registers you
intended.

Each effective address memory access has a default segment
register, to be used if you do not explicitly specify which
segment register you wish.  For most effective addresses, the
default segment register is DS.  The exceptions are those
effective addresses that use the BP register for indexing.  All
BP-indexed memory references have a default of SS.  (This is
because BP is intended to be used for addressing local variables,
stored on the stack.)

                                                          6-3
If you wish your memory access to use a different segment
register, you provide a segment-override byte before the
instruction containing the effective address operand.  In the A86
language, you code the override by giving the name of the segment
register you wish before the instruction mnemonic.  For example,
suppose you want to load the AL register with the memory byte
pointed to by BX.  If you code MOV AL,[BX], the DS register will
be used to determine which 64K segment BX is pointing to.  If you
want the byte to come from the CS-segment instead, you code CS
MOV AL,[BX].  Be aware that the segment-override byte has effect
only upon the single instruction that follows it.  If you have a
sequence of instructions requiring overrides, you must give an
override byte before every instruction in the sequence.  (In that
case, you may wish to consider changing the value of the default
segment register for the duration of the sequence.)

NOTE: This method for providing segment-overrides is unique to
the A86 assembler!  The assemblers provided by Intel and IBM (MS-
DOS) attempt to figure out segment allocation for you, and plug
in segment-override bytes "behind your back".  In order to do
this, those assemblers require you to inform them which variables
and structures are pointed to by which segment registers.  That
is what the ASSUME directive in those assemblers is all about.  I
wrote Intel's first 86 assembler, ASM86, so I have been watching
the situation since day one.  Over the years, I have concluded
that the ASSUME-mechanism creates far, far more confusion that it
solves.  So I scrapped it; and the result is an assembler with
far less red tape.  But if your program needs more than 64K, you
do have to manage those segment registers yourself; so take care!


Effective Use of Effective Addresses

Remember that all of the common instructions of the 86 family
allow effective addresses as operands.  (The only major functions
that don't are the AL/AX specific ones: multiply, divide, and
input/output).  This means that you don't have to funnel many
through AL or AX just to do something with them.  You can perform
all the common arithmetic, PUSH/POP, and MOVes from any general
register to any general register; from any memory location
(indexed if you like) to any register; and (this is most often
overlooked) from any register TO memory.  The only thing you
can't do in general is memory-to-memory.  Among the more common
operations that inexperienced 86 programmers overlook are:

   * setting memory variables to immediate values
   * testing memory variables, and comparing them to constants
   * preserving memory variables by PUSHing and POPping them
   * incrementing and decrementing memory variables
   * adding into memory variables

                                                          6-4
Encoding of Effective Addresses

Unless you are concerned with the nitty-gritty details of 86
instruction encoding, you don't need to read this section.

Every instruction with an effective address has an encoded byte,
known as the effective address byte, following the 1-byte opcode
for the instruction. (For obscure reasons, Intel calls this byte
the ModRM byte.)  If the effective address is a memory variable,
or an indexed memory location with a non-zero constant offset,
then the effective address byte will be immediately followed by
the offset amount.  Amounts in the range -128 to +127 are given
by a single signed byte, denoted by "d8" in the table below.
Amounts requiring a 2-byte representation are denoted by "d16" in
the table below.  As with all 16-bit memory quantities in the 86
family, the word is stored with the least significant byte FIRST.

The following table of effective address byte values is organized
into 32 rows and 8 columns.  The 32 rows give the possible values
for the effective address operand: 8 registers and 24 memory
indexing modes.  A 25th indexing mode, [BP] with zero
displacement, has been pre-empted by the simple-memory-variable
case.  If you code [BP] with no displacement, you will get
[BP]+d8, with a d8-value of zero.

The 8 columns of the table reflect further information given by
the effective address byte.  Usually, this is the identity of the
other (always a register) operand of a 2-operand instruction.
Those instructions are identified by a "/r" following the opcode
byte in the instruction list.  Sometimes, the information given
supplements the opcode byte in identifying the instruction
itself.  Those instructions are identified by a "/" followed by a
digit from 0 through 7.  The digit tells which of the 8 columns
you should use to find the effective address byte.

For example, suppose you have a perverse wish to know the precise
bytes encoded by the instruction SUB B[BX+17],100.  This
instruction subtracts an immediate quantity, 100, from an
effective address quantity, B[BX+17].  By consulting the
instruction list, you find the general form SUB eb,ib.  The
opcode bytes given there are 80 /5 ib.  The "/5" denotes an
effective-address byte, whose value will be taken from column 5
of the table below.  The offset 17 decimal, which is 11 hex, will
fit in a single "d8" byte, so we take our value from the "[BX] +
d8" row.  The table tells us that the effective address byte is
6F.  Immediately following the 6F is the offset, 11 hex.
Following that is the ib-value of 100 decimal, which is 64 hex.
So the bytes generated by SUB B[BX+17],100 are 80 6F 11 64.

                                                          6-5

Table of Effective Address byte values

s  =    ES   CS   SS   DS
rb =    AL   CL   DL   BL   AH   CH   DH   BH
rw =    AX   CX   DX   BX   SP   BP   SI   DI
digit=   0    1    2    3    4    5    6    7
                                               Effective
EA byte                                         address:
values: 00   08   10   18   20   28   30   38    [BX + SI]
        01   09   11   19   21   29   31   39    [BX + DI]
        02   0A   12   1A   22   2A   32   3A    [BP + SI]
        03   0B   13   1B   23   2B   33   3B    [BP + DI]
        04   0C   14   1C   24   2C   34   3C    [SI]
        05   0D   15   1D   25   2D   35   3D    [DI]
        06   0E   16   1E   26   2E   36   3E    d16 (simple var)
        07   0F   17   1F   27   2F   37   3F    [BX]
        40   48   50   58   60   68   70   78    [BX + SI] + d8
        41   49   51   59   61   69   71   79    [BX + DI] + d8
        42   4A   52   5A   62   6A   72   7A    [BP + SI] + d8
        43   4B   53   5B   63   6B   73   7B    [BP + DI] + d8
        44   4C   54   5C   64   6C   74   7C    [SI] + d8
        45   4D   55   5D   65   6D   75   7D    [DI] + d8
        46   4E   56   5E   66   6E   76   7E    [BP] + d8
        47   4F   57   5F   67   6F   77   7F    [BX] + d8
        80   88   90   98   A0   A8   B0   B8    [BX + SI] + d16
        81   89   91   99   A1   A9   B1   B9    [BX + DI] + d16
        82   8A   92   9A   A2   AA   B2   BA    [BP + SI] + d16
        83   8B   93   9B   A3   AB   B3   BB    [BP + DI] + d16
        84   8C   94   9C   A4   AC   B4   BC    [SI] + d16
        85   8D   95   9D   A5   AD   B5   BD    [DI] + d16
        86   8E   96   9E   A6   AE   B6   BE    [BP] + d16
        87   8F   97   9F   A7   AF   B7   BF    [BX] + d16
        C0   C8   D0   D8   E0   E8   F0   F8    ew=AX   eb=AL
        C1   C9   D1   D9   E1   E9   F1   F9    ew=CX   eb=CL
        C2   CA   D2   DA   E2   EA   F2   FA    ew=DX   eb=DL
        C3   CB   D3   DB   E3   EB   F3   FB    ew=BX   eb=BL
        C4   CC   D4   DC   E4   EC   F4   FC    ew=SP   eb=AH
        C5   CD   D5   DD   E5   ED   F5   FD    ew=BP   eb=CH
        C6   CE   D6   DE   E6   EE   F6   FE    ew=SI   eb=DH
        C7   CF   D7   DF   E7   EF   F7   FF    ew=DI   eb=BH

d8 denotes an 8-bit displacement following the EA byte,
to be sign-extended and added to the index.

d16 denotes a 16-bit displacement following the EA byte,
to be added to the index.

Default segment register is SS for effective addresses containing
a BP index; DS for other memory effective addresses.

                                                          6-6
How to Read the Instruction Set Chart

The chart below summarizes the machine instructions you can
program with A86.  In order to use the chart, you need to learn
the meanings of the specifiers (each given by 2 lower-case
letters), that follow most of the instruction mnemonics.  Each
specifier indicates the type of operand (register byte, immediate
word, etc.) that follows the mnemonic to produce the given
opcodes.

"c" means the operand is a code label, pointing to a part of the
    program to be jumped to or called.  A86 will also accept a
    constant offset in this place (or a constant segment-offset
    pair in the case of "cd").  "cb" is a label within about 128
    bytes (in either direction) of the current location.  "cw" is
    a label within the same code segment as this program; "cd" is
    a pair of constants separated by a colon-- the segment value
    to the left of the colon, and the offset to the right.  Note
    that in both the cb and cw cases, the object code generated
    is the offset from the location following the current
    instruction, not the absolute location of the label operand.
    In some assemblers (most notably for the Z-80 processor) you
    have to code this offset explicitly by putting "$-" before
    every relative jump operand in your source code.  You do NOT
    need to, and should not do so with A86.

"e" means the operand is an Effective Address.  The concept of an
    Effective Address is central to the 86 machine architecture,
    and thus to 86 assembly language programming.  It is
    described in detail at the start of Chapter 8.  We summarize
    here by saying that an Effective Address is either a general-
    purpose register, a memory variable, or an indexed memory
    quantity.  For example, the instruction "ADD rb,eb" includes
    the instructions: ADD AL,BL, or ADD CH,BYTEVAR, or ADD
    DL,B[BX+17].

"i" means the operand is an immediate constant, provided as part
    of the instruction itself.  "ib" is a byte-sized constant;
    "iw" is a constant occupying a full 16-bit word.  The operand
    can also be a label, defined with a colon.  In that case, the
    immediate constant which is the location of the label is
    used.  Examples:  "MOV rw,iw" includes the instructions: MOV
    AX,17, or MOV SI,VAR_ARRAY, where "VAR_ARRAY:" appears
    somewhere in the program, defined with a colon.  NOTE that if
    VAR_ARRAY were defined without a colon, e.g., "VAR_ARRAY DW
    1,2,3", then "MOV SI,VAR_ARRAY" would be a "MOV rw,ew" NOT a
    "MOV rw,iw".  The MOV would move the contents of memory at
    VAR_ARRAY (in this case 1) into SI, instead of the location
    of the memory. To load the location, you can code "MOV
    SI,OFFSET VAR_ARRAY".

"m" means a memory variable or an indexed memory quantity; i.e.,
    any Effective Address EXCEPT a register.

"r" means the operand is a general-purpose register.  The 8 "rb"
    registers are AL,BL,CL,DL,AH,BH,CH,DH; the 8 "rw" registers
    are AX,BX,CX,DX,SI, DI,BP,SP.