6-7

WARNING: Instruction forms marked with "*" by the mnemonic are
    part of the extended 186/286/NEC instruction set.
    Instructions marked with "#" are unique to the NEC
    processors.  These instructions will NOT work on the 8088 of
    the IBM-PC; nor will they work on the 8086; nor will the NEC
    instructions work on the 186 or 286. If you wish your
    programs to run on all PC's, do not use these instructions!

Opcodes    Instruction    Description
-------    -----------    -----------
37          AAA           ASCII adjust AL (carry into AH) after addition
D5 0A       AAD           ASCII adjust before division (AX = 10*AH + AL)
D4 0A       AAM           ASCII adjust after multiply (AL/10: AH=Quo AL=Rem)
3F          AAS           ASCII adjust AL (borrow from AH) after subtraction
14 ib       ADC AL,ib     Add with carry immediate byte into AL
15 iw       ADC AX,iw     Add with carry immediate word into AX
80 /2 ib    ADC eb,ib     Add with carry immediate byte into EA byte
10 /r       ADC eb,rb     Add with carry byte register into EA byte
83 /2 ib    ADC ew,ib     Add with carry immediate byte into EA word
81 /2 iw    ADC ew,iw     Add with carry immediate word into EA word
11 /r       ADC ew,rw     Add with carry word register into EA word
12 /r       ADC rb,eb     Add with carry EA byte into byte register
13 /r       ADC rw,ew     Add with carry EA word into word register
04 ib       ADD AL,ib     Add immediate byte into AL
05 iw       ADD AX,iw     Add immediate word into AX
80 /0 ib    ADD eb,ib     Add immediate byte into EA byte
00 /r       ADD eb,rb     Add byte register into EA byte
83 /0 ib    ADD ew,ib     Add immediate byte into EA word
81 /0 iw    ADD ew,iw     Add immediate word into EA word
01 /r       ADD ew,rw     Add word register into EA word
02 /r       ADD rb,eb     Add EA byte into byte register
03 /r       ADD rw,ew     Add EA word into word register
0F 20      #ADD4S         Add CL nibbles BCD from DS:SI into ES:DI (CL even,NZ)
24 ib       AND AL,ib     Logical-AND immediate byte into AL
25 iw       AND AX,iw     Logical-AND immediate word into AX
80 /4 ib    AND eb,ib     Logical-AND immediate byte into EA byte
20 /r       AND eb,rb     Logical-AND byte register into EA byte
81 /4 iw    AND ew,iw     Logical-AND immediate word into EA word
21 /r       AND ew,rw     Logical-AND word register into EA word
22 /r       AND rb,eb     Logical-AND EA byte into byte register
23 /r       AND rw,ew     Logical-AND EA word into word register
63 /r      *ARPL ew,rw    Adjust RPL of EA word not smaller than RPL of rw
62 /r      *BOUND rw,md   INT 5 if rw not between [md] and [md+2] inclusive
9A cd       CALL cd       Call far segment, immediate 4-byte address
E8 cw       CALL cw       Call near, offset relative to next instruction
FF /3       CALL ed       Call far segment, address at EA doubleword
FF /2       CALL ew       Call near, offset absolute at EA word
0F FF ib   #CALL80 ib     Call 8080-emulation code at INT number ib
98          CBW           Convert byte into word (AH = top bit of AL)
F8          CLC           Clear carry flag
FC          CLD           Clear direction flag so SI and DI will increment
FA          CLI           Clear interrupt enable flag; interrupts disabled
0F 12/0    #CLRBIT eb,CL  Clear bit CL of eb
0F 13/0    #CLRBIT ew,CL  Clear bit CL of ew
0F 1A/0 ib #CLRBIT eb,ib  Clear bit ib of eb
0F 1B/0 ib #CLRBIT ew,ib  Clear bit ib of ew

                                                          6-8

0F 06      *CLTS          Clear task switched flag
F5          CMC           Complement carry flag
3C ib       CMP AL,ib     Subtract immediate byte from AL for flags only
3D iw       CMP AX,iw     Subtract immediate word from AX for flags only
80 /7 ib    CMP eb,ib     Subtract immediate byte from EA byte for flags only
38 /r       CMP eb,rb     Subtract byte register from EA byte for flags only
83 /7 ib    CMP ew,ib     Subtract immediate byte from EA word for flags only
81 /7 iw    CMP ew,iw     Subtract immediate word from EA word for flags only
39 /r       CMP ew,rw     Subtract word register from EA word for flags only
3A /r       CMP rb,eb     Subtract EA byte from byte register for flags only
3B /r       CMP rw,ew     Subtract EA word from word register for flags only
0F 26      #CMP4S         Compare CL nibbles CD at DS:SI from ES:DI (CL even,NZ)
A6          CMPS mb,mb    Compare bytes ES:[DI] from [SI], advance SI and DI
A7          CMPS mw,mw    Compare words ES:[DI] from [SI], advance SI and DI
A6          CMPSB         Compare bytes ES:[DI] from DS:[SI], advance SI and DI
A7          CMPSW         Compare words ES:[DI] from DS:[SI], advance SI and DI
99          CWD           Convert word to doubleword (DX = top bit of AX)
27          DAA           Decimal adjust AL after addition
2F          DAS           Decimal adjust AL after subtraction
FE /1       DEC eb        Decrement EA byte by 1
FF /1       DEC ew        Decrement EA word by 1
48+rw       DEC rw        Decrement word register by 1
F6 /6       DIV eb        Unsigned divide AX by EA byte (AL=Quo AH=Rem)
F7 /6       DIV ew        Unsigned divide DXAX by EA word (AX=Quo DX=Rem)
C8 iw 00   *ENTER iw,0    Make stack frame, iw bytes local storage, 0 levels
C8 iw 01   *ENTER iw,1    Make stack frame, iw bytes local storage, 1 level
C8 iw ib   *ENTER iw,ib   Make stack frame, iw bytes local storage, ib levels
            Fany          Floating point set is in Chapter 7
F4          HLT           Halt
F6 /7       IDIV eb       Signed divide AX by EA byte (AL=Quo AH=Rem)
F7 /7       IDIV ew       Signed divide DXAX by EA word (AX=Quo DX=Rem)
F6 /5       IMUL eb       Signed multiply (AX = AL * EA byte)
F7 /5       IMUL ew       Signed multiply (DXAX = AX * EA word)
6B /r ib   *IMUL rw,ib    Signed multiply immediate byte into word register
69 /r iw   *IMUL rw,iw    Signed multiply immediate word into word register
69 /r iw   *IMUL rw,ew,iw Signed multiply (rw = EA word * immediate word)
6B /r ib   *IMUL rw,ew,ib Signed multiply (rw = EA word * immediate byte)
E4 ib       IN AL,ib      Input byte from immediate port into AL
EC          IN AL,DX      Input byte from port DX into AL
E5 ib       IN AX,ib      Input word from immediate port into AX
ED          IN AX,DX      Input word from port DX into AX
FE /0       INC eb        Increment EA byte by 1
FF /0       INC ew        Increment EA word by 1
40+rw       INC rw        Increment word register by 1
6C         *INS eb,DX     Input byte from port DX into [DI]
6D         *INS ew,DX     Input word from port DX into [DI]
6C         *INSB          Input byte from port DX into ES:[DI]
6D         *INSW          Input word from port DX into ES:[DI]
CC          INT 3         Interrupt 3 (trap to debugger) (far call, with flags
CD ib       INT ib        Interrupt numbered by immediate byte     pushed first)
CE          INTO          Interrupt 4 if overflow flag is 1
CF          IRET          Interrupt return (far return and pop flags)

                                                          6-9

77 cb       JA cb         Jump short if above (CF=0 and ZF=0)    above=UNSIGNED
73 cb       JAE cb        Jump short if above or equal (CF=0)
72 cb       JB cb         Jump short if below (CF=1)             below=UNSIGNED
76 cb       JBE cb        Jump short if below or equal (CF=1 or ZF=1)
72 cb       JC cb         Jump short if carry (CF=1)
E3 cb       JCXZ cb       Jump short if CX register is zero
74 cb       JE cb         Jump short if equal (ZF=1)
7F cb       JG cb         Jump short if greater (ZF=0 and SF=OF)  greater=SIGNED
7D cb       JGE cb        Jump short if greater or equal (SF=OF)
7C cb       JL cb         Jump short if less (SF/=OF)                less=SIGNED
7E cb       JLE cb        Jump short if less or equal (ZF=1 or SF/=OF)
EB cb       JMP cb        Jump short (signed byte relative to next instruction)
EA cd       JMP cd        Jump far (4-byte immediate address)
E9 cw       JMP cw        Jump near (word offset relative to next instruction)
FF /4       JMP ew        Jump near to EA word (absolute offset)
FF /5       JMP md        Jump far (4-byte address in memory doubleword)
76 cb       JNA cb        Jump short if not above (CF=1 or ZF=1)
72 cb       JNAE cb       Jump short if not above or equal (CF=1)
73 cb       JNB cb        Jump short if not below (CF=0)
77 cb       JNBE cb       Jump short if not below or equal (CF=0 and ZF=0)
73 cb       JNC cb        Jump short if not carry (CF=0)
75 cb       JNE cb        Jump short if not equal (ZF=0)
7E cb       JNG cb        Jump short if not greater (ZF=1 or SF/=OF)
7C cb       JNGE cb       Jump short if not greater or equal (SF/=OF)
7D cb       JNL cb        Jump short if not less (SF=OF)
7F cb       JNLE cb       Jump short if not less or equal (ZF=0 and SF=OF)
71 cb       JNO cb        Jump short if not overflow (OF=0)
7B cb       JNP cb        Jump short if not parity (PF=0)
79 cb       JNS cb        Jump short if not sign (SF=0)
75 cb       JNZ cb        Jump short if not zero (ZF=0)
70 cb       JO cb         Jump short if overflow (OF=1)
7A cb       JP cb         Jump short if parity (PF=1)
7A cb       JPE cb        Jump short if parity even (PF=1)
7B cb       JPO cb        Jump short if parity odd (PF=0)
78 cb       JS cb         Jump short if sign (SF=1)
74 cb       JZ cb         Jump short if zero (ZF=1)
9F          LAHF          Load: AH = flags  SF ZF xx AF xx PF xx CF
0F 02 /r   *LAR rw,ew     Load: high(rw) = Access Rights byte, selector ew
C5 /r       LDS rw,ed     Load EA doubleword into DS and word register
8D /r       LEA rw,m      Calculate EA offset given by M, place in rw
C9         *LEAVE         Set SP to BP, then POP BP (reverses previous ENTER)
C4 /r       LES rw,ed     Load EA doubleword into ES and word register
0F 01 /2   *LGDT m        Load 6 bytes at m into Global Descriptor Table reg
0F 01 /3   *LIDT m        Load 6 bytes at m into Interrupt Descriptor Table reg
0F 00 /2   *LLDT ew       Load selector ew into Local Descriptor Table reg
0F 01 /6   *LMSW ew       Load EA word into Machine Status Word
F0          LOCK (prefix) Assert BUSLOCK signal for the next instruction
0F 33/r    #LODBITS rb,rb Load AX with DS:SI,bit rb (incr. SI,rb), rb+1 bits
0F 3B/0 ib #LODBITS rb,ib Load AX with DS:SI,bit rb (incr. SI,rb), ib+1 bits
AC          LODS mb       Load byte [SI] into AL, advance SI
AD          LODS mw       Load byte [SI] into AL, advance SI
AC          LODSB         Load byte [SI] into AL, advance SI
AD          LODSW         Load byte [SI] into AL, advance SI

                                                          6-10

E2 cb       LOOP cb       noflags DEC CX; jump short if CX/=0
E1 cb       LOOPE cb      noflags DEC CX; jump short if CX/=0 and equal (ZF=1)
E0 cb       LOOPNE cb     noflags DEC CX; jump short if CX/=0 and not equal
E0 cb       LOOPNZ cb     noflags DEC CX; jump short if CX/=0 and ZF=0
E1 cb       LOOPZ cb      noflags DEC CX; jump short if CX/=0 and zero (ZF=1)
0F 03 /r   *LSL rw,ew     Load: rw = Segment Limit, selector ew
0F 00 /3   *LTR ew        Load EA word into Task Register
A0 iw       MOV AL,xb     Move byte variable (offset iw) into AL
A1 iw       MOV AX,xw     Move word variable (offset iw) into AX
8E /3       MOV DS,mw     Move memory word into DS
8E /3       MOV DS,rw     Move word register into DS
C6 /0 ib    MOV eb,ib     Move immediate byte into EA byte
88 /r       MOV eb,rb     Move byte register into EA byte
8E /0       MOV ES,mw     Move memory word into ES
8E /0       MOV ES,rw     Move word register into ES
8C /1       MOV ew,CS     Move CS into EA word
8C /3       MOV ew,DS     Move DS into EA word
C7 /0 iw    MOV ew,iw     Move immediate word into EA word
8C /0       MOV ew,ES     Move ES into EA word
89 /r       MOV ew,rw     Move word register into EA word
8C /2       MOV ew,SS     Move SS into EA word
B0+rb ib    MOV rb,ib     Move immediate byte into byte register
8A /r       MOV rb,eb     Move EA byte into byte register
B8+rw iw    MOV rw,iw     Move immediate word into word register
8B /r       MOV rw,ew     Move EA word into word register
8E /2       MOV SS,mw     Move memory word into SS
8E /2       MOV SS,rw     Move word register into SS
A2 iw       MOV xb,AL     Move AL into byte variable (offset iw)
A3 iw       MOV xw,AX     Move AX into word register (offset iw)
A4          MOVS mb,mb    Move byte [SI] to ES:[DI], advance SI and DI
A5          MOVS mw,mw    Move word [SI] to ES:[DI], advance SI and DI
A4          MOVSB         Move byte DS:[SI] to ES:[DI], advance SI and DI
A5          MOVSW         Move word DS:[SI] to ES:[DI], advance SI and DI
F6 /4       MUL eb        Unsigned multiply (AX = AL * EA byte)
F7 /4       MUL ew        Unsigned multiply (DXAX = AX * EA word)
F6 /3       NEG eb        Two's complement negate EA byte
F7 /3       NEG ew        Two's complement negate EA word
            NIL (prefix)  Special "do-nothing" opcode assembles no code
90          NOP           No Operation
F6 /2       NOT eb        Reverse each bit of EA byte
F7 /2       NOT ew        Reverse each bit of EA word
0F 16/0    #NOTBIT eb,CL  Complement bit CL of eb
0F 17/0    #NOTBIT ew,CL  Complement bit CL of ew
0F 1E/0 ib #NOTBIT eb,ib  Complement bit ib of eb
0F 1F/0 ib #NOTBIT ew,ib  Complement bit ib of ew
0C ib       OR AL,ib      Logical-OR immediate byte into AL
0D iw       OR AX,iw      Logical-OR immediate word into AX
80 /1 ib    OR eb,ib      Logical-OR immediate byte into EA byte
08 /r       OR eb,rb      Logical-OR byte register into EA byte
81 /1 iw    OR ew,iw      Logical-OR immediate word into EA word
09 /r       OR ew,rw      Logical-OR word register into EA word
0A /r       OR rb,eb      Logical-OR EA byte into byte register
0B /r       OR rw,ew      Logical-OR EA word into word register

                                                          6-11

E6 ib       OUT ib,AL     Output byte AL to immediate port number ib
E7 ib       OUT ib,AX     Output word AX to immediate port number ib
EE          OUT DX,AL     Output byte AL to port number DX
EF          OUT DX,AX     Output word AX to port number DX
6E         *OUTS DX,eb    Output byte [SI] to port number DX, advance SI
6F         *OUTS DX,ew    Output word [SI] to port number DX, advance SI
6E         *OUTSB         Output byte DS:[SI] to port number DX, advance SI
6F         *OUTSW         Output word DS:[SI] to port number DX, advance SI
1F          POP DS        Set DS to top of stack, increment SP by 2
07          POP ES        Set ES to top of stack, increment SP by 2
8F /0       POP mw        Set memory word to top of stack, increment SP by 2
58+rw       POP rw        Set word register to top of stack, increment SP by 2
17          POP SS        Set SS to top of stack, increment SP by 2
61         *POPA          Pop DI,SI,BP,SP,BX,DX,CX,AX (SP value is ignored)
9D          POPF          Set flags register to top of stack, increment SP by 2
0E          PUSH CS       Set [SP-2] to CS, then decrement SP by 2
1E          PUSH DS       Set [SP-2] to DS, then decrement SP by 2
06          PUSH ES       Set [SP-2] to ES, then decrement SP by 2
6A ib      *PUSH ib       Push sign-extended immediate byte
68 iw      *PUSH iw       Set [SP-2] to immediate word, then decrement SP by 2
FF /6       PUSH mw       Set [SP-2] to memory word, then decrement SP by 2
50+rw       PUSH rw       Set [SP-2] to word register, then decrement SP by 2
16          PUSH SS       Set [SP-2] to SS, then decrement SP by 2
60         *PUSHA         Push AX,CX,DX,BX,original SP,BP,SI,DI
9C          PUSHF         Set [SP-2] to flags register, then decrement SP by 2
D0 /2       RCL eb,1      Rotate 9-bit quantity (CF, EA byte) left once
D2 /2       RCL eb,CL     Rotate 9-bit quantity (CF, EA byte) left CL times
C0 /2 ib   *RCL eb,ib     Rotate 9-bit quantity (CF, EA byte) left ib times
D1 /2       RCL ew,1      Rotate 17-bit quantity (CF, EA word) left once
D3 /2       RCL ew,CL     Rotate 17-bit quantity (CF, EA word) left CL times
C1 /2 ib   *RCL ew,ib     Rotate 17-bit quantity (CF, EA word) left ib times
D0 /3       RCR eb,1      Rotate 9-bit quantity (CF, EA byte) right once
D2 /3       RCR eb,CL     Rotate 9-bit quantity (CF, EA byte) right CL times
C0 /3 ib   *RCR eb,ib     Rotate 9-bit quantity (CF, EA byte) right ib times
D1 /3       RCR ew,1      Rotate 17-bit quantity (CF, EA word) right once
D3 /3       RCR ew,CL     Rotate 17-bit quantity (CF, EA word) right CL times
C1 /3 ib   *RCR ew,ib     Rotate 17-bit quantity (CF, EA word) right ib times
F3          REP (prefix)  Repeat following MOVS,LODS,STOS,INS, or OUTS CX times
65         #REPC (prefix) Repeat following CMPS or SCAS CX times or until CF=0
F3          REPE (prefix) Repeat following CMPS or SCAS CX times or until ZF=0
64         #REPNC (prefix)Repeat following CMPS or SCAS CX times or until CF=1
F2          REPNE (prefix)Repeat following CMPS or SCAS CX times or until ZF=1
F2          REPNZ (prefix)Repeat following CMPS or SCAS CX times or until ZF=0
F3          REPZ (prefix) Repeat following CMPS or SCAS CX times or until ZF=1
CB          RETF          Return to far caller (pop offset, then seg)
C3          RET           Return to near caller (pop offset only)
CA iw       RETF iw       RET (far), pop offset, seg, iw bytes
C2 iw       RET iw        RET (near), pop offset, iw bytes pushed before Call

                                                          6-12

D0 /0       ROL eb,1      Rotate 8-bit EA byte left once
D2 /0       ROL eb,CL     Rotate 8-bit EA byte left CL times
C0 /0 ib   *ROL eb,ib     Rotate 8-bit EA byte left ib times
D1 /0       ROL ew,1      Rotate 16-bit EA word left once
D3 /0       ROL ew,CL     Rotate 16-bit EA word left CL times
C1 /0 ib   *ROL ew,ib     Rotate 16-bit EA word left ib times
0F 28/0    #ROL4 eb       Rotate nibbles: Heb=Leb   HAL,Leb=LAL  LAL=Heb
D0 /1       ROR eb,1      Rotate 8-bit EA byte right once
D2 /1       ROR eb,CL     Rotate 8-bit EA byte right CL times
C0 /1 ib   *ROR eb,ib     Rotate 8-bit EA byte right ib times
D1 /1       ROR ew,1      Rotate 16-bit EA word right once
D3 /1       ROR ew,CL     Rotate 16-bit EA word right CL times
C1 /1 ib   *ROR ew,ib     Rotate 16-bit EA word right ib times
0F 2A/0    #ROR4 eb       Rotate nibbles: Leb=Heb   Heb=LAL  AL=eb
9E          SAHF          Store AH into flags  SF ZF xx AF xx PF xx CF
D0 /4       SAL eb,1      Multiply EA byte by 2, once
D2 /4       SAL eb,CL     Multiply EA byte by 2, CL times
C0 /4 ib   *SAL eb,ib     Multiply EA byte by 2, ib times
D1 /4       SAL ew,1      Multiply EA word by 2, once
D3 /4       SAL ew,CL     Multiply EA word by 2, CL times
C1 /4 ib   *SAL ew,ib     Multiply EA word by 2, ib times
D0 /7       SAR eb,1      Signed divide EA byte by 2, once
D2 /7       SAR eb,CL     Signed divide EA byte by 2, CL times
C0 /7 ib   *SAR eb,ib     Signed divide EA byte by 2, ib times
D1 /7       SAR ew,1      Signed divide EA word by 2, once
D3 /7       SAR ew,CL     Signed divide EA word by 2, CL times
C1 /7 ib   *SAR ew,ib     Signed divide EA word by 2, ib times
1C ib       SBB AL,ib     Subtract with borrow immediate byte from AL
1D iw       SBB AX,iw     Subtract with borrow immediate word from AX
80 /3 ib    SBB eb,ib     Subtract with borrow immediate byte from EA byte
18 /r       SBB eb,rb     Subtract with borrow byte register from EA byte
83 /3 ib    SBB ew,ib     Subtract with borrow immediate byte from EA word
81 /3 iw    SBB ew,iw     Subtract with borrow immediate word from EA word
19 /r       SBB ew,rw     Subtract with borrow word register from EA word
1A /r       SBB rb,eb     Subtract with borrow EA byte from byte register
1B /r       SBB rw,ew     Subtract with borrow EA word from word register
AE          SCAS mb       Compare bytes AL - ES:[DI], advance DI
AF          SCAS mw       Compare words AL - ES:[DI], advance DI
AE          SCASB         Compare bytes AX - ES:[DI], advance DI
AF          SCASW         Compare words AX - ES:[DI], advance DI
0F 14/0    #SETBIT eb,CL  Set bit CL of eb
0F 15/0    #SETBIT ew,CL  Set bit CL of ew
0F 1C/0 ib #SETBIT eb,ib  Set bit ib of eb
0F 1D/0 ib #SETBIT ew,ib  Set bit ib of ew
0F 01 /0   *SGDT m        Store 6-byte Global Descriptor Table register to M
D0 /4       SHL eb,1      Multiply EA byte by 2, once
D2 /4       SHL eb,CL     Multiply EA byte by 2, CL times
C0 /4 ib   *SHL eb,ib     Multiply EA byte by 2, ib times
D1 /4       SHL ew,1      Multiply EA word by 2, once
D3 /4       SHL ew,CL     Multiply EA word by 2, CL times
C1 /4 ib   *SHL ew,ib     Multiply EA word by 2, ib times

                                                          6-13

D0 /5       SHR eb,1      Unsigned divide EA byte by 2, once
D2 /5       SHR eb,CL     Unsigned divide EA byte by 2, CL times
C0 /5 ib   *SHR eb,ib     Unsigned divide EA byte by 2, ib times
D1 /5       SHR ew,1      Unsigned divide EA word by 2, once
D3 /5       SHR ew,CL     Unsigned divide EA word by 2, CL times
C1 /5 ib   *SHR ew,ib     Unsigned divide EA word by 2, ib times
0F 01 /1   *SIDT m        Store 6-byte Interrupt Descriptor Table register to M
0F 00 /0   *SLDT ew       Store Local Descriptor Table register to EA word
0F 01 /4   *SMSW ew       Store Machine Status Word to EA word
F9          STC           Set carry flag
FD          STD           Set direction flag so SI and DI will decrement
FB          STI           Set interrupt enable flag, interrupts enabled
0F 31/r    #STOBITS rb,rb Store AX to ES:DI,bit rb (incr. DI,rb), rb+1 bits
0F 39/0 ib #STOBITS rb,ib Store AX to ES:DI,bit rb (incr. DI,rb), ib+1 bits
AA          STOS mb       Store AL to byte [DI], advance DI
AB          STOS mw       Store AX to word [DI], advance DI
AA          STOSB         Store AL to byte ES:[DI], advance DI
AB          STOSW         Store AX to word ES:[DI], advance DI
0F 00 /1   *STR ew        Store Task Register to EA word
2C ib       SUB AL,ib     Subtract immediate byte from AL
2D iw       SUB AX,iw     Subtract immediate word from AX
80 /5 ib    SUB eb,ib     Subtract immediate byte from EA byte
28 /r       SUB eb,rb     Subtract byte register from EA byte
83 /5 ib    SUB ew,ib     Subtract immediate byte from EA word
81 /5 iw    SUB ew,iw     Subtract immediate word from EA word
29 /r       SUB ew,rw     Subtract word register from EA word
2A /r       SUB rb,eb     Subtract EA byte from byte register
2B /r       SUB rw,ew     Subtract EA word from word register
0F 22      #SUB4S         Sub CL nibbles BCD at DS:SI from ES:DI (CL even,NZ)
A8 ib       TEST AL,ib    AND immediate byte into AL for flags only
A9 iw       TEST AX,iw    AND immediate word into AX for flags only
F6 /0 ib    TEST eb,ib    AND immediate byte into EA byte for flags only
84 /r       TEST eb,rb    AND byte register into EA byte for flags only
F7 /0 iw    TEST ew,iw    AND immediate word into EA word for flags only
85 /r       TEST ew,rw    AND word register into EA word for flags only
84 /r       TEST rb,eb    AND EA byte into byte register for flags only
85 /r       TEST rw,ew    AND EA word into word register for flags only
0F 10/0    #TESTBIT eb,CL Test bit CL of eb, set Z flag
0F 11/0    #TESTBIT ew,CL Test bit CL of ew, set Z flag
0F 18/0 ib #TESTBIT eb,ib Test bit ib of eb, set Z flag
0F 19/0 ib #TESTBIT ew,ib Test bit ib of ew, set Z flag
9B          WAIT          Wait until BUSY pin is inactive (HIGH)
0F 00 /4   *VERR ew       Set ZF=1 if segment can be read, selector ew
0F 00 /5   *VERW ew       Set ZF=1 if segment can be written to, selector ew

                                                          6-14

9r          XCHG AX,rw    Exchange word register with AX
86 /r       XCHG eb,rb    Exchange byte register with EA byte
87 /r       XCHG ew,rw    Exchange word register with EA word
86 /r       XCHG rb,eb    Exchange EA byte with byte register
9r          XCHG rw,AX    Exchange  with word register
87 /r       XCHG rw,ew    Exchange EA word with word register
D7          XLAT mb       Set AL to memory byte [BX + unsigned AL]
D7          XLATB         Set AL to memory byte DS:[BX + unsigned AL]
34 ib       XOR AL,ib     Exclusive-OR immediate byte into AL
35 iw       XOR AX,iw     Exclusive-OR immediate word into AX
80 /6 ib    XOR eb,ib     Exclusive-OR immediate byte into EA byte
30 /r       XOR eb,rb     Exclusive-OR byte register into EA byte
81 /6 iw    XOR ew,iw     Exclusive-OR immediate word into EA word
31 /r       XOR ew,rw     Exclusive-OR word register into EA word
32 /r       XOR rb,eb     Exclusive-OR EA byte into byte register
33 /r       XOR rw,ew     Exclusive-OR EA word into word register

* Starred forms will not execute on 8086/8088!  See note at top of chart.
# These instructions work only on NEC chips!  See note at top of chart.