b r a n d X  S Y M B O L I C  D E B U G G E R
                         version 2.1

                      by  Sonam G Gyato


INTRODUCTION:

This program is a full-screen software debugger for the IBM
PC/XT series of personal computers. Even though it has been
specifically written for these machines, it will also work on
others that are 100% compatible.

This release supports both the MONOCHROME (MDA) and the COLOR
GRAPHICS (CGA) display adaptors (not the EGA). For example,
you can trace through a graphics program, a pixel at a time.
bXd is able to do this by trapping the BIOS video calls found in
the IBM machines. Therefore, it is very important for non-IBM
users, that your computer's BIOS routines be very similar to
that of IBMs.

For proper operation, it is important that all video related
calls go via DOS or BIOS routines. In the case of the CGA
users, bXd screen always uses memory locations BB00:0 to BBFF:F
(in 80x25 text modes, this is the last of the four display
pages). Therefore you can write to the screen directly for the
first three pages, but for the last one you have to go via DOS
or BIOS routines.

Some of the other major features of this program are
    - Hardware Reset Switch
      This gives the user the ability to trap any runaway program
      dead in its track. It is really of great help.

    - Specify addresses by symbolic names
      bXd supports symbolic names by reading in files generated
      by your linker. Two formats are supported. One of them
      being the format generated by the MSDOS linker.

    - Online HELP
      Detailed help on the different commands are available.
      First time users are encouraged to go through them all
      atleast once.

When developing a new product, one of the biggest problems faced
by designers is the balance between the ability and the
complexity of the program. Make it simple to use...it has
little power, make it powerful...it becomes difficult to use.

I hope that users will find out that I have followed the middle
road. Even though this program will be used by mostly computer
literate people, I have made the program easy to learn and use.
At the same time, it has commands powerful enough to debug
programs easily.



LOADING bXd:

Below is the format of invoking bXd from the DOS prompt.

     A>bXd [userprog[.COM]] [user_arguments] [<userCON.txt]

1.   The first argument is the optional name of the program to be
     debugged. If no extension is given, then a COM file is
     assumed. In the case of EXE files, you have to specify the
     extension explicitly.

     If a filename is given, then bXd tries to load the symbol
     file associated with it.
     More on the symbol file format later.

2.   The second set of arguments is what will be passed to your
     program as its command line. This text is found at offset
     81H in your programs PSP (read DOS tech manual for more
     information on PSPs).

3.   The last argument enables you to redirect the input and
     output to another device besides the console. This might be
     of some help if you're debugging a program that expects
     input from DOS console i/o routines.


     EX:  A>bXd userprog

     In the above case, bXd will load the file <USERPROG.COM> and
     try to load the symbol file. After that it will print the
     status of the file loading procedure (whether the file was
     found or not...etc) and then prompt you will "press any
     key."

     After pressing a key, then the bXd debug screen will be
     displayed.




SCREEN FORMAT:

The bXd screen is divided into 6 different windows.


     +------------------------------------------+
     | DATA                                     |
     +-----------------------+------------+-----+
     | CODE                  | REGISTER   |     |
     |                       |            +-----+
     |                       |            |STACK|
     |                       |            |     |
     +-----------------------+------------+-----+
     | USER                  | CURNT WINDOW HELP|
     +-----------------------+------------------+

     USER
     This is the window from which all commands are issued. There
     are two ways to give the commands -
       -  Command Line Input
          this is the method implemented by most debuggers. You
          type in a line consisting of a command identifier
          alphabet and optional arguments.
       -  Single Key Input
          the second method is via special keys like the
          function and cursor keys.

     CODE
     The program code is disassembled in this window. You can
     scroll the information from the USER window with the cursor
     keys.

     REGISTER
     The current user register values are displayed here. All the
     values are in hex.

     DATA
     Memory is displayed in this window in both hex-ascii and
     ascii format. You can scroll the information from the USER
     window with the <cntrl-PgUp> and <cntrl-PgDn> keys.

     STACK
     The current values pointed to by the STACK POINTER (SP)
     register is displayed. The value at the bottom it the word
     pointed to by SS:SP and all the values above it are the
     contents of successive memory locations.

     CURRENT WINDOW HELP
     This window displays a brief HELP text on the current
     window. The current window is the window in which the cursor
     is positioned. The default is the USER window.



COMMANDS

There is online HELP available on all the commands. From the USER
window, press function key FK1. Pressing that key, will display
the HELP menu in the CODE window. Using the CURNT WINDOW HELP,
you can get help on all the commands.

     Single Key Input Commands:

     FK1  Display the HELP menu.

     FK2  Display the current user screen.
          This is the screen to which all the console output will
          go. If the current mode happens to be graphics, then
          the screen will be displayed in that mode. Once
          displayed, press any key to return to the debugger.

          For CGA users, if you're in a text mode and wish to see
          another page; instead of pressing FK2, press the shift
          key and a function key ranging from 1 to 8 (FK1-FK8).
          If the current display mode is 40x25 text modes then
          all the eight keys are valid. In 80x25 text modes, only
          the first four function keys are valid.

     FK5  Toggle the current condition for the INT and REPx
          instructions.
          Default is OFF.

     FK6  Toggle the current condition for the CALL instructions.
          Default is ON.

     FK7  Single step one instruction.
          The INT, REPx and the CALL instructions are treated in
          a special way. You can trace through or bypass them.

          The current trace conditions for these instructions are
          displayed at the bottom of the debug screen. The
          condition for the INT and REPx instructions are linked
          (meaning that one condition controls both instrs). If
          the condition is YES, then the instructions will be
          traced through. If the condition is NO, then the
          interim instructions are skipped.

     FK8  Edit breakpoints.
          There are ten breakpoints available. You can select a
          particular brkpt to edit by using the cursor keys.

          There are five fields for each brkpt. You can select a
          particular field by using the TAB (next field) and the
          shift-TAB (previous field) keys.

          ON/OFF    Press the SPACE key to toggle the current state.
          SEGMENT   Segment value of the breakpoint address
                    default is the current code segment value.
          OFFSET    offset value.
          HIT       number of times the above addr needs to be
                    executed before a brkpt is signalled.
                    default is 1.
          CONTROL   For each brkpt, one or two control conditions can
                    be set. Each condition consists of two
                    operands and a binary operator. The operands
                    can be either register names or hex
                    constants. If two such conditions are
                    specified, then both have to be met before a
                    brkpt is signalled.

                    When editing, type in the condition and press
                    the RETURN key, If there is a syntax error,
                    then cursor will be positioned under the
                    wrong letter. Below are few examples using
                    the eight operators allowed.

                                         Brkpt signalled when...
                    AX == 4;............ AX is equal to 4
                    DH != BH;........... DH is not equal to BH
                    CX & 0001;.......... bit#0 of CX is set
                    FL ^ 2;............. bit#1 of FLAG is reset
                    AX > 8;AX < 10...... AX gtr than 8 AND if less than 10
                    DH >= BH;456 <= AX.. DH gtr than equal to BH
                                         AND
                                         456 is less than equal to AX

     Command Line Input:

     This is the format most are familiar with. It consists of a
     command id followed by an optional argument. This argument,
     which is actually an address, can be specified in various
     ways. You can specify an offset value or a segment value
     (terminated by colon) or a value with both segment and
     offset (separated by colon).

     The values can be typed as hex constant, register names or
     as symbolic names (provided a symbol file has be read). Also
     the binary operators + and - are allowed.

     Below are few examples using the Display command.

          d ds:100
          d ds:MAIN
          d es-1:
          d bp+si

     For information on individual commands, refer to the
     online help facility.


SYMBOL FILE FORMAT:

When the user program is loaded for debugging, bXd tries to load
the symbol file associated with that program. These files are
usually generated by your linker. This version can read in upto
200 labels and supports two different file formats.

The first, is a file having the same name as the program but with
the extension SYM. For example, if the program name is PROG.EXE,
then the symbol file associated with it would be PROG.SYM.

The format of the file is lines consisting of hex constants,
space and the ascii symbolic name associated with it. Below is
such an example. Note that underscore and dollar characters are
valid.

     034F nmi_
     03C7 wrt_reg
     04DB continue
     046C wrt$hex
     052B start

The second format is the file that is generated by the MSDOS
linker and assumes the file extension MAP. This will be of use
to many users because this linker comes free with your DOS disk
and is used by many compilers and assemblers.

bXd will try to load a file of the SYM format file first. If that is
not found then it tries the MAP format file.



REGISTRATION INFORMATION:

If you use this software regularly and haven't registered, please
do so. The fee is thirty five dollars. For that, you receive the
latest version, instructions on how to build the switch, help
with the internals of the program and personal thanks.

Please send the fee to:

                          Sonam G Gyato
                   7018 Bergenline Avenue, 2a
                     North Bergen, NJ 07047

[SGG 6 Nov, 1986]