NOTE:

You can print out this file by pressing CTRL PrtSc and
then: TYPE CHASM.DOC.  Before you do, note the following:

   1. The documentation is about 30 pages long - have 
      lots of paper ready.

   2. If your printer has a condensed (132 column) mode, 
      turn it on before printing.  If you do, the resulting
      pages can be cut down to 5 1/4 X 8 1/2 inches to fit
      in an IBM document binder.

If you do not have access to a printer, the author
will provide a copy of the documentation for $5.
The $5 fee covers the cost of Xeroxing and mailing,
and is not included in the $20 suggested donation.























































     
     
     
     
     
     
     
     
     
     
                                   (tm)
                              CHASM
     
     
                        Cheap Assembler 
                  for the IBM Personal Computer
     
                     (1983) by David Whitman
                           Version 1.9













































                                                                      1 

                       Table of Contents
     
     Why Chasm?...........................................2
     
     What can Chasm do?...................................3
     
     What WON'T it do?....................................3
     
     Syntax...............................................4
     
     Operands.............................................6
     
     Resolution of Ambiguities...........................10
     
     Pseudo-Operations...................................13
     
     Outside the Program Segment.........................16
     
     Running Chasm.......................................18
     
     Error and Diagnostic Messages.......................20
     
     Execution of Assembled Programs.....................23
     
     Notes for Those Upgrading to This Version of Chasm..26
     
     Miscellaneous and A Word From Our Sponsor...........28





































                                                                      2 

     I. Why Chasm?
         
         Why go to the trouble to write an assembler, when
     one already exists?  The IBM Macro Assembler is a very
     powerful software tool available off the shelf.  It
     supports features such as macros, definition of
     multiple segments, and linking to external procedures.
         
         Unfortunately, all of this power doesn't fit into a
     64K machine, and even when using the small subset
     version, 64K users are limited by memory to only very
     small programs. The macro assembler is also very
     complex, hard to understand, and costs a hundred bucks.
         
         Even though the price of memory keeps dropping, I
     suspect that the majority of the IBM PC's out there have
     no more than 64K installed.  Also, I suspect that most
     end-user assembly language programmers are like myself,
     and are not interested in writing huge, complicated
     programs in assembler. I want to write short
     subroutines to call from BASIC, small patches to
     existing assembler programs (such as DOS), and perhaps
     some games. For such uses, I think the combination of
     the Macro Assembler and a tub full of extra memory
     represents an incredible overkill. Chasm is, I hope, a
     more reasonable compromise between power and
     accessability (both in cost and complexity).





































                                                                      3 

     II. What can Chasm do?
     
         Chasm takes a text file, consisting of mnemonics,
     user-defined symbols, numbers, and pseudo-ops, and
     produces a file of corresponding machine language for
     the 8088 processor. Chasm allows you to define labels
     for branching, rather than requiring you to figure out
     offsets or addresses to jump to.  It allows you to
     represent with a name any constants you want to use,
     making your programs easier to understand. Most
     importantly, it translates mnemonics to their machine
     language equivalents freeing you from the task of hand
     translation.
         
     III. What WON'T it do?
     
         In the interest of simplicity, Chasm has a number
     of restrictions:
     
         1. Statement syntax is not quite as free as in the
            macro assembler.
         
         2. The number of pseudo-ops is severely cut down
            from the macro assembler.
         
         3. Macros are not supported.  (Note that the IBM
            assembler doesn't support macros in systems
            smaller than 96K)
         
         4. Expressions (such as BUFFER - 2 ) are not
            supported, at least in version 1.0.
         
         5. Multiple segment definitions are not allowed, at
            least in version 1.0. Chasm assumes that your
            entire program fits in one segment, that the cs,
            ds, and es registers all point to this same
            segment, and that the ss register points to a
            valid stack area.
         
         6. External linking is not supported, at least in
            version 1.0.























                                                                      4 

     IV. Syntax
     
     Chasm accepts a standard DOS text file for input. Lines
     may be any combination of upper and lower case
     characters. Chasm does not distinguish between the two
     cases:  everything except single quoted strings are
     automatically converted to upper case during the
     parsing process. Thus, BUFFER, Buffer, buffer, and
     bUFFer all refer to the same symbol.
     
     The characters  blank ( ) , comma (,), single quote (')
     and semi-colon (;) are reserved, and have special
     meaning to Chasm (see below).
     
     Note also that Chasm is written in BASIC, and use of
     the double quote charactor (") may cause bizarre
     effects by confusing the interpreter into breaking down
     input lines in an undesirable way.  The double quote
     may be safely represented in a text message by
     declaring a byte containing its ASCII value. Thus, to
     represent the text:
     
     Use ASCII value for "double quotes"
     
     You may use:
     
     DB 'Use ASCII value for ' 22H 'double quotes' 22H
     
     Each line must be less than 256 characters long and
     have the following format:
     
     Label Operation Operand(s) ;comment
     
     The differant fields of an input line are separated
     by the delimiters blank ( ) or comma (,).  Any number of
     either delimiter may be used to separate fields. 
     
     Explanation of Fields:
     
     Label: A label is a string of characters, beginning in
        column 1. Depending on the operation field, the label
        might represent a program location for branching, a
        memory location, or a numeric constant. Note that
        anything  beginning in column 1, except a comment, is




















                                                                      5 

        considered a label.
     
     Operation: Either a pseudo-op (see section VII) or an
        instruction mnemonic as defined in "The 8086 Book" by
        Rector and Alexy.
     
        Note 1: Except as modified below,"The 8086 Book" is
           the definitive referance for use with Chasm.
     
        Note 2: There are several ways to resolve some
           ambiguities in 8086 assembly language. Please read
           page 3-285 of The 8086 Book, and section VI of
           this document. 
     
     Operand(s): A list of one or more operands,as defined
        in section V, separated by delimiters.
     
     Comment: Any string of characters, beginning with a
        semicolon (;).  Anything to the right of a semicolon
        will be ignored by Chasm.
     
     Note that except for the case of an operation which
     requires operands, or the EQU pseudo-op which requires
     a label, all of the fields are optional. The fields
     MUST appear in the order shown. 







































                                                                      6 

     V. Operands
     
     The following operand types are allowed.
     
     1. Immediate data: A number, stored as part of the
        program's object code.  Immediate data are classified
        as either byte, expressable as an 8 bit binary
        integer; or word, expressable as a 16 bit binary   
        integer. If context requires it, CHASM will left-pad
        byte values with zeroes to convert them to word values.     
        Attempts to use a word value where only a byte will    
        fit will cause an error message to be printed.
     
     Immediate data may be represented in 5 ways:
     
        A. An optionally signed decimal number in the range
           -32768 to 32767. Examples:
     
            MOV AL,21
            MOV BX,-6300
     
        B. A series of up to 4 hex digits, followed by the
           letter H. Examples:
     
           ADD CX,1234H
           ADD DL FDH
     
        C. A symbol representing types A or B above,
           defined using the EQU pseudo-op.  Examples:
     
           MASK EQU 10H
           MAX  EQU 1000
                AND  CL,MASK
                SUB  AX,MAX
     
        D. The offset of a label or storage location returned
           by the OFFSET operator.  OFFSET always returns a
           word value. OFFSET is used to get the address
           of a named memory location, rather than its contents. 
           Example:
     
                  MOV DI,OFFSET(BUFFER)
           BUFFER DS  FFH
     




















                                                                      7 

        E. The ASCII value of a printable character,
           represented by the character enclosed in single
           quotes (').  Thus, the following lines will
           generate the same object code:
     
                  MOV AL,41H  ;ascii code for 'A'
                  MOV AL,'A'
     
     2. Register Operands: One of the 8088's internal
        registers.
     
        A. An 8 bit register from the following list:
           AH    AL
           BH    BL
           CH    CL
           DH    DL
     
        B. A 16 bit register from the following list:
           AX   BX   CX   DX   SP   BP   SI   DI
     
        C. A segment register from the following list:
           CS   SS   DS   ES
     
     3. Memory Operands: The contents of a memory
        location addressed by one of the following
        methods. Note that none of the memory
        adressing options specifies the whether a
        byte or word operand is being referanced.
        See section VI for more on this topic.
     
        A. Direct address.
     
           1. A number, or symbol representing a
              number, enclosed in brackets, indicating
              an offset into the data segment. Example:
     
              BUFFER EQU 5A5AH
                     MOV BH,[BUFFER]
                     MOV [80H],DI
     
           2. A symbol, defined to be a variable (i.e.
              a named memory location) using the EQU
              pseudo-op. Example:
     




















                                                                      8 

                  FCB EQU [80H]
                      MOV DI,FCB
         
            3. A symbol, defined to be a variable by its
               use on a storage defining pseudo-op.
               Examples:
         
                    MOV AX,FLAG
                    MOV DATE,BX
               FLAG DS 1
               DATE DB 31
         
         B. Indirect Address:  The address of the operand is
            the sum of the contents of the indicated
            register(s) and a displacement. The register, or
            sum of registers, are enclosed in square
            brackets: [] 
     
            The displacement is optional, and takes the
            form of an immediate operand, placed without
            intervening delimiters to the left of the first
            bracket.  Displacements in the range -128 to 127
            (i.e. hex 0 - 7F, FF80 - FFFF) are interpreted as
            signed 8 bit quantities. All other displacements
            are interpreted as unsigned 16 bit quantities.
            (Note that although the 8088 supports unsigned 16
            bit displacements up to hex FFFF for indirect
            adressing, Chasm isn't smart enough to distinguish
            between -1 and FFFFH.)
     
            The following indirect modes are allowed:
         
            1. Indirect through a base register (BX or BP).
               Examples:
         
               ENTRYLENGTH EQU 6
                           MOV AX, ENTRYLENGTH[BP]
                           MOV DL, -2[BX]
                           MOV CX, [BP]
                           MOV 9A9AH[BX], AX
         
            2. Indirect through an index register (DI or SI).
               Examples:
         




















                                                                      9 

               MOV [DI], CX
               MOV CX, -5[SI]
         
            3. Indirect through the sum of one base register
               and one index register. Examples:
         
               MOV [BP+DI], SP      ;note that no spaces are
               MOV BX, 10H[BX+SI]   ;allowed within the
               MOV CL, [BP+SI]      ;brackets.
               MOV DH, -2[BX+DI]
     
       4. Labels
         
            A label on a machine instruction may be used as
            an operand for call and jump instructions.
            Examples:
        
               START PROC NEAR
                     CALL GETINPUT
                     JMPS START
                     ENDP
            GETINPUT PROC NEAR
         
       5. Strings
            A string is any sequence of characters (including
            delimiters) surrounded by single quotes (').
            Example:
     
            DB 'Copyright May 15,1982'
     


































                                                                      10 

     VI. Resolution of Ambiguities.
         
         The language defined in "The 8086 Book" contains a
     number of ambiguities which must be resolved by an
     assembler. This is discussed throughout the book, but
     pages 3-285 and 3-286 specifically cover this topic.
     Chasm's solutions of these problems are discussed in
     this section.
         
     A. Memory referances:
     
         When one specifies the address of a memory
     location, it is unclear how large an operand is being
     referanced. An operand might be a byte, or a word.
         
         1. If a register is present as an operand, it is
            assumed that the memory operand matches the
            register in size. An exception to this rule are
            the shift and rotate instructions, where the CL
            register is used as a counter, and has nothing
            to do with the size of the other operand. Examples:
         
            MOV MASK,AX   ;mask is a word
            MOV DH,[BX]   ;BX points to a byte
            NEG [SI]      ;error, operand of unknown size
            SHR FLAG,CL   ;error, flag is of unknown size
         
         2. If no register is present, (or if the only
            register is CL being used as a counter) the size
            of the memory operand is specified by adding the
            suffix "B" or "W" to the instruction mnemonic.
            Examples:
     
            NEGB [SI]       ;SI points to a byte
            SHRW FLAG,CL    ;flag is a word
            MOVW MASK,0AH   ;mask is a word
            MOVB MASK,0AH   ;mask is a byte
            MOVW MASK,9A9AH ;must specify size even though 
                            ;immediate operand implies word
            MOVB DH,[BX]    ;error(!), register already
                            ;specifies size
         
     B. Indirect Branching.
     




















                                                                      11 

         The 8088 supports two flavors of indirect
     branching: intra, and inter segment. A register is set
     to point at a memory location which contains a new
     value for the program counter, and in the case of
     intersegment branching, a new value for the CS register
     as well.
         
         The syntax of "The 8086 Book" does not specify
     which flavor of branch is being invoked.  Chasm adds
     the suffixes "N" (for near, or intrasegment) and "F"
     (for far, or intersegment) to the indirect CALL and JMP
     mnemonics. Examples:
         
         CALLN [BX]    ;intrasegment call
         JMPF  [DI]    ;intersegment jump
         JMP   [BP]    ;error, unspecified flavor
         
     C. Long and Short Jumps
         
     Two types of relative jumps are supported by the
     8088: short (specified by a signed 8 bit displacement)
     and long (specified by an unsigned 16 bit displacement).         
     Both are implemented in Chasm as a jump to a label.
     
     The short jump is specified by mnemonic JMPS, in accord       
     with the IBM disassembler, but not with The 8086 Book, which 
     uses JMP.  Since one of the displacement bits is used as a sign
     bit, only seven are left to express the magnitude of jump.  JMPS
     (and similarly, all the jump on condition instructions) is thus
     limited to branching to labels within a range of -128 to +127
     bytes.
     
     Chasm reserves mnemonic JMP for the long jump.  Note that JMP      
     may only be used to jump in the forward direction, since the       
     sixteen bit displacement is unsigned, and assumed to be positive.  
     Examples:
     
         START PROC NEAR
               JMPS START   ;short jump
               JMPS END     ;short jump
               JMP  END     ;long jump
               JMP  START   ;error: reverse long jump
         END   ENDP
     




















                                                                      12 

     D. Instruction Prefixes.
         
         The 8088 supports three instruction prefixes:
         
         1. SEG: segment override. An alternate segment
            register is specified for a referance to memory
         
         2. REP, REPE,REPNE,REPZ,REPNZ: repeat. A string
            primitive is repeated until a condition is met.
         
         3. LOCK: Turns on the LOCK signal. Only useful in
            multiprocessor situations.
         
         Chasm implements these prefixes as separate
     instructions, rather than prefixes to another
     instruction.  They appear on a separate line,
     immediately before the instruction which they modify.
     This is in accord with the output of the IBM
     disassembler, but not with the IBM macro assembler.
     Examples:
         
         SEG ES
         MOV AX,FLAG  ;flag is in the extra segment
         REP
         MOVSB        ;move bytes until CX decremented to 0







































                                                                      13 

     VII. Pseudo-Operations
         
         The following pseudo-ops are implemented:
         
         A. DB: Declare Bytes
         
            Memory locations are filled with values from the
            operand list. Any number of operands may appear,
            but all must fit on one line. Acceptable operands
            are numbers between 0 and FFH (0-255 decimal), or
            strings enclosed in single quotes (').  If a label
            appears, it is considered a variable, and the
            location may be refered to using the label, rather
            than an address. Examples:
         
                    MOV AX,MASK
              MASK  DB  00H,01H
              STG   DB  'A string operand'
         
         B. DS: Declare Storage
         
            Used to declare large blocks of identically
            initialized storage.  The first operand is
            required, a number specifying how many bytes
            are declared.  If a second operand in the form
            of a number 0-FFH appears, the locations will
            all be initialized to this value. If the second
            operand is not present, locations are initialized
            to 0. As with DB, any label is considered a 
            variable.  To save space, the object code does not
            appear on the listing. Examples:
     
            DS 10         ;10 locs initialized to 0
            DS 100H,1AH   ;256 locs initialized to 1AH
         
         C. ENDP: End of Procedure
         
            See PROC (below) for details.
         
         D. EQU: Equate
     
            Used to equate a symbolic name with a number.
            The symbol may then be used anywhere the
            number would be used.  Use of symbols makes




















                                                                      14 

            programs more understandable, and simplifies
            modification. 
         
            An alternate form of EQU encloses the number
            in square brackets: [].  The symbol is then
            interpreted as a variable, and may be used as an
            address for memory access.  This version is
            provided to allow symbolic referance to locations
            outside the program segment.
     
            Warning: Difficult to debug errors may result
            from using a symbol prior to its being defined
            by EQU.  I strongly urge that all equates be
            grouped together at the beginning of programs,
            before any machine instructions. See "Phase Error"
            in section IX. Examples:
         
                MOFFSET    EQU B000H
                MONOCHROME EQU [0000H]
         
         E. ORG: Origin
         
            Allows direct manipulation of the location
            counter during assembly.  By default, Chasm
            assembles code to start at offset 100H, the
            origin expected by COMMAND.COM for .COM
            programs.  Using ORG you may override this
            default. Example:
         
               ORG 0   ;Code will be assembled for starting
                       ;offset of 0
         
         F. PROC ...ENDP: Procedure Definition
     
            Declares a procedure.  One operand is required on
            PROC, either the word NEAR, or the word FAR.
            This pseudo-op warns Chasm whether to assemble
            returns as intra (near) or intersegment (far).
            Procedures called from within your program should
            be declared NEAR. All others should be FAR.
            ENDP terminates the procedure, and requires no
            operands.  If a RET is encountered outside of a
            declared procedure, an error occurs.  Procedures
            may be nested, up to 10 deep. Example:




















                                                                      15 

     
                MAIN   PROC  FAR
                       ...
                       ...      ;body of procedure
                       ENDP



























































                                                                      16 

     VIII. Outside the Program Segment
         
         As mentioned previously, Chasm does not support
     multiple segment definitions.  Provision is made for
     limited access outside of the program segment, however.
         
         A. Memory Referances
            To access memory outside the program segment, you
            simply move a new segment address into the DS
            register, then address using offsets in the new
            segment.  The memory option of the EQU pseudo-op
            allows you to give a variable name to offsets in
            other segments. For example, to access the graphics
            charactor table in ROM:
     
            BIOS       EQU  F000H
            CHARTABLE  EQU  [FA6EH]
                       MOV  AX,BIOS   ;can't move immed. to DS 
                       MOV  DS,AX
                       MOV  AL,CHARTABLE ;1st byte of char. table
         
         B. Code Branching
     
            Chasm supports 4 instructions for branching
            outside the program segment.
     
            1. Direct CALL and JMP
               New values for the PC and CS registers are
               included in the instruction as two immediate
               operands. Example:
         
               BIOS        EQU  F000H    ;RAM bios segment
               DISKETE_IO  EQU  EC59     ;disk handler
                           JMP  DISKETE_IO,BIOS
     
            2. Indirect CALLF and JMPF
               Four consecutive bytes in memory are
               initialized with new values for the PC and CS
               registers.  The CALLF or JMPF then referances
               the address of the new values. Example:
         
               BIOS        EQU   F000H    ;RAM bios segment
               PRINTER_IO  EQU   EFD2H    ;printer routine  
                           MOV   [DI],PRINTER_IO




















                                                                      17 

                           MOV   2[DI],BIOS
                           CALLF [DI]
         
     




























































                                                                      18 

      
     IX. Running Chasm
         
         From DOS, type:
         
         CHASM
         or
         BASIC CHASM/C:0
         
         After a few seconds, Chasm prints a hello screen,
     then prompts:
         
         Hit any key to continue...
         
         Chasm prompts:
         
         Source code file name? [.asm]
         
         Type in the name of the file which contains your
     program. If you do not include an extension for the
     filename, Chasm assumes it to be .ASM.  If Chasm is
     unable to find the file, it will give you the option
     of naming another file, or returning to DOS.
         
         Assuming your file is present, Chasm prompts:
         
         Direct listing to Printer (P), Screen (S), or Disk
     (D)?
         
         Respond with either an upper or lower case letter.
     If you select "D", Chasm will prompt:
         
         Name for listing file? [fname.lst] 
     
         Type in a name for the listing file.  If you just
     press ENTER, the name defaults to that of your source
     file, with an extension of .LST.
         
         The final prompt is:
         
         Name for object file? [fname.com]
         
         Type in a name for the assembled program.  If you
     just press ENTER, the name defaults to that of your




















                                                                      19 

     source file, with an extension of .COM.
         
         Chasm now assembles your program.  A status line is
     maintained on the screen, showing how many lines have
     been processed. Chasm makes two passes over your source
     file, outputting the listing and object code on the
     second pass.  Be patient, Chasm is written in BASIC,
     and does a good imitation of  a snail crawling through
     molasses.
     
     
         ****NOTE: I will send the Golden Bootstrap Award to
     the first person submitting a complete implementation
     of Chasm, rewritten in assembly language, and small
     enough to be assembled by Chasm version 1.0 on a 64K
     system.
          
         When finished, Chasm returns you to DOS, and you
     see the prompt:
         
         A>











































                                                                      20 

     X. Error and Diagnostic Messages
     
     Error messages generated on pass one appear on the 
     listing before any source code is printed, and mention
     the line number to which they refer.  The majority of
     messages occur during pass two, and will appear in the
     listing immediately prior to the line which caused the
     message.
         
     Could Use JMPS: Diagnostic.  The specified label
        requires an offset of less than 128 bytes; specifying
        the short jump would result in more compact code.
        The assembled code is correct, however.
         
     Data too Long: The value of a immediate byte is
        found not to be in the range 0-FFH
         
     Duplicate Definition of XXX in (linenum): Pass 1
        error. An attempt was made to define a symbol already
        present in the symbol table.
         
     ENDP without PROC: An ENDP was encountered, but no
        corresponding PROC was found.
         
     EQU Without Label: No symbol was found to equate
        with the operand
         
     Illegal or Undefined Argument for Offset: The
        argument for the Offset function was not present in
        the symbol table as a near label or memory location
        on pass 2.
     
     Illegal Reverse Long Jump: Long jumps must in the
        forward direction, since they are expressed with an
        unsigned displacement.
         
     Missing ENDP: The end of the input file was
        encountered, and at least one PROC had not been
        terminated by an ENDP.
         
     Phase Error: A near label or memory location is
        found to have differant values on pass 1 and pass 2.
        A difficult to debug error: generally the problem is
        not caused by the statement which received the error




















                                                                      21 

        message.
     
           The only documented way to generate this error is
        by using a symbol prior to defining it using EQU. On
        pass 1, Chasm assumes that unrecognized symbols are
        either labels or memory addresses which will be
        defined later in the program.  If the symbol is
        subsequently defined as immediate data, the location
        counter may get all messed up.  I would appreciate
        hearing about any other situations which cause this
        message to appear.
     
     Procedures Nested Too Deeply: Procedures may be
        nested no more than 10 deep.
         
     Specify Word or Byte Operation: Diagnostic. Chasm
        suggests that the Syntax Error might be resolved by
        adding the suffix "B" or "W" to the instruction
        mnemonic.  Most, but not all, ambiguous memory
        referances are flagged with this diagnostic. 
       
     Syntax Error: (OP) (DTYPE) (STYPE).  Chasm was
        unable to find a version of the instruction (OP)
        which allows the operand types (DTYPE) and (STYPE).
        Either the instruction doesn't exist, or it is misspelled, 
        or it is an inappropriate choice for the given operands.
        DTYPE and STYPE are numbers which encode Chasm's
        guess as to what the 1st and 2nd operands might be.
        The numbers are sums of the types given in the following
        list: 
     
          1 = 8 bit accumulator          2 = 16 bit accumulator
          4 = 8 bit register             8 = 16 bit register
         16 = a register or indirect    32 = CS register
              memory referance
         64 = other segment register   128 = memory location
        256 = immediate byte           512 = immediate word
       1024 = none                    2048 = string
       4096 = near label              8192 = far label
      16384 = CL (count) register
         
     Too Far For Short Jump: The displacement to the
        specified label is not in the range -128 to +127.
         




















                                                                      22 

     Too Many User Symbols in (linenum): Pass one error.
        The symbol table is full.
         
     Undefined Operand for EQU: Any operands on an EQU
        statement must have been previously defined.
         
     Undefined Symbol XXX: The symbol XXX was used as an
        operand, but never appeared as a label, and is not a
        predefined symbol.
         
     Unrecognized Operand XXX: XXX is used in the DB
        operand list, but is not a string or byte value.




















































                                                                      23 

     XI. Execution of Assembled Programs
     
     A. Object code format
     
     The object code file produced by CHASM is in the form
     of a memory image, exactly as will be present in your
     computer at run time.  No link step is required.
     Provided that the segment registers are set correctly,
     the architecture of the 8088 guarantees that code is
     self-relocating, and will run correctly loaded anywhere
     in memory. Storing a program as an exact image of
     memory at run time is called the COM format by IBM.
     
     This COM format is *not* that produced by the IBM
     assembler.  The output of the IBM assembler is in the
     form of an "object module" suitable for input to the
     linker.  To the best of my knowlege, the object module
     is not directly executable, but must first be "filtered"
     through the linker.  This adds an extra step to the
     process of producing a working program, but gives you
     the option of combining multiple object modules into
     one program.  The resulting linked program is *still*
     not a memory image, but has a header which is used to
     perform relocation during loading.  This linked program
     plus header is called the EXE format by IBM.
     
     B. Running Assembled Programs From DOS
     
     DOS provides a loader for running machine language
     programs.  To run a program, you merely type it's name,
     with or without the extension.  This is what you're
     doing every time you use a DOS external command such as
     FORMAT or CHKDSK.  In fact, the COM format is named
     after "external COMmand".
     
     When you type the name, DOS examines the file extension
     to determine what format the file is in, either COM or
     EXE.  This is why CHASM defaults to using the extension
     .com for your object file.  If you plan to run the
     program from DOS, don't change the extension. 
     
     For COM programs, DOS builds a 255 byte long "program
     segment prefix" and sets the segment registers to point
     to this PSP.  The contents of the file are then loaded




















                                                                      24 

     verbatim right after the PSP, at offset hex 100 in the
     segment defined by the segment registers.  As soon as
     loading is complete, your program is executed starting
     with the instruction at hex 100.  Although you can
     totally ignore the PSP, you should read pages E-3
     through E-11 of the DOS manual to see what DOS puts
     there for you.  It turns out there are some real goodies
     which your program might want to use.
     
     When your program is done, it must transfer control
     back to DOS, otherwise the 8088 will continue to fetch
     what it believes are instructions from whatever garbage
     or bit-hash happens to follow your program in memory.
     The easiest way to return to DOS is to execute the
     instruction:
     
     INT 20H
     
     This is the vectored interrupt reserved by DOS for
     program termination.
     
     While we're on the topic of vectored interrupts, you
     would be well rewarded to study both the DOS manual and
     Technical Referance to find out what happens when you
     execute some of the other interrupts.  Some very useful
     functions, such as file handling and screen i/o, are
     available at the machine language level through this
     mechanism.
     
     By changing the interrupt vector for a given function
     to point to your own code, you can overide the way DOS
     or the BIOS does something, and do it your way.  This
     document was produced from Easywriter directly, in
     standard DOS format, by printing it to disk.  It was
     not necessary to manually add an end of paragraph
     marker at the end of each line, and I didn't need to
     run it through the program TRANSFER which IBM provides.
     I had changed the vector for printer support to point
     to some code which sent the output to disk.  Easywriter
     thought it was using the printer, and formatted
     everything nicely.
     
     C. Debugging Assembled Programs
     




















                                                                      25 

     IBM provides an excellent utility with DOS, called
     DEBUG.COM.  By specifying your program's name as a
     parameter when invoking DEBUG, you can observe your
     program execute with DEBUG's trace and other functions.
     To debug your program from DOS, type:
     
     DEBUG progname.COM
     
     DEBUG builds a PSP and loads your program just like DOS
     does, but you have the added power of the debugging
     commands to monitor your program while it runs.  See
     chapter 6 of the DOS manual for more details about
     using DEBUG.
     
     D. Using Assembled Programs in BASIC
     
     To incorporate a machine language subroutine in a BASIC
     program, write it in assembly language, then assemble
     it with CHASM.  You should read page C-7 of the BASIC
     manual for some conventions to use in writing your
     subroutine.  In particular, note that you must declare
     the routine to CHASM as a FAR procedure using the PROC
     pseudo-op, and that the last instruction of the routine
     should be a RET.
     
     For short routines, probably the easiest way to get the
     code into a BASIC program is to just hand copy the
     object code from the listing into a DATA statement. The
     BASIC program can then READ the data and POKE it into
     memory.  An example program to do this is given on page
     C-6 of the BASIC manual.  An alternative approach would
     be to store the routine in a string variable, which
     could later be located with the VARPTR function.
     
     You transfer control to your routine with either the
     USR  function, or the CALL statement.  Syntax for these
     statements can be found in the BASIC manual.



























                                                                      26 

     XII. Notes for Those Upgrading to This Version of
          Chasm.
     
     Chasm is not yet cast in stone - improvements and
     corrections are made fairly frequently, based on both
     my own experiance in using the program, and the
     comments of outside users.  This section summarizes the
     changes which have been made since version 1.2 was
     released.
     
     The only change which could invalidate an already
     correct program involves the short jump instruction.
     Versions prior to 1.9 represented this instruction with
     mnemonic JP.  This mnemonic was chosen to be in accord
     with the output of the unassemble command of DEBUG.
     Either I simply made a mistake in this regard, or IBM
     changed the mnemonic in the DEBUG supplied with DOS
     1.1.  At any rate, DEBUG 1.1 represents the short jump
     with mnemonic JMPS, and CHASM now follows this syntax.
     JP is now recognized as an alternate form of
     instruction JPE (jump on even parity), in accord with
     The 8086 Book.
     
     Version 1.8 added the operand type "character" as a new
     way to represent immediate data.  A single character
     enclosed in single quotes (') is equivalent to the
     numeric value of the ASCII code for the character.  See
     section V-1-E of this document for details.
     
     As of version 1.7, the DS operator works for blocks
     larger than 255 bytes.  To keep the listing under
     control, object code generated by DS is no longer shown
     on the listing.
     
     Also corrected in version 1.7, the OFFSET function now
     works properly in the displacement field of an indirect
     memory referance.
     
     Version 1.6 was a revision of this document.  Some
     sections were improved slightly, and in response to
     user requests, a section on execution of assembled
     programs was added.
     
     Version 1.5 corrected an error which generated the




















                                                                      27 

     message "Data too Long" if the value FFH was used as 8
     bit immediate data.
     
     The user interface was improved as of version 1.4.
     Chasm now traps some common input errors such as
     misspelling a file name, or forgetting to turn on your
     printer, giving you a second chance rather than just
     crashing.
     
     Version 1.3 involved a speed improvement by a factor of
     5 over 1.2.  Users should note that a number of copies
     labeled as version 1.2 actually incorporate this
     improvement.
     
     As can be seen, revisions are made frequently.  It is
     my policy that after once contributing, users are
     entitled to all future versions free of charge, with no
     further donation expected.  Contributing users are
     encouraged to send a disk and return mailer from time
     to time, to receive the most current version.  Major
     improvements will be announced in IPCO INFO and
     Programmer's Journal.










































                                                                      28 

     XIII. Miscellaneous and A Word From Our Sponsor...
     
         There is a bewildering array of files on your disk.
     As you've discovered by now, the file CHASM.DOC is
     documentation, and need not be present for Chasm to
     run.  Some of the others may need explanation, however.
     
         The actual program is in CHASM.BAS.  To run the
     program, three other files *must* be present.  You must
     copy BASIC.COM from your DOS disk to interpret the
     program.  CHASM.DAT contains data about the various
     instruction mnemonics Chasm recognizes, and must be
     present.  The last file needed is CHASM.OVL.  OVL is an
     empty file, which is merged to fool BASIC into
     deleting some of the initialization code to make
     more room for the symbol table.
     
        The file CHASM.BAT is a batch file to make it easier
     to start Chasm from DOS.  With CHASM.BAT, you can just
     type: chasm.  Without it you'd type: basic chasm/c:0.
     
         TCHASM.BAT is a batch file use to breed new CHASM
     disks, if you want to give a copy to someone else.  It
     copys the program, documentation, data; the whole
     works.  Please only distribute the complete CHASM
     system, as generated by this batch file.
     
         CLS.ASM is provided as a sample source file.  You
     can try out Chasm using CLS as input.
         
     Programming Notes:
         
         1. Chasm is written in heavilly commented BASIC, so
            modifications would be easy, if you'd like to
            customize. I'd like to hear about any improvements
            people make, for possible inclusion in future
            releases.
     
         2. If you do try to modify Chasm, there is a quirk
            you should know about.  Most of the
            initialization code is in a "transient section"
            which is used once, then deleted to make more
            room for the symbol table.   Lines 50,000 -
            65529 are reserved as this transient section.




















                                                                      29 

            Note Well: If you run Chasm, then save it to
            disk, you save the program WITHOUT THE
            INITIALIZATION CODE.  The resulting program is
            non-functional.  Be careful! Keep a backup.
     
         3. Chasm truncates source lines to about 50
            characters in the listing, to avoid going over 
            an 80 charactor line. If your printer has a
            condensed mode with more than 80 characters/line,
            provision has been made for a simple
            customization to make Chasm turn on the
            special mode before listing, and print as many
            characters as possible.  The printer will be
            returned to normal when Chasm finishes.  The
            modification only affects listings to the
            printer, not to screen or disk.
     
            Find subroutine HEADER in the transient section.
            After the IF statement under the comment "printer
            set up?"  you must set the width of device #2 to
            the number of characters per line in condensed mode
            with a WIDTH#2 statement, and set the variable LWIDTH
            to this number minus 1.  Print whatever control
            sequence turns on your condensed mode, and set the
            variable PMODEOFF$ to a string which returns the
            printer to normal.  An example modification is embedded
            at the correct spot as a series of remarks.
     
     Disclaimer:  CHASM is distributed as is, with no guarantee
                  that it will work correctly in all situations.
                  I cannot be responsable for any damages 
                  associated with its use.  Nonetheless, it
                  is my intention to correct any genuine bugs
                  which are brought to my attention.  Drop
                  me a line if you think you've found a 
                  problem.
     
         I am joining the experiment started by the folks at
     Freeware (tm), by distributing un-protected software,
     and *encouraging* copying.  The catch, (of course
     there's a catch) is that I request that all users who
     think the program is worthwhile send a donation.  The
     suggested donation is $20, but send what you think the
     program is worth to *you*.  There is obviously no way I




















                                                                      30 

     can enforce payment, but I hope people will recognize
     the amount of work that went into writing and
     documenting Chasm, and will make a donation.  If the
     monetary response is great enough, I will release upgrades to 
     this program (version 2.0 is already in the works) and
     other programs of comparible magnitude (future projects
     include a macro pre-processor to run in 64K for use with 
     either CHASM or BASIC).  I hope folks find CHASM
     useful.
     
     
                    David Whitman
                    Department of Chemistry
                    Dartmouth College
                    Hanover, NH 03755
                    (603) 643-2115