CTask Manual          Version 1.1  88-07-01                Page 1




                                        CTask
                             A Multitasking Kernel for C

                            Version 1.1  Released 88-07-01

                          Public Domain Software written by

                                    Thomas Wagner
                                  Patschkauer Weg 31
                                   D-1000 Berlin 33
                                     West Germany

                                   BIXmail: twagner


                                     Introduction
                                     ============

          CTask  is a set of routines that allow your C program  to  execute 
          functions  in parallel, without you having to build  in  sophisti-
          cated  polling and switching schemes. CTask handles the  switching 
          of processor time with a priority based, preemptive scheduler, and 
          provides a fairly complete set of routines for inter-task communi-
          cation,  event signalling, and task interlocking.  CTask also  in-
          cludes  a  number of drivers for MS-DOS that build  on  the  basic 
          functions  to allow you to include serial I/O, printer  buffering, 
          and  concurrent  access to DOS functions into your  programs  with 
          little programming effort.

                                      An Example

          To  illustrate one possible use of CTask, let me elaborate on  the 
          following  example. Say you just finished your nifty  telecommuni-
          cations  program, complete with download protocols,  scripts,  and 
          everything.  But wouldn't it be nice to be able to print the  file 
          you  just downloaded while receiving the next, and edit a  comment 
          to some previous message without interrupting the transmission? So 
          you take those editor routines from a previous project, plug  them 
          in, and - oops, how do you switch back and forth between  editing, 
          communication  and  printing? The answer to this is  CTask.  CTask 
          allows your C program to do many different things at the same time 
          by switching the processor between the tasks you define. And since 
          most  of  the time your program is waiting for  some  slow  device 
          (like the human hand) to provide feedback, this switching is  com-
          pletely  transparent,  and will not noticeably slow  your  program 
          down.  

                                Switching the Context

          So  what is needed to allow the user to edit a file while  at  the 
          same  time  downloading another and printing a third?  First,  you 
          have to have some form of *context switching*. This means that you 
          have  to be able to interrupt the processing of the download  when 

          CTask Manual          Version 1.1  88-07-01                Page 2



          the  user presses a key, process the key, and return to the  down-
          load  *task*  at  the exact same point  it  was  interrupted.  One 
          solution  to this would be to include a poll for the  keyboard  at 
          several points in the download routine, and call the editor *task* 
          when a key is available.  But apart from cluttering your code with 
          lots  of unrelated calls, there is another problem.  What  if  the 
          operation  the user requested is more involved than  just  putting 
          the character on the screen, like writing the file to disk?   This 
          might  take so long that your download times out. There must be  a 
          way  to  pass control back and forth between the two  tasks,  such 
          that  no task is delayed for an extended period of time, and  also 
          to  activate  the print spooler task at some defined  interval  to 
          output  the data to the printer. This context switching is  called 
          *scheduling* in CTask. The *scheduler* is invoked on every  system 
          timer  tick,  and will save the context of the current  task.  The 
          scheduler  then  takes the first element from the queue  of  tasks 
          that  are  eligible to be run, and restores the  context  of  this 
          task, returning to the point where the task was interrupted.  This 
          switching  is completely automatic, and requires no  special  pro-
          gramming in the tasks itself. All you have to do is to tell  CTask 
          that  there are three tasks, the download task, the spooler  task, 
          and the editor task.

                                    You have Mail

          All  you have to do for context switching, that is. There's a  bit 
          more  to  multitasking  than meets the eye. How do  you  tell  the 
          spooler task what files to spool, and the download task what files 
          to  download? You can't call a task like an ordinary function,  so 
          what  you need for this is *inter-task communication*. There  must 
          be  a way to pass a message containing the filename to be  printed 
          to  the spooler task, and there are several in CTask, one of  them 
          the  *mailbox*.  The spooler can use a CTask call,  wait_mail,  to 
          wait  for a message to arrive at its mailbox. As long  as  nothing 
          arrives, the spooler task will no longer be scheduled, so if there 
          is nothing to print, it will not use any processor time. When  you 
          send  a  message with send_mail to the mailbox, the  spooler  will 
          wake  up, and process the file. You can also send more  file  name 
          messages to the spooler while it still prints a file, leaving  the 
          messages in the mailbox until the spooler is ready to process  the 
          next file.  

                               Reentrancy and Resources

          This  last  example  seems  innocent enough,  but  there's  a  big 
          stumbling block hidden in it. You allocate the file name  messages 
          in  the  controlling task with malloc, and you free  them  in  the 
          spooler  with  free,  no problem, right? Wrong,  there  is  a  big 
          problem,  *reentrancy*.  Reentrancy means that you can re-enter  a 
          routine while another task is already using it, and that this will 
          not disturb the operation of the interrupted task. But malloc  and 
          free  share  and  modify global data, the  chain  of  free  memory 
          blocks.  Imagine  the following: You just called malloc  from  the 
          controlling task. Malloc has loaded the address of a free  element 

          CTask Manual          Version 1.1  88-07-01                Page 3



          into  a local variable, and is about to write back the pointer  to 
          the  next free element into the last. At exactly this moment,  the 
          timer  ticks, and the spooler is activated.  It has just  finished 
          printing,  so it calls free. Free steps through the chain of  free 
          blocks  to find the right place to insert the block. According  to 
          Murphy's law, it will find just the place where malloc is about to 
          write back the pointer. Free coerces the elements, points the next 
          pointer  to the element malloc just wants to take off  the  chain, 
          and returns. Malloc writes its next pointer into the middle of the 
          newly coerced block, and now returns an element which is still  in 
          the  free list. Compared to the job of finding this kind  of  bug, 
          stepping  in for Tantalus may feel like a vacation. This  kind  of 
          problem  code is called a *critical region*.  There must be a  way 
          to make sure that no two tasks simultaneously enter such a region, 
          and, you guessed it, CTask provides one, the *resource*. When  you 
          call  request_resource  in  one task, all other  tasks  trying  to 
          request  the same resource after that are put to sleep  until  you 
          call  release_resource. Only then will the highest  priority  task 
          that waits for the resource wake up, and get access to the protec-
          ted region. So you would have to substitute malloc and free  calls 
          in  your  routines with calls to functions that  first  request  a 
          resource, execute the function, and then release the resource.

                                      DOS Access

          But, you might ask, isn't there another reentrancy problem in this 
          example, since both the spooler and the download task might simul-
          taneously call DOS to do their file-I/O, and DOS is not reentrant? 
          Do I have to substitute all my calls to fread and fwrite, too? The 
          answer  to this, luckily, is no. CTask traps all your  DOS  calls, 
          and automatically encloses them in the necessary resource  request 
          and release calls, so you don't have to worry about trashing  your 
          disk by simultaneous DOS requests. The limited multitasking  capa-
          bilities of DOS are exploited to allow some parallel processing in 
          DOS,  and CTask will also detect and handle DOS calls by  resident 
          background programs like the DOS PRINT utility. 

                                 Piping the Keyboard

          CTask  also  allows you to circumvent DOS for keyboard  input,  so 
          that  waiting  for the keyboard will not block  other  tasks  from 
          access  to  DOS functions. CTask uses another form  of  inter-task 
          communication  for  storing  keys entered  on  the  keyboard,  the 
          *pipe*.  The pipe is similar to the mailbox in that you  can  wait 
          for  items to be sent to a pipe. But unlike mailboxes,  pipes  use 
          their  own buffer to store the items (which are limited  to  bytes 
          and  words),  so you don't have to allocate mail blocks  for  each 
          item. When waiting on the pipe, your task is put to sleep, so  the 
          processor  is  free  to do more interesting things  than  to  loop 
          waiting for the user to press a key.  When a key is pressed, it is 
          written to the pipe, waking your task. 


          CTask Manual          Version 1.1  88-07-01                Page 4



                               Serial I/O and Timeouts

          Pipes are also used for the serial I/O handler included with CTask 
          that  makes some of the work you've put into  your  communications 
          package obsolete. When outputting data to the serial port via  the 
          CTask routines, the data is buffered in a pipe, and incoming  data 
          is  also  placed in a pipe. All interrupt handling, and  the  pro-
          cessing of modem status and XON/XOFF protocols, is done by  CTask, 
          so you can concentrate on implementing the higher level protocols. 
          Since CTask allows all calls that wait for pipes, mail, and  other 
          events, to specify a timeout that is based on the system tick, you 
          do  not have to resort to timed waiting loops to  detect  communi-
          cation line faults.  

                                      Priorities

          If the protocol you implement requires fast responses to  incoming 
          blocks,  you  can  influence the response of CTask  to  your  comm 
          task's  needs by giving this task a higher priority. CTask  allows 
          65535 different priority levels, and tasks having higher  priority 
          are  scheduled  before  tasks  with  lower  priority.  Also,  high 
          priority  tasks  will get access to mail,  pipes,  and  resources, 
          before  other tasks. It might even be sensible to split  the  comm 
          task into two separate tasks, one of high priority that  assembles 
          the  incoming  bytes into blocks and handles the protocol,  and  a 
          lower priority task that reads the received blocks from a  mailbox 
          and stores them on the disk. In extremely time critical applicati-
          ons, you can even turn off task preemption, so the timer tick will 
          no longer cause a task switch.  

                                Change to your liking

          CTask provides all basic building blocks for implementing  concur-
          rent  programs in an easy and comprehensible way. Since  CTask  is 
          mainly  implemented  in  C, it may not  be  the  fastest  possible 
          system,  but  due  to the straightforward design  which  uses  few 
          shortcuts, modifying the sources to suit your needs and taste  can 
          be  done  without weeks of studying assembler code  that  squeezes 
          every microsecond from the processor. CTask is public domain code, 
          and  there  are no restrictions on its use. It is  distributed  in 
          source form, so you are free to change all aspects of the package. 
          Multitasking  programs, especially in embedded applications,  tend 
          to  be  very diverse in their needs for  specific  constructs.  So 
          although CTask is ready to run under DOS, and is easily  adaptable 
          for embedded applications, you should see CTask more as a starting 
          point  for your own thoughts, and as a toolbox from which you  can 
          pick the instruments you need, than as a finished and fixed  block 
          of code you simply plug into your application.


          CTask Manual          Version 1.1  88-07-01                Page 5



                                 How does CTask work
                                 ===================

                                        Queues

          CTask  uses priority queues for most of its functions. A  priority 
          queue differs from the usual FIFO (first in, first out) queues  in 
          the insertion of elements into the queue. Rather than just placing 
          new elements after the last queue member, the priority of the task 
          determines  its place in the queue. A task is enqueued  after  all 
          queue members with higher or equal priority, but before any member 
          with  lower  priority. Removal from the queue takes place  at  the 
          first element. These queues are used with all operations in  which 
          a  task is made waiting, be it waiting to get run, or waiting  for 
          an event. The advantage of this is the simplicity of  implementing 
          priorities. Other schemes might rely on arrays of queues, or sear-
          ching  through  lists, to determine the highest  priority  waiting 
          task. With priority queues, the most time critical function, sche-
          duling, is very fast, since it can simply take the first task from 
          the  queue  of eligible functions. The disadvantage  is  the  time 
          required to step through all greater or equal priority members  of 
          a queue to find the right place to insert the task. But since  the 
          number of tasks simultaneously enqueued in the same queue is  nor-
          mally relatively small with most multitasking systems, this disad-
          vantage is more than offset by the simple, and thus easy to imple-
          ment  efficiently, scheme. The operation of removing a  task  from 
          somewhere in the middle of a queue is rare (it will only occur  on 
          task kill, task wake, or timeout), and thus the overhead of  mana-
          ging a doubly linked list is not justified.

                                    The Scheduler 

          In  a  CTask system, there is at least one  essential  queue:  the 
          eligible queue, which contains all tasks waiting to run. Each time 
          the scheduler is invoked, it will first save all processor  regis-
          ters  on the current stack, save the stack pointer in the  current 
          tasks  control block, and then enqueue the current task  into  the 
          appropriate  queue.   Normally, this will be the  eligible  queue. 
          Then  the first element in the eligible queue is removed from  the 
          queue,  the stack is switched to the stack of this task, and  pro-
          cessor registers are restored from the new stack, returning to the 
          point where the new task was interrupted. If the eligible queue is 
          empty  the scheduler will loop with interrupts enabled. The  queue 
          head pointer of the task control block of the current running task 
          determines  what  will happen to the task when  the  scheduler  is 
          invoked. If it points to an event control block, the task will  be 
          enqueued  as waiting for this event. If it is NULL, the task  will 
          not  be  enqueued  in any queue, effectively stopping  it.  If  it 
          points to the eligible queue, the task will be enqueued there.  In 
          any case, the scheduler does not care what queue the task is to be 
          enqueued  in, since all queues use the same priority based  order-
          ing. If a task is no longer in the eligible queue, it can only  be 
          returned to this queue by an external event. 


          CTask Manual          Version 1.1  88-07-01                Page 6



                                        Events 

          External  events  can  take several forms,  which  are  relatively 
          similar on the inside. All CTask events use a control block,  with 
          at  least one queue for tasks waiting for the event.  Although  it 
          would  have been possible to summarize all events under  a  global 
          structure,  this approach was not used in CTask, the main  reasons 
          being execution speed and ease of use. So if you scan through  the 
          source  files  for CTask events, you will see  many  very  similar 
          routines, which only differ in the types of data and the names  of 
          queues they process. In a class based language like C++, one would 
          certainly  define  all events as instances or derivations  of  one 
          class.  In plain C, the necessary type casting, and the  different 
          handling of certain cases, would clobber the code to the point  of 
          illegibility.

                                      Resources

          The  event types "resource", "flag", and "counter" differ only  in 
          the  kind of wait operations and the handling of the  state  vari-
          able.  The  resource is mainly for use  in  interlocking  critical 
          regions  of  code, to protect access to  non-reentrant  resources. 
          Only one task can "own" a resource, all other tasks requesting the 
          resource are delayed until the owning task releases it. For  added 
          protection,  CTask  stores the task control block address  of  the 
          current owner of the resource in the resource control block, so no 
          other task can erroneously release it. 

                                        Flags

          Flags, on the other hand, can be set and cleared by any task,  and 
          also by interrupt handlers. Tasks can wait on either state of  the 
          flag,  and all tasks waiting for a state are simultaneously  acti-
          vated  when  the flag is changed to this state. This  makes  flags 
          suitable for use as a global signalling mechanism.

                                       Counters

          Counters  are  a variation on the flag concept. A counter  can  be 
          incremented  and cleared by any task, and by  interrupt  handlers. 
          Tasks  can wait for a counter to be zero or nonzero.  Like  flags, 
          all tasks waiting for the zero state are activated simultaneously. 
          But  unlike  flags, only the first task waiting  for  the  nonzero 
          state of a counter will be activated on incrementing the  counter, 
          and  the  counter will be automatically decremented  by  one.  The 
          counter is used inside CTask to handle timer interrupts. The timer 
          counter  will  be incremented on each timer tick,  activating  the 
          timer task. If for any reason the timer task is unable to complete 
          its run until the next tick, this tick will not be lost, since the 
          counter  is incremented, and the timer task will continue  to  run 
          the next time it calls the counter wait request. 


          CTask Manual          Version 1.1  88-07-01                Page 7



                                 Mailboxes and Pipes

          The  "mailbox"  and  "pipe"  events can  be  used  for  inter-task 
          communication,   and  for  the  communication  between   interrupt 
          handlers and tasks.

                                      Mailboxes

          Mailboxes can hold an unlimited number of mail blocks. Mail blocks 
          have  no fixed structure, but the first doubleword in  each  block 
          passed  to  a  mailbox routine is used as a  chain  pointer.  Mail 
          blocks  are chained into a mailbox in FIFO order. Tasks  can  wait 
          for  mail to arrive, or can conditionally read mail if a block  is 
          available.  Tasks  and interrupt handlers can write  blocks  to  a 
          mailbox. Since mailboxes don't need any copying of data, they  are 
          suited  for high speed exchange of larger amounts of data  between 
          tasks. The disadvantage of sending mail this way is that you  have 
          to  make sure that a mail block is not re-used before it has  been 
          read  out  of the box and processed by the  receiving  task.  When 
          exchanging fixed length messages, you can build a free mail  block 
          chain by using a mailbox to hold the available blocks. 

                                  Pipes and Buffers

          Buffered message exchange is possible using pipes. When creating a 
          pipe,  you  specify  a buffer area and its length,  and  the  pipe 
          routines  will buffer all data written to the pipe in  this  area. 
          This implies that writing to a pipe may cause a task to be delayed 
          until  there  is space available in the pipe. To  allow  interrupt 
          handlers to write to pipes, there is a conditional write  request, 
          which  will simply return if the pipe is full. Tasks can wait  for 
          data  to  arrive  in a pipe, and for the pipe  to  be  emptied.  A 
          conditional  read  request is also provided. The  disadvantage  of 
          pipes  is that they are slightly slower than mailboxes due to  the 
          necessary copying, and that you can only place word or byte  sized 
          items  in  a pipe. When there is more than one  reader  or  writer 
          task,  you  can  not  rely on the bytes in a  pipe  being  in  any 
          specific  order.  A "buffer" construct is provided in  CTask  that 
          expands pipes to allow arbitrary length messages to be written and 
          read. This is implemented using a resource for reading and writing 
          to  the pipe associated with the buffer, so the message is  always 
          guaranteed  to  be  written  and read  in  one  piece.  But  since 
          resources  can  not  be used in  interrupt  handlers,  using  such 
          buffers is not allowed from interrupts.

                                     Applications

          There  are a number of routines included in the CTask package  for 
          PC-specific tasks. Although they will be of limited use for embed-
          ded  applications, studying the serial I/O and  printer  interface 
          routines  will give you some hints on how to use the CTask  kernel 
          for  implementing  your own device drivers. For  PC  based  appli-
          cations,  the routines should be usable with no or little  changes 
          for implementing complete communications packages.

          CTask Manual          Version 1.1  88-07-01                Page 8




          The  serial I/O handler uses interrupts for both input and  output 
          of data, and supports both XON/XOFF and RTS/CTS handshake methods. 
          The modem inputs can selectively be enabled to control data trans-
          mission.   Pipes are used for transmit and receive data, with  the 
          buffer  and  its size specified on initialization. Both  COM1  and 
          COM2 can be active simultaneously, and other ports can be  suppor-
          ted by editing a table in the source code. Since CTask allows  the 
          access  to  all events in interrupt  handlers,  writing  interrupt 
          based I/O drivers is relatively simple.  On receiving a character, 
          the character and any associated errors are placed in the  receive 
          pipe,  and the transmit pipe is read on transmit ready  interrupt. 
          Note  that  conditional reads and writes have to be  used  in  the 
          interrupt  handler,  since  you can't safely  delay  an  interrupt 
          handler.

          The  printer  output driver supports both  polling  and  interrupt 
          output.  Again, a pipe is used for the output characters. However, 
          since polling is supported, and because of the somewhat unreliable 
          interrupt  structure  of the printer ports, a driver task  is  re-
          quired.   This  task is automatically created  on  installing  the 
          driver.  The  task first waits on the pipe for a character  to  be 
          written  to  the printer.  When polling is enabled,  it  tries  to 
          output the character directly, using a short busy-waiting loop. So 
          as  not  to load the system too heavily by the polling,  the  task 
          will delay itself for a defined amount of timer ticks if it  can't 
          output  the character after a small number of loops.  When  inter-
          rupts  are  enabled, the process is essentially the  same  at  the 
          start,  but after the character is written to the port,  the  task 
          will wait on a flag to be set. The interrupt handler will set  the 
          flag  on  interrupt, enabling the task to get the  next  character 
          from the pipe. Since interrupts are unreliable with most  printers 
          due to the usually very short pulses on the acknowledge line,  the 
          task  uses a timeout on the flag wait, so it does not hang  if  an 
          interrupt  is missed. Studying the printer driver will  also  give 
          you  an idea what the optional parameter on task creation  can  be 
          used  for. In the printer driver, this parameter is used  to  pass 
          the address of the printer control block, which contains the pipe, 
          the  flag,  and the hardware info, to the task.  This  allows  the 
          printer  driver to be simultaneously installed for any  number  of 
          printers without having to write separate printer tasks. 

          CTask Manual          Version 1.1  88-07-01                Page 9



                                    General Notes
                                    =============

                           What can CTask NOT be used for?

          CTask  is not intended to provide for multitasking on the  command 
          level of MS-DOS.  Although CTask includes a module for  channeling 
          simultaneous  DOS requests inside a program,  the strategy used in 
          this module is not sufficient for the functionality required  when 
          switching between programs. Adding this functionality would not be 
          trivial (although certainly worthwhile).
          Also, there is no warranty that CTask does perform without errors, 
          or  does exactly what you or I intended.  So CTask should  not  be 
          used  in  applications  in which malfunction of routines  of  this 
          package would result in damage to property or health of any person 
          without  *very*  extensive testing under all kinds  of  loads.  In 
          using CTask, you do so at your own risk.


                            What is required to use CTask?

          To  compile  CTask,  Microsoft C 5.0 or later,  or Turbo C 1.0  or 
          later  are required.  Microsoft MASM 5.0 or later is required  for 
          the assembler parts.  Conversion to other compilers is possible if 
          they  conform to the new ANSI (draft) standard. Conversion of  the 
          assembler parts to other Assembler versions requires  substitution 
          of  the  simplified  model directives by  explicit  segment  defi-
          nitions, and adding the DGROUP to offsets referencing data.

          CTask will add 8-12k of code to your program, depending on options 
          and  installed drivers. The minimum static data used by  CTask  is 
          approximately 4k.

          Converting  CTask for stand-alone operation requires few  changes. 
          Mainly,  the  timer interrupt handler (in "tsktim.asm") has to  be 
          rewritten,  and the initialization code (in "tskmain.c") may  have 
          to  be  changed. Changes to other modules  (naturally  except  the 
          optional hardware drivers) should not be necessary.

          Another requirement is a good debugger.  If you never before wrote 
          multitasking  applications,  you're  in for  some  surprises.  The 
          normal debugging tools (Symdeb, Codeview) are of only limited use, 
          since they use DOS calls for their I/O, and thus may conflict with 
          your background tasks.  One safety measure is to first  thoroughly 
          test  your  program with preemption disabled,  possibly  inserting 
          some schedule() calls, and only allow task preemption if you found 
          most major bugs.  I personally recommend Periscope for  debugging, 
          since  it  can be made resident and so is  always  available,  and 
          because it does not use DOS.  Periscope III is the most  expensive 
          solution,  and the best tool you can imagine (except for Periscope 
          IV,  announced for April),  but the less costly versions will also 
          help a lot.



          CTask Manual          Version 1.1  88-07-01                Page 10



                          Do I have to pay for using CTask?

          No. One reason for writing CTask was to provide a free, no strings 
          attached,  utility, instead of the usual "for personal  use  only" 
          restriction.  Writing a multitasking application for personal  use 
          only doesn't seem too interesting to me. CTask is completely free, 
          and there is no restriction on its use. You may incorporate all or 
          parts of CTask in your programs, and redistribute it in source  or 
          binary form by any means. I also do not restrict the use of  CTask 
          in  commercial  applications.  Since  trying  to  distribute   the 
          unmodified CTask for money will only give you a bad name, you  may 
          even do that if you find someone dumb enough to buy it. Naturally, 
          if  you make a bundle from it, or simply like CTask, I  would  not 
          reject a donation. However, this is not required, and it will  not 
          give you any additional support.


                              What support can I expect?

          I  will try my best to eliminate any bugs reported to me,  and  to 
          incorporate suggested enhancements and changes.  However, my spare 
          time  is limited,  so I can not guarantee continued or  individual 
          support.  (But since I am a free-lance consultant,  you can always 
          hire me to do it...) 

          At the time of this writing,  I'm connecting to BIX almost  daily. 
          Problems  of limited general interest can be reported via BIXmail, 
          suggested enhancements and changes,  plus bug reports,  should  be 
          posted  in the c.language/tools conference on BIX (until responses 
          warrant a new conference,  or I can't afford BIX any  longer),  so 
          they can be discussed among all interested (I hope there will be a 
          few).  Normal  mail  can  be used,  too,  but  don't  expect  fast 
          responses.

                                  About this Release

          Since  the  Beta release of CTask in March, CTask has  been  down-
          loaded  from BIX more than 90 times. Of all downloaders, just  six 
          commented  on  CTasks  features, or sent bug  reports.  The  ideas 
          presented by the commentors are mainly integrated in this version, 
          as  are the fixes for the reported bugs. But since  comments  were 
          sparse,  this is not a revolutionary new release. Many  areas  are 
          completely unchanged, or just slightly modified to accommodate new 
          flags  and  options. See the accompanying file  "changes.doc"  for 
          a summary of the changes.

          Although I currently have no new ideas that would warrant  another 
          release,  I  again  would like to invite you to  voice  your  com-
          plaints, suggest enhancements, supply your own code for  inclusion 
          in  the package (note that any code submitted for  inclusion  must 
          not be copyrighted or usage restricted, but I'll naturally respect 
          copyrights  in  code  submitted for  demo  purposes),  or  suggest 
          additions to this manual.

          CTask Manual          Version 1.1  88-07-01                Page 11



                                 Multitasking Basics
                                 ===================

                                        Tasks

          In CTask, a "task" is defined as a (far) C function. The number of 
          tasks  is  not limited,  and one function may be used for  several 
          tasks.  There  is little difference between a task function and  a 
          normal function. The usual form of a task function is

               void far my_task (farptr arg)
               {
                    one-time initialization code
                    while (TRUE)
                      {
                      processing code
                      }
               }

          A task function is (usually) never called directly.  Rather, it is 
          specified  in the call to the create_task routine,  and started by 
          start_task.  It will then continue to run,  sharing the  processor 
          time  with  all other tasks,  until it is "killed"  by  kill_task. 
          Returning  from  the routine will have the same effect as a  kill. 
          The sharing of processor time is accomplished by "preempting"  the 
          tasks. Preemption means that the task is interrupted in the middle 
          of some statement by a hardware interrupt (usually the timer), and 
          is *not* immediately restarted when the interrupt handler returns. 
          Instead,  the  next  task that is able to run is activated by  the 
          "scheduler", with the interrupted task continuing its duty at some 
          (normally  unpredictable)  later time.  You can also  have  multi-
          tasking without preemption, and CTask supports this, too, but this 
          requires full cooperation of all tasks in the system, such that no 
          task  continues  to  run for an extended period  of  time  without 
          passing control to other tasks by an explicit scheduling  request, 
          or by waiting for an event.

          The  optional  argument  to the task function may be used  if  one 
          function is to be used for more than one task, for example to pass 
          a  pointer to a static data area for use by this specific instance 
          of the function.



          CTask Manual          Version 1.1  88-07-01                Page 12



                                        Events

          Tasks alone would be of limited use.  If you have several routines 
          which  just do number crunching or sorting or  such,  making  them 
          into  parallel  tasks would be sensible only on  a  multiprocessor 
          system.  Normally,  at least some of your tasks will wait for some 
          outside  "event" to happen,  be it the user pressing a key,  or  a 
          character  arriving from the modem.  Then there may be tasks which 
          have to wait until another task finishes processing on some  piece 
          of data before they can continue.  For this synchronization, there 
          are  a number of constructs in CTask,  which I summarize under the 
          name "event".  Common to all events are the operations of  waiting 
          for  an  event  to  happen,  and signalling  that  the  event  has 
          happened.  Using a CTask event is much more efficient than looping 
          while  waiting on some shared data location to change  state,  and 
          also  eliminates  concurrency problems inherent in such  a  simple 
          approach.  Tasks  waiting for an event are taken off the scheduler 
          queue, so they no longer use processor time.

                                      Reentrancy

          One of the biggest problem with multitasking in general,  and C on 
          the PC in particular, is reentrancy. Reentrancy means that you can 
          use  a routine,  be it you own,  or one of the C run-time library, 
          from different tasks at the same time. When writing your own code, 
          you can easily avoid problems, but when using the run-time library 
          routines,  you often can only guess if the routines are  reentrant 
          or not. 

          A routine is NOT reentrant if it modifies static data. This can be 
          illustrated by the following nonsense example:

               int non_reentrant (int val)
               {    static int temp;
                    temp = val;
                    return temp * 2;
               }

          Now take two tasks,  which call this routine.  Task1 calls it with 
          val=3,  Task2  with val=7.  What will be the return value for both 
          tasks? You never know. There are three possible outcomes:

            1) The tasks execute sequentially.  Task1 will get 6,  and Task2 
               14 as a result. This is what one normally expects.

            2) Task1  runs  up to "temp = val",  then is interrupted by  the 
               timer.  Task2  executes,  and gets 14 as result.  Then  Task1 
               continues. Return for Task1 is 14.

            3) Task2  runs up to "temp = val",  then is interrupted  by  the 
               timer.  Task1  executes,  and  gets 6 as result.  Then  Task2 
               continues. Return for Task2 is 6.


          CTask Manual          Version 1.1  88-07-01                Page 13



          add  to  this the effects of optimization,  and a  loop,  and  the 
          outcome is completely random. 

          Most  routines in the C library will not explicitly  do  something 
          like this, but all functions that 

               - do file I/O (read, write, printf, scanf, etc.) or
               - change memory allocation (malloc, free, etc.)

          have  to  use some static data to do buffering,  or to  store  the 
          chain of memory blocks in. Interrupting such an operation may have 
          disastrous effects.  The most devilish aspect of non-reentrancy is 
          that  the  effects are unpredictable.  Your program may  run  1000 
          times  without  any error,  and then on the 1001th time crash  the 
          system so completely that only the big red switch will help.

          So  what can you do about it?  A lot.  There are several  ways  to 
          protect  "critical  regions" from being entered in  parallel.  The 
          most simple method is to disable interrupts. This, however, should 
          be  used only for *very* short periods of time,  and not for  rou-
          tines  that  might themselves re-enable them  (like  file-I/O).  A 
          better  method  is to temporarily  disable  task  preemption.  The 
          routines  tsk_dis_preempt  and tsk_ena_preempt allow this form  of 
          short-term task switch disable. Interrupts may still be processed, 
          but  tasks  will  not  be preempted.  The best way  is  to  use  a 
          "resource".  A resource is a special kind of event, which only one 
          task  can  possess  at  a time.  Requesting  the  resource  before 
          entering the routine,  and releasing it afterwards,  will  protect 
          you  from  any  other task simultaneously  entering  the  critical 
          region (assuming that this task also requests the resource).

          It  is also reasonably safe to use file-I/O without protection  if 
          it  goes  to  different  files.  The C  file  control  blocks  for 
          different files are distinct, so there will be no conflict between 
          tasks.  Since  DOS  access is automatically  protected  by  CTask, 
          concurrent file I/O is possible.

          What  you  may NEVER do is to use a non-reentrant routine that  is 
          not  protected by an interrupt disable from an interrupt  handler. 
          An interrupt handler is not a task,  and so can not safely request 
          a resource or disable task preemption.  This is the reason why the 
          CTask  routines  generally disable interrupts before  manipulating 
          the internal queues rather than only disabling task preemption.


                                      Deadlocks

          One  thing to watch out for when using resources or similar  event 
          mechanisms is not to get into a situation where Task 1 waits for a 
          resource that Task 2 has requested,  while at the same time Task 2 
          waits  for a resource that Task 1 already has.  This situation  is 
          called a deadlock (or,  more picturesque,  deadly embrace), and it 
          can only be resolved with outside help (e.g.  waking up one of the 
          tasks forcibly). To illustrate, consider the following example:

          CTask Manual          Version 1.1  88-07-01                Page 14




               void far task_1 ()
               {
                 ...
                 request_resource (&rsc1, 0L);
                 request_resource (&rsc2, 0L);
                 ...
               }

               void far task_2 ()
               {
                 ...
                 request_resource (&rsc2, 0L);
                 request_resource (&rsc1, 0L);
                 ...
               }

          Since interrupts are always enabled on return from a task  switch, 
          even if the statements are enclosed in a critical region, there is 
          no  guarantee  that  the request_resource calls will  be  executed 
          without interruption. In this example, the problem is obvious, but 
          in  a more complex application,  where resource requests or  other 
          waits might be buried in some nested routine, you should watch out 
          for similar situations. One way to avoid problems would be in this 
          example to change task_2 to

               void far task_2 ()
               {
                    int again;
                    ...
                    do {
                         request_resource (&rsc2, 0L);
                         if (again = c_request_resource (&rsc1))
                            {
                            release_resource (&rsc2);
                            delay (2L);
                            }
                       } while (again);
                    ...
               } 
                       
          Note that this is only one of many possible approaches,  and  that 
          this approach favors task_1 over task_2.

          You  should also take care not to kill tasks that currently own  a 
          resource. CTask will not detect this, and the resource will  never 
          be freed.

          CTask Manual          Version 1.1  88-07-01                Page 15



                                 Multitasking and DOS

          CTask includes (and automatically installs) a routine which  traps 
          all  DOS  calls,  and makes sure that no two tasks  simultaneously 
          enter DOS. This is accomplished using the resource mechanism, with 
          special  provisions  for  the  limited  multitasking  capabilities 
          provided by DOS. There are a few calls, namely those with function 
          codes  <=  0x0c,  which allow functions with codes >  0x0c  to  be 
          executed  while  DOS is waiting for an external device  (generally 
          the keyboard) to get ready.  This, however, limits the use of some 
          C library functions,  namely scanf and fread,  for console  input. 
          Both  these  functions  use  handle input,  and thus  can  not  be 
          interrupted.  When  writing  routines  for  handling  user  input, 
          keyboard  read  functions should either use  the  low-level  calls 
          getch  and  gets,  or,  better yet,  the direct entries  into  the 
          keyboard  handler,  t_read_key and t_keyhit,  and then process the 
          string with sscanf if desired.  The keyboard handler (contained in 
          tskkbd.asm) traps all keyboard interrupts, storing entered keys in 
          a  pipe.  If a task reads from the keyboard,  it is  automatically 
          waiting  for  this pipe.  Using getch and gets is  less  desirable 
          since they use polling instead of waiting, and thus degrade system 
          performance.  Also,  the t_read_key and t_keyhit functions do  not 
          use DOS, so DOS functions <= 0C can be executed concurrently.

          You  should  NEVER  circumvent DOS by  calling  the  BIOS-disk-I/O 
          function (INT 13) directly.  This entry is not protected by CTask, 
          and  using it in parallel to DOS file-I/O may send your  hard-disk 
          FAT and directory into never-never land. If you really should need 
          this  interrupt,  you should consider adding support for it in the 
          DOS-handler module "tskdos.asm".  Using the direct sector read and 
          write interrupts 25 and 26 is supported, however. Using other BIOS 
          interrupts  directly  should  also  be  avoided,  unless  you  are 
          absolutely  sure they will not be used by other routines via  DOS, 
          or you provide your own critical region handling.  Using interrupt 
          16, the keyboard interrupt, is safe, since it is redirected to the 
          keyboard handler pipe.

          The DOS access module has been tested to work with DOS  3.30,  and 
          with the DOS 3.30 PRINT routine running in the background. Special 
          provisions  are built into the DOS module to detect background DOS 
          calls.  Using Sidekick also hasn't lead to any problems,  although 
          you  may trash Sidekick's screen display by writing to the  screen 
          while  Sidekick is active (note that your application  *continues* 
          to  run  while Sidekick or other pop-ups are active).  I  can  not 
          guarantee  complete compatibility with all background  and  pop-up 
          programs  under all versions of DOS.  Specifically,  DOS  versions 
          prior   to  3.1  have  significant  problems  with   multitasking. 
          Upgrading  to a newer DOS version is recommended if you are  still 
          using DOS < 3.2 (DOS 3.1 has some bugs in other areas).

          Critical  errors  and  Control C occurring  while  concurrent  DOS 
          access  takes  place may also be fatal.  Using the  ctrlbrk()  and 
          dosexterr() functions of Turbo C, or their equivalents in MS C, to 
          trap critical errors and Control C is highly recommended.

          CTask Manual          Version 1.1  88-07-01                Page 16




                                     Using CTask
                                     ===========

          CTask  comes  archived with both source and binaries.  The  binary 
          version is compiled in the large model, but since the pre-compiled 
          kernel  routines don't use any functions from the C  library,  you 
          can  use  all functions in small or other model  programs  (except 
          Tiny). The include files provided specify all model  dependencies, 
          so you don't have to use the large model for your application, but 
          always remember to include "tsk.h" for the type and routine proto-
          types.  The  C  source files will work without  changes  for  both 
          Microsoft  and Turbo C. The library files are not  compatible,  so 
          use "ctaskms.lib" for Microsoft, and "ctasktc.lib" for Turbo C. In 
          the distributed configuration (i.e. dynamic allocation of  control 
          blocks enabled), the file TSKALLOC.C must be added to the  library 
          or separately linked after compiling it *in the same model as  the 
          main  program*. This file uses C-library routines, and  thus  must 
          match  the  main  program's  memory  model.  The  same  goes   for 
          TSKSNAP.C, an optional snapshot-dump utility.


                                Configuration Options

          The  file TSKCONF.H contains a number of #define's that allow  you 
          to configure some CTask features. The entries are

          TSK_DYNAMIC
               If  1,  you can let CTask dynamically create task  and  event 
               control  blocks,  task stacks, and pipe buffers,  by  passing 
               NULL as the block address. Since this requires the C  runtime 
               allocation calls, it is not suitable for non-DOS applications 
               (except if you provide your own memory allocation routines).

               This option is normally enabled (1).
               Changing  this  option requires  changing  the  corresponding 
               option in the Assembler macro file TSK.MAC.


          TSK_NAMEPAR
               If  1, all create_xxx calls accept an  additional  parameter, 
               the name of the created control block. This name should  con-
               tain  only  printeable characters, and should not  be  longer 
               than  8 characters plus the zero terminator. This  option  is 
               used together with TSK_NAMED (see below).

               This option is normally enabled (1).
               Changing  this  option requires  changing  the  corresponding 
               option in the Assembler macro file TSK.MAC.


          TSK_NAMED
               If  1, all control blocks (except timer control  blocks)  are 
               named  and linked on creation. This allows the snapshot  dump 

          CTask Manual          Version 1.1  88-07-01                Page 17



               routine  to  display the system state.  TSK_NAMEPAR  must  be 
               defined for this option to work. Since it may be desirable to 
               switch  off  the handling of the names  after  the  debugging 
               phase, without having to change all create_xxx calls to  omit 
               the  name  parameter,  the  name  parameter  is  ignored   if 
               TSK_NAMED is undefined, but TSK_NAMEPAR is defined. 

               This option is normally enabled (1).
               Changing  this  option requires  changing  the  corresponding 
               option in the Assembler macro file TSK.MAC.


          CLOCK_MSEC     
               If  1, all timeouts are specified in milliseconds instead  of 
               timer  ticks. This allows programming of delays and  timeouts 
               independent of the speedup-parameter or the system tick rate. 
               Since  timeout calculations use floating point operations  if 
               this  option is enabled, a floating point library is  needed. 
               This precludes model independence of the CTask kernel.

               This option is normally disabled (0).


          PRI_TIMER
               Specifies the priority of the timer task. Normally the  timer 
               task should have a higher priority than any other task in the 
               system.

               The value is normally 0xf000.


          PRI_STD
               This  value  may  be used in your programs  as  the  standard 
               priority  of  user tasks. Its value is arbitrary. It  is  not 
               used in the kernel except for the definition of PRI_INT9 (see 
               below).

               The value is normally 100 (decimal).


          PRI_INT9
               Determines the priority of the "int9"-task. This task  chains 
               to  the previous interrupt vector for the sytem  timer  tick, 
               and  thus may activate resident TSR's. Since  TSR's  normally 
               use  polling when accessing the keyboard and  other  devices, 
               the  priority  of the int9-task should be equal to  or  lower 
               than normal user-defined tasks to allow your program to  con-
               tinue to run while the TSR is active. You can tune this value 
               so  that some tasks are blocked by the TSR to avoid  trashing 
               the screen.

               The value is normally  PRI_STD - 1.



          CTask Manual          Version 1.1  88-07-01                Page 18



          IBM
          DOS
               Both IBM and DOS are more or less of informative value  only, 
               to  point out those areas in the kernel that  need  attention 
               when converting to non-IBM or non-DOS environments. Disabling 
               one or both of this options requires the substitution of your 
               own routines for installation and keyboard handling.

               Both options must normally be enabled (1).


          AT_BIOS
               If enabled, the AT BIOS wait/post handler is installed. 
               May be disabled when compatibility problems arise.

               This option is normally enabled (1).
               

                                  Memory Allocation

          TSKALLOC.C  is  needed if TSK_DYNAMIC is enabled in  tskconf.h  to 
          handle  the allocation and free calls. If you want to use  dynamic 
          allocation  in your own tasks, you should also use  the  functions 
          tsk_alloc and tsk_free to avoid the reentrancy problems  mentioned 
          in the introduction. If you should need other forms of alloc (like 
          calloc)  the  recommended  way  is  to  add  those  functions   to 
          TSKALLOC.C, requesting the resource alloc_resource before  calling 
          the C memory-allocation function.


                                       Snapshot

          TSKSNAP.C is only needed if you want to include the snapshot  dump 
          into  your  program. Note that you can *not* use snapshot  if  you 
          disable TSK_NAMED in tskconf.h.


                                      Task Stacks

          When  compiling your application,  turn stack  checking  off.  The 
          standard  stack check is of little use with task stacks,  and  may 
          interfere with CTask's operation.  The stack area for tasks should 
          be  allocated  on the main program's stack,  not in the static  or 
          heap data space. The reason for this is that some of the C library 
          routines check for stack overflow regardless of your  compile-time 
          switches,  and  will  crash  your application if  you  use  stacks 
          outside the normal stack. The stack allocation parameter with LINK 
          (MS-C),  or the _stacksize variable (Turbo C) have to be increased 
          to reflect the additional stack space. When calculating task stack 
          sizes, keep in mind that library routines (esp. printf) allocate a 
          lot of space on the stack for temporary variables. A minimum of 1k 
          for  tasks using library routines is recommended,  2k puts you  on 
          the  safe  side.  Tasks  not using C library routines  may  use  a 
          smaller  stack,  about 256 bytes at a minimum,  plus space for any 

          CTask Manual          Version 1.1  88-07-01                Page 19



          local variables and nested routines. Then add up all task  stacks, 
          and   add   space  for  the  main  task  (the   function   calling 
          install_tasker), with this size also dependent on what you will do 
          in  the main task while CTask is active. Stacks for tasks that  do 
          not use C library routines may be allocated anywhere.


                                        Drivers

          The  keyboard  and DOS handlers are always installed  with  CTask. 
          Using the serial I/O and printer drivers is optional,  so you have 
          to  install them separately,  but only *after*  installing  CTask. 
          When  using  the serial driver,  include "sio.h" in your  modules, 
          when using the printer driver, include "prt.h".

          Another  driver  that  is  automatically  installed  is  the  BIOS 
          wait/post  handler  for  the IBM AT. The  AT  BIOS  contains  some 
          multitasking  hooks  to  avoid busy waiting in the  BIOS.  If  you 
          experience  problems with disk accesses or printer output  through 
          BIOS  (not through the CTask printer driver), you  should  disable 
          installation  of  this  driver  by  setting  AT_BIOS  to  zero  in 
          tskconf.h.  Normally,  no problems should arise with  this  driver 
          even in XT type machines.


                                   Things to remember

          Remember that tasks are not automatically started after  creation. 
          Use start_task to allow a created task to run.

          Always use create_xxx on resources,  pipes,  etc.  Using the event 
          routines without doing so will have unpredictable results.

          Before exiting the program, all installed drivers and CTask should
          be  explicitly  removed.  Although  the  DOS  handler  traps   the 
          terminate  call and automatically calls remove_tasker, you  should 
          make  sure  that  all  tasks  are  completed  properly,  and  call 
          remove_tasker yourself.

          Deleting events before exiting the program is not  mandatory,  but 
          recommended to kill all tasks waiting for the event. You should be 
          careful  not  to  kill tasks while they are  active  in  DOS.  The 
          kill_task routine should be reserved for fatal error handling. The 
          best  way  is to let the tasks kill themselves depending  on  some 
          global  variable or event.  If a task is killed while waiting  for 
          input  in DOS, DOS operation may be severely impaired. If you  use 
          the C console input routines, make sure that the task returns from 
          DOS  before it is killed, if necessary by requesting the  user  to 
          press a key.

          CTask Manual          Version 1.1  88-07-01                Page 20



                                  Priority Handling
                                  =================

          CTask   provides   for  prioritized  task  execution   and   event 
          processing. This means that a task that has a higher priority will 
          be  run  before any other tasks having  lower  priority.  Also,  a 
          higher  priority  task will gain access  to  resources,  counters, 
          pipes,   and  mail,   before  lower  priority  tasks.  With  fixed 
          priorities,  this  means that a high priority task can  monopolize 
          CPU  time,  even  if  it  calls  schedule()  explicitly.  Variable 
          priority  increases each eligible task's priority by one  on  each 
          scheduler  call,  so that lower priority tasks will slowly rise to 
          the head of the queue until they get executed.  The priority  will 
          be reset to the initial priority when a task is run.

          Since  variable priority increases processing time in the critical 
          region  of  the scheduler,  it is not recommended for  systems  in 
          which  a  larger  number  of tasks  is  expected  to  be  eligible 
          simultaneously.

          Usually,  all  tasks  in a system should have the  same  priority, 
          with   only  very  few  exceptions  for  non-critical   background 
          processing  (low  priority)  or  very  time-critical  tasks  (high 
          priority).  High  priority  tasks should be written in such a  way 
          that  they  either  reduce  their  priority  when  processing   is 
          completed,  or that they wait for an event. Busy waiting in a high 
          priority  task will severely impair system operation with variable 
          priority  enabled,  and  will stop the system until  the  task  is 
          placed in a waiting state with fixed priority.

          The  (automatically created) main task is started with the highest 
          possible priority below the timer task, so that it can process all 
          initialisations  before other tasks start running.  To  allow  the 
          system to operate,  the priority of the main task must be reduced, 
          or the main task must wait for an event or a timeout.

          CTask Manual          Version 1.1  88-07-01                Page 21



                                   CTask Data Types
                                   ================

          Note  that you do not have to know the innards of the  structures. 
          All  structure fields are filled by the "create_xxx" routines  and 
          modified  by the CTask functions.  You should NEVER modify a field 
          in  one of the structures directly.  The structures are  explained 
          here shortly only for those wanting to modify the routines. 

          If  you only want to use the routines,  you should simply  include 
          the file "tsk.h" in your source, and define variables of the types

                tcb         - for task control blocks
                tcbptr      - for far pointers to tcbs

                flag        - for flag events
                flagptr     - for far pointers to flags

                resource    - for resource events
                resourceptr - for far pointers to resources

                counter     - for counter events
                counterptr  - for far pointers to counters

                mailbox     - for mailbox events
                mailboxptr  - for far pointers to mailboxes

                pipe        - for pipe events
                pipeptr     - for far pointers to pipes

                wpipe       - for word pipe events
                wpipeptr    - for far pointers to word pipes

                buffer      - for buffer events
                bufferptr   - for far pointers to buffers

                tlink       - for timeout control blocks
                tlinkptr    - for far pointers to timeout control blocks

                namerec     - for control block names
                nameptr     - for name pointers

          without caring what's behind them.

          Additionally, you may use the types

                byte        - for unsigned characters
                word        - for unsigned short integers
                dword       - for unsigned long integers

                funcptr     - for pointers to task functions
                farptr      - for far pointers to anything
                byteptr     - for far pointers to byte arrays
                wordptr     - for far pointers to word arrays

          CTask Manual          Version 1.1  88-07-01                Page 22




          in  defining  or typecasting items to be passed as  parameters  to 
          CTask functions.


                  Typedefs used for simplified type specifications

             typedef unsigned char byte;
             typedef unsigned short word;
             typedef unsigned long dword;
             typedef void (cdecl far *funcptr)();
             typedef void far *farptr;
             typedef byte far *byteptr;
             typedef word far *wordptr;

                      Error return values for mailbox functions

             #define TTIMEOUT ((farptr) -1L)
               This value is returned if a timeout occurred during a mailbox 
               wait.

             #define TWAKE    ((farptr) -2L)
               This  value  is returned if the task was waked  up  during  a 
               mailbox wait.


                               The timer control block

          The  timer control block is included in every task control  block. 
          It  may  also be created as a separate entity to  specify  special 
          actions  to be executed after or every n timer ticks.  The  "next" 
          field links the active structures into the timer queue.

          "timeout"  gives the number of timer ticks, "reload" is  used  for 
          repetitive  timeout actions to reload the original timeout  value. 

          "strucp"  points  to  the  structure to  be  acted  upon,  "tkind" 
          specifies the kind of structure:

               #define  TKIND_TASK        1
                    Strucp  points  to the task control block of  which  the 
                    element is a member. The task will be awakened when  the 
                    timeout expires.

               #define  TKIND_WAKE        2
                    Strucp points to a task control block. Otherwise same as 
                    TKIND_TASK.

               #define  TKIND_PROC        3
                    Strucp  contains the address of a function to be  called 
                    on timeout.

               #define  TKIND_FLAG        4
                    Strucp points to a flag that should be set on timeout.

          CTask Manual          Version 1.1  88-07-01                Page 23




               #define  TKIND_COUNTER     5
                    Strucp  points to a counter that should be increased  on 
                    timeout.

               #define  TKIND_TEMP        0x80
                    This  is  a modifying flag. If set,  the  timer  control 
                    block was allocated dynamically, and should be freed  on 
                    timeout.


          "tstate" contains the state of the element:

               #define  TSTAT_REMOVE      -1
                    The  element should be taken off the queue on  the  next 
                    pass (if the TKIND_TEMP-flag is set, it will be freed).

               #define  TSTAT_IDLE        0
                    The element is not enqueued.

               #define  TSTAT_COUNTDOWN   1
                    The  timeout counter is counted down. If the timeout  is 
                    reached, the element is removed from the queue.

               #define  TSTAT_REPEAT      2
                    The  timeout counter is counted down. If the timeout  is 
                    reached, the timeout count is reloaded.


             typedef struct tlink_rec far *tlinkptr;

             struct tlink_rec {
                              tlinkptr next;
                              dword    timeout;
                              dword    reload;
                              farptr   strucp;
                              byte     tstate;
                              byte     tkind;
                              };

             typedef struct tlink_rec tlink;



                               The name link structure

          If  TSK_NAMED is enabled, all structures except the timer  control 
          block contain a name link. All control blocks are linked and named 
          via  this  element.  To facilitate removal from the  list,  it  is 
          doubly  linked  via  the pointers "follow"  and  "prev".  

          "strucp"  points to the head of the structure the name link is  an 
          element of, with "nkind" specifying the type of structure:


          CTask Manual          Version 1.1  88-07-01                Page 24



               #define  TYP_TCB        1     task control block
               #define  TYP_FLAG       2     flag event
               #define  TYP_RESOURCE   3     resource event
               #define  TYP_COUNTER    4     counter event
               #define  TYP_MAILBOX    5     mailbox event
               #define  TYP_PIPE       6     byte pipe
               #define  TYP_WPIPE      7     word pipe
               #define  TYP_BUFFER     8     buffer

          The head element of the name list has its nkind field set to zero.

          The  "name" field contains an up to 8-character name plus  a  zero 
          terminator.

               #define  NAMELENGTH     9

               typedef struct name_rec far *nameptr;

               struct name_rec {
                               nameptr    follow;    
                               nameptr    prev;      
                               farptr     strucp;    
                               byte       nkind;     
                               char       name [NAMELENGTH];
                               };

               typedef struct name_rec namerec;



                          The task control block structure

          The  "next" field points to the next tcb in a queue.  The  "queue" 
          pointer  points to the head of the queue the task is enqueued  in, 
          or will be enqueued in on the next schedule request in the case of 
          the current running task. 

          "stack" contains the saved task stack pointer (offset and segment) 
          if the task is not running. The field "stkbot" contains the bottom 
          address  of  the task stack.  It is set  by  create_task,  but  is 
          currently  not used anywhere else.  Stack checking routines  might 
          use this value to test for stack overflow and/or stack usage.

          "prior"  contains  the tasks current  priority,  with  0xffff  the 
          highest possible priority, and 0 the lowest. "initprior" initially 
          contains the same value.  If variable priority is enabled, "prior" 
          is  incremented on each scheduler call,  and reset to  "initprior" 
          when the task is activated.

          "state" and "flags" contain the tasks state and flags.

          "timerq" is a tlink structure used to chain the tcb into the timer 
          queue,  if  the  task is waiting for a timeout. See  above  for  a 
          description of the tlink structure.

          CTask Manual          Version 1.1  88-07-01                Page 25




          The fields "retptr" and "retsize" are used in event handling. They 
          are  used  when a task is waiting for an event by the  task  acti-
          vating the event,  and also by timeout and wake to indicate  error 
          returns.   The  use of these pointers eliminates the need to  loop 
          for  an  event,  which  requires slightly more code in  the  event 
          handling routines, but reduces the need for task switching.

          The  "name"  namerec  structure is present only  if  TSK_NAMED  is 
          enabled.  It  may  be  used in debugging  (see  tsksnap.c  for  an 
          example),  and in applications where the address of the  structure 
          can not be passed directly.

             typedef struct tcb_rec far *tcbptr;
             typedef tcbptr far *tqueptr;

             struct tcb_rec {
                             tcbptr   next;
                             tqueptr  queue;
                             byteptr  stack;
                             byteptr  stkbot;
                             word     prior;
                             word     initprior;
                             byte     state;
                             byte     flags;
                             dlink    timerq;
                             farptr   retptr;
                             int      retsize;
                            };

             typedef struct tcb_rec tcb;


                                     Task states

             #define  ST_KILLED   0
             #define  ST_STOPPED  1
             #define  ST_DELAYED  2
             #define  ST_WAITING  3
             #define  ST_ELIGIBLE 4
             #define  ST_RUNNING  5


          CTask Manual          Version 1.1  88-07-01                Page 26



                     Possible task states and queue association

          ST_KILLED      The  task has been killed.  Restarting the task  is 
                         not possible. Queue pointers are invalid.

          ST_STOPPED     The  task is not enqueued in any queue.  To be  in-
                         cluded  in  scheduling,  it  has to  be  explicitly 
                         started. The queue head pointer is NULL.

          ST_DELAYED     The task is enqueued in the timer queue only.  When 
                         the  timer expires,  it is placed in  the  eligible 
                         queue.  The queue head pointer is NULL.

          ST_ELIGIBLE    The  task  is  enqueued in the queue  of  processes 
                         eligible for running.  It can not be chained in the 
                         timer queue.  The queue head pointer points to  the 
                         eligible queue.

          ST_RUNNING     The task is the current running process.   Although 
                         it  is  not enqueued in any queue,  the queue  head 
                         pointer in its control block is valid and points to 
                         the  queue the process will be enqueued in  on  the 
                         next schedule request.

          ST_WAITING     The task is waiting for an event to happen.  It can 
                         also  be chained into the timer queue if a  timeout 
                         was specified in the call.   The queue head pointer 
                         points to the queue head in the event control block 
                         for the event the process is waiting on.


                    Possible state transitions and their reasons

             stopped  -> eligible    by start_task ()

             delayed  -> killed      by kill_task ()
                      -> eligible    by timer task, or wake_task ()
             
             eligible -> killed      by kill_task ()
                      -> running     by scheduler

             running  -> killed      by kill_task ()
                      -> stopped     by delay (0)
                      -> delayed     by delay (n != 0)
                      -> eligible    by scheduler
                      -> waiting     by wait_xxx ()

             waiting  -> killed      by kill_task ()
                      -> eligible    by event happening, timeout,
                                     or wake_task()



          CTask Manual          Version 1.1  88-07-01                Page 27



                                     Task flags

          System flags:

               #define  F_TEMP   0x80
                    This tcb was allocated automatically, and must be free'd 
                    on task kill.

               #define  F_STTEMP 0x40
                    The tasks stack was allocated automatically, and must be 
                    free'd on task kill.

          User changeable flags:

               #define  F_CRIT   0x01
                    This  task  may not be preempted. It will run  until  it 
                    clears  this  flag, delays itself, calls  the  scheduler 
                    explicitly, or waits for an event.



                               The event control blocks

          All event control blocks have two optional fields:

          "name"  is only present if TSK_NAMED is enabled. It is  a  namerec 
          structure as explained above.

          "flags" is only present if TSK_DYNAMIC is enabled. It contains

               F_TEMP    If this control block was allocated  automatically, 
                         and must be free'd on delete.

               F_STTEMP  If  the buffer for this event was  allocated  auto-
                         matically, and must be free'd on delete (pipes  and 
                         buffers only).




          CTask Manual          Version 1.1  88-07-01                Page 28



                              The flag event structure

          Contains  two queues for processes waiting on a flag state  (clear 
          or set), plus the flag state (0 = clear, 1 = set).

             typedef struct {
                            tcbptr  wait_set;
                            tcbptr  wait_clear;
                            int     state;
                            byte    flags;   (if TSK_DYNAMIC)
                            namerec name;    (if TSK_NAMED)
                            } flag;

             typedef flag far *flagptr;


                             The counter event structure

          Similar to a flag, but contains a doubleword state counter.

             typedef struct {
                            tcbptr  wait_set;
                            tcbptr  wait_clear;
                            dword   state;
                            byte    flags;   (if TSK_DYNAMIC)
                            namerec name;    (if TSK_NAMED)
                            } counter;

             typedef counter far *counterptr;


                            The resource event structure

          Contains a queue for the tasks waiting for access to the resource, 
          a  pointer  to  the current owner of the resource  (to  check  for 
          illegal "release_resource" calls),  and the resource state (0 = in 
          use, 1 = free).

             typedef struct {
                            tcbptr   waiting;
                            tcbptr   owner;
                            int      state;
                            byte     flags;   (if TSK_DYNAMIC)
                            namerec  name;    (if TSK_NAMED)
                            } resource;

             typedef resource far *resourceptr;



          CTask Manual          Version 1.1  88-07-01                Page 29



                             The mailbox event structure

          The msgptr type is only used internally to chain mail blocks  into 
          the  mailbox.  The  mailbox  type contains a queue  of  the  tasks 
          waiting  for mail,  and a first and last pointer for the chain  of 
          mail blocks.  

             struct msg_header {
                               struct msg_header far *next;
                               };

             typedef struct msg_header far *msgptr;

             typedef struct {
                            tcbptr  waiting;
                            msgptr  mail_first;
                            msgptr  mail_last;
                            byte    flags;   (if TSK_DYNAMIC)
                            namerec name;    (if TSK_NAMED)
                            } mailbox;

             typedef mailbox far *mailboxptr;


                        The pipe and word pipe event structure

          Contains queues of the tasks waiting to read or write to the pipe, 
          indices  for reading (outptr) and writing (inptr) into the buffer, 
          the  buffer size,  the number of bytes or words currently  in  the 
          pipe  ("filled"),  and the pointer to the buffer.  A word pipe  is 
          handled exactly the same as a byte pipe, the only difference being 
          the element size placed in the buffer.  With normal pipes, charac-
          ters are buffered, with word pipes, words.

             typedef struct {
                            tcbptr   wait_read;
                            tcbptr   wait_write;
                            tcbptr   wait_clear;
                            word     bufsize;
                            word     filled;
                            word     inptr;
                            word     outptr;
                            byteptr  contents;
                            byte    flags;   (if TSK_DYNAMIC)
                            namerec name;    (if TSK_NAMED)
                            } pipe;

             typedef pipe far *pipeptr;


          CTask Manual          Version 1.1  88-07-01                Page 30



             typedef struct {
                            tcbptr   wait_read;
                            tcbptr   wait_write;
                            tcbptr   wait_clear;
                            word     bufsize;
                            word     filled;
                            word     inptr;
                            word     outptr;
                            wordptr  wcontents;
                            byte    flags;   (if TSK_DYNAMIC)
                            namerec name;    (if TSK_NAMED)
                            } wpipe;

             typedef wpipe far *wpipeptr;


                              The buffer event structure

          Contains  resources for read and write access, the word pipe  used 
          for buffering, and a message counter.

             typedef struct {
                             resource    buf_write;
                             resource    buf_read;
                             wpipe       pip;
                             word        msgcnt;
                             byte        flags;   (if TSK_DYNAMIC)
                             namerec     name;    (if TSK_NAMED)
                            } buffer;

             typedef buffer far *bufferptr;



          NOTE:  When  modifying CTask structures,  take care to modify  the 
          equivalent  definitions  in the assembler include file  "tsk.mac". 
          Some  of  the assembler routines have to use  field  offsets  into 
          pointers,  so  having  different offsets in C and  assembler  will 
          crash the system.

          CTask Manual          Version 1.1  88-07-01                Page 31



                                   CTask Routines
                                   ==============

                              Installation and Removal

          void install_tasker (int varpri, int speedup);

               Installs  the multitasker.  Must be called prior to any other 
               routine. The calling routine is defined as the main task, and 
               assigned  the  highest priority.   To allow  other  tasks  to 
               execute,  the  main task must have its priority  reduced,  be 
               delayed,  or  wait  on an event.   

               The "varpri" parameter enables variable priority if nonzero.

               The  "speedup" parameter is defined for the IBM  PC/XT/AT  as 
               the clock tick speedup factor. The timer tick frequency  will 
               be set to

                    speedup  ticks/sec   msecs/tick
                      0        18.2        54.9     (normal clock)
                      1        36.4        27.5
                      2        72.8        13.7
                      3       145.6         6.9
                      4       291.3         3.4

               Note  that  all  timeouts are specified  in  tick  units,  so 
               changing  the speedup parameter will influence  timeouts  and 
               delays.  You  can enable CLOCK_MSECS in  tskconf.h  to  allow 
               timeouts to be specified in milliseconds.
               The system clock will not be disturbed by changing the speed. 
               Using values above 2 can lead to interrupt overruns on slower 
               machines and is not recommended.


          void remove_tasker (void);

               Uninstalls the multitasker. Must only be called from the main 
               task, and should be called before exiting the program.



                                    Miscellaneous


          void preempt_off (void);

               Disables task preemption. This is the default after installa-
               tion.  With preemption turned off,  only delays, event waits, 
               and explicit scheduler calls will cause a task switch.



          CTask Manual          Version 1.1  88-07-01                Page 32



          void preempt_on (void);

               Enables  task preemption.  Task switches will occur on  timer 
               ticks.


          void far schedule (void);

               Explicit  scheduling request.  The highest priority  eligible 
               task will be made running.


          void far c_schedule (void);

               Conditional  scheduling request.  Scheduling will take  place 
               only if preemption is allowed.


          void tsk_dis_preempt (void)

               Temporarily  disable task preemption.  Preemption will be re-
               enabled  by  tsk_ena_preempt or  an  unconditional  scheduler 
               call.


          void tsk_ena_preempt (void)

               Re-enable  task  preemption.  Note that  tsk_dis_preempt  and 
               tsk_ena_preempt do not change the global preemption state set 
               by preempt_off and preempt_on.


          int tsk_dis_int (void)

               Disable  interrupts.  Returns the state of the interrupt flag 
               prior to this call (1 if interrupts were enabled).


          void tsk_ena_int (int state)

               Enables  interrupts if "state" is nonzero.  Normally used  in 
               conjunction with tsk_dis_int.

          The routines tsk_dis_int and tsk_ena_int may be used in a  simpli-
          fied scheme with the defines

               CRITICAL;      Declares "int crit_intsav;".
               C_ENTER;       Expands to "crit_intsav = tsk_dis_int ();"
               C_LEAVE;       Expands to "tsk_ena_int (crit_intsav);".


          void tsk_cli (void)

               Disables interrupts (intrinsic function).

          CTask Manual          Version 1.1  88-07-01                Page 33





          void tsk_sti (void)

               Unconditionally enables interrupts (intrinsic function).


          void tsk_outp (int port, byte b)

               Outputs  the  value "b" to  hardware-port  "port"  (intrinsic 
               function).

          byte tsk_inp (int port)

               Returns the value read from port "port" (intrinsic function).


          The following entry points may be used from assembler routines:

          extrn scheduler: far

               Direct entry into the scheduler.  The stack must be set up as 
               for an interrupt handler, e.g.
                    pushf
                    cli
                    call  scheduler


          extrn _sched_int: far

               Conditional scheduling call.  The stack must be set up as for 
               an interrupt handler.




          CTask Manual          Version 1.1  88-07-01                Page 34



                                   Task Operations

          tcbptr create_task (tcbptr task, funcptr func, byteptr stack,
                              word stksz, word prior, farptr arg 
                              [, byteptr name]);

               Initialises a task.  Must be called prior to any other opera-
               tions  on this task.  The task is in the stopped state  after 
               creation. It must be started to be able to run.

               "task"    is  a  pointer to a tcb (NULL for  automatic  allo-
                         cation).
               "func"    is a pointer to a void far function, with a single 
                         dword sized parameter.
               "stack"   is a pointer to a stack area for the task (NULL for 
                         automatic allocation).
               "stksz"   is the size of the stack area in bytes.
               "prior"   is the tasks priority (0 lowest, 0xffff highest).
               "arg"     is an argument to the created task. It may be used 
                         to differentiate between tasks when using the same 
                         function in different tasks.
               "name"    is  the name of the task,  up to eight  characters, 
                         plus  zero-terminator.  This  parameter is  defined 
                         only if TSK_NAMEPAR is enabled in tskconf.h.


          void kill_task (tcbptr task);

               Kills a task. The task can no longer be used.


          int start_task (tcbptr task);

               Starts a task, i.e. makes it eligible for running.
               Returns  0  if  task  was started,  -1 if the  task  was  not 
               stopped.
               A value of NULL for "task" will start the "main task".


          int wake_task (tcbptr task);

               Prematurely wakes a delayed or waiting task.
               If the task was waiting for an event, it will be removed from 
               the  waiting queue,  with the operation terminating  with  an 
               error return value.
               Returns  0 if task was waked,  -1 if the task was not delayed 
               or waiting.
               A value of NULL for "task" will wake the "main task".



          CTask Manual          Version 1.1  88-07-01                Page 35



          void set_priority (tcbptr task, word prior)

               Sets the priority of the specified task to "prior".
               Note that you should NOT modify the priority field in the tcb 
               structure directly.
               A value of NULL for "task" will set the priority of the "main 
               task".


          void set_task_flags (tcbptr task, byte flags)

               Sets the flags of the task to "flags".  Currently,  the  only 
               flag that can be changed is

                         F_CRIT   the task can not be preempted if set.

               Note  that  you  may  NOT modify the flag field  in  the  tcb 
               structure directly.
               A  value of NULL for "task" will set the flags of  the  "main 
               task".


                                  Timer Operations

          Timeouts are normally specified in timer ticks. If CLOCK_MSECS  is 
          enabled, timeouts will be converted to the nearest number of timer 
          ticks  automatically.  The global  word  variable  "ticks_per_sec" 
          contains  a rough estimate of the number of ticks per second  even 
          if CLOCK_MSECS is not enabled.


                                 Event wait Timeouts

          When  waiting  for  an event,  a timeout may  be  specified.   The 
          operation will terminate with an error return value if the timeout 
          is reached before the event occurs.
          NOTE  that the timeout parameter is not optional.  To  specify  no 
          timeout, use the value 0.


                                       Delays

          int t_delay (dword ticks);

               Delay the current task for "ticks" clock ticks/milliseconds.
               If ticks is 0, the task is stopped.


                                    Timed Events

          You can create timer control blocks to

               - set a flag
               - increment a counter

          CTask Manual          Version 1.1  88-07-01                Page 36



               - wake up a task
               - call a function

          after  a specified timeout interval.  The operation may optionally 
          be  repeated.  For calling functions on a timeout,  the  following 
          must be noted:

               Timeout functions should be as short as possible, since they
               run at the highest priority.
               The  stack and data area is the area of the  timer  task.  Be 
               careful when referencing variables.
               Timeout  functions may not use any functions that could cause 
               the timer task to be made waiting.


          tlinkptr create_timer (tlinkptr elem, dword tout, farptr strucp,
                                 byte kind, byte rept);

               Create a timer control block.
               Returns the address of the control block, NULL on error.

               "elem"    is the control block to initialise (NULL for auto-
                         matic allocation).
               "tout"    specifies the timeout interval.
               "strucp"  points  to  the structure to be  used.  This  is  a 
                         flagptr  for  setting  a  flag,  a  counterptr  for 
                         increasing counters, a tcbptr for waking a task, or 
                         a funcptr for calling a function.
               "kind"    gives the kind of structure "strucp" points to.  It 
                         must be one of
                              TKIND_WAKE     for task-wakeup
                              TKIND_PROC     for function call
                              TKIND_FLAG     for flag set
                              TKIND_COUNTER  for counter increment.
               "rept"    if  nonzero,  the action will be repeated on  every 
                         "tout" timeout interval.

               NOTE: Timer control blocks can not be named.
               

          void delete_timer (tlinkptr elem);

               Deletes  a  timer  control block,  and removes  it  from  the 
               timeout queue.


          void change_timer (tlinkptr elem, dword tout, byte rept);

               Changes  the  timeout  value and/or the repeat  flag  for  an 
               existing timer control block. If "tout" is zero, the call has 
               the same effect as delete_timer.


          NOTE:  delete_timer  and change_timer should not be used on  auto-

          CTask Manual          Version 1.1  88-07-01                Page 37



          matically  allocated timer control blocks.  Since such blocks  are 
          deallocated   once   the  timeout  expires  (except   for   repeat 
          operations), the validity of the pointer is not guaranteed.


                                  Event Operations
                                  ================

                                      Resources

          A Resource is either in use or free, the default state is free.
          If a task has requested a resource, its state is in use.
          Tasks  requesting  a  resource  while it is in use  will  be  made 
          waiting. If the resource is released, the highest priority waiting 
          task is made eligible,  and is assigned the  resource.   Interrupt 
          handlers    may   not   use   resource   functions   other    than 
          "check_resource".


          resourceptr create_resource (resourceptr rsc [, byteptr name]);

               This initialises a resource.  Must be used prior to any other 
               operations on a resource.

               Returns the address of the control block, NULL on error.

               "rsc"     is  the resource control block (NULL for  automatic 
                         allocation).

               "name"    is   the  name  of  the  resource,   up  to   eight 
                         characters, plus zero-terminator. This parameter is 
                         defined only if TSK_NAMEPAR is enabled in tskconf.h.


          void delete_resource (resourceptr rsc);

               Calling  this  routine is optional.  It will kill  all  tasks 
               waiting for the resource.


          void release_resource (resourceptr rsc);

               Release the resource.  If the task does not own the resource, 
               the call is ignored.
               If  tasks  are waiting,  the highest priority task will  gain 
               access to the resource.


          int request_resource (resourceptr rsc, dword timeout);

               Requests the resource.  If it is not available,  the task  is 
               suspended. A timeout may be specified.
               Returns  0  if  resource  was  allocated,  -1  if  a  timeout 
               occurred, -2 on wake.

          CTask Manual          Version 1.1  88-07-01                Page 38



               This  call  is  ignored (returns a 0)  if  the  calling  task 
               already owns the resource.


          int c_request_resource (resourceptr rsc);

               Requests the resource only if it is available.
               Returns 0 if resource was allocated, -1 if unavailable.


          int check_resource (resourceptr rsc);
                
               Returns 0 if resource is allocated, 1 if free.


                                        Flags

          A Flag can be either on or off, the default state is off (0).
          Tasks  can  wait  on either state of the flag.  If  the  state  is 
          changed,  all  tasks  waiting  for the state  are  made  eligible.  
          Interrupt  handlers  may use  the  "set_flag",  "clear_flag",  and 
          "check_flag" functions.


          flagptr create_flag (flagptr flg [, byteptr name]);

               This  initialises  a flag.  Must be used prior to  any  other 
               operations on a flag. The state is set to 0.

               Returns the address of the control block, NULL on error.

               "flg"     is the flag control block (NULL for automatic allo-
                         cation).

               "name"    is  the name of the flag,  up to eight  characters, 
                         plus  zero-terminator.  This  parameter is  defined 
                         only if TSK_NAMEPAR is enabled in tskconf.h.


          void delete_flag (flagptr flg);

               Calling  this  routine is optional.  It will kill  all  tasks 
               waiting for the flag.


          void set_flag (flagptr flg);

               This sets the flag.  All tasks waiting for the set state will 
               be made eligible for running.



          CTask Manual          Version 1.1  88-07-01                Page 39



          void clear_flag (flagptr flg);

               This  clears the flag.  All tasks waiting for the clear state 
               will be made eligible for running.

                      
          int wait_flag_set (flagptr flg, dword timeout);

               Waits for the set state of the flag.  If the flag is not set, 
               the task is suspended. A timeout may be specified.
               Returns 0 if the flag was set, -1 on timeout, -2 on wake.


          int wait_flag_clear (flagptr flg, dword timeout);

               Waits  for the clear state of the flag.  If the flag  is  not 
               clear, the task is suspended. A timeout may be specified.  

               Returns 0 if the flag was cleared, -1 on timeout, -2 on wake.


          int clear_flag_wait_set (flagptr flg, dword timeout)

               Combines the operations clear_flag and wait_flag_set.
               Returns 0 if the flag was set, -1 on timeout, -2 on wake.

          int check_flag (flagptr flg);

               Returns 0 if flag clear, 1 if set.



                                      Counters

          A  Counter can have any value from 0L to 0xffffffffL,  the default 
          value is 0. Tasks can wait for a counter being zero or non-zero.
          If the counter is cleared or decremented to zero,  all tasks  wai-
          ting for the zero condition are made eligible.
          If  the counter is incremented,  the highest priority task waiting 
          for non-zero is made eligible,  and the counter is decremented  by 
          one.
          Interrupt handlers may use the "clear_counter", "inc_counter", and 
          "check_counter" functions.


          counterptr create_counter (counterptr cnt [, byteptr name]);

               This  initialises a counter.  Must be used prior to any other 
               operations on a flag. The value is set to 0.

               Returns the address of the control block, NULL on error.

               "cnt"     is  the  counter control block (NULL for  automatic 
                         allocation).

          CTask Manual          Version 1.1  88-07-01                Page 40




               "name"    is the name of the counter, up to eight characters, 
                         plus  zero-terminator.  This parameter  is  defined 
                         only if TSK_NAMEPAR is enabled in tskconf.h.


          void delete_counter (counterptr cnt);

               Calling  this  routine is optional.  It will kill  all  tasks 
               waiting for the counter.


          void clear_counter (counterptr cnt);

               Clears  the counter to zero.  All tasks waiting for the  zero 
               state will be made eligible for running.


          int wait_counter_set (counterptr cnt, dword timeout);

               Waits for the counter having a nonzero value. If the value is 
               zero,  the task is suspended.  The value is decremented  when 
               the task gets access to the counter.  A timeout may be speci-
               fied.
               Returns  0 if the counter was nonzero,  -1 on timeout,  -2 on 
               wake.  


          int wait_counter_clear (counterptr cnt, dword timeout);

               Waits  for the counter having a zero value.  If the value  is 
               nonzero, the task is suspended. A timeout may be specified.
               Returns 0 if the counter was zero, -1 on timeout, -2 on wake.


          void inc_counter (counterptr cnt);

               Increments the counter.  If tasks are waiting for the nonzero 
               state,  the  highest  priority task is given  access  to  the 
               counter.


          dword check_counter (counterptr cnt);

               Returns the current value of the counter.




          CTask Manual          Version 1.1  88-07-01                Page 41



                                      Mailboxes

          A Mailbox can hold any number of mail blocks.
          Tasks  can send mail to a mailbox and wait for mail to  arrive.  A 
          mail block is assigned to the highest priority waiting task.  Care 
          must  be  exercised not to re-use a mail block until it  has  been 
          processed  by the receiving task.   The mail block format is  user 
          defineable,  with the first doubleword in a block reserved for the 
          tasking  system.   Interrupt  handlers  may use  the  "send_mail", 
          "c_wait_mail", and "check_mailbox" functions.

          Note  that mailboxes are well suited to provide the mechanism  for 
          managing a chain of (equally sized) free mail blocks. On initiali-
          sation,  all  free  blocks  would be "sent" to  the  manager  box. 
          Requesting a free block would use "wait_mail",  and freeing a used 
          block would again "send" it to the manager mailbox.


          mailboxptr create_mailbox (mailboxptr box [, byteptr name]);

               This initialises a mailbox.  Must be used prior to any  other 
               operations on a mailbox.

               Returns the address of the control block, NULL on error.

               "box"     is  the mailbox control block (NULL  for  automatic 
                         allocation).

               "name"    is the name of the mailbox, up to eight characters, 
                         plus  zero-terminator.  This  parameter is  defined 
                         only if TSK_NAMEPAR is enabled in tskconf.h.


          void delete_mailbox (mailboxptr box);

               Calling  this  routine is optional.  It will kill  all  tasks 
               waiting for mail.


          void send_mail (mailboxptr box, farptr msg);

               Sends  a message to the specified mailbox.  If tasks are wai-
               ting for mail, the highest priority task will get it.  


          farptr wait_mail (mailboxptr box, dword timeout);

               Waits for mail.  If no mail is available, the task is suspen-
               ded. A timeout may be specified.
               Returns the pointer to the received mail block, TTIMEOUT 
               (-1) on timeout, TWAKE (-2) on wake.



          CTask Manual          Version 1.1  88-07-01                Page 42



          farptr c_wait_mail (mailboxptr box);

               Reads mail only if mail is available.
               Returns  NULL  if there is no mail,  else a  pointer  to  the 
               received message.


          int check_mailbox (mailboxptr box);

               Returns 0 if mailbox is empty, 1 otherwise.



                                        Pipes

          A Pipe has a buffer to hold character or word sized items.
          An  item may be written to a pipe if there is space in the buffer. 
          Otherwise,  the writing task will be made waiting.  A reading task 
          will be made waiting if the buffer is empty.   If an item has been 
          read,  the highest priority task waiting to write to the pipe will 
          be allowed to write.
          Interrupt  handlers  may  only use  pipe  functions  "check_pipe", 
          "c_write_pipe", and "c_read_pipe".

          Note  that  the  values -1 and -2 (0xffff and  0xfffe)  should  be 
          avoided when writing to word pipes.  These values are used to mark 
          timeout and wake when reading,  or pipe empty when checking a word 
          pipe, and thus may lead to erroneous operation of your routines.


          pipeptr create_pipe (pipeptr pip, farptr buf, word bufsize
                               [, byteptr name]);
          wpipeptr create_wpipe (wpipeptr pip, farptr buf, word bufsize
                                 [, byteptr name]);

               This  initialises  a pipe.  Must be used prior to  any  other 
               operations on a pipe.  "bufsize" specifies the buffer size in 
               bytes.  With word pipes,  the buffer size should be divisible 
               by two.

               Returns the address of the control block, NULL on error.

               "pip"     is the pipe/wpipe control block (NULL for automatic 
                         allocation).

               "name"    is  the name of the pipe,  up to eight  characters, 
                         plus  zero-terminator.  This  parameter is  defined 
                         only if TSK_NAMEPAR is enabled in tskconf.h.



          CTask Manual          Version 1.1  88-07-01                Page 43



          void delete_pipe (pipeptr pip);
          void delete_wpipe (wpipeptr pip);

               Calling  this  routine is optional.  It will kill  all  tasks 
               waiting to read or write messages.


          int read_pipe (pipeptr pip, dword timeout);
          word read_wpipe (wpipeptr pip, dword timeout);

               Read an item from a pipe.  If no item is available,  the task 
               is suspended. A timeout may be specified.
               Returns the item, or -1 on timeout, -2 on wake.


          int c_read_pipe (pipeptr pip);
          word c_read_wpipe (wpipeptr pip);

               Reads an item from a pipe only if one is available.
               Returns the received item, or -1 if none is available.


          int write_pipe (pipeptr pip, byte ch, dword timeout);
          int write_wpipe (wpipeptr pip, word ch, dword timeout);

               Writes an item to a pipe.  If the buffer is full, the task is 
               suspended. A timeout may be specified.
               If  tasks are waiting to read,  the item will be assigned  to 
               the highest priority waiting task.
               Returns 0 on success, or -1 on timeout, -2 on wake.
                      

          int c_write_pipe (pipeptr pip, byte ch);
          int c_write_wpipe (wpipeptr pip, word ch);

               Writes an item to a pipe only if enough space is available.
               Returns 0 on success, or -1 if no space available.
                      

          int wait_pipe_empty (pipeptr pip, dword timeout);
          int wait_wpipe_empty (wpipeptr pip, dword timeout);

               Waits  for  the pipe to be emptied.  If the pipe  is  already 
               empty  on  entry,  the task continues to run.  Returns  0  on 
               empty, -1 on timeout, -2 on wake.


          int check_pipe (pipeptr pip);
          word check_wpipe (pipeptr pip);

               Returns  -1 if the pipe is empty,  else the first item in the 
               pipe. The item is not removed from the pipe.



          CTask Manual          Version 1.1  88-07-01                Page 44



          word pipe_free (pipeptr pip);
          word wpipe_free (wpipeptr pip);

                    Returns the number of free items available in the pipe.



                                        Buffers

          A Buffer has a buffer to hold message strings.
          A  message may be written to a buffer if it fits into the  buffer. 
          Otherwise,  the writing task will be made waiting.  A reading task 
          will  be made waiting if the buffer is empty.   If a  message  has 
          been  read,  the  highest  priority task waiting to write  to  the 
          buffer  will  be  allowed to write if its message  fits  into  the 
          available space.
          Interrupt  handlers  may  not  use  buffer  functions  other  than 
          "check_buffer".
          The buffer routines are implemented using resources and pipes, and 
          thus are not part of the true "kernel" routines.


          bufferptr create_buffer (bufferptr buf, farptr pbuf, word bufsize
                                   [, byteptr name]);

               This  initialises a buffer.  Must be used prior to any  other 
               operations on a buffer.
               The minimum buffer size is the length of the longest expected 
               message plus two.

               Returns the address of the control block, NULL on error.

               "buf"     is  the  buffer control block (NULL  for  automatic 
                         allocation).

               "name"    is the name of the buffer,  up to eight characters, 
                         plus  zero-terminator.  This  parameter is  defined 
                         only if TSK_NAMEPAR is enabled in tskconf.h.


          void delete_buffer (bufferptr buf);

               Calling  this  routine is optional.  It will kill  all  tasks 
               waiting to read or write messages.



          CTask Manual          Version 1.1  88-07-01                Page 45



          int read_buffer (bufferptr buf, farptr msg, int size, 
                           dword timeout);

               Read a message from a buffer. If no message is available, the 
               task is suspended. A timeout may be specified.
               The  message  will  be copied to the  buffer  "buf",  with  a 
               maximum length of "size" bytes.
               Returns the length of the received message, -1 on timeout, -2 
               on wake.


          int c_read_buffer (bufferptr buf, farptr msg, int size);

               Reads  a  message  from a buffer only if  one  is  available.  
               Returns the length of the received message,  or -1 if none is 
               available.


          int write_buffer (bufferptr buf, farptr msg, int size, 
                            dword timeout);

               Writes  a message from "msg" with length "size" to a  buffer. 
               If not enough space for the message is available, the task is 
               suspended. A timeout may be specified.
               If tasks are waiting for messages,  the highest priority task 
               will get it.
               Returns the length of the message, -1 on timeout, -2 on wake, 
               -3 on error (length < 0 or length > buffer buffer size).

                      
          int c_write_buffer (bufferptr buf, farptr msg, int size);

               Writes  a  message  to  a buffer  only  if  enough  space  is 
               available.
               Returns the length of the message,  -1 if no space available, 
               or -3 on error (length < 0 or length > buffer buffer size).


          word check_buffer (bufferptr buf);

               Returns  the  current number of bytes (not messages)  in  the 
               buffer, including the length words.





          CTask Manual          Version 1.1  88-07-01                Page 46



                                 The Keyboard Handler
                                 ====================

          word t_read_key (void)

               Waits for a key to be entered.  Returns the ASCII-code in the 
               lower  byte,  and  the  scan-code in the upper  byte,  or  -2 
               (0xfffe) on wake.


          word t_wait_key (dword timeout)

               Waits for a key to be entered.  Returns the ASCII-code in the 
               lower  byte,  and  the scan-code in the  upper  byte,  or  -1 
               (0xffff) on timeout, -2 (0xfffe) on wake.


          word t_keyhit (void)

               Returns -1 (0xffff) if no key was entered,  else the value of 
               the key. The key is not removed.


                                The Serial I/O handler
                                ======================

          The  serial I/O handler provides full duplex interrupt driven  I/O 
          on the serial ports. Support for COM1 and COM2 is included, adding 
          other  ports  is possible by changing the source  and/or  defining 
          ports on-line.


          int v24_define_port (int base, byte irq, byte vector)

               Defines  a  new COM-port. This routine can only  be  used  if 
               TSK_DYNAMIC is enabled.

               "base" is the port base I/O address.

               "irq" is the IRQ-line number (0-7 for XT, 0-15 for AT) the
                     port uses for interrupts.

               "vector" is the interrupt vector number (0-0xff).

               The  return  value is the internal port number for  use  with 
               v24_install. -1 is returned on error (memory full). 



          CTask Manual          Version 1.1  88-07-01                Page 47



          sioptr v24_install (int port, int init,
                              farptr rcvbuf, word rcvsize, 
                              farptr xmitbuf, word xmitsize);

               Installs the handler for the specified port. Currently, ports 
               0  (COM1) and 1 (COM2) are supported. Both ports may be  used 
               simultaneously,  the buffer areas for the ports must  not  be 
               shared.

               "rcvbuf" is a word pipe buffer area for received  characters, 
               with "rcvsize" specifying the buffer size in bytes. Note that 
               the  buffer  will  hold  rcvsize  /  2  received  characters. 
               "rcvbuf" may be NULL for automatic allocation.

               "xmitbuf"  is  a byte pipe buffer for characters  waiting  for 
               transmissions, "xmitsize" gives its size in bytes.
               "xmitbuf" may be NULL  for automatic allocation.

               If  the  port number for v24_install is ORed with  0x80,  the 
               port  is  *relative*. This means that the entry in  the  BIOS 
               table for COM-Ports is used to search the tables internal  to 
               the  driver  for the port information, instead of  using  the 
               table  entry directly. If the port address cannot  be  found, 
               the  driver returns with an error code. Note that  ports  are 
               numbered from 0, so to specify COM1, pass 0x80 as parameter.  

               If the "init" parameter is non-zero, the port is  initialised 
               with  the  default  values specified in the  source.  If  the 
               parameter  is zero, the control registers and baud  rates  on 
               entry are not modified.

               The  return value is a pointer to the sio control  block  for 
               use with the other driver routines. NULL is returned on error 
               (invalid   port   number,  bad  buffer   sizes,   nonexistent 
               hardware, out of memory).


          void v24_remove (sioptr sio, int restore);

               Removes the driver for the specified control block.
               Should  be called for all ports installed before exiting  the 
               program.

               If the "restore" parameter is nonzero, the control  registers 
               and  the baud rate that were set before installation  of  the 
               driver  are  restored. If the parameter is zero,  the  values 
               are not changed.



          CTask Manual          Version 1.1  88-07-01                Page 48



          void v24_remove_all (void)

               Removes  all  installed serial i/o drivers. This  routine  is 
               automatically   called  on  remove_tasker  if  drivers   were 
               installed. Note that you can not specify a restore parameter, 
               the default restore parameter is used (constant in tsksio.c).


          void v24_change_rts (sioptr sio, int on);

               Changes the state of the RTS output line. A nonzero value for 
               "on" will turn the output on.


          void v24_change_dtr (sioptr sio, int on);

               Changes the state of the DTR output line. A nonzero value for 
               "on" will turn the output on.


          extern void far v24_change_baud (sioptr sio, long rate);

               Changes  the baud rate.  The following baud rates are suppor-
               ted:

               50,  75, 110, 134, 150, 300, 600, 1200, 1800, 2000, 
               2400, 3600, 4800, 7200, 9600, 19200L, 38400L.

               Note  that baud rates above 9600 may cause problems  on  slow 
               machines.

          extern void far v24_change_parity (sioptr sio, int par);

               Changes  parity.  The parameter must be one of the  following 
               values defined in "sio.h":

                    PAR_NONE  no parity checks
                    PAR_EVEN  even parity
                    PAR_ODD   odd parity
                    PAR_MARK  mark parity
                    PAR_SPACE space parity


          extern void far v24_change_wordlength (sioptr sio, int len);

               Changes word length. Values 5, 6, 7, 8 may be given.


          extern void far v24_change_stopbits (sioptr sio, int n);

               Changes Stopbits. Values 1 and 2 are allowed.



          CTask Manual          Version 1.1  88-07-01                Page 49



          extern void far v24_watch_modem (sioptr sio, byte flags);

               The  modem  status  input  lines  specified  in  the  "flags" 
               parameter must be active to allow transmission.  Transmission 
               will  stop if one of the lines goes inactive.  The  parameter 
               may be combined from the following values defined in "sio.h":

                    CTS  to watch clear to send
                    DSR  to watch data set ready
                    RI   to watch ring indicator
                    CD   to watch carrier detect

               A  value  of  zero  (the  default)  will  allow  transmission 
               regardless of modem status.


          extern void far v24_protocol (sioptr sio, int prot, 
                                        word offthresh, word onthresh);

               Sets the handshake protocol to use.  The "prot" parameter may 
               be combined from the following values:

                    XONXOFF   to enable XON/XOFF (DC1/DC3) handshake
                    RTSCTS    to enable RTS/CTS handshake

               The  "offthresh"  value specifies the minimum number of  free 
               items in the receive buffer. If this threshold is reached, an 
               XOFF is transmitted and/or the RTS line is inactivated.
               The  "onthresh"  value specifies the minimum number of  items 
               that  must be free before XON is transmitted and/or  the  RTS 
               line is re-activated.

               Enabling XONXOFF will remove all XON and XOFF characters from 
               the input stream.  Transmission will be disabled when XOFF is 
               received, and re-enabled when XON is received.

               Enabling RTSCTS will stop transmission when the CTS modem 
               input line is inactive.


          int v24_send (sioptr sio, byte ch, dword timeout);

               Transmits the character "ch". A timeout may be specified. 
               Returns -1 on timeout, -2 on wake, else 0.



          CTask Manual          Version 1.1  88-07-01                Page 50



          int v24_receive (sioptr sio, dword timeout);

               Waits  for  a  received  character.   A  timeout  may  be 
               specified.  Returns -1 on timeout,  -2 on wake,  else the 
               character  in the lower byte,  plus an error code in  the 
               upper byte. The error code is the combination of

                    0x02      overrun error
                    0x04      parity error
                    0x08      framing error
                    0x10      break interrupt.


          int v24_check (sioptr sio);

               Returns -1 if no receive character is available, else the 
               next  character  from  the pipe.  The  character  is  not 
               removed.


          int v24_overrun (sioptr sio);

               Checks for receive pipe overrun.  Returns 1 if an overrun 
               occurred, 0 otherwise. Clears the overrun flag.


          int v24_modem_status (sioptr sio);

               Returns the current modem status word.  The CTS, DSR, RI, 
               and  CD  defines may be used to extract the  modem  input 
               line status.


          int v24_complete (sioptr sio);

               Returns  1 if all characters in the transmit pipe  have  been 
               sent, else 0.


          int v24_wait_complete (sioptr sio, dword timeout);

               Waits  for  the  transmit pipe to be  empty.  Returns  -1  on 
               timeout, -2 on wake, else 0.




          CTask Manual          Version 1.1  88-07-01                Page 51



                              The Printer Output Driver
                              =========================

          The  printer output driver provides for buffered output to  up  to 
          three  printer  ports (more can be added by editing  the  source). 
          Interrupt  or polling may be selected. Due to the  usual  hardware 
          implementation  of  printers  and  the  printer  interface,  using 
          polling  is  recommended. When using interrupts,  you  should  not 
          simultaneously  install  both  port 0 and port  1  with  interrupt 
          enabled, since both ports share the same interrupt line.


          int prt_install (int port, byte polling, word prior, 
                           farptr xmitbuf, word xmitsize);

               Installs the printer driver for the specified port.  Ports  0 
               (LPT1), 1 (LPT2), and 2 (LPT3) are supported.

               The   "polling"  parameter  specifies  polling  output   when 
               nonzero, interrupt output when zero.

               The "prior" parameter sets the priority of the printer output 
               task.

               "xmitbuf"  is  a buffer area for the printer  output  buffer, 
               "xmitsize" specifies its size in bytes.
               The  buffer  pointer  may be specified as  NULL  for  dynamic 
               allocation if TSK_DYNAMIC is enabled.

               If  the  port number for prt_install is ORed with  0x80,  the 
               port  is  *relative*. This means that the entry in  the  BIOS 
               table for LPT-Ports is used to search the tables internal  to 
               the  driver  for the port information, instead of  using  the 
               table  entry directly. If the port address cannot  be  found, 
               the  driver returns with an error code. Note that  ports  are 
               numbered from 0, so to specify LPT1, pass 0x80 as parameter.  

               The return value is the internal port number for use with the 
               other driver routines. -1 is returned on error (invalid  port 
               number, bad buffer sizes, nonexistent hardware).


          void prt_remove (int port);

               Removes  the  printer  driver for  the  specified  port.


          void prt_remove_all (void)

               Removes  all installed printer ports. This routine  is  auto-
               matically called on remove_tasker if ports were installed.



          CTask Manual          Version 1.1  88-07-01                Page 52



          void prt_change_control (int port, byte control);

               Changes  the  printer control output lines of the  port.  The 
               value for "control" may be combined from the following values 
               defined in "prt.h":

                    AUTOFEED  will enable printer auto feed if set
                    INIT      will initialise (prime) the printer if clear
                    SELECT    will select the printer if set


          int prt_write (int port, byte ch, dword timeout);

               Write a byte to the printer.  A timeout may be given. Returns 
               0 on success, -1 on timeout, -2 on wake.


          int prt_status (int port);

               Returns the current printer status lines,  combined from  the 
               values

                    BUSY      Printer is busy when 0
                    ACK       Acknowledge (pulsed 0)
                    PEND      Paper End detected when 0
                    SELIN     Printer is selected (on line) when 1
                    ERROR     Printer error when 0


          int prt_complete (int port);

               Returns 1 if the printer buffer has been completely transmit-
               ted, 0 otherwise.


          int prt_wait_complete (int port, dword timeout);

               Waits for printer output to complete.  Returns 0 on  success, 
               else -1 on timeout, -2 on wake.