CLIB Documentation
 
 
        Purpose
        -------
        CLIB (in its current form) provides C-like printf(), fprintf(),
        and sprintf() functions for Macro Assembler programmers.
        Included are a macro header (which must included in assembly)
        and a library containing runtime support.  This document assumes
        that you know pretty much what you're doing.
 
 
        Using CLIB
        ----------
        1. Include CLIB.MAC at the top of your assembler module.
        2. Link the library "CLIB.LIB" when you link, e.g.,
 
                link foo,,,clib
 
        You MUST have a PUBLIC segment called CODE.  The macros will
        assemble into this segment, and the runtime support is in
        segment CODE.  This was done so that there would be no need for
        GROUPing, etc., and so that CLIB would work with both COM and
        EXE file types.
 
 
        Argument passing
        ----------------
        Some conventions must be observed when passing parameters to the
        macros.  These are:
 
        1.  All variables passed as arguments are assumed to be
        addressable via the DS register.
 
        2.  The list of arguments for the format string MUST be enclosed
        in angle brackets.  E.g.,
 
                printf "ES:DI is %04x:%04x\n", <es, di>
 
        3.  All of the functions use AX; all other registers are
        unchanged.  You CANNOT pass AX as an argument!  That is,
 
                printf "DX:AX is %04x:%04x\n", <dx, ax>
 
        will NOT work.  You may be able to print the contents of AX if
        it is the first or only argument:
 
                printf "AX is %04x\n", <ax>
 
        but it is best to be safe:
 
                mov bx,ax
                printf "AX is %04x\n", <bx>
                mov ax,bx
 
        4.  To pass a the address of a variable, use the format "@ var"
        The space after the @ is mandatory.
 
                printf "Hello there %s\n", <@ username>
                printf "Address of memvar is %04x\n", <@ memvar>
 
        5. In the true spirit of C, virtually no checking of any kind is
        performed.  It's up to you to see that the number and type of
        arguments match the format string.
 
 
        Data types
        ----------
        CLIB can deal with several data types.  They are:
 
        1.  Int (word quantities).  May be signed or unsigned; register,
        immediate, memory variables, or near pointers:
 
                printf "%d",<bx>
                printf "%u",<bx>
                printf "%d",<117>
                printf "Addr of x is %04x", <@ x>
                printf "Val of x is %04x", <x>
 
        2.  Long (doubleword quantities).  Signed or unsigned; for
        normal use, these must be memory variables defined as DD:
 
                longint dd 12345678
                ...
                printf "%U", <longint>
 
        You can, however, pull the old C trick:
 
                printf "%U", <dx,ax>
 
        3.  Short (byte quantities).  Promoted to unsigned int before
        being passed, thus unsigned only.  May be immediate, or memory.
        Registers won't work because MASM provides no way for the macros
        to distinguish between 8-bit and 16-bit registers; the macros
        assume 16 bits for greater flexibility.
 
                somevar   db 1
                othervar  db -1
 
                printf "%u", <16>
                printf "%u", <somevar>
                printf "%d", <othervar>
 
        The last one is wrong!  It will display as 255; the macros will
        not sign extend byte quantities when they are pushed onto the
        stack as words.
 
        4. Char.  Same as byte:
 
                printf "%c", 114
 
        The following C-standard special chars are supported:
 
                \n              Newline, translated as CR/LF (13/10)
                \b              Backspace (08)
                \r              Carriage return (13)
                \t              Tab (9)
 
        Because the macros will have problems outputting the characters
        "<" and ">" (printf "A > B" will NOT work), the following two
        nonstandard special characters are supported:
 
                \g              > (Greater then)
                \l              < (Less than)
 
        Also, you may use a C-like "\nnn" character specifier, BUT the
        number is decimal (rather than C's octal) and it is not
        necessary to pad the number to three characters.  E.g.:
 
                printf "Hello \t\t world\n"
                printf "This is char 63: \63"
 
        To display a "\", use the "\\" convention:
 
                printf "File is \\util\\edlin.exe\n"
 
        5.  Strings.  These are standard ASCIIZ strings ('\0'
        terminated).  As arguments, they are always passed via pointer:
 
                printf "%s\n", <@ somestring>
 
        The format string may be either a literal (delimited by " or '),
        or an ASCIIZ string in storage:
 
                data segment
                format db "Value of di is %u\n",0
                data ends
 
                printf "This is a literal\n"
                printf 'So is this\n'
                printf format,<di>
 
        Literal strings are constructed in the code segment as they are
        encountered; thus, it is to your advantage to use stored strings
        if any format is used more than once.  Stored format strings
        must be accessible via DS at run time.  Note that the @ is NOT
        necessary (and in fact won't work) in order to give CLIB the
        address of a stored format string.
 
 
        printf format, <arglist>
        -----------------------------------
        Prints a formatted string to the standard output device
        (normally con:, but redirectable).  A typical use:
 
                printf "File contain %u lines\n", <numlines>
 
        The first parameter is a format string; as described above, it
        is either a literal string or the name of a stored format string
        accessible via DS.  The conversion specifiers % and \ are
        described below.
 
        The second parameter (actually a list of parameters enclosed in
        <> angle brackets) is the list of arguments to be converted.
        If there are no conversion arguments listed in the format string
        (printf "Hello world\n"), this parameter may be omitted.
 
        The format string contains literal characters and spaces (which
        are copied to the output file literally) and/or a set of
        conversions.  Each conversion specification begins with a %
        character and ends with a conversion type character.  Valid
        conversion types are:
 
                d       The argument is a signed integer; it is to be
                        output in decimal.
 
                u       The argument is an unsigned integer; it is to be
                        output in decimal.
 
                x       The argument is an unsigned integer; it is to be
                        output in hexadecimal.
 
                b       The argument is an unsigned integer; it is to be
                        output in binary.
 
                o       The argument is an unsigned integer; it is to be
                        output in hexadecimal.
 
                c       The argument is a character code.  One ASCII
                        character will be displayed (code 0..255).
 
                s       The argument is THE OFFSET ADDRESS OF a string
                        within the DS segment.  The string is ASCIIZ and
                        will be copied directly to the output.
 
        The numeric conversion types (d, u, x, b, o), if in upper case
        (D, U, X, B, O), indicate that the corresponding argument is
        long (32-bits, or dwords)
 
        Between the conversion character % and the conversion type may
        appear several optional fields.  These are (in required order):
 
                A minus sign    Indicates that the output argument is to
                                be left-justified within the output
                                field rather than the default
                                right-justified.
 
                A zero          Indicates that the field is to be padded
                                with zeroes rather than blanks.
 
                A field width   A decimal number which inidicates the
                                minimum number of positions to be taken
                                up by the formatted argument.  That is,
                                the integer 7, if formatted via "%4d",
                                will appear as "   7".
 
                                The field width may be an asterisk (*),
                                which indicates that the next argument
                                is an integer and it is the field width.
                                This allows computed field widths.
 
        If the first character following a "%" is not one of the valid
        conversion specifiers, or part of a valid optional field, it is
        output as is.  Thus, "%%" cann be used to display "%".
 
        Unsupported from C's printf(): floating point conversion types
        (e, f, and g); and the use of "L" as a long specifier.  That is,
        you MUST use "%08X" rather than "%08xL".
 
        Printf returns (in register AX) the I/O error result of the
        operation.  If it is zero, there was no error; if nonzero, there
        was an error and AX is the DOS error code.  Errors here are
        likely only if console output has been redirected.
 
 
        fprintf file, format, <arglist>
        -----------------------------------
        Just like printf except that an output device or file can be
        specified.  A typical use:
 
                fprintf stderr,"Error code %u returned\n", <bx>
 
        The first parameter is a file handle which identifies where the
        output is to be sent.  The following handles are predeclared and
        preopened by CLIB and DOS; you may use them without further ado:
 
                stdout          Console device; redirectable
                stderr          Console device; not redirectable.
                aux             Standard auxiliary output
                prn             Standard printer output
 
        If you wish to fprintf to a file, you must first open the file,
        and then pass fprintf the file handle returned by DOS:
 
                <open the file>
                mov fout,ax        ; Save file handle
                fprintf fout,"format",<arglist>
 
        The other two parameters are identical to printf.  In fact,
        printf is converted by macro into:
 
                fprintf stdout,format,<args>
 
        Returns the error code (or zero if no error) in AX.  An example
        of use:
 
                fprintf fout,format,<args>
                or ax,ax
                jz no_error
                mov bx,ax
                fprintf stderr,"DOS error %04x!!\n",<bx>
        no_error:
 
 
        sprintf string, format, <arglist>
        ---------------------------------
        Operates like fprintf except that the formatted output is
        "written" to an in-memory string rather than to a file.
        For example:
 
                data segment
                outstr db 256 dup (?)
                data ends
 
                code segment
                     .....
                     sprintf outstr,"Current flags are %08b\n",<flags>
 
        The string "Current flags are 00010010\n\0" will be placed in
        memory beginning at outstr.  This is helpful if you have further
        work to do with the string after formatting.
 
        The output string must be accessible via DS at runtime.  You're
        responsible for ensuring that there's adequate space for the
        output string.
 
        Returns no particular value in AX.
 
 
        Formatting examples
        -------------------
 
        Assuming the following:
 
        data segment
        num8            db 12H
        num16           dw 1234H
        num32           dd 12345678H
        minusone        dw -1
        oops            db -1
        name            db "Chris",0
        fmtstr1         db "Val of num16 is %x\n",0
        fmtstr2         db "Addr of num16 is %04xH\n",0
        fwidth          db 6
        data ends
 
        Also, DS=1111, DX=2222, and CX=3344.
 
        These macros will produce these results:
 
        printf "Hello dere\n"              Hello dere
        printf "Num8 is %b\n",<num8>       Num8 is 10010
        printf "Num8 is %o\n",<num8>       Num8 is 22
        printf "Num8 is %d\n",<num8>       Num8 is 18
        printf "Num8 is %h\n",<num8>       Num8 is 12
        printf "Num8 is %4h\n",<num8>      Num8 is   12
        printf "Num8 is %04h\n",<num8>     Num8 is 0012
 
        printf "[%s]\n",<@ name>           [Chris]
        printf "[%10s]\n",<@ name>         [     Chris]
        printf "[%-10s]\n",<@ name>        [Chris     ]
 
        printf "[%*x]\n,<fwidth,num16>     [  1234]
        printf "[%-*x]\n,<fwidth,num16>    [1234  ]
        printf "[%0*x]\n,<fwidth,num16>    [001234]
 
        printf "%u\n",<minusone>           65535
        printf "%d\n",<minusone>           -1
        printf "%d\n",<oops>               255
 
        printf fmstr1,<num16>              Val of num16 is 1234
        printf fmstr2,<@ num16>            Addr of num16 is xxxx
 
        printf "%X",<num32>                12345678
 
        printf "DX is x'%04x'",<dx>        DX is x'2222'
        printf "DS:DX = %04x:%04x",<ds,dx> DS:DX is 1111:2222
 
 
        Limitations
        -----------
        All formatting must result in total output length of 255
        characters or less.  The routines will NOT check this for you.
 
        The format strings must ditto be of length 255 or less.
 
        FAILURE TO HEED THESE TWO LENGTH WARNINGS MAY HAVE THE MOST DIRE
        CONSEQUENCES, AS CODE WILL BE OVERWRITTEN BY DATA!
 
        Everything must be defined by the time the assembler encounters
        one of these macros on the first pass, else phase errors will
        result.
 
 
        The Usual Suspects
        ------------------
 
        All of this stuff (macros, library modules, and documentation)
 
                                      is
 
                            Copyright (c) 1985  by
                            Christopher J. Dunford
                           10057-2 Windstream Drive
                           Columbia, Maryland 21044
                            CompuServe  76703,2002
 
        and all rights are reserved.  However, I am placing the work in
        the public domain, which means to me that you may: use the
        macros and library modules for you personal use; modify said
        macros or modules as you see fit; copy any of this for your
        friends' similar personal use.
 
        However, you may not: engage in any commercial use of this
        material; sell it or otherwise copy it for profit; charge for
        making the copies authorized above (except that recognized
        user's groups may charge a nominal postage/handling fee); or in
        any other way try to make a buck from my work, no matter how you
        modify the code or macros.
 
        Of course, I don't warrant that any of this code does anything
        at all, or behaves in any manner similar to what is described in
        the documentation.