Installable Device Drivers in C


     This document is intended to describe a method for using 
Lattice C (small model) to develop Installable Device Drivers for 
MS-DOS.  Additionally, a number of C functions (provided in 
library format) are defined.

     Installable Device Drivers are created by first writing the 
functions to be supported, then linking these functions with the 
Driver Header.  A prototype header file is provided in the file 
HDR.ASM.  Note that two data items (the Attribute and Name/unit 
fields) must be filled in with information specific to your 
driver before this file will assemble properly.

     The driver header file assumes the existence of the 
following functions (stubs are provided in the DRIVER.LIB library 
file), which perform the various operations described in the 
Installable Device Drivers chapter of the DOS Reference Manual:

          Init()
          MediaCheck()
          BuildBPB()
          IoCtlIn()
          Input()
          ndInput()
          InputStatus()
          InputFlush()
          Output()
          OutVerify()
          OutStatus()
          OutFlush()
          IoCtlOut()
          DevOpen()
          DevClose()
          RemMedia()

     A sample character device driver is included in this 
package, which allows for a device named "MON".  Outputting to 
this device will cause characters to appear on the IBMPC 
monochrome screen.  Study of the file MONO.C should reveal the 
details of this implementation.

     Questions or comments on this package may be directed to:

                          Frank Whaley
                       7211 Camino Colegio
                     Rohnert Park, CA  94928


     Through the balance of this document, the pseudo-type "Addr" 
is used to describe a long integer value (32-bits) which is used 
to contain a memory address.  Note that the Segment:Offset 
addressing method used in the 8086 family of processors causes 
this data type to be incompatible with true long integers.  The 
following definition is assumed:

                      typedef   long Addr;


Addr EndAddr();

     EndAddr() returns the driver's ending address, as required 
     by the Init function call.


Addr Dword(ptr)
     	char	*ptr;

     Dword() converts a 16-bit pointer (into the driver's data 
     segment) to a 32-bit pointer.


int CopyB(from, to, len)
	Addr	from,
		to;
	int	len;

     CopyB() copies a section of memory "len" bytes in length 
     from the area whose address is "from" to the area whose 
     address is "to".  Note that this code assumes that the 
     memory sections do not overlap and that a forward copy is 
     correct.  This function returns the number of bytes copied.


int CopyW(from, to, len)
	Addr	from,
		to;
	int	len;

     CopyW() copies a section of memory "len" words in length 
     from the area whose address is "from" to the area whose 
     address is "to".  Note that this code assumes that the 
     memory sections do not overlap and that a forward copy is 
     correct.  This function returns the number of words copied.


char InB(port)
	int	port;

     InB() inputs and returns a byte from the hardware port 
     described by "port".


int InW(port)
	int	port;

     InW() inputs and returns a word from the hardware port 
     described by "port".


char OutB(byte, port)
	char	byte;
	int	port;

     OutB() outputs the byte "byte" to the hardware port 
     described by "port".  This function returns the output byte.


char OutW(word, port)
	int	word,
		port;

     OutW() outputs the word "word" to the hardware port 
     described by "port".  This function returns the output word.


char PeekB(addr)
	Addr	addr;

     PeekB() returns the byte value found at the absolute address 
     given by "addr".


int PeekW(addr)
	Addr	addr;

     PeekW() returns the word value found at the absolute address 
     given by "addr".


char PokeB(val, addr)
	char	val;
	Addr	addr;

     PokeB() stores the value "val" into the absolute byte 
     address given by "addr".  This function returns "val".


int PokeB(val, addr)
	int	val;
	Addr	addr;

     PokeB() stores the value "val" into the absolute word 
     address given by "addr".  This function returns "val".


int SetB(start, len, byte)
	Addr	start;
	int	len;
	char	byte;

     SetB() initializes a section of memory "len" bytes in 
     length, beginning with the address given by "start", to the 
     value "byte".  This function returns the number of bytes 
     set.


int SetW(start, len, word)
	Addr	start;
	int	len,
     		word;

     SetW() initializes a section of memory "len" words in 
     length, beginning with the address given by "start", to the 
     value "word".  This function returns the number of words 
     set.