HISTORY.DOC      Version 1.3  30 April 87           Page 1


        Copyright 1985-7  Michael M Rubenstein
        Portions Copyright 1988, Russell Nelson

        This software and the accompanying documentation may be
        distributed freely for noncommercial use.


        Changes by David Polansky 4-7-88

                 -     Because of the enhanced console IO added in
                       version 1.5 use of putch increased the executable
                       size to over 9K and memory usage to over 11K.  By
                       using the OLD putch (rather the current library
                       version) you get the small executable (see edit.c).

                 -     I made the history buffers circular (my preference).
                       If you do not like this uncomment the code in
                       history.c and recompile.

                 -     Added setup.obj for those who don't have MASM.

        Changes in Version 1.4R

                  -    Cleaned up memory usage.  Went from 27K to 7.7K.

        Changes in Version 1.3R

                  -    Ported to Turbo C.
                  -    Added filename completion.  See the LF command below.
                  -    Split into two files, one for editing and one for
                       history, to hide the history data structure.
                  -    Fixed some hokiness regarding the second history buffer.


        Changes in Version 1.3

                  -    Added second history buffer for use of programs
                       other than COMMAND.COM.

        Changes in Version 1.2

                  -    Corrected handling of long lines when screen
                       scrolls.

        Changes in Version 1.1.

                  -    Function keys 1-5 have been implemented in a
                       manner much more consistent with the standard
                       MSDOS function keys.

                  -    If supplied by the calling program, the buffer
                       line may be used.  This allows use of the function
                       keys in the few programs (such as EDLIN) which are
                       designed for use of the keys.



        Description.

        HISTORY is a history processing terminate and stay resident
        program.  It provides the ability to recall and edit previous
        commands and allows much more sophisticated editing than is found
        in the normal MSDOS system.

        HISTORY includes a search mechanism to handle relatively large
        histories.



        Requirements.

        HISTORY requires about 5500 bytes of memory plus whatever is
        required for the history storage.



        Running HISTORY.

        HISTORY takes two optional argument son the command line -- the
        number of bytes (256 - 32767) to use for history storage for
        COMMAND.COM and the number of bytes (256 - 32767) to use for
        other programs.  If only one argument is given, it is taken as

        HISTORY.DOC      Version 1.3  30 April 87           Page 2


        the number of bytes for COMMAND.COM.  If an argument is missing,
        the minimum, 256, is used.  If a number less than 256 is given,
        it is silently treated as 256.  If a number larger than 32767 is
        given, it is silently treated as 32767.  The history buffer is
        circular; i.e, when space is exhausted the oldest commands are
        deleted.  The sum of the two arguments should not be greater than
        about 55,000 (usually a much smaller sum is appropriate).

        A value of 1000-2000 is generally appropriate for the first
        argument.  A much smaller value is usually adequate for the
        second argument;  the default of 256 bytes is generally adequate.

        Entering commands with HISTORY is similar to doing so in the standard
        command processor, but there are numerous additional editing
        options.

             Left arrow        -  Back one character.

             Right arrow       -  Forward one character.

             Ctrl left arrow   -  Back one word.

             Ctrl right arrow  -  Forward one word.

             Home              -  Go to start of line.

             End               -  Go to end of line.

             Del               -  Delete current character.

             Backspace         -  Delete previous character.

             Line Feed         -  Complete the filename to the left of the
                                  cursor.  If the filename contains wildcards,
                                  copy all the matching filenames in.

             Ctrl Q            -  Remove any special meaning from the
                                  next character.  For example, Ctrl Q
                                  Ctrl H inserts a Ctrl H (backspace)
                                  into the line.

             Ctrl T            -  Delete to beginning of next word.
             F10

             Ctrl W
             F9                -  Delete back to beginning of word.

             Ctrl U            -  Delete entire line.
             Ctrl X
             Esc

             Ctrl Y            -  Delete to end of line
             F8

             Ins               -  Toggle insert mode.

             F1                -  If the current line is empty, copy the
                                  template from the buffer. Otherwise
                                  advance one character.

        HISTORY.DOC      Version 1.3  30 April 87           Page 3



             F2                -  If the current line is empty, copy the
                                  template from the buffer.  In any case,
                                  waits for another character and
                                  advances to the next occurrence of that
                                  character.

             F3                -  If the current line is empty, copy the
                                  template from the buffer.  In any case,
                                  advance to the end of the line.

             F4                -  If the current line is empty, copy the
                                  template from the buffer.  In any case,
                                  waits for another character and deletes
                                  to the next occurrence of that
                                  character.

             F5                -  Make the current line the template.
        The command will be processed when RETURN or ENTER is pressed.
        The cursor need not be at the end of the line.

        The real power of HISTORY, however, is in the ability to recall
        and edit previous command lines.  This is controlled by several
        additional command keys:

             Up arrow          -  Recall previous command line.  Repeated
                                  application gets successively earlier
                                  command lines.  If there is no previous
                                  command line (or it has not been kept
                                  in the history), the bell will sound.
                                  The Ctrl U, Ctrl X, and ESC editing
                                  commands reset the internal pointer to
                                  the end so the next up arrow gets the last
                                  command line executed again.

             Ctrl L            -  Searches for a previous command line
             F7                   which matches the current line to the
                                  left of the cursor.  Case is
                                  immaterial.  If none is found, the bell
                                  will sound.  For example, if the
                                  previous command lines were

                                  dir
                                  ws test.doc
                                  type whatever.c
                                  whatever
                                  ws what.out
                                  dir

                                  then typing

                                      w Ctrl L

                                  would recall the command "ws what.out".
                                  The cursor is left after the "w", so

        HISTORY.DOC      Version 1.3  30 April 87           Page 4


                                  typing Ctrl L again would recall
                                  "whatever".  If ws Ctrl L were typed
                                  initially, the "whatever" command would
                                  be skipped and the two "ws" commands
                                  would be recalled.

             Down arrow        -  Recalls the next command (assuming a
                                  previous command has been recalled with
                                  up arrow and is being edited).  If
                                  there is no next command, the bell
                                  sounds.

        While the editing commands may seem a bit complex at first, a
        little playing at the terminal will make them very natural and
        easy to use.  The Ctrl L command, in particular, is quite
        different from the commands found in most editors.  With a very
        little practice, command line editing with HISTORY becomes almost
        automatic and one soon wonders how one lived without it.

        The history commands are available in any program (e.g., DEBUG)
        which uses BDOS function 10 for input.  Two history buffers are
        used -- one for COMMAND.COM and one for all other programs.


        For the Hacker.

        HISTORY was written in C and compiled with the Aztec C.  Source
        code is included.  A small assembly language interface is used to
        make the program memory resident and communicate with the get
        console buffer interrupt.

        The C code is fairly standard and should be reasonably easy to
        convert to other versions.  The assembly language interface will
        require more work if another C compiler is used.

        <End of Document>