October 3, 1987

                             TCdebug Version 0.04

                    (C) Copyright 1987 by L. David Baldwin.  
                             All Rights Reserved.

  Further copyright information given below


  OVERVIEW

  TCdebug is an experimental source code debugger for use in debugging Turbo 
  C (tm) Programs on the IBM-PC (tm).  Its goal is to allow source code 
  debugging in all of Turbo C's memory models and with most of the possible 
  compile and link options.  TCdebug allows you to:

       1.  View your source code (and, optionally, the assembly language 
           code) while debugging.
       2.  Trace the operation of your program by source code lines or by 
           assembly language instructions.
       3.  Insert breakpoints in your program by function name, by line 
           number, or hexadecimal address.
       4.  Examine (and change) simple global variables by symbolic name.  
           Local variables may also be examined and changed, but require that 
           the proper displacement on the stack be known. 
       5.  Set up a Watch window to keep continuous tabs on a variable.

  TCdebug is not a finished program.  It is being released at this time to 
  get an indication of interest and to obtain assistance in finding bugs and 
  other problems.

  TCdebug is designed exclusively for debugging Turbo C programs.  It should 
  not be used on programs generated by other compilers.


  SYSTEM REQUIREMENTS

       1.  An IBM-PC, AT, or compatible.  Screen compatibility is a must.
       2.  PC-DOS 2.0 or above.
       3.  Approximately 135k more memory than would normally be required to 
           run the program to be tested.


  PREPARATION

  TCdebug requires that a Map file for your program be present to supply 
  information on the program symbols and line number locations.  When 
  compiling and linking with TC, the options can be set with O/C/C/L and 
  O/L/M/P.  With TCC use -M and -y.




                                      1











  It is also highly desirable that the program to be tested be compiled with 
  the 'standard stack frame' option on.  Using TC, set this option with 
  O/C/C/S.  With TCC, use -k (The manual says -Y but that's apparently a 
  typo).

  When starting a debugging session, the following files should be on the 
  default drive:

    PROG.EXE    (or, optionally, .COM for the Tiny Model)
    PROG.MAP    the map file
    various.C   all the source files for the program (or at least all that 
                will be accessed.)



  OPERATION

  TCdebug may be started by entering the filename of the program to be 
  debugged and any parameters which it requires on the command line, as:

    TCdebug PROG <other stuff>

  Here, PROG is the name of the program to be tested with EXE being the 
  default extension.  <other stuff> will be passed on to PROG as its command 
  line when execution begins.  If TCdebug is called without parameters, a 
  request will be made for them.

  When execution begins, TCdebug loads the Map file, the EXE file and reports 
  some facts about the program.  Note should be made of whether pointers are 
  regarded as Near or Far by default as this will be important when 
  displaying pointers later.

  After "hitting any key", the program is executed to "main()" and the 
  debugging screen appears.  The debugging screen is divided into two parts.  
  The lower section is the command and data section.  The '*' is a prompt for 
  one of the commands described later.  The top part of the screen displays 
  the program source code text which at this point will be centered at the 
  first statement in main().  Source code line numbers appear at the left 
  with the current line (the one to be executed next) being highlighted.

  Dividing the two portions of the debugging screen is a line which shows the 
  name of the source file presently displayed.

  Two keys which can be tried at this point are the F9 and F10 keys.  The 
  F9 key toggles into and out of the assembly mode.  When in assembly mode, 
  the assembly language instructions of the program are displayed with the 
  source code lines interspersed.  The F10 key toggles between the debugger 
  screen and the screen which receives program output.






                                      2











  SPECIAL KEYS FOR VIEWING TEXT

  The following keys may be used to change the text being displayed:

       Pg Up
       Pg Dn       Move the display up or down one page.

       ^Pg Up
       ^Pg Dn      Move to the start or end of the current file.

       Up arrow
       Down arrow  Scroll up or down one line.

       ^Left Arrow  (with Scroll Lock on)
       ^Right Arrow (with Scroll Lock on)
                   Scroll horizontally left and right.

       F9 key      Toggle in and out of assembly mode.

       F10 key     Toggle between the debug screen and the screen
                   of the program under test.

       Alt-U       Move dividing line up one line.
       Alt-D       Move dividing line down one line.

  Note that the toggling of the Scroll Lock key effects the action of some of 
  the special keys.  The text display may also be changed using the View 
  command described later.


  COMMAND EDITOR

  Commands are entered at the '*' prompt.  When entering commands, the 
  following keys may used to edit the command:  (They perform the same 
  functions as they do in the Turbo C editor.)

       ^A,^S,^D,^F,^G,^T,^H,^V,^Y,LFARW,RTARW,^LFARW,^RTARW,
       Ins, Del, Backspace

  The Insert mode (default) is indicated by a slightly fatter cursor.  The 
  cursor is normal in the Overwrite mode.

  In addition, a stack of the last 6 commands (those having more than 3 
  characters) is maintained.  The F3 key accesses the stored commands from 
  the most recent to the oldest and the F5 key accesses them in the reverse 
  order.  These old commands may be used as is or may be modified by editing 
  them.

  Note that commands are not acted upon until the Enter key is hit.  (The 
  cursor does not have to be at the line end to enter the command.)




                                      3











  COMMAND PARAMETERS

  TCdebug uses one or two letter commands.  The command is often followed by 
  one or more parameters.  Parameters are delimited from the command and each 
  other using spaces.  The one exception to this is the format parameter 
  which is preceded by a comma.  The parameters which may be used are:

    <Symbol>
       A C source code symbol representing a function name or variable as 
       appropriate.  The leading underbar added by the compiler has been 
       stripped off, so symbols are entered exactly as used in the source 
       program.  Case is significant (unless the non case sensitive link 
       option was selected).

       The special symbols, _AX, _AL, _BX, etc. may be used to refer to the 
       hardware registers.

       A special symbol, rtn (or RTN), refers to the return address of the 
       current function.  For this symbol to function reliably, the program 
       should be compiled with the 'standard stack frame' option on.  
       Currently, this symbol can only be accessed if the current CS:IP is on 
       an exact source line number.

         Examples:
           V rtn    Find out who called this function.
           G RTN    Execute the remainder of this function, return to caller.


    <Line Number>
       Line numbers are entered as <filename>\<number> as:
           myprog.c\345

       In most cases, the <filename> part can be dropped.  An entry of the 
       form

           \345

       implies line number 345 in the currently displayed source file.  
       (Currently, the '\' also may be dropped and a simple decimal entry will 
       do.  However, the '\' may be required in future versions.)

    <Hexaddress>
       Normal numerical entry in TCdebug is decimal with hex entries allowed 
       by preceding them with '0x'.  However, numerical address entries must 
       be entered in hex to distinguish them from line numbers.  A 
       <hexaddress> takes the following form:

           0x1234:0x1ABC
           es:bx+2
           SS:BP-0X5a




                                      4











       As indicated above, register names are allowed in address 
       specifications.  The _current_ value in the register is used--the 
       address does not change if the register value later changes.  The 
       segment part of the <hexaddress> may be dropped as in:

           bp-0xA
           0x123
           bx

       If no segment is present in the entry, there is an implied segment.  
       The rules for determining the implied segment are:

       1.  If the BP register is used, SS is implied.
       2.  If BX,SI,DI are used (but not BP), DS is implied.
       3.  If none of the above and a data entry is expected, DS is implied.
       4.  If a code address is expected, the current CS is implied.

    <Format>
       Format parameters are entered as one or two letters preceded by a 
       comma.  Case is significant.  The purpose of the <format> parameter is 
       to inform TCdebug of the size and type of a variable as this 
       information is not available in the Map file.  <format> parameters 
       correspond to those used in the C 'printf' function.  Currently 
       supported are:

           c,s,i,d,u,x,X,o,p,g,G,li,ld,lx,lX,lo,Np,Fp,lg,lG

       For the p (pointer) format, the default pointer size for the selected 
       memory model is used.  This size is indicated in the information 
       presented at startup.  To override the default, use either N or F as 
       appropriate.

       The c (character) format has been used as a catchall for byte size 
       items.  Display is in quoted character form, decimal, and hex.  Change 
       entries may be made using any of those forms.


  COMMANDS

  G    (Go)

    Format:
       G [<parameter> [<parameter..]]

    The Go command starts execution of the program under test.  Execution 
    will continue until a breakpoint is reached or the program terminates.

    One or more breakpoints may be entered with the Go command.  These 
    breakpoints are called temporary breakpoints as they are in effect only 
    until the first stopping point is reached.  Any temporary breakpoint 
    would then have to reentered with the next Go command if desired.



                                      5











    Examples:

       G   Start execution with no temporary breakpoints. (There might be 
           some permanent breakpoints, however.)

       G \345 funct1 0x113
           Start execution with temporary breakpoints at line number 345, at 
           the start of function, funct1, and at address CS:0x113. In 
           addition, there might be other permanent breakpoints in effect.

  T    (Trace)

    Format:
       T   (or F7 key)

    In source code mode, execute the code on the current line.  Execution 
    will stop at the next encountered line number.  If the current line 
    contains a function call, the break will be at the start of the 
    function.

    In assembly mode (assembly code is displayed), execute the next assembly 
    language instruction.


  N    (Next)

    Format:
       N    (or F8 key)

    In either the source code or assembly mode, Next will execute the 
    program, stopping at the next line number.

    The difference between the Trace and the Next command is that, if the 
    current line contains a function call, Next will completely execute the 
    function whereas Trace will Trace through the function.


  P    (Permanent breakpoint)

    Format:
       [-]P [<parameter>]  [<pass count>]

    The P command is used to specify permanent breakpoints.  Unlike temporary 
    breakpoints, permanent breakpoints remain in effect until removed (using 
    a '-' preceding the P command).  

    If no parameter is entered, the breakpoints in effect are listed.

    An optional pass count may be included when adding a breakpoint.  The 
    pass count indicates how many times the breakpoint will be passed 
    before the program is actually interrupted.



                                      6











    Examples:

       P              List all permanent breakpoints.
      -P              Delete all permanent breakpoints.
       P moda.c\345   Install a breakpoint at line 345 in file moda.c.
      -P funct1       Remove a breakpoint at function funct1.
       P 0x34b 10     Install a breakpoint at CS:034B.  The break will
                      occur at the 11th execution of the instruction.


  BE, BC      (Conditional Breakpoints)

    Formats:
       BE <parameter>, <format> <value>   (Break when Equal to value)
       BC <parameter>, <format>           (Break when there is a Change)
       B                                  (List conditional breakpoints)
      -B  [<number>]                      (delete one or more conditionals)

    Conditional breakpoints allow TCdebug to interrupt program execution 
    whenever it finds that a variable has changed or becomes equal to a 
    specified value.  TCdebug checks each one of the conditional breakpoints 
    whenever it regains control of the program.  Normally, when using 
    conditional breakpoints, the GT (Go in Trace mode) command should be used 
    to allow the variable checks to be made at each source line.

    String variables are compared over the first 10 characters.

    Examples:

       BC str,s        Break when the string variable, str, changes.
       BE *np,i  39    Break when the integer pointed to by np equals 39.
       -B2             Delete conditional breakpoint #2.       
      

  GT   (Go in Trace mode)

    Format:
       GT [<parameter> [<parameter..]]

    The GT command is a special version of the G (Go) command for use with 
    conditional breakpoints.  Both commands have the same syntax.  When the 
    GT command is used, the execution of the program is interrupted briefly 
    at each source line so that the specified conditions can be checked.  

    Because of the extra overhead involved with the GT command, program 
    execution is very much slower than with the G command.

    Example:
       GT \334   
           Start execution of the program stopping at the first occurrence of: 
           line 334, reaching a permanent breakpoint, or one of the 
           conditions specified by a conditional breakpoint.       


                                      7













  V    (View text)

    Format:
       V [<parameter>]

    The View command may be used to change the text being observed in the 
    text window.  If no parameter is entered, the text will be centered 
    around the current line.

    Examples:

       V initscreens   View text at function initscreens.
       V \545          View text around line 545.


  VF   (View File)

    Format:
       VF <filename>

    The View command is for viewing the program source files.  The VF 
    command allows any ASCII file to be displayed.


  E    (Examine/change variable) 

    Format:
       E <symbol>|<hexaddress> , <format>

    The Examine/change command allows the the value of a simple variable to 
    be displayed and optionally changed.  Global variables may be referred to 
    symbolically.  Auto and static variables must be referred to by a 
    <hexaddress>.  Pointers may be resolved using one or more '*'s preceding 
    the symbol or address.  <format> indicates the type of display wanted.

    After a variable value is displayed in response to the Examine/change 
    command, a new value may be optionally entered followed by the Enter key.  
    The Enter key by itself is used if no new value is desired.

    String variables are displayed as a string within quotes.  When 
    specifying a change to a string variable, the new string should be 
    enclosed in double quotes.  A null string is specified by two quotes 
    enclosing nothing.









                                      8











    Examples:

       E flt,g
       E dble,lg
       E *st,c
       E es:bx,u
       E bp-0x52, s

    When referring to registers, note that there is a difference between the 
    register symbols with underbars and those without the underbars, so that:

       E ds:bx,x  Examine/change the hex integer at the address ds:bx.
       E bx,x     The same thing (DS is implied).
       E _BX,x    Examine/change the BX register.


  W    Watch variable

    Format:
       W <symbol>|<hexaddress> , <format>
    [-]W [<number>]

    The Watch command opens up a watch window so that the specified variable 
    is displayed continuously.  The value displayed is updated whenever 
    TCdebug regains control.  The syntax for watch variable entry is 
    identical to that used with the Examine command.  

    When watch variables are displayed, they are given a number.  The number 
    is useful for selectively deleting them using the -W command.

    Examples:
       W var1, u    Watch the unsigned variable, var1
       W *bp-4,c    Watch the char variable pointed to by SS:BP-4
       W _AL,c      Watch the AL register
      -W 1          Delete watch variable #1
      -W            Delete all watch variables  


  D    (Display Memory)

    Format:
       D <symbol>|<hexaddress> , <format>
      -D

    The Display command opens up a three line display window displaying 
    memory contents at the address given by <parameter> in the format given 
    by <format>.  This display window may be scrolled using the following 
    keys when Scroll Lock is toggled on:

       Up Arrow
       Down Arrow    Move up or down one line (Scroll Lock on)



                                      9











       Pg Up
       Pg Dn         Move up or down two lines (Scroll Lock on)

    Examples:

       D ptrs,Fp   Display memory at ptrs in far pointer format.
       D dbles,lG  Display memory at dbles in double format.
       D *es:bx,s  Display memory as pointed to by es:bx in string or 
                   character format.
      -D           Close the display window.


  X    (Translate symbols to addresses or addresses to symbols)

    Format:
       X <symbol>
       X <address>

    The X command allows the address associated with a symbol to be 
    determined or vice versa.


  R    (Register Display)

    Format:
       R

    The Register display command displays the current machine register 
    contents.  


  RE   (Restart program under test)

    Format:
       RE

    Reloads a fresh version of the test program and restarts it from the 
    beginning.  Breakpoints and watch variables remain in effect.


  WD   (Window Divide)

    Format:
       WD [n]

    The Window Divide command allows the line dividing the screen to be moved 
    up or down.  n is the desired line position.  If n is not entered, the 
    line position is not changed but the screen is refreshed.

    The line dividing the screen may also be moved one line at a time using 
    Alt-U (Up) or Alt-D (Down).



                                     10











  Q    (Quit)

    Format:
       Q

    The Quit command ends debugging without running the program under test to 
    completion.  However, the program's exit() routine is executed, so that 
    files are closed, etc.  You will be asked if you wish to restart the 
    program.  


  DG   (DebuG)

    Format:
       DG

    This command is used to enter an optional external assembly language 
    debugger.  It is used mainly for debugging TCdebug.


  HINTS

  It is possible to insert breakpoints in the source code using 
  geninterrupt(3).  These breakpoints cannot be removed by TCdebug but may be 
  useful for conditional breaks.  For instance:

    if (i==49) geninterrupt(3);

  If you mistakenly Trace into a function you wanted to skip using Next, use 
  G rtn.  Actually, it's best to do a V rtn first to make sure that the 'rtn' 
  symbol is working correctly.

  If, in the assembly mode, you trace into a library routine and can't find 
  your way out, toggle out of assembly mode (F9).  Even if the source code 
  screen is blank at this time, a single Trace will get you to the next line 
  number.

  Avoid assembly tracing of the 8087 emulation code.

  Auto (stack) variables can be Examined or Watched by using the disassembly 
  listing to determine their position on the stack relative to the BP 
  register.  When doing this, be sure that the BP register is valid.  In 
  particular, the BP register is not valid immediately on entry to the 
  function.  One source line trace must be made (or several assembly 
  instructions passed) before the BP register is correct.

  The Huge memory model has the same sort of problem with the DS register 
  which changes between modules.  In this case, it only effects the 
  disassembly listing.  The data symbols will not be correctly listed until 
  the DS register has been setup.




                                     11











  RESTRICTIONS, PROBLEMS, BUGS

  The following are current limits (somewhat arbitrarily set).  

    Permanent and temporary breakpoints are limited to 5 each.
    Maximum file size for displayed files = 40k.
    Maximum number of line numbers (only those with code count) = 3000.
    Maximum number of program modules accommodated = 20.
    Maximum number of symbols = 700.
    Maximum number of watch variables = 4
    Maximum number of conditional breakpoints = 3

  A simple screen swap is currently used.  This limits debugging to text only 
  programs.  Snow may be horrendous at this time.

  The map file for the Tiny memory model has some peculiarities in data 
  addresses which I haven't got figured out yet.  This affects a number of 
  library data symbols but only seems to affect one or two source symbols.  
  The problem shows up in the assembly listing where the affected symbols are 
  not correctly displayed.

  The 8087 emulation code turns into a mess when disassembly is attempted.

  Currently, non default pointers cannot be resolved by the 'E' or 'W' 
  commands.  That is:

    E *st,c

  will always resolve st as a far pointer if the default is far.  Probably 
  some sort of cast will have to allowed, as:

    E *(near*)st,c


  COPYRIGHT

  Documentation and Program (C) Copyright 1987 by L. David Baldwin.  
  All Rights Reserved.

  TCdebug may be copied and distributed freely by individuals to friends and 
  acquaintances providing that no fee is charged and it is not part of a 
  package for which a charge is made.

  The uploading of TCdebug to any bulletin board except that of the Borland 
  Sig (CompuServe) is expressly forbidden.









                                     12











  TRADEMARKS

       IBM-PC is a trademark of International Business Machines 
       Corporation.
       Turbo C is a trademark of Borland International Inc.



  Please report all bugs, suggestions, and problems to Dave 
  Baldwin, CompuServe ID #76327,53.












































                                     13











  APPENDIX A -- COMPILER OPTIONS

  As mentioned earlier, it is mandatory that the map file generation and line 
  number options be turned on.  The effect of some of the other compiler 
  options on debugging are discussed below.  Some of this is just guess work 
  at this stage as not all have actually been tested.

  Standard Stack Frame
    This option is highly desirable as the BP register must be set up in 
    order for the 'rtn' symbol to work.  If this option is not used, any 
    function which has many auto variables will still have a standard stack 
    frame, so it is still possible to use 'rtn' in some cases.  The safest 
    method is to do a V rtn or X rtn first to see if the return address makes 
    sense before committing yourself to a G rtn.

  Register Optimization
    Borland suggests off.  I haven't tried this one but I suspect that it 
    confuses things somewhat.  Those adept at assembly language may not have 
    too much trouble.

  Jump Optimization
    Same as register optimization.

  80186/80286 Code Generation
    Off is best here.  The disassembler in TCdebug currently does not 
    understand the new instructions.

  Use Register Variables
    When this option is on, you may have to figure out which variables the 
    compiler decided to store in registers.  

  8087 vs Emulation
    If you have a choice, by all means select straight 8087.  The emulated 
    code does not disassemble in any meaningful way.

  Non Case Sensitive Link
    If this option is selected, symbols will appear in uppercase.  Symbol 
    entries may be made in either case.
















                                     14











  APPENDIX B -- SOURCE CODE FORMATTING

  With modern compilers, line numbers often do not correspond to the code 
  generated in the manner that you might expect.  Layout of the source code 
  can help in this respect.  While you probably don't want to reformat all 
  your present code, you may want to change your formatting for code yet to 
  be written.

  The most obvious format change is to only have one source statement per 
  line.  With more than one statement on a line, line numbers can't be used 
  to set a breakpoint on the second statement and the Trace command will 
  trace multiple statements.

  Statements split between two lines do not cause much trouble.

  The 'else' in an 'if' statement causes a difficulty.  Consider the 
  following code:

  100  if (...)
  101     {..do something..}
  102  else {..do something else..}
  103

  To put a breakpoint on the ..do something else.. one might try a break on 
  line 102.  But the else here actually generates a jump instruction (to line 
  103) so ..do something else.. is inaccessible except by using a code 
  hexaddress.  A better format is:

  100  if (...)
  101     {..do something..}
  102  else 
  103     {..do something else..}
  104

  The 'for' statement also causes problems.  The decision code for the 'for' 
  statement is actually done at the bottom of the loop and often is included 
  as part of the next line where you would normally think the statement was 
  completed.  The best solution here is to add a blank line after the 'for' 
  statement loop.

  In short, it's best to use plenty of vertical spacing and blank lines.  
  Also take a peek at the assembly code to see what's going on.












                                     15