TERMINATE AND STAY RESIDENT
		       --------- --- ---- --------
			      Brian Irvine


   STAYRES.C was written for the Cware C Development System ( DeSmet C ).
It uses library functions and other features ( such as in-line assembly
language ) which might not be available with other C compilers.  However, the
basic stuff is there and it should be a trivial task to convert it to be
compilable under other C compilers.

   When a resident program takes over from DOS, if the program uses DOS I/O, it
will most likely leave the local DOS stack and register values changed from
what they were when the program gained control.  When control is returned to
DOS, then it gets very confused and usually ends up doing something completely
unpredictable, or just going off into j-space.	As a result, most programs
which terminate and stay resident take care of their own disk and screen I/O,
and are written in assembly language.  This does not have to be the case,
however.  Programs can be written in high-level languages as long as a little
stack management is performed before and after program use.

   The programming in STAYRES.C proposes one solution to the problem.  It saves
the top of the DOS stack and all of the processor registers on the local
program stack before the program is entered.  The program can then perform
normal operations like disk access and formatted screen output.  On exit, all
of the information saved on the local stack is transferred back to the DOS
stack and to the processor registers, creating virtually the same machine state
as was present before the program took control.

STAYRES works by intercepting the software interrupt 16H, which is called by
DOS to get a character from the keyboard.  Now when DOS issues a request for
the next character from the queue, we can examine the character before passing
it on to DOS.  If it is the character or keypress combination which we have
designated as that required to activate the TSR program, then we make a further
check to see if the program is already active.	If not, then we go through the
process of saving the machine state, then call the entry point of the TSR
program.

   The TSR code is contained in a module which requires the modification of
only one line of code to suit the name of the function which will be designated
as the main entry point to your program.  The module can then be compiled and
linked in with any other object modules to produce a complete program.

   The code contained in STAYRES.C is inspired by a set of Turbo Pascal
routines written by Lane H. Ferris.  I have taken the central idea of Lane's
code and used it in this program.  The Turbo routines are available on the
Borland SIG on Compuserve.

   I realize that I don't know all there is about this process, so if you have
any further information you would like to impart, or if you have any comments
or suggestions for modifications or improvements, please leave a message for me
on Compuserve.	Use Easyplex or leave a message addressed to me on one of the
IBM PC Sig's.

   I am releasing this code to the Public Domain so that others can use the
information for non-profit purposes.  If you do use the code in any of your
applications, I ask only that you give credit for the source.  Feel free to
copy and distribute these files as you wish, but please ensure that the credits
are included.

					Brian Irvine
					3379 St Marys Place
					Santa Clara, CA 95051
					Compuserve User ID [71016,544]