IMCAP 3.1

            IBM-PC Screen Capture Utilities

                 Version 3.1, May 1986

                          by

                    ImageSet Corp.







                    ImageSet Corp.
                    555 19th Street
                San Francisco, CA 94107

          Copyright (C) 1985, ImageSet Corp.



             * PLEASE COPY THIS SOFTWARE *

     Permission to make and distribute unlimited
     copies of this document and computer software
     FOR NONCOMMERCIAL PURPOSES ONLY is granted
     provided that the above information remains
     intact.








                        Summary

     ImageSet Corp. provides IBM-PC screen-dump
     utilities to assist in preparing orders for
     ImageSet processing.  The utilities are used
     to capture screen information, to review cap-
     tured images and to specify the desired
     options for each repro galley or film being
     ordered.  There are three utilities on a 5
     1/4" single-sided double-density diskette.
     The diskette is labelled "IMCAP 3.1 Image
     Capture Utility for the IBM-PC".

     The first utility, "Image Capture" (IMCAP),
     is a special driver program which loads along
     with an application program to "capture"
     screen images on disk (via the SHIFT-PRTSC
     key).

     The second utility, "Image Manager" (IMMGR)
     is a menu-driven application program which
     allows review of the captured screens,
     selection of colors, selection of repro
     galley options, and preview of the repro
     galley with the sections applied.

     The third utility, "Image Show" (IMSHOW) is a
     batch orientated application program which
     allows rapid review of captured screens.






















     What is Supported

     The following hardware and modes are
     supported:

          [1]  IBM-PC Color/Graphics Adapter (all
               modes).

          [2]  IBM-PC Enhanced Graphics Adapter
               (all modes).

          [3]  IBM-PC Monochrome Adapter.

          [4]  Hercules Graphics Card for the IBM-
               PC (character and graphics modes).

          [5]  AT&T 6300 (all IBM compatible modes
               plus super-high resolution black &
               white graphics mode).

          [6]  Most other compatible machines
               which provide emulation of any of
               the above hardware and/or modes.



























     What ImageSet Does

     From screen images captured on the IBM-PC
     with these utilities ImageSet digitally
     reproduces the images for prepress production
     in one of the following forms:

          [1]  Black and white on repro paper, no
               half-tone areas (gray tints).

          [2]  Process color separation on film.

          [3]  Gray-tone conversion on film.

     Not all supported video modes can be produced
     in all forms.  TABLE 1 outlines the output
     forms available each supported screen mode.









                                       TABLE 1

                           Screen Modes Supported by IMCAP

     Mode           Description                    B & W     Color Sep.
     Number         of Mode                        Repro     & Gray Tone

       00    40 x 25 Black & White Character        Yes         No
       01    40 x 25 16-Color Character             Yes         Yes
       02    80 x 25 Black & White Character        Yes         No
       03    80 x 25 16-Color Character             Yes         Yes
       04    320 x 200 4-Color Graphics             Yes         Yes
       05    320 x 200 Black & White Graphics       Yes         No
       06    640 x 200 Black & White Graphics       Yes         No
       07    80 x 25 Monochrome Character           Yes         No
       08*   720 x 348 Monochrome Graphics (Hercules)           Yes   No
       09*   640 x 400 Black & White Graphics (AT&T)            Yes   No
       13    320 x 200 16-Color Graphics            No          Yes
       14    640 x 200 16-Color Graphics            No          Yes
       15+   640 x 350 Monochrome Graphics          No          No
       16    640 x 350 16-Color Graphics            No          Yes


            *does not correspond with any IBM ROM BIOS video mode number.
            +images may be captured and reviewed but no production facility is
     currently available.






     How to Capture Screen Images

          [1]  Boot your IBM-PC with PC-DOS
               (release 2.0 or greater is
               required).

          [2]  Insert the ImageSet Utility
               Diskette in any drive.

          [3]  To capture screen images on all
               supported hardware except the
               Hercules Graphics Card in graphics
               mode enter the command:

                           imcap

               To capture images on the Hercules
               Graphics Card in graphics mode
               enter the command:

                          imcap /h

               You will see a copyright message
               and the message "LOADED" displayed
               on your screen.

          [4]  Remove the ImageSet Utility
               Diskette.

          [5]  Start your application program.

          [6]  Use the application in the normal
               way to display the exact screen
               that you wish to capture.  Press
               SHIFT-PRTSC to capture it.  IMCAP
               will write a file with a unique
               name on the current drive.  Repeat
               this step for each screen that you
               wish ImageSet to process.

        NOTE:  If your application implements its
               own print-screen function via the
               SHIFT-PRTSC key combination it will
               be disabled when the IMCAP driver






               has been loaded.  You will still be
               able to capture your screens by the
               above procedure.

               If you do not want to override your
               application's print-screen function
               in this way you may alternatively
               use the ALT-PRTSC combination for
               IMCAP.  See the section entitled
               "What is Really Going On" for
               details about how to do this.










     What You Hear

     While each screen is being captured (in step
     6 above) you will hear a low-pitched buzz
     from the speaker.  This indicates that IMCAP
     is in control and doing its job.  When you
     hear this sound PLEASE DO NOT TOUCH THE PC.
     The sound will stop when the screen has been
     successfully captured.  At that point you may
     continue using your application program to
     set up the next screen.

     If you hear a rising series of high pitched
     tones it means that a DOS error has occurred.
     This is usually due to a "disk full"
     condition.  To determine the cause of the
     error do the following:

          [1]  Exit from your application program
               without re-booting PC-DOS.

          [2]  Insert the ImageSet Utility
               Diskette.

          [3]  Enter the command "imcap".

     IMCAP will say "Already Resident" and report
     the cause of the last error.

     If you hear a pulsating tone (like a busy
     signal) you have interrupted DOS while it was
     processing a request from your application.
     As soon as the application's request is com-
     pleted the capture will commence at which
     time you will hear the familiar buzzing
     sound.















     What You Get

     For each SHIFT-PRTSC that you do, IMCAP
     creates a file with a unique file name in the
     form "SCREENxx.CAP" where xx is replaced by a
     number from 00 to 99.  IMCAP will never
     overwrite an existing file.  Actually, you
     can have complete control over the names and
     location of the files created (see the
     section entitled "What is Really Going On
     below").

     For output on film (process color separation
     or gray tone conversion) these ".CAP" files
     are sent to ImageSet along with a completed
     "transmittal form" provided by ImageSet for
     this production service.  Be sure to use the
     Image Manager or Image Show utilities to
     review the images that you have captured in
     the files before sending them for production.

     For black and white output on repro paper,
     these ".CAP" files may not be sent to
     ImageSet to be processed "as is".  You must
     use the Image Manager utility program to
     review the captured images, make selections
     of various production parameters and create
     ".SET" files which can then be sent to
     ImageSet for processing.  The Image Manager
     utility is described in a later section.





















     What is Really Going On

     The first time you run IMCAP it is loaded and
     made resident in low memory.  Each time you
     run it after that (until the next time you
     boot) the command only serves to change or
     re-assert the command line arguments and to
     report the current status of the resident
     driver.  The whole command line for IMCAP is
     as follows (square brackets indicate optional
     items, vertical bar indicates a choice or one
     item or the other):

     imcap [ /h[<page>] | /i[<mode>] ]  [ /b | /q]
                  [ /a ]  [ <path> ]

     where

     /i        (without <mode>) enables the
               capture of all IBM supported
               color/graphics, enhanced graphics
               and monochrome modes as well as the
               Hercules Graphics Card monochrome
               character mode and the AT&T super
               high-resolution graphics mode (the
               default when the program is first
               loaded).

                             WARNING

               When operating in this mode IMCAP
               relies on the ROM BIOS to tell it
               the color palette, video mode,
               cursor position, and cursor mode
               when it attempts to capture the
               image.  If the application does not
               set these entities via the ROM BIOS
               then random results will occur.
               This is not disastrous in the case
               of the cursor information since you
               may repair it by means of the Image
               Manager.  Similarly, the color
               palette in mode number 04 (see
               TABLE 1) can be reselected with
               Image Manager.  The color palette






               associated with the enhanced
               graphics adapter, however, cannot
               be recovered.  If the ROM BIOS is
               not used to set the video mode,
               chaos will ensue.  In this latter
               case use the <mode> operand as
               described below.

     /i<mode>  Use this form when capturing
               screens from applications like
               LOTUS 123 which do not always set
               the video mode via the ROM BIOS.
               Specify the <mode> operand
               (immediately following the "/i"
               with no intervening spaces) as the
               two-digit mode number (see TABLE 1)
               which represents the video mode for
               the screens to be captured.  All
               captures that you make via SHIFT-
               PRTSC after entering this command
               line assume that the selected mode
               is active.  If a different mode is
               active you will capture garbage.
               You should always use Image Manager
               or Image Show to verify that you
               have captured the screen that you
               want.

               This technique may also be used for
               capturing screens from non-DOS or
               protected applications when all
               other attempts at using IMCAP fail.
               Refer to the section entitled
               ""Capturing Screens from Non-DOS or
               Protected Applications".

     /h<page>  Enables the capture of graphics
               mode images on the Hercules
               Graphics Card.

               The /h without <page> or /h0 on the
               command line causes page 0 of the
               Hercules Graphics Card to be
               captured.







               A /h1 causes page one of the
               Hercules Graphics Card to be
               captured.

               Or /h? allows either page to be
               captured:  When SHIFT-PRTSC is
               pressed the operator is asked to
               locate the correct image by
               pressing the SPACE BAR to swap
               between the two pages.  When the
               correct display is obtained, Enter
               is pressed to make the capture.

     /b        Enables the "noisy" mode of IMCAP
               which will cause it to emit a slow
               clicking sound at all times.  This
               is primarily used for trouble
               shooting but is available to users
               who need to be reminded that IMCAP
               is resident.

     /q        Disables "noisy" mode which is
               turned on by "/b" above.

     /a        Causes screens to by captured by
               the ALT-PRTSC key combination
               instead of the SHIFT-PRTSC
               combination.  This may only be
               specified on the initial invocation
               of IMCAP the first time it is
               actually loaded into memory.  It
               may only be disabled (i.e. reverted
               to SHIFT-PRTSC) by re-booting the
               PC and reloading IMCAP without the
               "/a" argument specified.  When "/a"
               has been specified all references
               to SHIFT-PRTSC in this document
               should be taken as ALT-PRTSC.

     <path>    Specifies where the captured files
               will go and what their names will
               be according to the following
               rules:








                 [1]     If <path> ends with a
                    colon (:) or a backslash (\)
                    then it tells the drive and/or
                    directory where the
                    SCREENxx.CAP files are to be
                    written.  The xx will be re-
                    placed by digits which make
                    the file names unique in the
                    given directory.

                 [2]     If <path> does not end
                    with a colon (:) or backslash
                    (\) then it tells the drive,
                    path and file name for the
                    next image to be captured.  It
                    may not contain an extension
                    since ".CAP" will always be
                    automatically appended.  Names
                    created thusly are made unique
                    by replacing the rightmost
                    characters with digits and se-
                    quentially incrementing them.
                    If the rightmost characters of
                    the name are already numeric
                    then they will be incremented.

     REMEMBER:    IMCAP always creates a unique
                  name and never overwrites an
                  existing file, in fact, it will
                  never use a file name if any
                  file by that name exists
                  regardless of its extension.

     Whenever IMCAP is run it always reports the
     last DOS error that occurred (if any), the
     current capture mode (IBM or Hercules),the
     key combination being used for capture, and
     the next file name to be used.













     How To Use Image Manager

     Image Manager is only used for Black & White
     Repro Paper output.  It will only work for
     captured screen mode numbers which can be
     produced on this type of medium (see TABLE
     1).

     After having captured your screen images (in
     ".CAP" files) you must use Image Manager to
     review them and to select the production
     options for each image.  The reviewed images
     must be written into files with the ".SET"
     extension.  If you have a large number of
     ".CAP" files all requiring the same
     production options ImageSet can set the
     options for you.  Please call to make special
     arrangements for this service.

     ImageSet will produce one or more repro
     galleys from each ".SET" file that you send.
     In addition to containing the screen image
     itself, a ".SET" file also contains all other
     information which we need to produce the
     galley.  This information consists of size,
     color selection, registration-mark & cut-line
     insertion, borders, cursor inclusion &
     positioning, etc.  All of these items can be
     selected and changed by use of the Image
     Manager Utility provided on the ImageSet
     Utility Diskette.

     If you want more than one repro galley
     produced from the same ".CAP" file (different
     sizes, color selection, cursor position,
     etc.) you must make and send multiple ".SET"
     files to ImageSet.  Copies can be made with
     the PC-DOS "copy" command or by use of the
     load/save functions within Image Manager.
     The exception to this rule is the Automatic
     Color Splitting feature (described later)
     that is available for mode number 04 (320 x
     200 4-Color Graphics mode, see TABLE 1).








     Image Manager (IMMGR) is a menu-driven
     application program which allows you to load,
     modify and re-save your captured screen image
     (".CAP" or ".SET") files.  To start Image
     Manager insert the ImageSet Utility Diskette
     and enter the command:

                         immgr

     The program is very simple to use.  Menu
     items are chosen by use of single keystrokes.
     Briefly, you load a file by use of function
     <1>, view the captured image via function
     <3>, modify the production parameters with
     functions <5> through <E>, preview the repro
     galley through function <4> and save the
     changes under function <2>.

     Following is a short summary of each
     function.

     <1> Load Image File

     You work on one file at a time by using this
     function to "load" it into memory.  You are
     asked to provide the file name.  Type the
     drive specifier, directory path and file
     name.  The extension ".SET" is assumed if
     such a file exists otherwise the extension
     ".CAP" is assumed.  You may type the exten-
     sion but it must be either ".CAP" or ".SET".
     Remember that unless you tell it otherwise,
     IMCAP names the image files "SCREENxx.CAP"
     where xx is a number from 00 to 99 and puts
     them on the current drive.

     If you type a name containing one or more
     wildcard characters ("Global Filename
     Characters * and ?") you will get a directory
     listing of all files which match the string;
     no file will be loaded and you will be asked
     to enter another name.

     When a file has been successfully loaded, the
     video mode description (see TABLE 1) and the






     production parameters will be displayed.  All
     further operations until the next Load Image
     File pertain to the file currently loaded in
     memory.

     <2> Save Image File

     After you have reviewed the image and
     possibly made changes to the parameters you
     must write the image into a ".SET" file.  You
     are asked to provide the file name.  You may
     use the same name that you loaded the file
     from or may choose any other name.  Using the
     same name overwrites the old version of the
     file.  The default extension is ".SET"; you
     may enter it but it must be ".SET".

     After using this function the image still
     remains in memory and you may make further
     changes and save it again into the same or a
     different file.

     <3> Display Captured Screen

     Use this function to look at the image you
     have captured.  This is not a repro galley
     preview; it shows you the image exactly as
     you have captured it without applying any of
     the color selection parameters.  After
     viewing it press the <ESC> key to return to
     the menu.

     When viewing an image captured in mode number
     04 (320 x 200 4-Color Graphics, see TABLE 1)
     the palette and background colors will be set
     to those which were in effect when the image
     was captured.  This is not completely
     reliable, especially when working on a PC
     compatible system, since IMCAP must "steal"
     these values from the ROM BIOS's RAM data
     area which may not always be located in the
     same place on all systems.  If these are
     wrong or if you wish to change them you may
     do so while viewing the captured image by
     pressing the F9 and F10 function keys to






     rotate through the palettes and background
     colors, respectively.  These settings are
     like any other parameter in that the file
     must be saved in order to make them
     permanent.

     <4> Preview Typeset Galley

     You can use this function to preview the
     output galley exactly as it will be produced.
     It takes into account all of the options and
     color selections that you have made.  Certain
     attributes of the repro galley, however,
     cannot be previewed: on monitor sizes other
     than full size cannot be shown; cut lines,
     borders and registration marks cannot be
     shown.  Also, for screen dumps from the IBM
     monochrome adapter a negative image (black
     characters on a white background) is not
     shown as negative.  (This is due to the
     "underline inconsistency" of the IBM
     monochrome adapter.)  Also, for the
     monochrome display, characters which will be
     in boldface are shown intensified on the
     preview screen.

     REMEMBER:    You will otherwise get exactly
                  what you see. A white graphic on
                  a black screen will be produced
                  as white on a black field.

     When you have finished viewing the image
     press the <ESC> key to return to the menu.

     <5> Color Select

     This is the most important parameter.
     Depending on the video mode number there may
     be from 2 to 16 different colors comprising
     the image.  Use this parameter to select (set
     to YES) each color you want to appear as
     black.  All other colors (set to NO) will be
     left white.  2-color modes only ask you to
     select the background color; the foreground
     is automatically taken as the opposite.  Use






     the galley preview function (<4>) to verify
     that you will get what you want.

     If you select (set to YES) all of the colors
     for a multiple-color image, obviously, you
     will get a completely black repro galley.
     The single exception to this rule is in the
     case of a mode number 04 (320 x 200 4-Color
     Graphics, see TABLE 1) image.  Selecting all
     four colors for this mode enables the Au-
     tomatic Color Splitting feature.  In this
     case ImageSet will produce four repro galleys
     from the one ".SET" file, one for each color.
     THIS IS THE ONLY CASE IN WHICH MORE THAN ONE
     REPRO GALLEY WILL BE PRODUCED FROM A SINGLE
     ".SET" FILE.

     WARNING:  IF YOU SKIP THIS STEP, YOUR IMAGE
               MAY COME OUT SOLID BLACK.

     <6> Galley Size

     This feature is no longer applicable. Size
     designations (small, medium or large) are
     ignored.

     On orders of more than five images,  ImageSet
     will set screens to size.  Screen images are
     set to the width dimension only and must be
     specified in millimeters e.g. to the width of
     80 mm.

     The height varies depending on the mode of
     the image captured.

     REFER TO TABLE 3 FOR THE DEFAULT SIZES OF THE
     VARIOUS MODES AND THEIR WIDTH TO HEIGHT
     RATIOS.

     REMEMBER:    The repro galley size is not
                  reflected in the preview screen
                  obtained by menu function <4>.









     <7> Cut Line Select

     This option controls cut lines and
     registration marks (you can't have one
     without the other).  You may request that cut
     lines and registration marks be placed around
     the image.  An example of these are shown in
     one of the attached figures.  YES for this
     parameter causes cut lines and registration
     marks to be set in each corner of the repro
     galley.  NO causes neither to be appear.

     You will most likely want these when
     specifying color splits to facilitate
     registration at printing time.  All images
     for a given video mode number (see TABLE 1)
     are centered within the same sized cut line
     area for these purposes regardless of which
     other options (especially borders) are
     selected.  For the Automatic Color Splitting
     facility (described under function <5> above)
     the cut lines and registration marks will be
     generated in all four repro galleys.

     REMEMBER:    Cut lines and registration marks
                  are not shown in the preview
                  screen obtained by menu function
                  <4>.

     <8> Border Select

     You may choose one of six kinds of borders
     around the galley or no border.  Refer to
     TABLE 3 and the attached "Border Selections"
     page for examples of the available types of
     borders.  In the case of the Automatic Color
     Splitting facility for mode number 04 (320 x
     200 4-Color Graphics, see TABLE 1) the
     selected border (if any) is placed only in
     the galley for the background color.

     <9> Galley Title

     You may enter a string of up to 40 characters
     to be set as text in the header of the output






     repro  galley.  The header always contains
     the ImageSet job title and the ".SET" file
     name.  If you provide a galley title it will
     be concatenated on to those.

     In the case of the Automatic Color Splitting
     facility available for mode number 04 (320 x
     200 4-Color Graphics, see TABLE 1) the color
     for each repro galley along with its process
     ink color equivalents will also appear in the
     title.

     <A> Cursor Select
     <B> Cursor Position
     <C> Cursor Lines

     These parameters are only applicable to
     character mode screens (see TABLE 1).

     When you captured the screen image the
     position and size of the cursor were recorded
     with it.  If you set Cursor Placement to NO
     the cursor will not appear in the galley.  If
     you set Cursor Placement to YES then the
     cursor will appear as shown by the row,
     column and lines parameters.  You may change
     these parameters to move the cursor anywhere
     on the screen or to change its size.

     <D> Blinking Select
     <E> Intensity Select

     These parameters are only applicable to
     character mode screens (see TABLE 1).

     You may elect to do one of four things with
     screen characters which have the blinking
     attribute and/or the high-intensity at-
     tribute:

          [1]  Exclude them completely.  In this
               case the positions in which the
               characters appear will appear as
               blank spaces.  For color modes,
               they will be subject to inclusion






               or exclusion under control of the
               Color Selection parameter for their
               background color.

          [2]  Include them.  The characters will
               appear just as ordinary unblinking
               characters.  For color modes, they
               will still be subject to inclusion
               or exclusion under control of the
               Color Selection parameters.

          [3]  Include them as boldface
               characters.  The characters are
               placed in the galley with the ap-
               pearance of being slightly darker
               than the normal characters.

               This option is quite effective for
               the color/graphics text modes.
               However, it is NOT RECOMMENDED FOR
               USE WITH MONOCHROME since the
               preview function (<4> on the main
               menu) for monochrome cannot
               accurately depict what the final
               output will look like.

               For color modes, the characters
               will still be subject to inclusion
               or exclusion under control of the
               Color Selection parameters.

          [4]  Include Only these characters.  All
               other characters, regardless of
               their color will be excluded.  This
               is most commonly used when you are
               planning to make a separate
               printing pass to insert the
               blinking and/or intensified charac-
               ters in your final work.  For color
               modes, the characters will still be
               subject to inclusion or exclusion
               under control of the Color
               Selection parameters.








     When a character has both the blink and
     intensity attributes an attempt is made to do
     something logical by combining the two
     parameters that you have selected.  Be sure
     to use the preview function (<4> on the main
     menu) to verify that you will get what you
     want.

     <DEL> Exit to System

     This function exits from Image Manager to the
     PC-DOS system.  If you have changed the
     parameters of the current image file and have
     not saved them you will be asked to verify
     that you want to exit, thus abandoning those
     changes.



































     Capturing Screens from Non-DOS or

     Protected Applications

     Use this technique if all other attempts at
     using IMCAP fail. It is a relatively slow
     process and requires you to have two video
     adapters and two monitors attached to your
     system.

     For purposes of this discussion we will refer
     to the monitor which displays the image you
     want to capture as "Monitor-1" and to the
     other monitor as "Monitor-2".

     Set your system configuration switches so
     that your system boots DOS on Monitor-2.  Use
     the DOS "mode" command to switch to Monitor-1
     then run your application program and get the
     image you want to capture displayed on
     Monitor-1. With the image displayed use Ctl-
     Alt-Del to boot the system from you DOS disk.
     Do not be alarmed when Monitor-1 clears; the
     image will still be preserved in the video
     adapter's memory.

     When DOS comes up on Monitor-2 load IMCAP
     with the following command line:

                     imcap /i<nn>

     substituting for <nn> the two-digit mode
     number (see TABLE 1) that Monitor-1 was in
     when you booted.  Press SHIFT-PRTSC once to
     capture the image.  Use the DOS "mode"
     command to switch to Monitor-1 then run IMMGR
     or IMSHOW to review the just-captured screen.

     Note that when mode number 04 (320 x 200 4-
     Color Graphics) is captured in this manner
     the color palette information may not be
     captured properly. Use function <3> in Image
     Manager to determine if this has occurred and
     to adjust to the correct colors.  This
     technique may not be used on the EGA (mode






     numbers 13, 14, 15 and 16 in TABLE 1) when a
     non-standard color palette is in effect.

















































     How to Use Image Show

     This facility may be used for all captured
     screen modes listed in TABLE 1.

     The utility program "Image Show (IMSHOW) is
     provided on the utility diskette.  You may
     use it to review your captured image files in
     a manner similar to the "<3> Display Captured
     Screen" function in IMMGR.  Insert the
     ImageSet Utility Diskette and enter a command
     line of the form:

          imshow [/a] <file> <file> <file>...

     Any number of file parameters may be
     specified.  Each may be an individual ".CAP"
     or ".SET" file name or may contain DOS
     wildcard characters ("Global File Name
     Characters * and ?" as the DOS manual calls
     them) which specify a collection of ".CAP" or
     ".SET" files

     Each file's name and screen mode is displayed
     with a menu which allows you to choose
     between "Skip" the file, "Display" the file,
     "Enter AUTO Mode", or "Quit".  Upon choosing
     "Display" you will see the image exactly as
     captured.  Press any key to continue.

     You may run the utility in "Automatic" mode
     by specifying "/a" on the command line or by
     choosing the "Enter AUTO Mode" menu item.
     The captured images will be displayed, one
     after another for about 3 seconds each with
     no operator intervention.  To stop AUTO mode,
     press any key.














     Border Types

     Borders are only available when output is on
     Black & White Repro Paper and therefore only
     for screen modes for which this medium is
     available (see TABLE 1).

     TABLE 2 contains a list of the available
     border types and a brief description of each.
     A sample of each type is given on the fol-
     lowing pages.

     Since the borders are all formed from the
     same dimension rectangular pixels as the
     screen image itself there is a slight
     ceration ("jaggies") apparent on the rounded
     borders.


















                        TABLE 2

                    Border Descriptions

          None:     No border around screen.

          Narrow:   A black rectangle rule
                    (approximately 5 pixels wide)
                    is placed around the screen
                    extending 9 pixels from the
                    edge of the image.  Border
                    butts up against the screen
                    image.

          Wide:     A black rectangle 15 pixels
                    wide is placed around the
                    screen extending approx 9
                    pixels from the edge of the
                    image.  Border butts up
                    against the screen image.

          Narrow Outline: A white rectangle ap-
                    proximately 5 pixels  wide is
                    left around the screen and a
                    black rectangle approximately
                    5 pixels wide is placed around
                    that.

          Thin Outline:       A white rectangle
                    approximately 15 pixels wide
                    is left around the screen and
                    a black rectangle 1 pixel rule
                    is placed around that.

          Thin Outline Rounded:              Same
                    as Thin Outline except that
                    the corners of the rectangles
                    are rounded instead of square.
                    This simulates a monitor
                    screen.

          Wide Rounded:                 Same as
                    Wide except that the corners
                    of the rectangle are rounded







                    instead of square to simulate
                    a monitor screen.








     Screen Measurements

     TABLE 3 shows the default sizes available in
     Black and White on Repro Paper and through
     the separation and half-toning process.  Any
     smaller sizes are available by indicating
     screen width in millimeters for orders over
     five images.

     TABLE 3 gives measurements for images
     captured from the IBM Color/Graphics Adapter
     and from the AT&T Super-Hi resolution mode
     (mode numbers 00-06 & 09 in TABLE 1, not
     including optional borders).

     Also given are  measurements for images
     captured from the IBM Monochrome adapter and
     the Hercules graphics card (mode numbers 07 &
     08, not including optional borders).

     The mode of any captured screen can be
     determined when processed through the IMSHOW
     utility.

     For Process Color Separation or Gray Tone
     Conversions on film specify exact width of
     screen image required in millimeters on
     transmittal form.






                        TABLE 3

           Image Measurements Default Sizes

      Black & White Output

     Mode      Approximate     Approximate  H to W
                Width (MM)          Height   Ratio

     1,4 and 5  169                 119     .7

     2,3,6,7    166                 121     .73

     8          186                 126     .68

     9          169                 121     .72

     Color Separation and Gray Tones

     Mode        Base Width         Height  Ratio

     1,4        100                 70      .7
     13,14,16   100                 76      .76