VGA Computer-Assisted Design v1.40
              Copyright (c) 1988 Lawrence Gozum & Marvin Gozum

                            U S E R  M A N U A L

      DISCLAIMER

      This  product is distributed AS IS.  The authors specifically disclaim
      all  warranties,  expressed or implied, including, but not limited to,
      implied  warranties  of  merchantability  and fitness for a particular
      purpose  with  respect  to  defects in the diskette and documentation,
      and  program  license  granted herein, in particular, without limiting
      operation  of  the program license with respect to any use or purpose.
      In  no  event  shall  the  authors be liable for any loss of profit or
      damage   including   but   not   limited   to   special,   incidental,
      consequential or other damages.  


      LICENSING AGREEMENT

      You  may  use this program on a TRIAL BASIS only;  this means that you
      may  freely  evaluate  the usefulness of this program for a REASONABLE
      period.    Should  you  find this program useful, you must register by
      sending  in  registration  form  with  a check payable to Marvin Gozum
      with a minimum registration fee of $8.95.

      You  may  freely  distribute  copies of this program in its UNMODIFIED
      state  provided you do not include it in other software packages, with
      the  exception of distributing it as part of a bundle of Public Domain
      or 'shareware' programs on a single diskette.


      1.   Introduction

      VGACAD's  strength  is  graphics  editing  and  support for gray image
      digitizers;    you  can  use  VGACAD  as  a paint program or use it to
      enhance your digitized images and colorize them.

      VGACAD,  is  "living  software";  it  will evolve into a VERY powerful
      program  as long as YOU support it.  Many purists may argue that it is
      not  a  full-fledged  CAD  program,  since  "computer-assisted design"
      (CAD)  has  been associated with manufacturing and technical drafting,
      it  will be as more and more updates are released.  We envision VGACAD
      as  an  all-purpose  painting/   graphics editor/ image processor/ CAD
      program.    Help  us  realize  its  full-potential  by  supporting the
      'shareware' effort.


      2.   Requirements

      IBM  PS/2 or IBM PC/XT/AT with VGA compatible graphics card capable of
      displaying  mode  13H (MCGA 300x200x256 color mode), 512k free memory,
      analog  or  multifrequency  monitor.    We  strongly suggest you get a
      mouse since VGACAD was designed with a mouse device in mind.

      PLEASE READ 'README.2ND' REGARDING HARDWARE COMPATIBILITY.










      3.   Installation

      Make  sure  all  the  required files (listed in README.1st) are in the
      same  default  drive  and/or  subdirectory,    type  "VGACAD"  and hit
      <enter>.    You  will be prompted if a mouse driver is absent.  To use
      the  keyboard mouse emulator, run "KEYME.com" prior to running VGACAD;
      you can review the keyboard commands at the start of each session.

      If  you  have insufficient memory, you will be prompted to remove your
      resident  programs  to  allow  more memory.  After initialization, the
      total  amount  of  free memory will be shown - this indicates how much
      resident software can be installed prior to running VGACAD.


      4.   Command Line Options

      There are five command line options.

      Switch  "/Q"  for  "Quiet"  will  silence all the audio feedback beeps
      except in the case of error messages.

      Switch  "/FK"  for "Force Keyboard" will disregard mouse detection and
      the  mouse  device  and  operate  in  mouse emulation mode through the
      keyboard.   "KeyME.com" MUST be resident if you use this switch or the
      system  will  HANG !  This option is provided for certain systems that
      write   to  the  mouse  interrupt  address  which  fools  VGACAD  into
      recognizing a mouse device which does not exist.

      Switch  "/MX:n" adjusts the mickeys/8 pixels ratio on the X axis.  The
      default  is 8/8.  "n" is any number from 1 and 16.  "1" will make your
      mouse  travel  8  times  faster while 16 will make your mouse travel 2
      times slower on the x axis.

      Switch "/MY:n" adjusts the mickeys/8 pixel ration on the Y axis.

      Switch  "/MT:n" adjusts the "motion threshold" for doubling your mouse
      speed.    The default is 64 mickeys/second.  If your mouse seems to be
      returning  to  its  same  position  or  seems  retrained after zipping
      quickly  from  any  direction,  its  movement was successively doubled
      resulting  in  the  mouse returning to its former location.  This is a
      function  of  your  CPU  speed.    "n" is any number between -32767 to
      32767.  Refer to your mouse manual for more information.

      Use  a "BATCH" file to keep your desired settings.  The sample "BATCH"
      file  below turns the sound off, doubles the speed in both the x and y
      axes and keeps the motion threshold at its maximum.

                      VGACAD /Q /MX:4 /MY:4 /MT:-32767


      5.   Testing

      VGACAD  was  tested  on  a  8MHz IBM XT compatible with an ATI VIP VGA
      card  on a Princeton Ultrasync.  For comments, especially bug reports,
      we  would deeply appreciate it if you would leave E-Mail at CompuServe
      for Marvin Gozum [72307,2362] or Lawrence Gozum [73437,2372].










      6.   Main Menu

      While  in  your  picture,  clicking  your RIGHT mouse button, the Main
      Menu  screen  will  pop-up.   There are seven (8) boxes; these are the
      Undo  command,  ImgP(Image  Process  Menu), Edit Menu, Text Menu, Shps
      (Shapes Menu), Color Menu and File Menu.

:

                ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
     Main Menu  ³ÚÄÄÄ¿ÚÄÄÄ¿ÚÄÄÄ¿ÚÄÄÄ¿ÚÄÄÄ¿ÚÄÄÄ¿ ÚÄÄÄ¿ ÚÄÄÄ<Åcurrent
     option   ÄÄÅÅ>  ³³   ³³   ³³   ³³   ³³   ³ ³   ³ ³   ³³background
     filled with³ÀÄÄÄÙÀÄÄÄÙÀÄÄÄÙÀÄÄÄÙÀÄÄÄÙÀÄÄÄÙ ÀÄÄÄÙ ÀÄÄÄÙ³color
     current    ³ Undo ImgP Edit Text Brsh Shps Color File ³
     foreground ³{²²±°°±°°²²ÛÛ²²±±ÛÛ²²±±°°±±°°²²±±°°²²ÛÛ²} ³ <Ä¿
     color      ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ   ÃÄ Color
                 {²²±°°±°°²²ÛÛ²²±±ÛÛ²²±±°°±±°°²²±±°°²²ÛÛ²}   <ÄÙ  Bars
                 ^                                       ^
                 ÀÄÄÄÄÄÄÄÄÄÄÄÄÄ Scroll Arrows ÄÄÄÄÄÄÄÄÄÄÄÙ

      At  start-up,  you will be in 'brush' mode and can begin painting.  If
      you  move your cursor below the Main Menu, the menu will disappear and
      will  reappear  when you press the RIGHT mouse button. Clicking a Main
      Menu  box  will  operate  immediately  or  will  bring you deeper into
      another menu.

      Use  the  local  color  bars  to  select current foreground/background
      colors.    Place the "arrow" cursor over a desired color and click the
      LEFT  mouse  button  for  a  new  foreground  color or the RIGHT mouse
      button  to  select  a  new background color.  You will immediately see
      the selected colors replace the Main Menu boxex.

      The  local  color  bars  provide  you with a 32, 64 or 128 colors from
      your  256  color  palette.    At  default,  each color bar contains 16
      colors.    Use the scroll arrows to change the colors selections.  The
      upper  and  lower color bars play an important role in colorizing gray
      pictures.  This will be explained further.

      To  exit,  without  choosing  any  option  put  your  cursor below the
      screen.    In almost all cases, the RIGHT mouse button will be used to
      exit  or  abort,  while  the  LEFT  mouse  button  will  be used to do
      everything else or ACCEPT a change.


      7.   Undo Function

      Whenever  the  Main  Menu screen pops-up, your current screen is saved
      and  your  can 'undo' all the changes from the last time the Main Menu
      was  invoked.    No matter what changes were made, your screen will be
      restored.    If  you pop-up the Main Menu screen and do not select any
      option,  your  next  UNDO  will  be  based on that screen.  The latest
      screen  saved  is  the  screen last modified when you invoked the Main
      Menu.    This  applies to most cases, except in image processing loops
      where your last change will be your last image modification.












      8.   Brush Menu

      Selecting the Brush option will pop-up this sub-menu.

               ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
               ³ÚÄÄÄÄ¿ÚÄÄÄ¿ ÚÄÄÄ¿ ÚÄÄÄ¿ ÚÄÄÄ¿ ÚÄÄÄ¿ ÚÄÄÄ¿ ÚÄÄÄ¿³
           ÄÄÄÄÅÅ>   ³³   ³ ³ÛÛÛ³ ³   ³ ³   ³ ³   ³ ³   ³ ³   ³³
       Active  ³ÀÄÄÄÄÙÀÄÄÄÙ ÀÄÄÄÙ ÀÄÄÄÙ ÀÄÄÄÙ ÀÄÄÄÙ ÀÄÄÄÙ ÀÄÄÄÙ³
       BRUSH   ³        <>   SPRY  Rect  Circ  Line  Diag  ERSR³
               ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

      The  Active  box  will  show  the  current  "brush" selected.  You can
      choose  from a (Rect)angle, (Circ)le, Horizontal or Vertical (Line) or
      (Diag)onal brush by clicking the brush shape box.

      The  "<>"  box  cycles through the different brush sizes or variations
      until  you  stop at a selected variant.   At present there are 6 sizes
      of   the  RECTangular  types,  3  sizes  for  CIRCular,  3  sizes  for
      Horizontal  LINEs,  3  sizes  for  Vertical  LINEs,  and  6  different
      DIAGonal brushes - 21 BASIC brushes to choose from.

      The  SPRaY  paint  mode  works when you select either a RECTangular or
      CIRCular  brush.    This  gives  you another 8 spray brushes to choose
      from, bringing the total to 29 brushes.

      The  ERaSeR  mode  will  use the color BLACK (color 0) as the selected
      foreground  color  (remember,  you cannot choose BLACK as a foreground
      color)  until  you  disable  this  mode  by selecting any brush shape.
      Use  the  Rectangular  brushes for quicker erasures.  WHEN PAINTING IN
      BRUSH  MODE AND NOTHING IS HAPPENING ON A "BLANK" SCREEN THEN YOU KNOW
      THAT THE ERaSeR MODE IS "ON" SINCE YOU WILL BE ERASING NOTHING !

      As  with  other  sub-menus,  dragging  your "brush" (cursor) below the
      pop-up menu will exit whether or not you have made any selection.


      9.   Color Menu

      Selecting "COLOR" from the Main menu brings you to this sub-menu.

              ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
              ³ÚÄÄÄ¿ ÚÄÄÄ¿ ÚÄÄÄ¿ ÚÄÄÄ¿ ÚÄÄÄ¿ ÚÄÄÄ¿ ÚÄÄÄ¿ ÚÄÄÄ¿³
              ³³   ³ ³   ³ ³   ³ ³ÛÛÛ³ ³   ³ ³   ³ ³   ³ ³   ³³
              ³ÀÄÄÄÙ ÀÄÄÄÙ ÀÄÄÄÙ ÀÄÄÄÙ ÀÄÄÄÙ ÀÄÄÄÙ ÀÄÄÄÙ ÀÄÄÄÙ³
              ³ SCRN  BRSH  SWAP  CBAR  ZOOM  AREA COLOR  UNDO³
              ³ -Replace--  SCRN  - Colorization -  MAP   mode³
              ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

      "SCReeN"  replaces  all  occurences  of your selected background color
      with  your  selected  foreground color.  You can use this function for
      finding  specific  colors.    For example, you may have a gray picture
      and  want  to  find all occurrences of a particular shade; select your
      suspected  gray  shade  as the background color and select a new color
      (e.g.,  RED)  as  the foreground color; on exit, if that shade of gray
      exists,  it will be replaced by red which you can "UNDO" from the Main
      Menu to restore your picture.










      "BRuSH"  will  replace  only  the  selected background color that your
      current  brush will paint over with the selected foreground color.  If
      that  color  does  not exist (although may look like it does), it will
      not  be  changed.   Use this function as you would a stencil.  You can
      create  elaborate  patterns  by  painting over colors selectively.  AS
      WITH  THE  ERaSer  MODE,  PAINTING  OVER  COLORS THAT DON'T EXIST WILL
      RESULT IN NOTHING HAPPENING ON THE SCREEN.

      "SWAP"  will exchange all selected background color occurrences on the
      screen with the selected foreground color and vice-versa.

      "UNDO"  deactivates all color editing modes before exiting.  If any of
      the  options  above have their box highlighted upon exit, it will take
      effect  (e.g.,  SWAP)  and you will have to "UNDO" from the Main Menu.
      Clicking this box deactivates all modes.

      "ColorBAR" changes your COLOR RANGE into 16, 32 or 64.

           ³{²²±°°±°°²²ÛÛ²²±±ÛÛ²²±±°°±Û²±±°ÛÛ°°²²±±°°²²ÛÛ²}³ <Ä¿  
           ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ   Color
            {²²±°°±°°²²ÛÛ²²±±ÛÛ²²±±°°±±°°²²±±°ÛÛ²²Û²²²²ÛÛ²} <ÄÄBars
            ^                                             ^
            ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ  Scroll Arrows ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

      Clicking  "ColorBAR"  will make the Scroll Arrows cycle through 16,32,
      or  64  COLOR  RANGE  colorbars.  Use the 32 or 64 COLOR RANGE to view
      and  select  more  colors  at  any time.  COLOR RANGES are extensively
      used by the "AREA colorization" and "ZOOM" functions.

      The  upper  and  lower colorbars will change when you select any color
      belonging  to  the  16,32,  or  64  color range of the colorbar if you
      directly  select  a  foreground  or background color in the COLOR MAP.
      The  lower  colorbar  will  correspond  to the range where the current
      background  color was selected while the upper colorbar corresponds to
      the range of the current foreground color.

      In  "Area" (colorization), the upper and lower colorbar selections are
      significant.    When you select this option, all colors from the lower
      colorbar  will  be  replaced by all the colors from the upper colorbar
      in  a  one-to-one  correspondence to "colorize" an area. Once you have
      selected  this  option and exit the menu, the arrow cursor will appear
      instead of your current brush.

      AS  A  RULE, THE APPEARANCE OF THE ARROW CURSOR INDICATES A BLOCK FORM
      OF  EDITING OR SETTING OF A STARTING POSITION WHEN PERFORMING ANY FULL
      SCREEN  EDITING  FUNCTION.    Pick a starting point on your screen and
      drag  the  cursor  while  keeping  the  LEFT  mouse button down.  Upon
      releasing  the  mouse  button,  all  colors in the upper colorbar will
      replace  all the colors in the lower colorbar.  The selected area will
      then  be  highlighted by a blinking outline of the changed area; click
      the RIGHT mouse button to reject change or the LEFT to accept change.

      AREA  colorization  is  a  very  powerful  feature that lets you apply
      false  colorization to gray images of any range (16, 32 or 64)).  Gray
      images  provide  you  with the "luminance" information of your picture
      by virtue of its gray scale (16, 32 or 64); by altering color ranges,
                                                                            









      you  can  select  any  range  of  a  gray scale and replace the colors
      within  the  new range with any other color range defined in the COLOR
      MAP.    You can selectively increase the contrast on a particular area
      with  this  function.    For  example,  you  may  want  to highlight a
      particular  gray  area  by selectively increasing "brightness" on a 64
      gray  level  picture by selecting a 32 or 16 Color RANGE and replacing
      a  lower  gray  range with a higher gray range.  The minimum range you
      can  effect  is  a 16 color range change.  Use the SCReen Replace mode
      or BRuSH mode to selective replace individual colors.

      "ZOOM"  (colorization)  works the same way as "Area" but on a "zoomed"
      area.    ZOOM  has  three  modes  - NORMAL, XCOLOR and SMOOTH.  XCOLOR
      (eXchange  COLOR)  mode replaces individual colors using the colorbars
      as  reference; only selected colors on the lower color bar are changed
      with  the  upper colorbar.  ZOOM lets you change those "hard to reach"
      areas  where  objects  border other objects or the background.  NORMAL
      mode  works  like  any  other  ZOOM function where your paint over any
      color.    The ZOOM functions will bring you to more menu options while
      performing  "ZOOM"  editing.  The SMOOTH mode "blurs jaggies" while in
      ZOOM; all these functions are discussed further.

      The  "COLOR  MAP"  will  show  the entire plethora of 256 colors.  The
      colors  are arranged in lines of 16 colors by 16 lines - totalling 256
      colors.    Each  line  has  16  color  boxes.  See Appendix A (Palette
      Organization  Map)  for full details.  Each color box is configured to
      show  its  complimentary  or  inverse color.  This is done so that you
      may experiment with creative color inversing techniques.

                                ÚÄÄÄÄÄÄÄÄ¿
             Main Color    ÄÄÄÄÄÅ>ÛÛÛÛ   ³
                                ³ÛÛÛÛÛ   ³
                                ³       <ÅÄÄÄÄÄ Inverse color
                                ÀÄÄÄÄÄÄÄÄÙ

      You  can  choose  any  color  for  foreground or background EXCEPT the
      COLOR  0 (refer to Appendix A) as foreground. To use COLOR 0 (normally
      BLACK),  you  will have to use the ERaSeR brush.  Click the LEFT mouse
      button  over any color to select a foreground color or the RIGHT mouse
      button  to  select  a  background color; they will be displayed in the
      RGB boxes at the lower left.

            ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
            ³  R=10    G=20    B=30   ³
            ³ ÚÄÄÄÄ¿  ÚÄÄÄÄ¿  ÚÄÄÄÄ¿  ³
            ³ ³ ^  ³  ³ ^  ³  ³  ^ ³ <ÅÄÄÄÄÄ background color
            ³ ÀÄÅÄÄÙ  ÀÄÅÄÄÙ  ÀÄÄÅÄÙ  ³
            ÀÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÅÄÄÄÄÙ
                ³       ³        ³
                ÀÄÄ foreground color

      The  COLOR  MAP  is  arranged from the LEFT to RIGHT starting from the
      TOP  TO  BOTTOM  for the first 128 colors (COLORS 0 to 127).  The next
      128  colors (COLORS 128 to 255) are arranged in the reverse order from
      RIGHT  to  LEFT  starting from the BOTTOM to the TOP; this enables you
      to see its inverse organization.  See Appendix A for details.











      Palette  editing  is  accomplished  by  alteringthe  RGB  values  of a
      selected  foreground  color.   Place your cursor on any of the 3 boxes
      labelled  "R"(red),  "G"(green)  and  "B"(blue).    Clicking the RIGHT
      mouse  button  will  quickly  increase  the  mixture  of  the color by
      increasing the proportion of red, blue or green "quanta".

      Clicking  the LEFT mouse button will decrease the RGB values of either
      the  R(ed), G(reen) or B(lue) box in single increments.  As you modify
      the  mixture,  you  will  see  the color change, as well as the number
      representing  the  primary  "quanta"  (RGB  values) of that particular
      color.  You can change all the colors.

      IF  YOUR PALETTE CHANGE RESULTS IN ANY TWO INVERSELY RELATED COLORS IN
      A  COLOR BOX TO BE THE SAME, A BEEP WILL SOUND AND YOUR CHANGE WILL BE
      REJECTED  (E.G.  CHANGING  COLOR 0 = COLOR 255) SINCE IT WILL MAKE THE
      MENUS  AND/OR  CURSORS  INVISIBLE.  As a precaution, you cannot select
      COLOR  "0"  as  a foreground color.  If you want to modify it, use the
      editing functions below.

      To  the lower right corner are four boxes.  Copy, Swap, Digi and Reset
      provide extensive palette editing functions.

      The  COPY  box  is  particularly useful in modifying very subtle color
      differences.   An increase in the "QUANTA" of R(ed), G(reen) or B(lue)
      by  1 will be hardly noticeable.  To copy a color, select the color to
      be  copied  as  BACKGROUND  then  select  the  color to be replaced as
      FOREGROUND.  Click the COPY box with your LEFT mouse button.

      SWAP  works  the  same  way  as COPY except that it swaps the selected
      foreground  color  with the selected background color.  This helps you
      rearrange your entire palette.

      DIGI  is a very powerful; it will modify the selected foreground color
      to  the  selected background color and fill-in all the shades between.
      To  select  a range, pick a foreground color as your starting position
      and  a  background color as your end of the range.  Click the DIGI box
      and  all the colors in the range will be spread between the "anchors":
      the  selected  foreground  and  background  colors.  CLICK UNDO BOX TO
      RESTORE  YOUR  PALETTE  BEFORE  DOING ANYTHING ELSE IF YOU DO NOT WANT
      THE CHANGE; THIS IS YOUR ONLY CHANCE TO UNDO THE MODIFICATION.

      RESET  restores  a  selected  color's  registers  or the whole palette
      after  any  modification  or editing BEFORE selecting a new foreground
      or background color to edit.

      To  exit,  click EXIT box with the LEFT mouse button.  The quicker way
      to  exit  is  to  click both buttons in succession.  After selecting a
      new  foreground  color,  BEFORE releasing the LEFT mouse button, click
      the  RIGHT mouse button or after selecting a new background color then
      hit the LEFT mouse button before releasing the RIGHT mouse button.
















      10.   Zoom Menu

      When  you  select  the  ZOOM option from the "COLOR" menu, you will be
      presented  with  an  inversed  cursor  the  size of the Viewing Window
      below;  place  the  Viewing  Window  over  the are you will "ZOOM" and
      click  the  LEFT  mouse  button  to  accept or the RIGHT to reject and
      exit.   While in "ZOOM" mode you will have several option depending on
      the  "ZOOM  MODE"  you select.  In any case, after editing and exiting
      (i.e.,  clicking  "*OK*") you can again select another area for "ZOOM"
      editing  until  you  exit  with the RIGHT mouse button. The area being
      edited will be displayed at the upper left box - the Viewing Window. 

       VIEWING  ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
       WINDOW   ³ÚÄÄÄÄÄ¿     ÚÄÄÄ¿ ÚÄÄÄ¿ ÚÄÄÄ¿ ÚÄÄÄ¿ ÚÄÄÄ¿ ÚÄÄÄ¿³
        ÀÄÄÄÄÄÄÄÅÅ>    ³     ³ÛÛÛ³ ³   ³ ³   ³ ³   ³ ³   ³ ³   ³³
       CURRENT  ³ÀÄÄÄÄÄÙ     ÀÄÄÄÙ ÀÄÄÄÙ ÀÄÄÄÙ ÀÄÄÄÙ ÀÄÄÄÙ ÀÄÄÄÙ³
       MODE ÄÄÄÄÅ>NORMAL      MODE  UNDO  FIND  CBAR  COLOR *OK*³
                ³{²²±°°±°°²²ÛÛ²²±±ÛÛ²²±±°°±Û²±±°ÛÛ°°²²±±°°²²ÛÛ²}³ <Ä¿  
                ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ   Color
                 {²²±°°±°°²²ÛÛ²²±±ÛÛ²²±±°°±±°°²²±±°ÛÛ²²Û²²²²ÛÛ²} <ÄÄBars
                 ^                                             ^
                 ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ  Scroll Arrows ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

      MODE  toggles  between  the  XCOLOR (eXchange COLOR) mode, NORMAL mode
      and  SMOOTH  mode.    As  explained in the AREA colorization function,
      XCOLOR  mode  replaces  each  pixel  belonging  to the range of colors
      specified  in  the  lower  color  bar with corresponding colors in the
      upper  color  bar.    NORMAL  mode  lets you change any pixel with the
      current  foreground  color, indicated by the color of menu boxes.  The
      SMOOTH  mode  will  "smooth"  any pixel in relation to all neighboring
      pixels; more on this later.

      By  clicking  the  pixel  on  the  "zoomed"  image with the LEFT mouse
      button,  the color will be replaced by the present foreground color in
      NORMAL  mode  or replaced with the corresponding color in XCOLOR mode.
      In  SMOOTH  mode,  the  pixel  with  will be replaced with a different
      pixel  which  will  vary with its neighbors and the parameter settings
      for  smoothing;  this  is  discussed  separately.    As  you edit, the
      changes will be reflected in the Viewing Window.

      In  XCOLOR  mode,  all  incidences of any color in the lower color bar
      will  be  replaced  by  the upper color bar.  Only colors belonging to
      the  lower colorbar will be affected.  If no color exists which belong
      to  the  lower colorbar then nothing will be modified !  If background
      (COLOR  0)  is  replaced with some other color, the colorbars selected
      have included COLOR 0 for replacememt.
 
      Clicking  the  "RIGHT" mouse button will reset any particular pixel to
      its  original  color, prior to any modification or replacement despite
      the number of times you have changed the pixel color in ANY mode.

      ColorBAR  (CBAR)  is  basically  the  same function in the COLOR menu.
      This  is  an  added  convenience  so that you can change the lower and
      upper color bar ranges while you work on the "Zoomed" image.

      "Color"  - works just like the "Color" option on COLOR menu. This will
      bring you to the COLOR MAP for editing the palette an return here.









      "Find"  will  mark all existing pixels in your zoomed image that match
      your  current foreground color with an "*".  This identifies "hard-to-
      distinguish" hues.

      "UNDO"  -  will  restore  the ALL of the "Zoomed" area to its original
      state despite any change in any mode.

      "*OK*"  - will include your edited area in your picture and return you
      to  the  main  screen;    all  changes  are final.  You can now select
      another area for "ZOOM" editing or exit.


      SMOOTH MODE will change the menu boxes and will deactivate colorbars.

       VIEWING  ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
       WINDOW   ³ÚÄÄÄÄÄ¿     ÚÄÄÄ¿ ÚÄÄÄ¿ ÚÄÄÄ¿ ÚÄÄÄ¿ ÚÄÄÄ¿ ÚÄÄÄ¿³
        ÀÄÄÄÄÄÄÄÅÅ>    ³     ³ÛÛÛ³ ³   ³ ³   ³ ³   ³ ³   ³ ³   ³³
       CURRENT  ³ÀÄÄÄÄÄÙ     ÀÄÄÄÙ ÀÄÄÄÙ ÀÄÄÄÙ ÀÄÄÄÙ ÀÄÄÄÙ ÀÄÄÄÙ³
       MODE ÄÄÄÄÅ>SMOOTH      MODE  UNDO  TYPE  HUES  RATE  *OK*³
                ³{²²±°°±°°²²ÛÛ²²±±ÛÛ²²±±°°±Û²±±°ÛÛ°°²²±±°°²²ÛÛ²}³
                ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ
                Type:1    Hue Factor:60    Precision:24

      There  are  3  parameters  that affect the smoothing function.  Simply
      keep clicking (with LEFT BUTTON) parameter boxes to change settings.

      "TYPE"  affects  the  level or degree of smoothing, "0" gives the most
      smoothing effect while "9" gives the least.

      "HUES"  determines how much priority is given to selecting the correct
      hue  in  relation to 2 factors: Saturation and Value.  Every color has
      a  hue,  saturation  and  value  index.    Hues determine where in the
      spectrum  of  the  rainbow,  a particular color belongs.  The spectrum
      moves  from  red-orange-yellow-green-blue-violet.    Saturation is how
      much  "white"  there  is  in  a  color while Value is how much "black"
      there  is.    The  TV  set  is  a  good  analogy for understanding the
      Hue-Saturation-Value  (HSV)  Concept.    Think  of  Hue  as the "Tint"
      control,  Saturation  as  the  "Brightness"  control  and Value as the
      "Contrast" control.

      A  Hue  Factor  of  50  will  give  50%  priority  to  Hue  and 25% to
      Saturation  and  25%  to  Value  when  looking  for the correct color.
      Depending  on  how  "rich"  your current palette is (remember you only
      have  256  colors  from  262,144  possible  colors),  changing the Hue
      Factor  will  have  a  big  impact  on  the quality of smoothing.  For
      example,  if  you  have  a picture filled with 3 different blue pixels
      but  your palette has 5 different colors with blue hues but 100 colors
      with  violet hues, then a closer match can be found with less priority
      give  to  the  Hue Factor since these violet shades may come closer to
      the  "gray"  or  "luminance" level required to smooth your image.  The
      Hue Factor can be varied from 20% to 80% in increments of 4.















      RATE  is  how  fast  the  smoothing will be performed.  The faster the
      smoothing,  the  less accurate the search for the right color will be.
      RATE  limits  where in your palette colors will be searched.  Although
      you   will  not  be  concerned  with  speed  since  you  are  changing
      individual  pixels,  this  is significant when you are selecting areas
      to  smooth  in  the  Image Processing Menu.  RATE can be varied from 4
      (fastest) to 128 (slowest) in increments of 4.


      11.  Image Processing Menu

      Selecting  the  ImgP (Image Processing) Menu option from the Main menu
      brings you here.

              ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
              ³ÚÄÄÄ¿ ÚÄÄÄ¿ ÚÄÄÄ¿ ÚÄÄÄ¿ ÚÄÄÄ¿ ÚÄÄÄ¿ ÚÄÄÄ¿ ÚÄÄÄ¿³
              ³³   ³ ³   ³ ³   ³ ³ÛÛÛ³ ³   ³ ³   ³ ³   ³ ³   ³³
              ³ÀÄÄÄÙ ÀÄÄÄÙ ÀÄÄÄÙ ÀÄÄÄÙ ÀÄÄÄÙ ÀÄÄÄÙ ÀÄÄÄÙ ÀÄÄÄÙ³
              ³ TYPE  HUES  RATE  CNVT  CONT  BLUR  KERNL  GO ³
              ³ Color Smoothing   -- Gray Image Processing -- ³
              ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

      COLOR SMOOTHING (Anti-Aliasing)

      The  "Color  Smoothing"  options  discussed  apply here.  RATE becomes
      particularly  important  if  you  intend to smooth large areas of your
      picture.    With  a  8MHz PC XT Turbo, regardless of the Hue Factor or
      Type  setting,  it  will  take  x  minutes to smooth an entire screen.
      These estimates will vary with the speed of your machine.
 
          RATE                 Estimated Time (minutes) for FULL SCREEN
          FACTOR               4.77 MHz  8 MHz     12 MHz   20 MHz
                               PC        TurboXT   PC AT    Compaq

            4                   5.2       4         2.6      1.0
            8                   9.1       7         4.6      2.8
           24                  14.3      11         7.3      4.4
           48                  23.4      18        12.0      7.2
          128                  48.1      37        24.6     14.8

      As  you  can  see, you can eat your dinner if you use RATE=128n an old
      IBM  PC  (4.77  MHz).    A  RATE  of 128 will always give you the MOST
      ACCURATE  smoothing  results.  However, I have found RATE=24 to differ
      only  very slightly from 128.  This, ofcourse, depends on the richness
      of  your  palette.  The best way to find the most effective compromise
      is  to  experiment  with  small  areas  with different settings before
      smoothing  the  entire  screen.    The total number of combinations is
      6400; you have all that flexibility.

      TO  PROCESS  ANY  GIVEN AREA (any method in this menu), determine your
      process  and  parameters  by clicking the appropriate boxes then CLICK
      "GO".    Select  a  starting  point  and drag your mouse with the LEFT
      button  pressed until you have defined a given area.  Once you release
      the  LEFT button, the area will be processed.  The processed area will
      be  highlighted by a blinking frame which you can accept with the LEFT
      mouse  button  or  reject with expected RIGHT.  If you reject, you can
      again select another area or hit the RIGHT button again to exit.  









      GRAY SCALE CONVERSION

      CoNVerT  will  convert  any  image to 6 different types.  Palettes and
      pictures  are permanently altered after conversion.  Select any of the
      option  listed  below  and click the "GO" box.  To select a conversion
      option,  keep  clicking  the  CNVT  box  until  the  desired option is
      displayed.    After  conversion,  the picture will be highlighted by a
      blinking  frame.    Hit the LEFT mouse button to accept or RIGHT mouse
      button to reject.

      "Stretched  64"  -    This is the highest gray scale resolution.  Your
      picture  will  be converted and stretched to simulate a 256 gray scale
      (although  you actually have 64 gray shades maximum).  Use this option
      before  processing  your  image.    The included palette "GRAY256.PLT"
      will view all pictures saved with this option.

      "Stretched  32"  -   This option is results in a medium yet acceptable
      gray  scale  resolution.    It  is  useful when you intend to increase
      contrast  or  use  more colors when colorizing after image processing.
      Your  image  is  converted  to  a  256  gray scale with 32 gray shades
      distributed  evenly  throughout  the  scale.    The  included  palette
      "GRAY256.PLT" will view all pictures saved with this option.
 
      "Stretched  16"  -  This option results is a low resolution gray scale
      but  with  very  high  contrast.    It  is useful for getting the most
      number  of  colors  when  colorizing.   16 gray shades are distributed
      evenly  along  a  256  gray scale.  The included palette "GRAY256.PLT"
      will view all pictures saved with this option.

      REMEMBER  TO  USE ONLY PICTURES CONVERTED WITH THE "STRETCHED" OPTIONS
      FOR  IMAGE  PROCESSING.  THE IMAGES MAY BE CORRUPTED IF YOU USE ANY OF
      THE  CONVERSION  OPTION BELOW.  THE OPTIONS BELOW ARE FOR COLORIZATION
      AND SAVING OF A PROCESSED IMAGE.

      "COLORS  16-31"  -  After  processing  your  image by using any of the
      "stretched"  gray  scales  above, use this option to change your image
      and  palette to fit the default 16 gray scale and palette that the VGA
      or  MCGA  card  initializes  to.   The image is converted as you would
      view  it under the "Stretched 16" option.  When you save an image that
      was  converted  with  this option, your image can be "Bloaded" without
      any  palette  or  loaded  into VGACAD at start-up without any palette.
      All  colors  are  converted  to fit the default 16 gray colors (COLORS
      16-31)  in  the  VGA  or  MCGA palette.  In addition, you will have 16
      color ranges to colorize your image.

      "COLORS  32-63" - This option works the same way "COLORS 16-31" option
      does  but  converts  you  image  to correspond to the colors 32 to 63.
      The  image  is  converted as you would view the "Stretched 32" option.
      Whatever  you  set  the palette to contain in those colors is what the
      picture  will  show.   The included palette "GRAY32.PLT" will show all
      pictures  converted  with  this  option.    Ofcourse,  you can use any
      palette  or  modify  "GRAY32.PLT" to your hearts content.  This option
      will allow you 8 color ranges to colorize your image.

      "COLORS  64-128"  -  This option converts your image with as you would
      view  it  with  the  "Stretched  64"  option.    The  included palette
      "GRAY64.PLT will view pictures saved under this option.









    CONTRAST STRETCHING & ENHANCEMENT

    CONTrast  Stretching  is  performed  using  a "histogram" of your pixel
    value  distribution.    Each pixel can have a gray value 0 to 255 which
    corresponds  to  each  of  the colors 0 to 255.  For this reason, it is
    important  to  use  only  the  "stretched nn" options when converting a
    picture for image processing.

    What  Contrast  Stretching does it to equalize the distribution of gray
    scales  to  evenly  span  the  range of gray values from 0 to 255.  For
    example   a   typically   unequalized  image  may  have  the  following
    distribution  of  pixels.    The low and high bins are the edges of the
    histogram  distribution.   All pixels between the edges (i.e., the high
    and low bin) will be stretched to fill the entire 256 gray range.


        N  ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
           º low                   ²²                  high      º
        P  º bin ÄÄ¿          ²   ²²²²                 bin       º
        i  º       ³         ²²   ²²²²                 ³         º
        x  º       ²     ²  ²²²²  ²²²²                 ²         º
        e  º ²     ²     ²²²²²²²² ²²²²²           ²²  ²²²        º
        l  º ²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²º
        s  ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼
           0 -------------------------127----------------------255


    After Contrast Stretching the distribution will approximate this.


        N  ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
           º                         ² ²                         º
        P  º                ²      ² ² ² ²                       º
        i  º              ² ²      ² ² ² ²                 ²     º
        x  º²     ²     ² ² ² ²    ² ² ² ²                 ²    ²º
        e  º²     ² ² ² ² ² ² ² ²  ² ² ² ² ²       ² ²  ²  ² ²  ²º
        l  º²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²º
        s  ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼
           0 -------------------------127----------------------255

    You  will  note  that the pixels now span the entire range and contrast
    is  improved.   Bright pixels will become brighter and dark pixels will
    become darker,  everything in between will be affected the same way.

    Upon  selection  of  this  option,  you  will requested for a "Minimum"
    number.    This  number is the threshold for selecting the high and low
    bins.    The  higher  the  number,  the  more likely that the bins will
    center on the middle and increase the Contrast Stretching effect.

    Since  the  histogram  distribution is based on your selected area, the
    expected  number  of pixels per gray value will be much less in smaller
    areas  than a larger area.  Selecting a large "Threshold Minimum" for a
    small  area  may  result  in  no  change since no bins will be located.
    Experiment  with  the  Threshold  Value  to see which will generate the
    desired effect.











    GRAY BLURRING (Monochrome ANTI-ALIASING)

    BLURring  or  anti-aliasing  is  used  in  the same fashion as CONTrast
    Stretching  but  with  different  results.    The  resulting  image  is
    smoothed  to  reduce the "jaggies".  The "Threshold Minimum" value here
    adjusts  the  amount  of  "spikes",  edges  or  details  that  will  be
    retained.    The  higher  this  value, the smoother your image will be;
    ofcourse,    this  will  result in blurring other details as well.  You
    will  have  to  experiment with the right "Threshold Minimum" that will
    smooth  your  picture yet keep significant detail intact.  The function
    uses  a "3x3 Pixels Averaging" algorithm with variable threshold.  This
    method  has  advantages  in  adding more gray scale values in a picture
    with  narrow  gray  scale distributions.  For example, if you converted
    an  EGA  320x200x16  color  picture,  by  using  this  method  you will
    introduce  intermediate  gray  values  between the 16 gray scales which
    will make it more lifelike and approach photographic quality.

    There  is  a  special mode.  If you select a "Threshold Minimum" of 256
    the  function  that will be used is a "3x3 Pixels Median Filter";  this
    mode  is  effective  in  removing  random  noise while maintaining edge
    details.    This  method  is  slower  than  "3x3  Pixels Averaging" but
    results  in  a  smoother picture with more edge detail.  The "downside"
    is  how  it  smooths  the  picture;  by  using  the median, it does not
    introduce any new pixel values.


    KERNEL CONVOLUTION (EDGE DETECTION & HIGH FREQUENCY BOOSTING)

    KERNeL  Convolution  will  detect  edges  in  your  picture;  there are
    several  options.   You can detect only vertical or horizontal edges or
    all  edges.    The  Kernel with the following configuration detects all
    edges:

                              ÉÍÍÍËÍÍÍËÍÍÍ»
                              º-1 º-1 º-1 º
                              ÌÍÍÍÎÍÍÍÎÍÍÍ¹
                              º-1 º 8 º-1 º
                              ÌÍÍÍÎÍÍÍÎÍÍÍ¹
                              º-1 º-1 º-1 º
                              ÈÍÍÍÊÍÍÍÊÍÍÍ¼

    This  Kernel  is a "High Frequency Boost" and results in "feeding back"
    the  edges  of your picture.  The resulting picture is much sharper but
    noisier and rougher.


                              ÉÍÍÍËÍÍÍËÍÍÍ»
                              º-1 º-1 º-1 º
                              ÌÍÍÍÎÍÍÍÎÍÍÍ¹
                              º-1 º 9 º-1 º
                              ÌÍÍÍÎÍÍÍÎÍÍÍ¹
                              º-1 º-1 º-1 º
                              ÈÍÍÍÊÍÍÍÊÍÍÍ¼

    The  center value can be varied up to 12,  this results in even greater
    boosts.  You can create "overexposed" effects with this function.
                                                                           









    All  image  processing  option  follow  the  same  user interface.  You
    select  a  starting point with the "arrow" cursor and capture a desired
    area  with the LEFT mouse button down.  After releasing the button, the
    image  is  processed and highlighted by a blinking frame for acceptance
    or  rejection.   You can then repeat the process or exit by hitting the
    RIGHT mouse button before selecting another area to process.

    This  is  only  the  beginning,  next versions will allow the design of
    your  own  KERNEL  MATRIX  as  well  as  large  matrices  for all image
    processing  functions  (e.g.,  5x5  and 7x7), and a host of other image
    processing capabilities for monochrome images and COLOR !


    12.   Edit Menu

           ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
           ³ÚÄÄÄ¿ ÚÄÄÄ¿ ÚÄÄÄ¿ ÚÄÄÄ¿ ÚÄÄÄ¿ ÚÄÄÄ¿ ÚÄÄÄ¿ ÚÄÄÄ¿³
           ³³ÛÛÛ³ ³   ³ ³   ³ ³   ³ ³   ³ ³   ³ ³   ³ ³   ³³
           ³ÀÄÄÄÙ ÀÄÄÄÙ ÀÄÄÄÙ ÀÄÄÄÙ ÀÄÄÄÙ ÀÄÄÄÙ ÀÄÄÄÙ ÀÄÄÄÙ³
           ³ AUTO  USER  EDIT  Port  90'  Horz   180'  Vert³
           ³ Size  Size  Menu  -- FLIP & CONVERT SCREEN -- ³
           ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ


    AUTO  Size  will  shrink  or  expand  any  defined area with its aspect
    ratios  intact.  Your picture will always be proportional regardless of
    your  sizing  changes.   After clicking this box, the arrow cursor will
    appear.   Select a starting point then keep the LEFT mouse button down,
    the  captured  area  will  be  higlighted  by  a dotted rectangle.  Now
    select  a  new  starting position and define an area which the captured
    image  will  either  shrink  or  expand into.  After releasing the LEFT
    mouse  button,  the  image  will  proportionally  fill  the new defined
    area.    The  shrunken  or  expanded image will then be higlighted by a
    blinking  box;  hit  the  LEFT mouse button to accept the change or the
    RIGHT  to  reject and try again.  Once you accept a change the image is
    permanently set; you cannot "undo" the change after accepting it.

    USER  Size  works the same way AUTO sizing does without maintaining the
    aspect  ratio.    Your  new image will be stretched or distorted anyway
    you  like.    This  is  particularly  useful when correcting the aspect
    ratios  of  digitized  image  when captured and/or converted from other
    graphic modes or correcting aspect ratios of your digitizer.

    FLIPPING IMAGES

    "Port"  (PORTRAIT)  will  rotate  you  entire  picture  90  degrees and
    correct  the aspect ratio automatically:  Upon selecting this feature a
    frame  will  appear which you can move around until you set the desired
    location  for  your  portrait.   This is useful for converting captured
    images  that  are  placed  sideways;  you will lose some details in the
    process (i.e., smaller picture).

                 ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿        ÚÄÄÄÄÄ¿
                 ³ÛÛÛÛÛÛÛÛÛÛÛÛÛÛ³        ³Û²²±±³
                 ³²²²²²²²²²²²²²²³  --->  ³Û²²±±³
                 ³±±±±±±±±±±±±±±³        ³Û²²±±³
                 ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ        ÀÄÄÄÄÄÙ
                      BEFORE              AFTER








    "90'"  will  flip any captured area 90 degrees.  Like portrait, it will
    correct  the  aspect  ratio  by  correcting  your  captured area into a
    perfect  square  rectangle.  Almost no detail is lost; the maximum size
    for conversion is the largest perfect square on your screen.

    "Horz"  (Horizontal  Flip)  will flip any area as you would see it in a
    mirror.  No detail is lost.

    "180'"  (180  degree  Flip)  will  flip  any  area  as you would see it
    "upside down".  No detail is lost.

    "Vert"  (Vertical  Flip)  will  flip  any area as you would see it in a
    mirror, but "upside down".  No detail is lost.


    THE EDIT SUB-MENU

    The "EDIT Menu" trasnfers you to ar "CUTTING and PASTING" menu area.

             ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
             ³ÚÄÄÄ¿ ÚÄÄÄ¿ ÚÄÄÄ¿ ÚÄÄÄ¿ ÚÄÄÄ¿ ÚÄÄÄ¿ ÚÄÄÄ¿ ÚÄÄÄ¿³
             ³³   ³ ³   ³ ³ÛÛÛ³ ³   ³ ³   ³ ³   ³ ³   ³ ³   ³³
             ³ÀÄÄÄÙ ÀÄÄÄÙ ÀÄÄÄÙ ÀÄÄÄÙ ÀÄÄÄÙ ÀÄÄÄÙ ÀÄÄÄÙ ÀÄÄÄÙ³
             ³COPY   CUT  FILE  DRAG  INVS  NORM  OVRLY  EXIT³
             ³-Clipboard- Menu  -----Paste Options-----      ³
             ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ 

    YOU  CAN  ONLY  EXIT  THIS  MENU BY CLICKING THE EXIT BOX.  "FILE Menu"
    will transfer to the file routines then return you to this menu.

    To  capture an image first choose either COPY or CUT; the latter option
    deletes  the  image  from your screen.  Move your cursor (arrow) to the
    start  of  your  image  (normally  the  upper right side) then drag the
    mouse  with  the LEFT mouse button down until you outline an area to be
    captured.    After  releasing the mouse button,  the outline will blink
    signaling  you to either accept it or reject it.  The LEFT mouse button
    will  accept  your  ClipArt while the RIGHT mouse button will reject it
    and you can try again or  hit the RIGHT mouse button again to escape.

    You  can  now  paste  it  or  save  it  to a file through the FILE Menu
    transfer.  There are 4 ways to paste a captured image.

         OVeRLaY  will  probably  be  your  most  often used mode.  It will
         paste  an  image  without  destroying  the  background.    This is
         particularly  useful  if your captured image has a BLACK (color 0)
         background.    In  effect  you will have the features of a "lasso"
         wherein  only  the  foreground  portion  of  the captured image is
         placed on the screen.

         NORMal  and  INVerSe  will  replace  any background image with the
         captured image.

         DRAG  will  continuously  OVeRLaY  your  captured  image until you
         release  the  LEFT  mouse  button.    Use this feature for special
         effects.











    As  you  probably  have  figured  out, to paste, simply select the mode
    then  place  your  cursor at a starting location.  The moment you press
    the  LEFT mouse button, the image will appear (flashing);  you can then
    move  your  captured  image  to the desired location.  Once you release
    the  LEFT  mouse  button the image will be set and a box around it will
    blink.    You  can  reject  its  current position by pressing the RIGHT
    mouse  button  or  accept  it with the LEFT mouse button.  If rejected,
    you  can  simply start all over.  You can only paste after capturing an
    image  or  retrieving  one  from  a file.  When you exit the EDIT menu,
    your image will not be saved; be sure to save it from the FILE Menu.


    13.   Shapes Menu

    Selecting the "Shapes" option brings you to this pop-up menu.

             ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
             ³ÚÄÄÄ¿ ÚÄÄÄ¿ ÚÄÄÄ¿ ÚÄÄÄ¿ ÚÄÄÄ¿ ÚÄÄÄ¿ ÚÄÄÄ¿ ÚÄÄÄ¿³
             ³³   ³ ³   ³ ³ÛÛÛ³ ³   ³ ³   ³ ³   ³ ³   ³ ³   ³³
             ³ÀÄÄÄÙ ÀÄÄÄÙ ÀÄÄÄÙ ÀÄÄÄÙ ÀÄÄÄÙ ÀÄÄÄÙ ÀÄÄÄÙ ÀÄÄÄÙ³  
             ³ FILL  LINE  HCir  HBox  FCir  FBox Curve->.05 ³<ÄÄ¿
             ³{Û²²Û²²°°²²ÛÛ²²±±²²ÛÛ²²±±²²±±²²±±ÛÛ²²±±²²±±²²±}³   ³
             ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙresolution
              {²ÛÛ²²²±±²²ÛÛ²²±±²²ÛÛ²²±±²²ÛÛ²²±±ÛÛ²²±±²²±±²²±} of splines


    HCirc  and  HBox  are  Hollow  Circles  and  Hollow Boxes respectively.
    FCirc and FBox are Filled Circles and Filled Boxes respectively.

    As  a  rule,  hitting  the  RIGHT  button will first abort placing your
    shape.    Hitting  the RIGHT button with the "arrow" cursor exits.  The
    LEFT button constructs or sets a constructed shape.

    There  are  two  shapes  that  are  supported  -  circles/ellipses  and
    rectangles;  which  may  be  filled  or  hollow.     Filled circles and
    rectangles  use  the selected foreground color.  Select the appropriate
    box  and  place  your  cursor  at any starting position (normally upper
    right  for  rectangles  or  center  for ellipses).  Filled shapes paint
    over  the  current  screen  up  to borders with the selected foreground
    color regardless of the image.
  
    For  circles,  ellipses  and  rectangles,  drag your cursor keeping the
    LEFT  mouse  button down; dragging the cursor down increases the lenght
    of  the  rectangle  or  Y  radius  of  an  ellipse; moving to the right
    increases  the  width  of  a  rectangle  or the X radius of an ellipse.
    When  you are satisfied with the size and shape, release the LEFT mouse
    button.    You  can  place your new shape anywhere by moving your mouse
    even  if  an  ellipse/circle was partially clipped during construction;
    hit the LEFT button to set its position or RIGHT button to abort.

    LINEs  begin  when  you  hit  the  LEFT  mouse  button and end when you
    release  it.    Once  released  the  line  will  blink  in the selected
    foreground  color.    Hitting the LEFT mouse button sets the line while
    the RIGHT aborts.












    FILL  will only fill colors in a replace mode.  THE SELECTED FOREGROUND
    COLOR  WILL  PAINT  OVER  ALL CONNECTED PIXELS THAT HAVE THE SAME COLOR
    UNDER  THE  ARROW  CURSOR.   It is a very selective fill routine; thus,
    you  can pick any enclosed or filled region and it will treat the color
    under the "arrow" as the boundaries of that region.

    CURVE  will  let  you plot up to 16 points connected by straight lines.
    You  can  plot  less  than 16 by hitting the RIGHT mouse button.  After
    plotting  your  16th point or escaping with the RIGHT mouse button, the
    program  will  calculate splines to connect all your point.  The number
    beside  "Curve->"  is  the  degree of resolution;  the lower the number
    the  smoother  your  curves  will  be  (it  will  also  take  longer to
    calculate).   During calculation you will hear random beeps to tell you
    that  it is working.  You can UNDO your curves by "UNDOing" at the MAIN
    MENU.


    14.   Text Menu

             ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
             ³ÚÄÄÄ¿ ÚÄÄÄ¿ ÚÄÄÄ¿ ÚÄÄÄ¿ ÚÄÄÄ¿ ÚÄÄÄ¿ ÚÄÄÄ¿ ÚÄÄÄ¿³
             ³³   ³ ³   ³ ³ÛÛÛ³ ³   ³ ³   ³ ³   ³ ³   ³ ³   ³³
             ³ÀÄÄÄÙ ÀÄÄÄÙ ÀÄÄÄÙ ÀÄÄÄÙ ÀÄÄÄÙ ÀÄÄÄÙ ÀÄÄÄÙ ÀÄÄÄÙ³
             ³NORM  INVS  NORM  INVS   MIX   ---- COLOR  ----³
             ³--Overlay-- ----Replace------        BAR       ³
             ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

    At  present  there  is  only one font - the system font.  You can place
    text  anywhere  on  your  screen  in  5 different ways, in any selected
    color.  Future versions will load different fonts.

    COLOR  BAR  will activate the upper and lower color bars for foreground
    and  background  color  selection.    This  is  particularly useful for
    selecting MIXED color text.

    NORMal  (Overlay) will write over your image in the selected foreground
    color  without  destroying  the  background.  Thus an "O" will have the
    image still showing through its center.

    INVerSe  (Overlay)  will  place  an  inverse  letter  in  the  selected
    foreground color without destroying the background.

    NORMal  (Replace)  is  the  typical  way  BASIC would place text on the
    screen - destructively - background is not preserved.

    INVerSe (Replace) will, destructively, place the inverse font image.

    MIXed  (Replace)  will  place  text  with  both the selected foreground
    color  and  background.   Thus, you can have text with Blue backgrounds
    with Yellow foregrounds, and so on...

    To  place  text  on  your  screen,  first select the mode and drag your
    cursor  out  of  the  menu area - the screen will return to your normal
    image.    An inverse box will appear as your cursor.  Place this cursor
    at  the  starting point of for placing your text and hit the LEFT mouse
    button.    A  rectangular  box will now appear and you can begin typing
    your text.









    Text  will "wraparound" and go to the next line.  Pressing the <return>
    key  will move the cursor to the next line.  <Backspace> will undo your
    typos  and restore the original screen image.  Press <Esc> to keep your
    text  and  move  on  to a new location and repeat the process.  You can
    always "undo" everything when you return to the Main menu.

    To  be  able to go back and change your text to different colors at the
    their  present positions,  I suggest always starting your cursor at the
    "HOME"  position  which is the upper-right corner (just move your mouse
    up  to upper right corner until it will stops).  Then move around using
    <return>.    If  you are in any of the two "Overlay" modes you can move
    the  cursor  forward  with  the  <SpaceBar>  and your image will not be
    touched.    This  ensures  that all text is in perfect alignment should
    you wish to type over and change colors with their exact positions.


    15.   File Menu

    Selecting the file option will pop-up this menu.

           ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
           ³ÚÄÄÄ¿ ÚÄÄÄ¿ ÚÄÄÄ¿ ÚÄÄÄ¿ ÚÄÄÄ¿ ÚÄÄÄ¿ ÚÄÄÄ¿ ÚÄÄÄ¿³
           ³³   ³ ³   ³ ³ÛÛÛ³ ³   ³ ³   ³ ³   ³ ³   ³ ³   ³³
           ³ÀÄÄÄÙ ÀÄÄÄÙ ÀÄÄÄÙ ÀÄÄÄÙ ÀÄÄÄÙ ÀÄÄÄÙ ÀÄÄÄÙ ÀÄÄÄÙ³
           ³.BLD  .PLT  .CLP   List  Load  Save Clear  EXIT³
           ³ ---FileType----                               ³
           ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

    Clear  will  clear your screen and everything you did will be lost.  Do
    not select this box unless you have saved your work.

    Over  "FileType"  are  three  types  of  extensions.  You must select a
    filetype before LISTing, SAVing or LOADing.

         ".BLD"  are  "BLoaDable"  pictures  that correspond to the typical
         BASIC format and can be used in other BASIC programs.

         ".PLT"  are  "PaLeTte"  files,  also in a "bloadable" format which
         can  be  used to save and restore ranges of palette information by
         using  one BIOS call to reactivate the whole palette.  It is saved
         in a compatible format to call such an interrupt.

         ".CLP"  are  "CLiP"  art  files;  basically these are cutouts that
         were  captured  with  the  BASIC "GET" command and can be reloaded
         with  the "PUT" command in another BASIC program. ".CLP" art files
         cannot  be  LISTED,  SAVED  or  LOADED  unless you invoke the File
         Sub-Menu from the EDIT menu;  an error warning will remind you.

    "LIST"  will  list  all  files with the selected extension (BLD, PLT or
    CLP);  no other extensions are permitted.  If there are more files that
    the  screen  will hold, then click "LIST" again for the remaining files
    until you reach the end and the list cycles from the beginning.














    To  change  your  drive  or  sub-directory  click the word PATHNAME and
    key-in  your new drive and/or sub-directory.  The incorrect syntax will
    result  in a warning beep and reject your input.  Below are examples of
    correct pathnames:

                         A:\MYDISK\
                         B:\
                         C:\VGACAD\PICS\

    Notice that all pathnames must end with a backslash.

    Save  and  Load  will load a PALETTE (.PLT), BLOADABLE SCREEN (.BLD) or
    CLIPART  (.CLP) file into memory.  Once you select this box, an inverse
    cursor  will appear; use that cursor to highlight the filename that you
    want  to save or load.  If the filename does not exists (i.e., you want
    to  create  a new file) then click the word FILENAME and enter any name
    up  to eight letters long.  Incorrect filename lengths will also result
    in  a  warning  beep  and  reject your input.  Once you have selected a
    filename  by  either highlighting it or keying-in a new name, click the
    "OK"  box  and  your  filename  will be saved or loaded.  A single beep
    followed  by  a  change  in  the "OK" sign means all is well.  A second
    beep with a lower tone means you did not select any filename.

    "Exit" will bring you back to where you were.

    "End"  will  terminate  the program and and will ask you if you want to
    return  to DOS.  A "Y"es response will terminate the program, any other
    response will bring you back to this file menu.


    16.  VGACAP (Screen Capture Utility)

    VGACAP  is  a  terminate-stay-resident (TSR) utility that allows you to
    capture  the 256 color palette and screen in the 320x200x256 color mode
    and  save  both the palette and screen in "Bloadable" formats.  You can
    convert  ANY picture (.GIF of Compuserve, .PCX of PCPaintbrush, .PIC of
    Windows  Paint+, .LBM  of DeluxePaint II or any other viewable picture)
    to  the  "Bloadable" (.BLD and .PLT) format used by BASIC.  ANY PICTURE
    (320x200x256color)  THAT  YOU  CAN  VIEW  CAN  BE CONVERTED TO THE .BLD
    FORMAT.   In this respect it is "universal".  There are many viewers in
    the  Public  Domain that read virtually every format (notable is OPTIKS
    by  K.Graham for different formats, VGAGIF by M. Vigneau and VGIF by B.
    Montgomery  for  VGA  pictures in GIF files); use these viewers to view
    different formats then capture your picture with VGACAP.

    VGACAP  uses less than 2k of your free memory. Simply run VGACAP before
    entering  your  painting/CAD  or  digitized  picture  viewer.     After
    loading,    press  <Alt-F10>, while viewing your picture in any viewing
    or  drawing/paint/CAD program.  Your current screen and palette will be
    saved  in your default drive and directory in the standard Bsave format
    for all BASIC programs.















    The  first  time  you  run  the  program  it  will save your screen and
    palette  to  SCREEN00.BLD and SCREEN00.PLT respectively.  The former is
    the  actual picture data while the latter is the palette (the 256 color
    selection  from  256K  combinations).    It  will  then  save  up to 99
    pictures  (i.e.,  SCREEN99.BLD  and  SCREEN99.PLT).    If  there  is an
    existing  SCREENxx.BLD  or SCREENxx.PLT file, then it will increment to
    the  next  higher  number.    This  can  be  confusing  if you keep the
    captured  files  without  renaming  them  since  you can have unmatched
    screens  and  palettes.    You can use your favorite memory managers to
    remove this TSR or reboot to release it from memory.

    When  in  DOS or using a picture viewer or application which requires a
    keypress  to  continue,  it  is necessary to hit any key or a specified
    key  (e.g.,  spacebar  or  return)  after  hitting  the 'HOTKEY' before
    VGACAP  saves  the screen and palette.  After capturing any screen, you
    can  then  rename  the captured files or load them directly into VGACAD
    and save edited pictures (BLD and PLT files) under new names.


    17.  CGA2VGA (Screen Capture & Convert Utility)

    CGA  (Color  Graphics  Adaptor)  used to be the most popular format for
    color  pictures  on  IBM and compatibles; as such, massive libraries of
    CGA  pictures are available or are in your personal libraries.  This is
    particularly  true  for  various  "ClipArt"  pictures  used  in desktop
    publishing  or  other  uses.    For  example,  you  may  have amassed a
    collection  of PrintShop clips (which are primarily in CGA) and now you
    would  want  to  convert  and  latter  extend  the color range of these
    picture.    CGA2VGA  will  capture and convert ANY VIEWABLE CGA picture
    and  convert  it  to a 256 color picture in the same "Bloadable" format
    as VGACAP does.  This can then be edited with VGACAD or in BASIC.

    CGA2VGA  need 64k of your free memory and saves pictures in the 4 color
    graphics  mode.   CGA2VGA works the same way VGACAP does.  The "Hotkey"
    is  <Alt-F2>.    CGA2VGA  does  not  save  any palette; when you load a
    picture  captured  with CGA2VGA it will have 4 colors (Color 0-3).  You
    can  convert  these  colors  to  other  colors  (using Replace and Swap
    functions  for  global  color  changes)  or extend their range with the
    image processing functions or simply add new colors to the picture.


    18.   Registration

    You  can  expect MAJOR improvements in the versions to come.  There are
    algorithms  for 3D and 2D transformations, gradient fills and patterns,
    more  image  processing,  extensive  palette  management  routines  and
    saving  and  loading  in  different  picture  formats/standards; all of
    these  routines  are  in  "C"  or  assembly and work very fast.  If you
    continue  to  support  maverick  authors  like  us, we will continue to
    develop  this  product  like nothing ever seen in commercial packages -
    otherwise  it  will,  as many (sigh!) good "shareware" packages have to
    go commercial or simply "die" from lack of support.

    Registration  for  this  program  is  soooo  cheap  (I  mean  cheap not
    inexpensive  !); it seems ridiculously low - a measly sum of $8.95 (the
    cost of 2 magazines).










    For  $14.95 you will be entitled to the latest update of VGACAD without
    those  20  minute  reminders.  Also, you will be entitled to the latest
    update of the following utilities to support VGA graphics:

         1)   VGACAP (included in this package)

         2)   CGA2VGA (included in this package)

         3)   VGABLD  (BASIC  source  included  in  this  package)  -  This
              utility views captured pictures.

         4)   BLD2GIF  -  This  NEW  utility  converts ANY viewable VGA pic
              (320x200x256  colors) or VGACAD pics to CompuServe's Graphics
              Interchange  Format  or  GIF files; this format allows you to
              port  your  pics  to  non-IBM  machines  (Macintosh, Amiga or
              Atari)  in  different  graphic  modes,  making  your  picture
              universally accessible by everyone.

         5)   VGAPRN  -  This  NEW  utility prints ANY viewable 320x200x256
              color  pic  or  VGACAD  pic in 7 user-selected gray shades on
              Epson or IBM compatible dot matrix printers.

    For  $19.95  you  will  be  entitled to the next TWO (2) updates of the
    latest  of everything; this means that from the date of receipt of your
    registration  we will send you the latest version of VGACAD and all the
    related  utilities  developed  and  a  premier  copy of any new utility
    developed  as  well  as the next releases of all the aforementioned and
    any new fonts (with the font editor) and Clipart files when available.

    In  the  pipeline  is  QBVGA an extensive library of QuickBASIC VGA 256
    color  graphics  routines,  VGASHW  (graphics  presentation  program to
    showoff  your  captured  pics  or  your  own paintings/design), EGA2VGA
    (converts  EGA  640x350x16  color  pics to VGA 320x200x256 color pics),
    and  VGA3DM  (a 3D wire-frame object editor with hidden surface removal
    and shading for including models in VGACAD).

    Hurry!    Support  us  and  we will keep developing.  Send registration
    form and a check made payable to:

                             Dr. Marvin Gozum
                      2 Independence Place Apt. 303-2
                            6th & Locust Street
                          Philadelphia, PA 19106
























                         Palette Organization Map
                                Appendix A


The  following  diagram  shows where each of the 255 color registers of the
256  color  palette  are  located.  Please note the inverse color relation-
ships  for  each  color  box.   For example, if you are modifying color 13,
you  must ensure that color 242 is significantly different that color 13 to
maintain cursor visibility when placed over either color 13 or 242.

A  16  color  set is a line of 16 colors as illustrated below.  Colors 0 to
16 is considered a color set, as well as colors 255 to 240 or 48 to 63.


                                                                               
ÄÄÄÂÂÄÄÄÂÂÄÄÄÂÂÄÄÄÂÂÄÄÄÂÂÄÄÄÂÂÄÄÄÂÂÄÄÄÂÂÄÄÄÂÂÄÄÄÂÂÄÄÄÂÂÄÄÄÂÂÄÄÄÂÂÄÄÄÂÂÄÄÄÂÂÄÄÄ
  0³³  1³³  2³³  3³³  4³³  5³³  6³³  7³³  8³³  9³³ 10³³ 11³³ 12³³ 13³³ 14³³ 15
ÄÄÄÙÃÄÄÄÙÃÄÄÄÙÃÄÄÄÙÃÄÄÄÙÃÄÄÄÙÃÄÄÄÙÃÄÄÄÙÃÄÄÄÙÃÄÄÄÙÃÄÄÄÙÃÄÄÄÙÃÄÄÄÙÃÄÄÄÙÃÄÄÄÙÃÄÄÄ
255 ³254 ³253 ³252 ³251 ³250 ³249 ³248 ³247 ³246 ³245 ³244 ³243 ³242 ³241 ³240
ÄÄÄÂÅÄÄÄÂÅÄÄÄÂÅÄÄÄÂÅÄÄÄÂÅÄÄÄÂÅÄÄÄÂÅÄÄÄÂÅÄÄÄÂÅÄÄÄÂÅÄÄÄÂÅÄÄÄÂÅÄÄÄÂÅÄÄÄÂÅÄÄÄÂÅÄÄÄ
 16³³ 17³³ 18³³ 19³³ 20³³ 21³³ 22³³ 23³³ 24³³ 25³³ 26³³ 27³³ 28³³ 29³³ 30³³ 31
ÄÄÄÙÃÄÄÄÙÃÄÄÄÙÃÄÄÄÙÃÄÄÄÙÃÄÄÄÙÃÄÄÄÙÃÄÄÄÙÃÄÄÄÙÃÄÄÄÙÃÄÄÄÙÃÄÄÄÙÃÄÄÄÙÃÄÄÄÙÃÄÄÄÙÃÄÄÄ
239 ³238 ³237 ³236 ³235 ³234 ³233 ³232 ³231 ³230 ³229 ³228 ³227 ³226 ³225 ³224
ÄÄÄÂÅÄÄÄÂÅÄÄÄÂÅÄÄÄÂÅÄÄÄÂÅÄÄÄÂÅÄÄÄÂÅÄÄÄÂÅÄÄÄÂÅÄÄÄÂÅÄÄÄÂÅÄÄÄÂÅÄÄÄÂÅÄÄÄÂÅÄÄÄÂÅÄÄÄ
 32³³ 33³³ 34³³ 35³³ 36³³ 37³³ 38³³ 39³³ 40³³ 41³³ 42³³ 43³³ 44³³ 45³³ 46³³ 47
ÄÄÄÙÃÄÄÄÙÃÄÄÄÙÃÄÄÄÙÃÄÄÄÙÃÄÄÄÙÃÄÄÄÙÃÄÄÄÙÃÄÄÄÙÃÄÄÄÙÃÄÄÄÙÃÄÄÄÙÃÄÄÄÙÃÄÄÄÙÃÄÄÄÙÃÄÄÄ
223 ³222 ³221 ³220 ³219 ³218 ³217 ³216 ³215 ³214 ³213 ³212 ³211 ³210 ³209 ³208
ÄÄÄÂÅÄÄÄÂÅÄÄÄÂÅÄÄÄÂÅÄÄÄÂÅÄÄÄÂÅÄÄÄÂÅÄÄÄÂÅÄÄÄÂÅÄÄÄÂÅÄÄÄÂÅÄÄÄÂÅÄÄÄÂÅÄÄÄÂÅÄÄÄÂÅÄÄÄ
 48³³ 49³³ 50³³ 51³³ 52³³ 53³³ 54³³ 55³³ 56³³ 57³³ 58³³ 59³³ 60³³ 61³³ 62³³ 63
ÄÄÄÙÃÄÄÄÙÃÄÄÄÙÃÄÄÄÙÃÄÄÄÙÃÄÄÄÙÃÄÄÄÙÃÄÄÄÙÃÄÄÄÙÃÄÄÄÙÃÄÄÄÙÃÄÄÄÙÃÄÄÄÙÃÄÄÄÙÃÄÄÄÙÃÄÄÄ
207 ³206 ³205 ³204 ³203 ³202 ³201 ³200 ³199 ³198 ³197 ³196 ³195 ³194 ³193 ³192
ÄÄÄÂÅÄÄÄÂÅÄÄÄÂÅÄÄÄÂÅÄÄÄÂÅÄÄÄÂÅÄÄÄÂÅÄÄÄÂÅÄÄÄÂÅÄÄÄÂÅÄÄÄÂÅÄÄÄÂÅÄÄÄÂÅÄÄÄÂÅÄÄÄÂÅÄÄÄ
 64³³ 65³³ 66³³ 67³³ 68³³ 69³³ 70³³ 71³³ 72³³ 73³³ 74³³ 75³³ 76³³ 77³³ 78³³ 79
ÄÄÄÙÃÄÄÄÙÃÄÄÄÙÃÄÄÄÙÃÄÄÄÙÃÄÄÄÙÃÄÄÄÙÃÄÄÄÙÃÄÄÄÙÃÄÄÄÙÃÄÄÄÙÃÄÄÄÙÃÄÄÄÙÃÄÄÄÙÃÄÄÄÙÃÄÄÄ
191 ³190 ³189 ³188 ³187 ³186 ³185 ³184 ³183 ³182 ³181 ³180 ³179 ³178 ³177 ³176
ÄÄÄÂÅÄÄÄÂÅÄÄÄÂÅÄÄÄÂÅÄÄÄÂÅÄÄÄÂÅÄÄÄÂÅÄÄÄÂÅÄÄÄÂÅÄÄÄÂÅÄÄÄÂÅÄÄÄÂÅÄÄÄÂÅÄÄÄÂÅÄÄÄÂÅÄÄÄ
 80³³ 81³³ 82³³ 83³³ 84³³ 85³³ 86³³ 87³³ 88³³ 89³³ 90³³ 91³³ 92³³ 93³³ 94³³ 95
ÄÄÄÙÃÄÄÄÙÃÄÄÄÙÃÄÄÄÙÃÄÄÄÙÃÄÄÄÙÃÄÄÄÙÃÄÄÄÙÃÄÄÄÙÃÄÄÄÙÃÄÄÄÙÃÄÄÄÙÃÄÄÄÙÃÄÄÄÙÃÄÄÄÙÃÄÄÄ
175 ³174 ³173 ³172 ³171 ³170 ³169 ³168 ³167 ³166 ³165 ³164 ³163 ³162 ³161 ³160
ÄÄÄÂÅÄÄÄÂÅÄÄÄÂÅÄÄÄÂÅÄÄÄÂÅÄÄÄÂÅÄÄÄÂÅÄÄÄÂÅÄÄÄÂÅÄÄÄÂÅÄÄÄÂÅÄÄÄÂÅÄÄÄÂÅÄÄÄÂÅÄÄÄÂÅÄÄÄ
 96³³ 97³³ 98³³ 99³³100³³101³³102³³103³³104³³105³³106³³107³³108³³109³³110³³111
ÄÄÄÙÃÄÄÄÙÃÄÄÄÙÃÄÄÄÙÃÄÄÄÙÃÄÄÄÙÃÄÄÄÙÃÄÄÄÙÃÄÄÄÙÃÄÄÄÙÃÄÄÄÙÃÄÄÄÙÃÄÄÄÙÃÄÄÄÙÃÄÄÄÙÃÄÄÄ
159 ³158 ³157 ³156 ³155 ³154 ³153 ³152 ³151 ³150 ³149 ³148 ³147 ³146 ³145 ³144
ÄÄÄÂÅÄÄÄÂÅÄÄÄÂÅÄÄÄÂÅÄÄÄÂÅÄÄÄÂÅÄÄÄÂÅÄÄÄÂÅÄÄÄÂÅÄÄÄÂÅÄÄÄÂÅÄÄÄÂÅÄÄÄÂÅÄÄÄÂÅÄÄÄÂÅÄÄÄ
112³³113³³114³³115³³116³³117³³118³³119³³120³³121³³122³³123³³124³³125³³126³³127
ÄÄÄÙÃÄÄÄÙÃÄÄÄÙÃÄÄÄÙÃÄÄÄÙÃÄÄÄÙÃÄÄÄÙÃÄÄÄÙÃÄÄÄÙÃÄÄÄÙÃÄÄÄÙÃÄÄÄÙÃÄÄÄÙÃÄÄÄÙÃÄÄÄÙÃÄÄÄ
143 ³142 ³141 ³140 ³139 ³138 ³137 ³136 ³135 ³134 ³133 ³132 ³131 ³130 ³129 ³128
ÄÄÄÄÁÄÄÄÄÁÄÄÄÄÁÄÄÄÄÁÄÄÄÄÁÄÄÄÄÁÄÄÄÄÁÄÄÄÄÁÄÄÄÄÁÄÄÄÄÁÄÄÄÄÁÄÄÄÄÁÄÄÄÄÁÄÄÄÄÁÄÄÄÄÁÄÄÄ


















                     How to Colorize Gray Shade Images
                                Appendix B


    False  Colorization is the process by which you are now viewing Black &
    White  movie classics like "The Wizard of OZ" in living color.  You can
    do  the  same  thing, particularly if you own a digitizer that supports
    gray  scales.    I  have  selected  16 gray shades as the main focus of
    VGACAD's  support,  primarily  since it is aimed at the low-end market.
    If  you  want  to colorize gray images with more that 16 shades use the
    ColorBAR (CBAR) option to change the range of local colors.

    Let  us colorize one of the famous GIF pics in BBSs - MONROE.GIF (which
    is being distributed with Michael Vigneau's VGAGIF in VGADEMO.arc).

    MONROE.GIF  is  a  16 gray level picture with colors 0 to 15 containing
    the  entire  gray  scale.    The  first  thing to do is to increase the
    number of gray scale elements.  From the IMAGES menu:

         1)   Convert  (CNVT)  the  picture  into the "Streched 64" format.
              This  will give you the maximum range of gray levels although
              the picture will remain unchanged.

         2)   Next  BLUR  the  picture with a Threshold "Minimum =12"; this
              will  smoothen  the picture yet keep most of the edge detail.
              The  smoothing  will introduce intermediate gray scale values
              making  your  picture  richer.    You  will  notice "salt and
              pepper"  random  noise;  these are the edges or "spikes" that
              were not touched to keep details.

         3)   Now  BLUR  the  picture  using  the  "3x3  Median"  filter by
              reaching  a  Threshold  "Minimum =256".  All the noise should
              now be gone and the picture should be smoother.

         4)   Covert  (CNVT) the picture into "Colors 64 - 127);  this will
              now change all your pixels to correspond to colors 64 - 127.

    Now  that  you  have  a  good gray scale image (you can experiment with
    various  settings  and  techniques to enhance the picture even further)
    the next task is to color the picture.

    Load  the  "GRAY64.plt",  which is included in your disk.  This palette
    has  4  ranges  of  64  colors  each.   Flesh tones and hair color have
    already  been  created  with  the DIGI function.  Without this palette,
    you  would  have  to  create  your  own  color  ranges  by  editing the
    "anchors"  of  each range with the RGB palette boxes then using DIGI to
    spread  the  colors  between  the  range (i.e., between the "anchors").
    Using the DIGI function is explained fully in this manual.

















    Since  you  are  using 64 color ranges, click the COLOR menu and select
    ColorBAR  (CBAR); keep clicking until the color range is 64; each click
    will  cycle  through  16,  32 then 64 color bars.  Now with the "scroll
    arrows"  make  the lower color bar show the 64 gray scale and the upper
    color  bar  the  64 skin tone scale.  Click the AREA colorize function.
    An  arrow  will  appear.    Select any starting position in the picture
    (e.g.,  the  torso) and by keeping the LEFT mouse down, capture an area
    to  colorize.    After  releasing  the  button,  all gray colors in the
    captured  area  will  be  replaced  with  the  corresponding skin tone.
    Repeat  the  process  until you have colorized most of the flesh areas;
    try  to  avoid  as  much  of  the  hair  and  background as possible by
    colorizing small areas near the hair and background.

    You  now  should  have  colorized  most  of  the  flesh areas with many
    overlaps  with  the  background and hair.  Exit and go bak to the COLOR
    menu  and select ZOOM.  Use zoom to colorize or "uncolorize" individual
    pixels  that  have  these  unwanted  overlaps.  Remember that the upper
    color  bar  will  always  replace each corresponding color in the lower
    color  bar,  so by having the gray scale on top of the flesh tone scale
    you  will  be able to "uncolorize" the overlapping regions.  Repeat the
    "ZOOM" editing process for each overlapping area.

    What  you have just done for all of the flesh areas can now be done for
    the  hair  the  lips  and  the  background.  Interpreting when the hair
    stops  and the background begins will be a matter of judgement; this is
    where  the  art  comes in.  Most of the art is in modifying the palette
    with  the DIGI function to get the right shades for blonde hair or skin
    tones.    Your monitor's contrast and brightness levels will affect how
    you interpret these shades.

    With  the  new color smoothing functions, use the SMOOTH mode in "ZOOM"
    editing to smooth the transition of colors (e.g., lips, hair).

    For  reference  skin  shades  use VGACAP to capture the palettes of GIF
    pics  like LYNNEA.GIF and LISAW.GIF from your favorite BBS; examine and
    analyze  the  palettes  for  different  skin shade combinations and jot
    these  down  the  RGB  numbers  for  reference  or  use them to build a
    library of palettes.

    By  using  CGA2VGA  you  can  capture and convert your old libraries of
    4-color  CGA pictures, expand the gray levels as we did with MONROE.GIF
    and colorize them.  Keep experimenting, that is where the fun is.

    GIF   and   "Graphics   Interchange  Format"  are  trademarks  (tm)  of
    CompuServe Inc., an H&R Block Company.