The  following  are the known patches for DOUBLEDOS version  4.0.  You 
     should  always work with a copy of the file and not the original.  The 
     DEBUG  program should be available via path or be  called  explicitly. 
     The patch dialog would be something like the following:

     C:\dirname\>DEBUG DOUBLED2.PGM (may also be called DOUBLEDO.PGM)
     -       enter changes as specified in patch
     -W
     writing xxxx bytes
     -Q

     ----------------------------------------------------------------------

     Revert to old version 'V' of DoubleDOS
     COPY A:\DBLDVPGM.DRV C:\dirname\DOUBLED2.PGM (or DOUBLEDO.PGM)
     note: this is not a permanent change. re-installing the program will
     restore it to version 4.0

     ----------------------------------------------------------------------

     Hewlett Packard Vectra                                         1/14/87
     -E 85D5 F5        (old value BA)
     note: will not work with International Quartz laptop after this patch.

     ----------------------------------------------------------------------

     very slow printing w/clock or interrupt
     -E 116 EA 83      (old values 6E B0)
     -E 24A9 21 90     ( "    "    E8 BD)
     note: only use with clock or interrupt when very slow printing occurs.

     ----------------------------------------------------------------------

     IBM DOS 3.3                                                    4/24/87
     -E 2130 20        (old value 10)
     -E 878C C0 A1     ( "    "   41 81)
     -E 8B7D 03 50     ( "    "   6C 4C)
     -E 9487 7F FF B7 6E 20 80 C2 ( " " A7 E0 C5 32 0B 33 FF)
     note: will not work with any other operating system after this patch.

     ---------------------------------------------------------------------

     Columbia DOS 3.20
     -E 8B7D CE        (old value 6C)
     note: will not work with any other operating system after this patch.

     ---------------------------------------------------------------------

     Drives with volumes larger than 32 megabytes
     -E 4E3A 5F B8     (old values 5C F8)

     ---------------------------------------------------------------------

     COMx=BOTTOM 
     -E 1237 1F         (old value 1B)
     -E 1256 1F         ( "    "   1B)
     note: caused junk to be written to random locations in memory.

     ---------------------------------------------------------------------

     Sanyo MBC-990                                                  7/2/87
     -E 99DB 12 09     (old values 8E B4)
     note: problem is due to a hardware bug. this patch removes an I/O
     word read instruction that fails on the Sanyo.

     ---------------------------------------------------------------------

     IBM PS/2 model 30                                             4/28/87
     -E 9075 BA 42 21   (old values 47 FE 45)
     -E 9829 09 71      ( "    "    E0 F8)
     -E 982E AF 3A 58 A9 ("    "    47 87 3D D0)
     note: since this machine requires DOS 3.3, the patch for that will 
     also be needed.

     ---------------------------------------------------------------------

     REMM.SYS and other expanded ram boards                         8/4/87
     -E 1AA1 83 E3 E0 38 D2 9C A0 56 0D
                        (old values 23 19 E8C6 3A 81 B8 01 93)
     -E 2366 63 81 95 43 10 AF 12 FD
                        (old values 47 81 FC D0 31 2E 7C 96)
     note: the symptom is that DoubleDOS will work correctly without the
     expanded driver present, but will fail with it installed.

     ---------------------------------------------------------------------