The following are the known patches for Disk Optimizer. You should always
work with a copy of the file and not the original. The DEBUG program should
be available via path or be called explicitly. The patch dialog would be
something like the following:

C:\dirname\>DEBUG OPTIMIZE.PGM
-       enter changes as specified in patch
-W
writing xxxx bytes
-Q

-------------------------------------------------------------------------
Stops at 'testing dma to selected drive'                          12/4/86
-E 2698 3A CC 6E 93 D4 B0
-E 26D2 61 D3 7A FF
note: If drive is improperly set up, this may take up to 1/2 hour.
-------------------------------------------------------------------------
Gives message 'crosslinked clusters' during part 3
-E 1B7B F1
note: make sure CHKDSK is reporting no errors
-------------------------------------------------------------------------
CHKDSK says 'probable non-DOS disk'
-L 0 2 1 1     (if drive d, use 3 not 2)
-D 0           (retain these values just in case)
-E 0 (values as below)
      Hard Disk   - F8 FF FF
      9 sector, ds- FC FF FF
      9 sector, ss- FD FF FF
      8 sector, ss- FE FF FF
      8 sector, ds- FF FF FF
-W 0 2 1 1
note: THIS IS INHERENTLY DANGEROUS. DO NOT USE THIS PATCH UNLESS YOU HAVE A
SENIOR SUPPORT PERSON ASSISTING.
--------------------------------------------------------------------------