Fixing a Bug in the AT's ROM BIOS

			  Michael J. Markowitz
		      Department of Math. Sciences
			Loyola Univ. of Chicago
			   Chicago, IL	60615
			     (312) 508-3567

After installing an 18MHz crystal in my AT, it scored between 8.4 and 9.4
on Peter Norton's SYSINFO (SI) benchmark, i.e., it clocked in at roughly
8.5 times the speed of an IBM PC.  That's 50% faster than a standard
factory-shipped AT!  But I had one problem--approximately 1 out of every
10 floppy disk accesses would result in a "Disk Read Error" and I'd see
the familiar "Abort, Retry, Ignore?" prompt.  While the retry option
always worked, the interruption of long batch commands began to drive me
crazy.	(I had had absolutely no trouble with the floppy drive prior to
installing the new crystal.)

Checking with a friend at a major software house, I found that this
problem is quite common in speeded-up AT's and that most users have just
learned to live with it.  I considered reinstalling the original crys-
tal, but having become accustomed to "real" speed, could not quite bring
myself to do it.  So suspecting that the problem was in the software--
not the hardware--I began poking around in the ROM BIOS listing in the
Technical Reference Manual and found what I believe is the cause of the
errors.

In the handling of disk I/O requests, the INT 13h service routine goes
into several timing loops while waiting for a response from the NEC
floppy disk controller.  If the NEC fails to respond (via a hardware
interrupt) within a certain time period, the routine "times out" and
returns an error code.	One of these loops (in the WAIT_INT routine)
repeats at most 256K times and would require 25 clock cycles per iter-
ation if executed on an Intel 8088.  On an IBM PC running at 4.77 MHz,
where each clock cycle takes 210 nanoseconds, this would represent a
maximum delay of 2.09 seconds.	A comment in the AT ROM BIOS states that
this loop provides a delay of 2 seconds.  It seems that the folks at IBM
forgot that they were writing code for an 80286 running at 6MHz!

Although incorrectly coded, this timing loop seems barely adequate for
the proper functioning of a standard AT.  Install a faster crystal,
however, and it executes much more quickly, providing a delay which
is often too short for the detection of a response from the (inde-
pendently clocked) floppy disk controller.

It seemed to me that the simplest solution was to write a short routine
which attaches itself permanently to DOS and intercepts all disk I/O
requests through INT 13h (SEE *).  When activated, this routine simulates the
original software interrupt, then checks to see if the BIOS routine has
returned an error code.  If so, and it's a timeout error, the INT 13h (SEE *)
request is repeated, otherwise control returns to the caller.  By the
second request the NEC controller should have issued the expected ack-
nowledgement.

Placing FIXDSK in your autoexec.bat file should completely eliminate
disk access errors.  It has been tested and found to work on three
different AT's, with their original ROMs and crystals ranging in speed
from 16 to 18MHz.  It has not been tested with the BIOS in the new 30MB
AT.

* NOTE: FIXDSK.ASM modified 12/22/85 by C. Washburn to use INT 40H instead of
  13H, and to restore contents of AH when retrying. INT 40H change was based
  the notion that NOTHING should get in the Fixed Disk INT 13H code path if
  at all possible! INT 40H is the relocated address of the BIOS Diskette code,
  after the Fixed Disk Controller ROM installs itself, and is only and exclu-
  sively for Floppy I/O.