VGIF.EXE ver 1.4 by Bob Montgomery [CIS 73357,3140]           2-9-88
See revision history for new items.

This is a GIF file viewer for EGA with the following features:
     Very fast GIF decoding.
     Menu driven for selecting file(s) to view; returns with cursor at last 
          position.
     Shows specified files like a slide show.
     /R option allows an application program to show a file and regain control.
     Creates PC Paint, ZSoft, or EGA PAint file from current pic.

The commands are:
1. vgif [path\]filename[.ext] [/r] to show a single file. The default path is 
     the current directory, and the default extension is GIF.
     The /r option shows the file and then returns to DOS (or a calling appli-
     cation program) with the picture still on the screen in EGA mode (mode 16).
     It is not necessary to change video mode between viewing each file, but it
     is up to the calling program to reset text mode (mode 3) after all viewing 
     is done.

2. vgif [.ext] to get a menu of up to 80 files in current dir with extension ext.
     The default extension is GIF. This is handy if you have some pictures that
     you don't want to come up in the normal menu; ie, adult and nude pics can
     be renamed to ADL extension. 

3. vgif [#path\][filespec] to get a menu of all files in the specified path
     meeting filespec (may contain wildcards). The default path is the current
     directory, and the default filespec is *.GIF; just entering 'vgif' will
     give a menu of all GIF files in the current directory. The # was necessary 
     to specify that a path is being requested. Consider the command 'dg \gif'. 
     Does this say you want to view a GIF file named GIF in the root directory,
     or does it say you want a menu of all GIF files in the subdirectory \GIF? 
     The # makes clear that you want a menu of all GIF files in the subdrectory
     GIF. Entering dg \gif\d*.adl would get a menu of all files starting with 
     the letter d and having an extension adl in the subdirectory \GIF of the 
     current drive. The only type commands it doesn't understand is a path of 
     the form .\dir (indicating a subdir of the current dir); it does understand
     a full filespec of the form .\dir\*.gif.

4. vgif @[path\]filename[.ext]  to do a slide show from commands in filename. The
     default path is the current directory, and the default extension is SLD.
     The commands are placed on seperate lines, and consist of either a filename
     (GIF extension assumed), or a delay (viewing time) spec of the form  d n
     where n is the desired viewing time in seconds. The default viewing time is
     5 seconds if no delay spec is given. Press any key to end the slide show.
     Pictures that are 320 or less pixels wide are displayed double size.

5. vgif ?  gives a help screen.

The # and @ commands can both be given on the command line. The # specifies the
path and filespec (* and ? OK) of the GIF picture files, and the @ specifies
the path/filename of the slide file. The @ has higher precedence than #, and you
will get a slide show. Thus, if the slide command file and the GIF files are in
the \GIF directory, and you are somewhere else, you can do a slide show by
either dg @\gif\cmds #\gif  or  dg #\gif @\gif\cmds.

The # and . commands can also be given on the same command line, where the #path
specs the path and the .ext specs the extension to look for. This is the same
as giving #path\*.ext

Commands in menu mode:
1.   The up, down, right, and left arrow keys move the cursor around the menu
     of files.
2.   Pressing the spacebar marks a file for viewing or slides, and moves to the 
     next file; it will also unmark a previously marked file.
3.   Pressing enter will display the marked files in the order they were marked.
     If no files were marked, pressing enter displays the file at the cursor.
4.   Pressing S will do a slide show of marked files until a key is pressed.
5.   Pressing ESCape ends the program and returns to DOS.
All other keys are ignored. If errors are encountered, an error message appears
on the next to last line, and disappears when the cursor is moved. 
The menu title is the search spec.

Commands while viewing a file (except in slide mode):
1.   The up/down arrow keys will scroll the picture if longer than 350 lines.
2.   If it is 320 or less pixels wide, pressing 2 will give a double size image
(which may be scrollable) and pressing 1 will give the normal size again.
3.   Pressing Z will create a ZSoft (PC Paintbrush) file with the same filename
     and extension PCX. The file will be a 640x350 paint file of what is
     currently on the screen.
4.   Pressing P will create a PC Paint 2.0 file with the same filename and 
     extension PIC. The file will be a 640x350 paint file of what is currently
     on the screen.
5.   Pressing R will create a RIX (EGA Paint) file with the same filename and 
     extension SCR. 
6.   Pressing enter will return to menu or DOS, or show next file for marked
     menu mode.
7.   Pressing ESCape will end the display and return to the menu.
All other keys are ignored. Pressing Ctrl Break (or Ctrl C) will go to DOS.

PC Paint and ZSoft files are saved as 640x350 images so that these programs will 
not force you to a smaller screen size. They can be saved as clippings, and then
combined to produce a composite picture.

The program was first written in C, and then the following parts were rewritten
in assembly language (which increased the speed by a factor of 2):
1.  GIF decoder for speed.
2.  EGA screen writing for speed.
3.  Part of PC Paint encoder for speed.
3.  File search module for menu mode, since can't do conveniently from C.

The program requires an IBM or compatable with at least 256K of RAM, and a EGA
adapter (256K) and monitor. If you like and use the program, please support it
by sending $10 to:

     Bob Montgomery
     123 Parsons Road
     Longwood, Fl 32779

If you use it as part of another application, registration is mandatory, and
credit must be given to me for the viewer portion in your documentation.
If you are a registered user of one of my other viewers, $5 is sufficient.
This will encourage me to update the program periodically, and to upload other
picture viewers/converters. The next program will be a PC Paint picture viewer
which can save the EGA screen to ZSoft, RIX, and GIF files. The program took 
about 1 month to write in its final form. If you use it, $10 is not much to pay
for a useful tool; not much more than a typical session on a long distance BBS.
Please don't rip me off. Any suggestions or comments can be mailed directly to 
me, or left on the following BBS's:
     Compuserve
     Tsunami BBS, Half Moon Bay, Calif. (415) 726-2726
     PC Rockland, Nyack, NJ (914) 353-2176

Revision history:
ver 1.1   1-13-88
          Added test for EGA adapter.
          Fixed menu colors.
          Allow ESCape from marked file viewing.
          Added Ctrl Break (or Ctrl C) exit to DOS anywhere.
          Added 'disk full' notification when creating picture file.
          Added critical error handler for 'drive not ready' errors.
ver 1.2   1-15-88
          Changed name to vgif.
          Slide mode now ignore the end of file mark in slide file, and any key
               will now end slide mode.
          Added slides to menu mode if S pressed-shows marked files as slides
               until a key is pressed.
ver 1.3   1-21-88
          Added better error checking to GIF file decoding. Notifies if bad GIF
               file.
          Fixed error reporting bug in single file mode.
ver 1.4   2-9-88
          Added instantaneous screen update in slide mode from menu or command
               (sld) file.
          Added the /r option which allows an application program to call VGIF 
               to view a file and then regain control.