ADJRAM -- Adjustable RAM Disk
                                     
                                by Gary Cramblitt

                                   Version 3.1

        (c) Copyright 1986 by Gary Cramblitt.  All rights reserved.
            Permission is granted to copy and use this software for
            non-commercial purposes only.  

            NOTICE:  This program is provided on an "as is" basis 
            without warranty of any kind, expressed or implied, 
            including but not limited to the implied warranties of 
            mercantability and fitness for a particular purpose.  The 
            entire risk as to quality and performance of this program is 
            with you, the user.  Should the program prove defective, you 
            assume the entire cost of all necessary repair, servicing, 
            or correction.  In no event will the author be liable to you 
            for any damages, including any lost profits, lost savings, 
            or other incidental or consequential damages arising out of 
            the use or inability to use this program.


        This program, although copyrighted, may be freely copied and 
        used, so long as it is not used for commercial purposes.  It is 
        NOT shareware or user-supported software.  You are not expected 
        to make a donation to the author for using this program.  Enjoy 
        -- and try to do the same for others some day.  


        What Is ADJRAM?
        ---------------
        ADJRAM is a RAM disk program.  Sometimes, RAM disks are called 
        "virtual disks" like the VDISK supplied with PC-DOS.  Sometimes 
        they are called "memory disks" like MEMBRAIN.  Whatever you call 
        it, a RAM disk is a program that makes a section of the Random 
        Access Memory (RAM) of your computer look like a floppy disk 
        drive to DOS.  The advantage is that RAM is many hundreds of 
        times faster than a floppy disk -- even faster than a hard disk.  

        Why use ADJRAM, when you already have VDISK or MEMBRAIN or some 
        other RAM disk?  Because ADJRAM allows you to vary the size of 
        the RAM disk without rebooting, and without loss of existing 
        data stored in the RAM disk.  For example, you can start out 
        with 64K of your memory allocated for the RAM disk, expand it 
        later to 320K, copy a document file of 60K to the RAM disk, and 
        still later reduce the RAM disk capacity back down to 128K -- 
        without losing your document file.

        ADJRAM is ideal for those who do not have a hard disk.


        Requirements
        ------------
        ADJRAM is designed to run under MS-DOS version 2 or greater.  It 
        has been tested on the following machines:

             1.  Zenith Z100 under MS-DOS version 2.21
             2.  Zenith Z171 (an IBM PC compatible) under MS-DOS version 
                 2.11
             3.  KayPro 16 also under MS-DOS 2.11
             4.  Zenith Z158 (another IBM PC compatible) under MS-DOS 
                 3.1 with a 2 Mbyte JRAM 3 card 

        It is the author's belief that it will run under PC-DOS version 
        2 or higher, but this has not been tested.  It requires 
        approximately 10K bytes of disk space.  Memory usage is, of 
        course, a function of the RAM disk's size, but it requires a 
        minimum of 65K free RAM.


        Installation
        ------------
        Note: If you have a computer with LOTUS/INTEL/Microsoft Expanded 
              Memory and you want ADJRAM to use the Expanded Memory, 
              please read the section below entitled "Expanded Memory 
              Support" before you install ADJRAM.  

        Copy the following files to your boot disk: 

             AMDISK.DVD
             ADJRAM.EXE

        Edit your CONFIG.SYS file and place the following line in it:

             device = amdisk.dvd

        Reboot your computer.  If all goes well, you should see the 
        following message appear near the beginning of your boot 
        sequence:

             AMDISK v3.1 (c) Copyright 1986 by Gary Cramblitt--
                    Initialized as disk C:

        The disk drive letter will vary according to your system 
        configuration.  Remember that drive letter, since it is that 
        disk which is your RAM disk.  

        If you use any memory resident programs, such as Sidekick (a 
        trademark of Borland International), load them before attempting 
        to change the size of the RAM disk (as explained in the next 
        section).  
        
                                                        
        Using the RAM Disk
        ------------------
        The RAM disk is used just like any floppy disk drive.  You can 
        copy files to or from it, create directories on it, erase files, 
        etc.  You may NOT do the following things with the RAM disk:
        
             1.  You may not FORMAT the RAM disk.
             2.  You may not DISKCOPY from or to the RAM disk.
             3.  You may not run SYS against the RAM disk.
             4.  You may not boot from the RAM disk.
             5.  You may not use any program on the RAM disk that 
                 accesses the disk controller circuitry directly.  Some 
                 anti-copy protection programs fall into this category.
             6.  You may not use any program that depends upon IBM
                 standard disk media codes.  One such program is CHKDSK.  
                 My version of CHKDSK will report that my RAM disk is a 
                 non-standard format and ask me if I wish to continue.  
                 If I say yes, everything works normally thereafter.

        Restrictions 1 through 5 are generally true of any RAM disk.  
        Restriction 6 is unique to the Adjustable RAM Disk because it 
        uses a non-standard disk media code.  This shouldn't cause great 
        hardship though.  

        Also, keep in mind that anything stored in the RAM disk can 
        potentially be lost.  For example, should your power fail and 
        you don't have an Uninterruptible Power Source (UPS), then 
        everything in the RAM disk will be lost.  If you reboot (by 
        pressing CTRL-ALT-DEL for example), the contents of the RAM disk 
        are lost.  It is a good idea to periodically copy important 
        files to a more permanent medium, such as floppy disk.  

        The RAM disk defaults to a size of 64K bytes when you first boot 
        the system.  The ADJRAM program is used to change this size.  
        For example, to increase the size of the RAM disk by 64K bytes, 
        enter the following command to the DOS prompt: 

             ADJRAM C: +64

        The spaces after "ADJRAM" and after "C:" are required.  The 
        drive letter (C:) will vary according to your system's 
        configuration.  Use whatever letter was displayed by AMDISK when 
        you booted the system.
        
        When ADJRAM is run, you should see something like this displayed 
        on your screen: 

             Adjust Memory Disk v3.1 (c) Copyright 1986 by Gary Cramblitt
             Drive C:   Total Size: 64K        Free Space: 61K
                      Desired Size: 128K    Desired Change: 64K
             Allocating new 32K memory block #1
             Allocating new 32K memory block #2

                        Memory Block Table
             Block #      Paragraph      Size(sectors)
             --------     ---------      -------------
                0            604              128
                1           26A9               64
                2           2EAA               64

        The drive letter displayed will vary, as I've already explained.  
        The exact paragraph numbers will also vary according to your 
        system configuration and whatever other software is loaded.

        ADJRAM always increments its size in 32K junks, called "memory 
        blocks".  The change you specify is always rounded up to the 
        next closest multiple of 32.  In the example above, two new 32K 
        memory blocks are created for the additional 64K of space.  The 
        Memory Block Table is displayed for your information only.  For 
        the most part, you can ignore it.  

        You must have sufficient free memory to allocate the additional 
        size.  Run CHKDSK if you are unsure about how much free memory 
        you have.

        You can also shrink the RAM disk.  For example, the following 
        command would decrease the size of the RAM disk by 32K: 

             ADJRAM C: -32

        You must have sufficient free space in the RAM disk in order to 
        shrink it.  To find out how much free space you have in the RAM 
        disk, enter the following command:

             ADJRAM C:

        Notice how there is no size parameter.  The program will display 
        the current size and free space of the RAM disk.  If you have 
        insufficient space, you must erase enough files to get 
        sufficient space.  Then enter your ADJRAM command again.  

        You can not shrink the RAM disk to less than 64K.

        Instead of giving the size of the RAM disk as a plus or minus 
        figure, you can specify the desired size of the RAM disk like 
        this:

             ADJRAM C: 320

        This command will set the RAM disk to 320K.  If it is currently 
        larger than 320K, it will shrink it down to 320K (provided there 
        is sufficient free space to do so).  If it is currently smaller 
        than 320K, it will expand the size to 320K by allocating new 
        memory blocks.  Remember that ADJRAM will round the figure you 
        specify to the next higher multiple of 32.  

        If you want to adjust the size of the memory disk so that it has 
        200K of free space, enter a command like this:

             ADJRAM C: f200

        Notice the letter "f" in front of the size.  This command will 
        expand or shrink the RAM disk so as to ensure there is about 
        200K of free space IN THE RAM DISK.  

        If you want to ensure there is at least 128K of free space in 
        the RAM disk, enter a command like this:

             ADJRAM C: m128

        Notice the letter "m" in front of the size.  This command will 
        never shrink the RAM disk, but it may expand it to make sure 
        there is a minimum of 128K of free space.  This form of the 
        command is particularly handy within batch files to make sure 
        the RAM disk is large enough to hold a file before it is copied 
        into the RAM disk.


        Online Help
        -----------
        If you can't remember the format for all these commands, fear 
        not.  Simply enter 

             ADJRAM

        and it will display a help message showing the formats described 
        above.


        Hint for Floppy Disk Systems
        ----------------------------
        If you do not have a hard disk, soon after booting your 
        computer, copy file ADJRAM.EXE to the RAM disk, for example:

             COPY A:ADJRAM.EXE C:

        You can then modify the size of the RAM disk at any time 
        thereafter without needing the boot disk.  Just put the RAM disk 
        drive letter in front of any ADJRAM commands.  For example:

             C:ADJRAM C: -32

        You can put the COPY command into your AUTOEXEC.BAT file.


        Expanded Memory Support
        -----------------------
        ADJRAM provides limited support for LOTUS/INTEL/Microsoft 
        Expanded Memory (EMS version 3.2 compatible).  

        If you have a computer with LOTUS/INTEL/Microsoft Expanded 
        Memory and you want ADJRAM to use that memory, the installation 
        is a little different.  Instead of copying ADJRAM.EXE to your 
        boot disk, copy file ADJRAMEM.EXE and then rename it to 
        ADJRAM.EXE.  The rest of the installation is the same as was 
        described before.  
        
        If you want the program to create new memory blocks in 
        LOTUS/INTEL/Microsoft Expanded Memory, add a "/E" option, like 
        this:

             ADJRAM C: +32 /E

        This command will expand the memory disk by 32K.  The additional 
        32K memory block will be created within LOTUS/INTEL/Microsoft 
        Expanded Memory.  If ADJRAM ends up shrinking the RAM disk, the 
        "/E" switch is meaningless.  Remember that ADJRAM will always 
        shrink the RAM disk by freeing memory blocks in reverse of the 
        order inwhich they were created.  

        The version of ADJRAM that supports Expanded Memory can not be 
        used in conjunction with the version that does not support it.  
        Don't get them mixed up.  Use ADJRAMEM.EXE (renamed to 
        ADJRAM.EXE) or use ADJRAM.EXE -- but not both.
        
        There are a couple of restrictions with the Expanded Memory 
        version of ADJRAM.  First, some Expanded Memory systems have a 
        limited number of Expanded Memory handles.  ADJRAM uses one 
        handle for each 32K Memory Block it creates.  This means that 
        one megabyte of RAM disk from Expanded Memory will use up 32 
        handles.  The Expanded Memory Manager provided with the JRAM 3 
        board I tested (JPAGER) had only 32 handles, so creating a one 
        megabyte RAM disk used up all of the EM handles.  

        Even if you have lots of EM handles, the largest RAM disk that 
        can be created using Expanded Memory is 2016K or about 2 
        Megabytes.  EMS supports up to 8 Megabytes.  If you want more 
        RAM disk, add additional "device = amdisk.dvd" statements to 
        your CONFIG.SYS file.  This will create additional RAM disks 
        with different drive letters.  

        I'm looking for feedback from users on this feature.  Is it 
        worth it?  I suspect that most people who own Expanded Memory 
        boards prefer to use the RAM disk software that comes with those 
        boards.  Right now, fixing these problems doesn't seem 
        worthwhile.  If I'm wrong about that, please let me know.

        If you think the Expanded Memory support is needed, what size 
        increment should it use?  128K? 256K?

        The Expanded Memory support in this version of ADJRAM was coded 
        based on information from the book "Advanced MS-DOS" by Ray 
        Duncan.  The code was tested on a Zenith Z158 with a 2 Mbyte 
        JRAM 3 memory board installed (JBOOT and JPAGER loaded).  I 
        don't own a computer with Expanded Memory, so this part of the 
        program is the least tested.  Please be cautious until you've 
        had time to thoroughly check out the program -- and let me know 
        if you encounter difficulty.  

        
        Error Messages
        --------------
        Any time that an error occurs, the phrase "Error -- " is 
        displayed, followed by one of the following messages.  In 
        addition, the program sometimes displays the help message if an 
        error is detected -- on the assumption that you may have given 
        an incorrect command.  
        
        Here is a list of possible error messages you might see 
        displayed by the ADJRAM.EXE program and their probable cause 
        (the numbers in parenthesis are explained in the next section): 

             Error -- could not read boot sector.  Error code xx (15)

        The program could not read the boot sector (logical sector 0) of 
        the RAM disk.  An invalid drive letter was specified or the RAM 
        disk has become corrupted.  In the latter case, reboot is 
        recommended.  

             Error -- that drive is not the adjustable RAM disk. (15)

        An invalid drive letter was specified.  Use the letter that was 
        reported by AMDISK when you booted the computer.  Make sure you 
        used the correct command syntax.  A space must follow "ADJRAM".

             Error -- could not free environment block.  Error code xx 
        (7)

        This error would indicate you have an incompatible version of 
        MS-DOS.  The error codes are those returned by DOS function 49H.

             Error -- Invalid drive letter or memory disk is not loaded 
        (15)

        ADJRAM reports this error if DOS returns an error code from 
        function 36H (get free disk space).  Check your drive letter and 
        command syntax.

             Error -- NOT enough room to do the shrink. (0)

        You do not have enough free space in the RAM disk to shrink it 
        by the requested amount.  First erase some files from the RAM 
        disk, then reenter you command.

             The disk is already that size!  Nothing to do. (0)

        You told ADJRAM to set the size to what it already is.  ADJRAM 
        does nothing and exits.  Remember that your specified size is 
        rounded up to the nearest multiple of 32K.

             Error -- could not modify memory block size.  Error code xx 
        (8)

        This error occurs when expanding the RAM disk.  The program 
        received an error code from DOS function 4AH (modify memory 
        allocation) on the first new 32K memory block to be created.  It 
        would indicate that you don't have enough free memory to expand 
        the RAM disk at all.  It could also be caused by corrupted 
        memory allocation, possibly caused by incompatibility with other 
        memory resident programs.  Reboot is recommended in the latter 
        case.

              Error -- could not allocate new memory block.  Error code 
        xx (8) 

        This error is similar to the one above except that it occurs on 
        the second and subsequent new 32K memory blocks when the program 
        invokes DOS function 48H (allocate memory).  The program will 
        attempt to keep going without expanding the disk any further.  
        This condition is not well tested though, so to be safe, reboot 
        is recommended.  

             Error -- could not allocate new memory block from EMM.  
                      Error code xx (8) 

        This error is similar to the one above except that it occurs in 
        conjunction with creating new 32K memory blocks in 
        LOTUS/INTEL/Microsoft Expanded Memory.  The program will attempt 
        to keep going without expanding the disk any further.  This 
        condition is not well tested though, so to be safe, reboot is 
        recommended.  

             Error -- could not write boot sector back.  Code: xx (15)

        This is most likely an internal program error.  The program got 
        an error code from DOS interrupt 26H (write absolute disk 
        sector).  Reboot is required.  

             Error -- could not free allocated memory block #xx.  Error 
        code xx 
        
        This error occurs when shrinking the RAM disk.  The program got 
        an error code from DOS function 49H (release memory).  Could be 
        caused by an internal program bug, incompatible memory resident 
        program, or incompatible version of DOS.  The program attempts 
        to exit gracefully so that you can recover data files from the 
        RAM disk, but you should reboot as soon as possible.  

             Error -- could not free EM pages for memory block #xx.  
        Error code xx 
        
        This error occurs when shrinking the RAM disk.  The program got 
        an error condition from the LOTUS/INTEL/Microsoft Expanded 
        Memory Manager.  Could be caused by an internal program bug, 
        incompatible memory resident program, or incompatible version of 
        DOS.  The program attempts to exit gracefully so that you can 
        recover data files from the RAM disk, but you should reboot as 
        soon as possible.  

             Error -- Insufficient stack space to pack subdirectory 
        xxxxxxxx.  Too many subdirectories.  Shrink abandoned. (8)

        This error occurs when shrinking the RAM disk.  The DeSmet C 
        stack space was insufficient to handle the depth of 
        subdirectories you have on your RAM disk.  The program attempts 
        to exit gracefully without completing the shrink.  This 
        condition has not been fully tested, so caution, your files may 
        have been corrupted.  In the future, don't use so many 
        subdirectories.  

             Error -- Error while packing file xxxxxxxx

        This error occurs when shrinking the RAM disk.  It will usually
        be displayed after the previous message.  It may also appear if
        an internal error occurs, such as inability to read or write
        sectors of the file.  The program attempts to exit gracefully
        without completing the shrink.

             Error -- Expanded Memory Manager is not avaiable.
                      Error code: xx (15)

        You specified the "/E" option, but the LOTUS/INTEL/Microsoft 
        Expanded Memory Manager (EMM) is not loaded.  Load the EMM and 
        try again.

             Error -- Expanded Memory Manager could not report page 
        frame.  Error code: xx (8)

        The EMM was detected by ADJRAM, but the EMM reported an error 
        when ADJRAM asked for the page frame segment address (EMM 
        function 41H).  This could be caused by a corrupted EMM, or an 
        incompatible version of the EMM (ADJRAM requires version 3.2 
        compatibility), or possibly ADJRAM encountered a "busy" 
        condition from the EMM.  Try again.  If it still fails, you'll 
        have to stick with normal memory.  

        There are two other conditions which do not display an error 
        message.  In these cases, the program simply displays the help 
        message and exits:

             1.  Invalid drive letter specified.  Must be in range A 
                 through I. (15)

             2.  Invalid size specified.  Must be in range 64 to 2016.  
                 (1).  

        There are also a large number of possible errors that MS-DOS will 
        display while you're working with the RAM disk.  Consult your 
        DOS manual.  One message I'd like to point out.  If you see

             Bad File Allocation Table

        (or something similar) the RAM disk is probably corrupted.  
        Carefully check your files.  If they are OK, copy them to a more 
        permanent medium, such as floppy disk, then reboot.  
        

        Using ADJRAM in Batch Files
        ---------------------------
        If an error occurs while running ADJRAM, it will return a DOS 
        error code when it exits back to DOS.  The error codes returned 
        are shown in parenthesis in the error message section above.  
        These error codes can be used in a batch file via the DOS 
        ERRORLEVEL subcommand.  See your DOS manual.  

        Some versions of MS-DOS (Z100 v2.21 for example) have a command 
        which will cause error codes to be displayed.  It is: 

              XYZZY ON


        Compatibility and Memory Usage
        ------------------------------
        The Adjustable RAM Disk falls into a class of programs known as 
        Memory Resident programs.  Sidekick is one such program.  These 
        programs are sometimes incompatible with one another.  It is 
        impossible for me to test the Adjustable RAM disk in combination 
        with every available memory resident program, so I'll apologize 
        ahead of time -- some incompatibilities are almost certain to 
        crop up.  

        Sometimes, changing the order inwhich the programs are loaded 
        makes a difference.

        Generally, you should load all of your memory resident programs 
        BEFORE you run ADJRAM.  (I know, every memory resident program 
        wants to be loaded last, but please bear with me!)  You should 
        do this to make the most efficient use of memory.  Here's why.  
        When you expand the RAM disk, ADJRAM allocates 32K memory blocks 
        using the DOS memory allocation functions.  Once that is done, 
        any subsequent memory resident programs you load will generally 
        get loaded above these new memory blocks.  When you later shrink 
        the RAM disk, ADJRAM deallocates the memory blocks.  If you have 
        loaded a memory resident program after expanding the RAM disk 
        with ADJRAM, then "holes" in the memory allocation will be 
        created when you later shrink the RAM disk.  These holes will 
        generally not be usable for transient programs until you unload 
        the memory resident program (which might not even have that 
        capability).  
        
        You generally shrink the RAM disk because you want to make more 
        memory available for other programs.  But it defeats this 
        objective to load memory resident programs after expanding the 
        RAM disk.  So...

             First load the memory resident programs, then use ADJRAM to 
             expand your RAM disk.  

        The Adjustable RAM disk doesn't "steal" interrupts from the 
        system, so expanding the RAM disk after loading programs that 
        intercept interrupts, such as Sidekick, SHOULDN't cause any 
        problems.

        If you encounter compatibility problems, please let me know at 
        the address I'll give at the end of this document.  I'd like to 
        know about them so I can fix them if possible.  Please be as 
        complete as possible when you explain the problem.  What memory 
        resident programs did you have loaded and in what order?  How 
        much memory do you have in your computer?  What computer and 
        operating system were you running?  Exactly what happened when 
        it didn't work?  I won't guarantee that I can fix the problem, 
        but I'll try.  
        
                 
        Known Compatibility Problems
        ----------------------------
        When using ADJRAM with DoubleDOS, new memory blocks are created 
        within whichever partition is active at the time you run ADJRAM.  
        If you attempt to shrink the RAM disk to gain additional room in 
        the first partition, you may find that you didn't gain any room 
        in the first partition!  Instead, the room gained was in the 
        second partition (because that's where the memory blocks were 
        created).  

        Also, DoubleDOS doesn't know about ADJRAM creating new memory 
        blocks.  This causes DoubleDOS to tell you there is more room in 
        partitions than actually exists.  Use CHKDSK to find out how big 
        your partitions really are.  In general, you should try to run 
        ADJRAM before activating DoubleDOS, to avoid this problem.

        ADJRAM is somewhat incompatible with MARK/RELEASE.  You can't 
        expand the RAM disk after you've run MARK, because when you run 
        RELEASE, AMDISK won't know that some of its memory blocks have 
        been freed.  As long as you expand before you run MARK for the 
        first time, you should be OK.  I have not tried MARK/RELEASE in 
        conjunction with ADJRAM, so there may be other problems as well.  
        The Referee, being a program similar to MARK/RELEASE, will 
        problably also have these problems.  
                 
        
        Other Known Problems
        --------------------
        If you expand the RAM disk into all available memory, you will 
        probably die.  You can't get enough room to run ADJRAM again so 
        as to shrink it back down.  The program does not check to see if 
        you're expanding the RAM disk into all free memory, so be 
        careful.
        
        By the way, the coding fix to this problem is not as simple as 
        you might think (my Z100 has 768K of user memory, not 640K.  
        What about Expanded Memory?  etc.).  If someone can tell me a 
        fullproof way to determine how much free memory exists, let me 
        know.  
        
        Some programs, such as PC-WRITE have a "shell" or "hotkey" 
        command that allows you to suspend the program, keeping it in 
        memory, and execute other DOS commands.  You may be tempted to 
        use this capability to increase or decrease the size of the RAM 
        disk in the middle of running another program.  But be careful 
        here.  Consider the following sequence of events:

             1.  You're running PC-WRITE, editing file C:MYFILE.DOC on 
                 the RAM disk.

             2.  You use PC-WRITE's "shell" command to get the DOS 
                 prompt.
        
             3.  You use ADJRAM to expand the size of disk C, the RAM 
                 disk.  

             4.  You use the DOS EXIT command to go back into PC-WRITE.

             5.  Upon exiting PC-WRITE, you're horrified to learn that 
                 it was unable to successfully save all your work in 
                 C:MYFILE.DOC.

        The problem here is that ADJRAM told DOS that the "media has 
        changed" on disk C.  But PC-WRITE had a file open on disk C!  
        DOS can't properly close the file.  This sort of problem will 
        generally occur with any program that has a "shell" command but 
        fails to close all open files before executing the shell.  [By 
        the way, I haven't actually checked that PC-WRITE does keep 
        files open.  It may well be that there is no problem.  Indeed, 
        it would surprise me to learn that PC-WRITE does have this 
        problem.  PC-WRITE is a dynamite program!] 

        This kind of problem can also occur with certain memory resident 
        programs that, in effect, give you a "shell" command from within 
        any program.

        Remember that whenever you expand or shrink the RAM disk, you 
        have, conceptually, removed the current "floppy disk" in the RAM 
        drive, and replaced it with another "floppy disk" that just 
        happens to have the same files as the one removed.  You wouldn't 
        change a real floppy disk in the middle of editing a Wordstar 
        file, so don't expand or shrink the RAM disk either.  


        Planned Enhancements
        --------------------
        I'm planning on making the following enhancements at some time 
        in the future: 
        
             1.  Fix the problem mentioned above about expanding into 
                 all available memory.

             2.  Allow the initial RAM disk size to be specified at boot 
                 time in the CONFIG.SYS file, like this

                 device = amdisk.dvd SIZE=32

        If you can think of other useful enhancements, let me know about 
        them please.  


        History
        -------
        3.0   This was the first version of ADJRAM to be released.  It
              was released to the public in September 1986.
        3.1   This version fixed a bug.  3.0 did not properly pack files
              in subdirectories under certain conditions.  This lead to
              a "bad file allocation table" error.  Release October 1986.


        Internals
        ---------
        This section is for anyone interested in the internal workings 
        of the Adjustable RAM Disk.  It is not necessary to know this 
        information to use the Adjustable RAM Disk, but it may be 
        helpful for resolving compatibility problems.  This section is 
        for advanced DOS programmers only.  

        AMDISK.DVD is a loadable device driver, just like VDISK or 
        ANSI.SYS.  By itself, it is a complete 64K RAM disk.  A 64K 
        "memory block" is allocated immediately after the AMDISK code.  
        A Memory Block Table is maintained in logical sector 0 (the boot 
        sector) of the RAM disk beginning at offset 1EH.  For each 
        memory block, this table contains a seven byte entry as follows: 

             1.  A byte indicating the type of memory block.  0 means 
                 the block is allocated in normal DOS memory.  1 means 
                 the block is allocated in Expanded Memory.  
        
             2.  A word giving the starting paragraph number of the 
                 memory block.  A paragraph of memory is simply 16 
                 bytes, so this number is just the absolute memory 
                 address shifted right by 4 bits.  All memory blocks 
                 begin on an even paragraph boundary.  This word is zero 
                 if there are no more memory blocks.  It is meaningless 
                 for Expaned Memory blocks.

             3.  A word giving the size of the memory block in 512-byte 
                 sectors.

             4.  A word giving the Expanded Memory handle for the memory 
                 block.  Zero for normal memory blocks.

        Immediately after booting, there is exactly one 64K (128 sector) 
        memory block in the Memory Block Table.

        Note:  Don't confuse the memory blocks defined here with those 
               defined for DOS functions 48H thru 4AH.  To avoid 
               confusion -- and though not strictly accurate -- I'll 
               refer to DOS's memory blocks as "program segments".  
        
        The number of memory blocks allocated is stored in the media 
        descriptor byte at offset 15H of the boot sector (and also in 
        the first FAT entry).  Any time DOS requests a media code from 
        the AMDISK device driver, it returns the number of memory blocks 
        allocated.  In this way, any time that the RAM Disk has been 
        shrunk or expanded, DOS will know that the "media has changed" 
        and will rebuild its internal BPB tables.  This lets DOS know 
        what the new size of the RAM disk is.  
        
        Upon startup of the ADJRAM program, DOS function 49H (release 
        memory) is used to deallocate its own environment segment.  This 
        doesn't seem to hurt a running program, and it is necessary to 
        insure that this memory can be used later when the RAM disk is 
        shrunk.

        At startup, the Expanded Memory version of ADJRAM tests whether 
        the Expanded Memory Manager (EMM) is loaded by opening device 
        "EMMXXXX0".  If the open fails, the EMM is not loaded.  If the 
        open succeeds, then the output status is requested from the 
        device using DOS function 44H (IOCTL).  If IOCTL reports a 
        status of 0, then coincidentally a file named "EMMXXXX0" existed 
        on the default disk, and the EMM is still not available.  If the 
        EMM is not available, ADJRAM reports an error and exits.

        Also upon startup, ADJRAM checks that the specified drive letter 
        corresponds to the AMDISK device.  The boot sector of the RAM 
        disk contains the string "AMDISK" at offset 03H.  The boot 
        sector is read using DOS interrupt 25H (absolute disk read).

        When the ADJRAM program increases the size of the RAM disk, it 
        does so by allocating additional 32K (64 sector) memory blocks.  
        Normal memory blocks are allocated in two ways:

             1.  If it is the first memory block to be created (in this 
                 run of ADJRAM), then the memory block is allocated 
                 using DOS function 4AH (modify memory allocation).  
                 ADJRAM's own program segment is the one modified.  
                 Hence, the first memory block overwrites the ADJRAM 
                 program itself.

             2.  Additional memory blocks are allocated using DOS 
                 function 48H (allocate memory).  

        In either case, an appropriate entry is made in the Memory Block 
        Table, which is in the boot sector, for each new memory block.  
        At the end of the program, the boot sector is written back out 
        using DOS interrupt 26H (absolute disk write).  
        
        When ADJRAM exits normally, it uses DOS function 31H (terminate 
        and stay resident) to permanently allocate the new memory 
        blocks.  
        
        Expanded Memory blocks are allocated via EMM function 43H (Get 
        handle and allocate memory).
                 
        When ADJRAM shrinks the RAM disk, it does these steps:
                 
             1.  It checks to insure there is sufficient free space in 
                 the RAM disk to do the shrink.  
             2.  The File Allocation Table (FAT) is read using DOS 
                 interrupt 25H.  The first available cluster number is 
                 determined.  
             3.  The first sector of the directory is read in using DOS 
                 interrupt 25H.
             4.  For each file, any clusters located after the first 
                 available cluster are moved down to the first available 
                 cluster.  Then the next available cluster is 
                 determined.  Clusters are moved in the RAM disk using
                 DOS interrupts 25H and 26H.  As clusters are moved, the
                 directory and FAT in memory are updated.  After all the
                 clusters of the file are packed down, and if the file
                 is a subdirectory, then the clusters of the directory
                 are read in and the file packing algorithm (steps 3 and
                 4) is recursively applied to each directory entry in
                 the file.
             5.  Step 4 is repeated for each additional directory 
                 sector.  Updated directory sectors are written back to 
                 the disk using DOS interrupt 26H.
             6.  The necessary number of memory blocks are deallocated, 
                 either using DOS function 49H (release memory) or EMM 
                 function 45H (release handle and memory).  The Memory 
                 Block Table is updated accordingly.  Blocks are 
                 deallocated in reverse of the order inwhich they are 
                 created.  
             7.  The updated FAT and boot sector are written back to the 
                 disk using DOS interrupt 26H.  
             8.  ADJRAM exits normally via DOS function 4CH (exit with 
                 return code).

        An excellent book for understanding DOS memory allocation and 
        disk structure is the "MsDOS Developer's Guide", written by the 
        Waite Group and published by SAMS.  Another excellent book, 
        which includes documentation on Expanded Memory, is "Advanced 
        MS-DOS" by Ray Duncan.
        
        In the course of developing this program, I discovered a couple 
        of interesting things about the DOS version 2 memory allocation 
        functions (48H thru 4AH).  

             1.  Transient programs are always loaded after the last 
                 allocated memory block, even if there is sufficient 
                 memory available in "holes" below the last allocated 
                 memory block.  Such holes could be created by loading a 
                 memory resident program, such as Sidekick, and then 
                 shrinking the RAM disk.

             2.  The allocate memory function (48H), on the otherhand, 
                 will use holes if they exist and if they are large 
                 enough to contain the requested block.

             3.  If a program modifies a DOS memory block (function 
                 4AH), it becomes the "owner" of that block, even if it 
                 didn't create the block in the first place.  When such 
                 a program exits, the block will be automatically 
                 deallocated by DOS unless the program exits via 
                 terminate and stay resident.   This is why ADJRAM must 
                 allocate memory blocks in fixed 32K increments.  
                 Ideally, it should allocate exactly the requested size 
                 and no more.  The DOS quirk described here prevents 
                 that though.

        The source code for the Adjustable RAM Disk is included with the 
        program.  AMDISK.DVD is coded in MASM; ADJRAM.EXE is coded in 
        DeSmet C version 2.4.  Even though I've included the source 
        code, I would nevertheless like to act as the clearinghouse for 
        all future versions and modifications.  If you make a change to 
        the program, or fix a bug, PLEASE let me know about it -- I may 
        want to include the change in future versions. 
        
        If you modify the program, you agree to maintain my copyright.  
        You should indicate that you've modified the program by changing 
        the version number, for example "version 3.1A", or by putting 
        some other distinguishing message in the signon of the program, 
        for example "custom version by John Doe".  The rational for this 
        is simple -- I don't won't to be blamed for your bug.  

        My address, as of October 1986 is:

             GARY CRAMBLITT
             105 TENNESSEE RD
             STEVENSVILLE, MD  21666

        Please do not telephone.  I'd like to receive your letter.

                       * * * *  END OF ADJRAM.DOC * * * *