Most owners of the Z150 are probably not aware of the presence of 
an  alternate  character set that may be selected  via  software.  
This character set is a single-dot set very much like the H19 and 
Z100  default character sets,  and,  according to taste,  may  be 
preferable  to  the "fat" double-dot character set  that  is  the 
default  for the Z150.   This character set is especially  better 
suited to monochrome than the double-dot character set.

The  accompanying  program allows the selection of the  character 
set  from the command line by examining the parameters passed  to 
the  program from the command line when the program  is  started.  
If the user enters:

     CHARSET

with no parameters,  the double-dot (fat) character set is selec
ted.  If the user enters:

     CHARSET <anything>

with  anything  on  the command  line  following  "CHARSET",  the 
single-dot character set is selected.

Programmers will notice that the ISZ150 and GETCMD function calls 
may  seem  like  over-kill,  due to the saving of  registers  and 
passing of parameters;  but, these functions were borrowed from a 
C function library where this kind of thing is necessary.

To assemble, link, and convert the source:

     MASM CHARSET;
     LINK CHARSET;
     EXE2BIN CHARSET.EXE CHARSET.COM

The  resultant  495  byte .COM file is very  quick  to  load  and 
execute.

If  you  use the single-dot character set,  you  will  eventually 
notice  that the graphics characters in this set are very differ
ent from the graphics characters in with the double-dot character 
set.


Todd Merriman
Future Communications
Atlanta, Georgia