page 1 


            HOW TO UPGRADE TO EMM 4.0

            This pamphlet explains how to upgrade your Above Board
            software to EMM 4.0.  The easiest and quickest way is to let
            the INSTALL program do it for you.  This section explains
            how to run INSTALL.

            If you need to install EMM 4.0 yourself, refer to the
            instructions on page 2.

            There are also optional programs available on this upgrade
            diskette -- three programs that run various tests (CHKCOP,
            CHKMEM, and TESTAB) and one program that sets up the
            hardware configuration for the Above Board 286 and PS/286
            (SETBOARD).  Refer to page 14 for details.

            Here's all you need to do to upgrade your Above Board
            software to EMM 4.0:

            1    With your screen displaying the DOS prompt, insert a
            copy of the Intel upgrade diskette into drive A.

            2    Type

            A:INSTALL

            and press Enter.  Follow INSTALL's directions and answer the
            questions.  INSTALL does the rest.  That's all you need to
            do for your EMM 4.0 upgrade.





                                                           page 2

            INSTALLING EMM 4.0 YOURSELF

            This section explains the installation of EMM 4.0 without
            using the INSTALL program.  Installing the software involves
            these steps:

            o    Copying files (page 2).
            o    Setting up expanded memory (page 3 through 10).
            o    Setting up RAM disks and a clock (page 11) -- optional.
            o    Setting up a print buffer (page 11 through 13) --
                 optional.

            If you boot from floppy disks, install the Above Board
            software on each system diskette from which you boot.  If
            you boot from a hard disk, install the software just once in
            the root directory.

            Copying files

            Before you can use the Above Board software, you must copy
            the files you need from the Intel upgrade diskette to your
            hard disk's root directory or to your system diskettes.
            Copy only the files you need.

            Table 1 describes the files you may need on the Intel
            upgrade diskette.  To upgrade to EMM 4.0, you must copy the
            EMM.SYS file.

            Table 1   Intel diskette file descriptions


                 File name        Description                 


                 EMM.SYS          To use expanded memory.

                 QUIKMEM2.SYS     To use an expanded memory RAM
                                  disk.

                 QUIKMEM1.SYS     To use a conventional memory
                                  RAM disk.

                 QUIKBUF2.COM     To use an expanded memory print
                                  buffer.

                 QUIKBUF1.COM     To use a conventional memory
                                  print buffer.

                 CLOCK.SYS        To use the Above Board PS/PC
                                  clock ONLY.


                                                          page 3
            Setting up Expanded Memory

            This section explains how to edit the CONFIG.SYS file to use
            EMM 4.0.  To use EMM 4.0, you'll need to add new commands to
            your CONFIG.SYS file.  Use any ASCII file editor (such as
            EDLIN) to view and edit the file.  Then perform the
            following steps to add the commands:

            1    Copy the parameters (for example, M5 and I5) currently
                 in the DEVICE=EMM.SYS line here:

                 ________________________________

                 If you write down these parameters, you won't
                 need to remove your computer's cover to see
                 your Above Board's switches.  You can use the
                 old parameters to help you choose the new parameters.

            2    Replace the DEVICE=EMM.SYS line in your CONFIG.SYS
                 file with the following new parameters:

            DEVICE=EMM.SYS Computer  Memory_Address  I/O_Address1...16
                           [EXP=x]  [ND]  [NP]  [NE]  [H=x]

                 The parameters in italics are required for using
                 expanded memory; the other parameters in brackets []
                 are optional.  The order of the parameters doesn't
                 matter.  Be sure you have only one DEVICE=EMM.SYS line
                 in your CONFIG.SYS file.


                                                              
                                                           page 4

            Required EMM command line parameters

            The Computer parameter defines the type of computer in which
            the Above Board is installed.  Replace the Computer
            parameter with one of the choices listed in Table 2.  The
            Computer parameter is required in the EMM command line.

            Table 2   Computer parameter choices

                 Computer parameter       Type of computer

                 pc                       COMPAQ DESKPRO
                                          IBM PC
                                          IBM PC XT
                                          IBM PC or PC XT
                                            compatibles


                 at                       COMPAQ DESKPRO 286
                                          COMPAQ DESKPRO 386
                                          IBM PC AT
                                          IBM PC XT 286
                                          IBM PC AT compatibles


                 mod30                    IBM Personal System/2
                                            Model 30



                                                           page 5

            The Memory_Address parameter specifies the address of the
            64K-byte block of memory to which expanded memory is mapped.
            If your old DEVICE=EMM.SYS line has an M parameter, replace
            the M parameter with the corresponding Memory_Address listed
            in

            o    Table 3 (for Above Boards installed in 80286-
                 based computers) or

            o    Table 4 (for Above Boards installed in 8088-
                 or 8086-based computers).

            Table 3   M parameter and corresponding Memory_Address
                      parameter (AboveTM Boards installed in 
                      80286-based computers)

                          M Parameter    Memory_Address

                             1             C000
                             2             C400
                             3             C800
                             4             CC00
                             5             D000



            Table 4   M parameter and corresponding Memory_Address
                      parameter (AboveTM Boards installed in 8088-
                      and 8086-based computers)

                          M Parameter    Memory_Address

                             0*            C400
                             1             C800
                             2             CC00
                             3             D000
                             4             D400
                             5             D800
                             6             DC00
                             7             E000

                     *for an Above Board PC or PS/PC only



                                                           page 6

            If you don't have an old DEVICE=EMM.SYS line, use a memory
            address listed in Table 5.  Be sure you use a memory address
            listed for your specific Above Board.

            If in doubt of which address to choose, use address D000.
            The Memory_Address parameter is required in the EMM command
            line.

            Table 5   Memory_Address parameter choices


                        AboveTM Board AboveTM Board AboveTM Board 
                        PC & PS/PC     AT, PS/AT,   286 & PS/286
                                       286 & PS/286 (in 8088- or
                                       (in 80286-   8086-based
                                       based        computers)
                                       computers)   


                           C400          C000         C800
                           C800          C400         CC00
                           CC00          C800         D000
               Memory      D000          CC00         D400
               Address     D400          D000         D800
                           D800                       DC00
                           DC00                       E000
                           E000



                                                           page 7

            The I/O_Address parameters specify which I/O addresses Above
            Boards use to access expanded memory.  Assign a unique I/O
            address to each board.  No boards in your computer can share
            I/O addresses.  Use one I/O address for each Above Board
            with expanded memory.  Piggyback Memory boards don't need
            I/O addresses.

            If your old DEVICE=EMM.SYS line has an I parameter, replace
            the I parameter with the corresponding I/O_Address listed in
            Table 6.

            Table 6   I parameters and corresponding I/O_Address
                      parameters

                          I parameter    I/O_Address

                              0             208
                              1             218
                              4             248
                              5             258
                              6             268
                              A             2A8
                              B             2B8
                              E             2E8



                                                         page 8

            If you don't have an old DEVICE=EMM.SYS line, use an I/O
            address listed in Table 7.  Be sure your I/O_Address
            parameter values match the I/O addresses you selected when
            you set your Above Board switches or ran the SETBOARD
            program.

            If in doubt, use the addresses at 208 or 258.  The
            I/O_Address parameter is required in the EMM command line.

            Table 7   I/O_Address parameter choices

                          AboveTM Board AboveTM Board AboveTM Board
                          PC & PS/PC    AT & PS/AT    286 & PS/286

                              208           208         208
                 I/O          218           218         218
                 Address      258           258         248
                              268           268         258
                              2A8           2A8         2A8
                              2B8           2B8         2B8
                              2E8           2E8         2E8


            Example.  You're using two Above Board 286s in an IBM PC AT.
            You're installing expanded memory at D000.  One board is set
            for I/O address 208 and the other for 258.  Use this
            command:

            DEVICE=EMM.SYS at D000 208 258



                                                        page 9    

            Optional EMM command line parameters

            The EXP=x (expanded memory amount) parameter lets you 
            verify the amount of expanded memory in your 
            computer, where x is the amount in K bytes.  The 
            value for x must be a multiple of 16 and less than or 
            equal to 32768.

            The EXP=x parameter is optional.  If this parameter is in
            the command line, the EMM compares the number you specify
            (for example, EXP=512 for 512K bytes) with the amount of
            expanded memory it finds.  If the numbers aren't the same,
            you'll receive an error message.

            The ND (no diagnostics) parameter tells software to run
            abbreviated memory tests after a warm boot (Ctrl-Alt-Del).
            The ND parameter is optional.  If ND is in the command line,
            the EMM will run abbreviated memory tests; if ND is absent,
            the EMM will run full tests.  In either case, full tests are
            run during a cold boot (power-on).

            The NP (no pause) parameter lets you set the EMM not to
            pause after an EMM error or advisory message.  The NP
            parameter is optional.  If NP is in the command line, the
            EMM won't pause after errors or messages.  If NP is absent,
            the EMM will pause.

            CAUTION   
            Using the NE parameter can damage the data on your hard disk
            if extended memory exists on your Above Board.

            The NE (no extended memory tests) parameter lets you set the
            EMM so it won't run extended memory tests in an 80286-based
            computer when no extended memory exists on any Above Board.
            The NE parameter will save installation time since extended
            memory tests aren't run.

            The NE parameter is optional.  If NE is in the command line,
            no extended memory tests are performed.  If NE is absent,
            tests are performed.  Don't use the NE parameter if any
            extended memory exists on your Above Board.

            The H=x (handle count) parameter lets you tell the EMM to
            support as many handles as a particular application program
            needs.  A handle is a value that the EMM assigns and uses to
            identify a block of memory requested by an application
            program.  The EMM allocates memory based on the number
            entered.  Specifying a small EMM handle count can save
            conventional memory and allow EMM to run faster.

            The EMM handle count default is 64 handles.  Application
            programs written to use EMM versions below EMM 4.0 use a
            maximum of 32 handles.  If you're using older application
            programs, you may change the EMM handle count to H=32, but
            using the default of 64 handles will work fine.  The maximum
            value for x is 254 handles.



                                                         page 10

            The H=x parameter is optional.  If the H=x parameter is in
            the command line, the EMM will support the number of handles
            specified by x.  The handle count will appear on the screen
            when EMM is installed.  If H=x is absent, the EMM uses 64
            handles.  You won't see a handle count on the screen when
            EMM is installed.

            Example.  You're using one Above Board 286 in an IBM PC AT.
            Expanded memory is installed at D000.  The board is set for
            I/O address 208.  You have 1.5M bytes of expanded memory and
            no extended memory.  You want abbreviated diagnostics and
            your application program uses 128 handles.  Use this
            command:

            DEVICE=EMM.SYS at D000 208 EXP=1536 ND H=128

            Now that you're finished editing the CONFIG.SYS file, reboot
            your computer.  EMM 4.0 is installed and ready to go.

            If you want to set up RAM disks, a clock, or print buffer,
            go on to the next page.  If you already have RAM disks, a
            clock, or print buffer installed, you don't need to re-
            install them.



                                                        page 11

            Setting up RAM Disks and Clock

            To set up Above Board RAM disks or clock, copy QUIKMEM2.SYS
            (for expanded memory RAM disks), QUIKMEM1.SYS (for
            conventional memory RAM disks), or CLOCK.SYS (for the Above
            Board PS/PC clock) from this upgrade diskette to your hard
            disk or system diskettes.  (Refer to Table 1 for a list of
            the files.)  Then refer to your Above Board Shortcuts or
            Hacker's Guide for instructions to set up Above Board RAM
            disks or clock.

            Setting up a Print Buffer

            To install a print buffer, copy QUIKBUF2.SYS (for expanded
            print buffers) or QUIKBUF1.SYS (for conventional memory
            print buffers) from this upgrade diskette to your hard disk
            or system diskettes.  (Refer to Table 1 for a list of the
            files.)  Follow these instructions to create a print buffer
            -- don't use your Above Board Shortcuts or Hacker's Guide.

            To set up a print buffer each time you turn on or restart
            your computer, you'll need to add a command to your
            AUTOEXEC.BAT file.  Use any ASCII file editor (such as
            EDLIN) to edit your file.

            NOTE 
            You can have only one print buffer.  If a command in your
            AUTOEXEC.BAT file already sets one up, delete that command
            before adding a command described in this section.

            Creating a print buffer in expanded memory

            To set up the print buffer in expanded memory, use this
            command:

            QUIKBUF2  c  x  d  t

            The c parameter tells the QUIKBUF program what type of
            computer you're using.  The choices for the c parameter are:

                 at   For the IBM Personal System/2 Model 30
                      and 80286-based computers such as the
                      IBM PC AT and IBM PC XT 286.

                 pc   For 8088- and 8086-based computers
                      such as the IBM PC, IBM PC XT, and
                      COMPAQ DESKPRO 86.


            The x parameter specifies the size of the buffer in K bytes
            and must be 16 or greater.  Any value that isn't a multiple
            of 16 is treated as the next-higher multiple of 16.



                                                          page 12

            The d parameter tells the QUIKBUF program what display
            adapter your computer uses.

            Choices for the d parameter are:

                 M (or m)  IBM Monochrome Adapter.
                 H (or h)  Hercules Monochrome Graphics Adapter.
                 G (or g)  IBM, COMPAQ, Zenith, AT&T, or Hercules
                           Color Graphics Adapter.
                 E (or e)  IBM Enhanced Graphics Adapter.
                 O (or o)  All other adapters, including the
                           Hercules Graphics Plus Adapter.
                           Choosing this option disables the
                           print buffer command menu.  The
                           print buffer will still work, but you
                           won't be able to control it from the
                           command menu.

            The t parameter indicates the type of port to be buffered.
            The choices are:

                 P    Parallel (LPT1, LPT2, or LPT3)
                 S1   Serial (COM1)
                 S2   Serial (COM2)

            If you choose P, the first thing you print or the print
            buffer commands you use will determine whether the buffered
            port is LPT1, LPT2, or LPT3.  See the print buffer chapter
            in your Above Board manual for details.  If you omit the t
            parameter, the print buffer defaults to parallel.

            If you choose S1 or S2 as the type of port to be buffered,
            you may have to add one or two MODE commands to your
            AUTOEXEC.BAT file.  See the DOS manual or the serial port
            chapter in your Above Board manual for details.

            Example.  You have an IBM PC AT and an IBM Enhanced Graphics
            Adapter.  If you want a 160K-byte print buffer in expanded
            memory and you want to print your data on a serial printer
            attached to COM1, use this command:

            QUIKBUF2 at 160 E S1


                                                          page 13

            Creating a print buffer in conventional memory

            To set up the print buffer in conventional memory, use the
            QUIKBUF1 command, which is like QUIKBUF2 with one
            difference.  The x parameter value can be a decimal integer
            greater than or equal to 3.

            Example.  You have an IBM PC XT and a Hercules Monochrome
            Graphics Adapter.  If you want a 20K-byte print buffer in
            conventional memory and you want to print your data on a
            parallel NEC 3550 Spinwriter, use this command:

            QUIKBUF1 pc 20 H P


                                                         page 14

            Using the optional programs

            The programs listed here don't need to be run.  They're
            included on this diskette for your convenience.

            Table 8 describes the optional programs available on this
            upgrade diskette.  Here's how to start these programs:

            1    With your screen displaying the DOS prompt,
                 insert a copy of the Intel diskette into drive A.

            2    Type

            A:[command]

            and press Enter.  Replace the command parameter with the
            command listed in Table 8 for the specific program you want
            to run.

            Table 8   Optional programs on the Intel diskette


                 Program        Description             Command


                 CHKCOP.EXE     Tests the Intel math    CHKCOP
                                coprocessor.

                 CHKMEM.EXE     Confirms the amount of  CHKMEM
                                conventional, extended
                                (80286-based computers
                                only), and expanded
                                memory in your computer.

                 SETBOARD.EXE   Sets up the hardware    SETBOARD
                                configuration for the
                                Above Board 286 and
                                PS/286 ONLY.

                 TESTAB.EXE     Tests and pinpoints     TESTAB
                                bad RAM chips on your
                                Above Board.



                                                        page 15

            Customer support

            If, after reading these instructions, you have questions
            about the EMM 4.0 upgrade, please contact Intel's Customer
            Support at one of these numbers.

            o    From the United States and Canada, call
                 (800) 538-3373.

            o    From outside the United States and Canada,
                 call (503) 629-7354.

            If your computer has a modem and you subscribe to
            CompuServe, you can reach Customer Support through:

            o    CompuServe mailbox 70307,461.

            Bulletin board service

            In addition to toll-free customer support, Intel also
            maintains an electronic bulletin board.  This bulletin board
            contains software updates, helpful tips, and the latest news
            about our products.

            If you have a modem and a terminal emulation program (such
            as CROSSTALK, PROCOMM, or Smartcom) you can call our
            bulletin board 24 hours a day at the following number:

                 (503) 645-6275

            To access the bulletin board, your modem must operate at
            300, 1200, or 2400 bits per second (BPS).  Set the modem for
            no parity, eight data bits, and one stopbit.  For example,
            if you're using a 1200 BPS modem, set the parameters as
            follows:

                 1200,N,8,1

            The bulletin board will ask you for information and then
            list the services available.