LIGHT PEN TESTER


	 The Light Pen Tester program will run some fairly simple tests
	 of your light pen including color sensitivity, and pen circuitry
	 accurracy in both text (40 and 80) columns and in low-resolution
	 graphics mode.

	 The light pen was never intended as a precision drafting device,
	 most sophisticated CAD systems use pens as menu selectors and
	 gross area pointing devices.

	 As you will notice while running the program, it is quite likely
	 that the coordinates returned by the pen circuitry do not match
	 the known coordinates of the point on the screen.  In the majority
	 of cases, the Y coordinate is accurate, but the X coordinate is
	 less than actual.

	 Pen coordinates are computed based on the amount of time it takes
	 the CRT beam to reach the pen location.  The circuitry then
	 computes how many scan lines have been drawn (Y coordinate), and
	 how far into the current line the pen detected the beam (X
	 coordinate).  Thus, there is much more room for error on the X
	 coordinate computation.  This explains why a point at the very
	 beginning of a line may be detected at the end of the previous
	 line.

	 With an FTG light pen (good quality), the error is approximately 7
	 or 8 pixels in medium resolution.

	 The color being detected also has a bearing on the pen response.
	 Most phototransistors or photodiodes used in modern light pens are
	 much more sensitive to blue than they are to red.  The color
	 sensitivity test will show this characteristic if you turn the
	 intensity of your monitor down.  With a standard IBM C/G adapter
	 and an IBM RGB monitor, the FTG pen is insensitive to red, almost
	 insensitive to brown, and erratic on grey.  Pen response will also
	 be faster in the blue end of the spectrum.

	 A common programming technique used to compensate for pen error is
	 to compute the average error in the desired resolution.  The
	 program should then take two consecutive X-coordinate readings.
	 If the difference between readings exceeds two or three pixels,
	 two additional readings should be taken etc... until the two
	 readings are reasonably close.  The error should then be added to
	 the X coordinate to compensate for timing delays.  The following
	 BASICA sample illustrates this technique:

	 100 x%=pen(4):x1%=pen(4):if 2>abs(x%-x1%) then 100

	 Light pens are great menu selectors.  Just stay away from the last
	 couple of positions in a line to avoid problems.

	 Address any comments to Dan Moore, Arvin Industries, 1531 13th.
	 St. Columbus, IN 47201