NMI Version 1.01





       Have you ever seen the message 'PARITY CHECK' on your display?  If
    you have, you've probably noticed that it always seems to happen at the
    most inopportune time.  You're cruising along putting the finishing
    touches on something that you've worked long and hard, just to look up
    from the keyboard to a blank display with only the words 'PARITY CHECK'
    in the upper left corner.  Your heart sinks into your shoes, your face
    gets flush, and palms begin to sweat, as you try franticly to figure a
    way out of this one... but you KNOW that you've lost everything!  Your
    only option is to power off and start over.

       The IBM-PC is a great machine, and parity checking is a wonderful
    concept, but I've always wished that I had been given a choice before
    the machine was put to sleep.  Even more, I've wished that somehow the
    machine could have told me where it hurts before it died.  I've never
    gotten much of anything by wishing, so I sat down to attempt to remedy
    the situation.

       NMI is a resident program to replace the non-maskable interrupt
    handler that the PC uses to handle parity errors.  In the event of a
    parity error, NMI will interrupt the currently executing program(s) and
    begin testing memory, looking for the error.  It will continue testing
    until either it locates a failing address, or you interrupt it by
    pressing a key.  If a failure is located, NMI will display the failing
    64K bank, exact memory address, and bit(s).  You have the option to
    continue or terminate testing.  If you interrupt the memory test, or
    elect not to continue testing after an error is detected, you are given
    the options to return to the interrupted program(s) with or without
    parity checking enabled, or to reboot the system.

       The memory test is of a non-destructive type, in that it will
    preserve the current contents of memory.  It can be executed any time
    without regard for concurrently executing processes.  It's also a very
    thorough test, reading and writing each byte of memory with several
    different bit patterns and checking for parity errors following each
    read or write operation.  Every memory location is tested, including
    the locations used by NMI.

       This all sounds a bit like insurance doesn't it?  It doesn't do you
    a bit of good unless you have a tragedy on your hands.  Well, I like
    programs that you can play with, and since you've got this neat little
    memory test just sitting there in memory, why not be able to use it?
    NMI will execute the memory test any time you like, as many times as
    you like!

       If you're like me (a memory miser), the question in your mind right
    now is... 'Just how much memory does this thing eat?'.  The answer,
    approximately 1.8K including the Program Segment Prefix and a normal
    size environment.  In English, that means about 1.8K TOTAL!  Even I can
    afford that.


                          NMI (Non-Maskable Interrupt)





    PROGRAM LOADING
    ---------------

       NMI /N/I/T####
            | | |
            | | Test memory #### times.
            | |
            | |   If the number of test repetitions is 0 or blank, then the
            | | memory test loops indefinitely until an error is detected
            | | or you interrupt it by pressing a key.  This option may be
            | | used to invoke the memory test from the command line or a
            | | batch file.  NMI need not be installed to run the memory
            | | test.
            | |
            | Install NMI.
            |
            |   This option must be selected the first time NMI is executed
            | if you desire to replace the current non-maskable interrupt
            | handler.  It need not, and should not be specified again.         |
            |
            No program logo display.

              This option is selected to suppress display of the program
            logo when NMI is installed.


    *  If no parameters are specified, or the specified parameters are
       invalid, NMI will display the program logo followed by a summary of
       valid parameters.

    *  Parameters need not be separated, however, they may be separated by
       one or more spaces, tabs, commas, slashes, or semi-colons.

    *  Alphabetic parameters may be upper or lower case.

    *  Parameters may be entered in any order or combination so long as the
       number of test repetitions follows the 'T' parameter and they are
       not separated by another parameter.


                          NMI (Non-Maskable Interrupt)





    +--------------------------+
    |   TESTING ####K MEMORY   |
    | Bank    Bit     Address  |
    |  00  P76543210 0000:0000 |
    |        0000 Passes       |
    +--------------------------+

       When the memory test is invoked, either as the result of a parity
    error, or from the command line, the above window will be displayed in
    the upper left corner of the screen.  This window indicates the size of
    the memory being tested, as sensed by NMI, the 64K bank currently being
    tested, and the number of successful test repetitions.  In the interest
    of speed, the 'Address' field is updated only for each 64K bank in this
    window.  The 'Bit' field is used to indicate failing bits and will not
    change unless an error is detected.

       If the 'Esc' key is pressed, the memory test will be terminated with
    parity checking enabled, and control passed to the interrupted process.
    Any other key will exit the memory test and display the termination
    options.

       The memory test takes approximately 35 seconds per 64K bank, longer
    depending upon other system activity.



    +--------------------------+
    |   ** ERROR DETECTED **   |
    | Bank    Bit     Address  |
    |  00  P76543210 0000:0000 |
    | Continue testing? _      |
    +--------------------------+

       In the event that an error is detected during the memory test, the
    above window will be displayed.  This window indicates the failing 64K
    bank, exact address, and bit(s).  Depending upon the display type and
    video mode active at the time of the failure, the failing bit(s) will
    be indicated either by blinking, or non-display.  These bit(s) directly
    correspond to the failing chip(s) in the indicated 64K bank.

       Pressing 'Y' (or DDY) will continue the memory test starting with
    the next byte.  The number of successful passes will be reset to zero.
    Pressing 'N' will exit the memory test and display the termination
    options.


                          NMI (Non-Maskable Interrupt)





    +--------------------------+
    | 1) Continue with parity  |
    | 2) Continue w/o  parity  |
    | 3) Reboot system         |
    | Enter selection: _       |
    +--------------------------+

       The termination option window is displayed as a result of any key
    other than 'Esc' being pressed during the memory test, or electing not
    to continue testing following an error detection.  Selecting option 1
    will return to the interrupted process with parity checking enabled.
    Selecting option 2 will resume the interrupted process without parity
    checking.  Option 3 will reboot the system.  Pressing DDY will restart
    the memory test.



    RETURN CODES
    ------------

       If NMI is invoked from within a batch file, or by another process, a
    return code may be retrieved indicating any errors.  For batch files,
    the return code may be interrogated using the 'IF ERRORLEVEL' batch
    subcommand.  The following table indicates possible return codes for
    the current release.

          0 - Successful, no errors detected.

          1 - Error detected in parameters, program aborted.

          2 - NMI was invoked with the 'I' parameter, but is already
              installed.  Installation aborted.

          4 - Memory test already active, no memory test performed.  This
              error can occur in multi-partition systems if memory test is
              called while active in another partition.

       It is possible for more than one error to be returned in the return
    code.  For example, a return code of 6 indicates both errors 2 and 4
    occurred.




    PROGRAM DESIGN CONSIDERATIONS
    -----------------------------

       Certain performance and function trade-offs are made in the design
    of every program.  These trade-offs are usually made in an attempt to
    provide the most function within the constraints imposed by the
    operating environment in which the program must run.  In this case, the
    following criteria were taken into consideration.

    1) All resident programs must use the smallest possible amount of
       memory.

    2) During the memory test, it is assumed that a memory failure has
       occurred.  It is possible that the memory failure occurred in the
       resident portion of DOS.  For this reason, DOS function calls must
       not be used within the resident NMI code.

             No attempt is made to save and restore the contents of
           graphics screens.  This would have required additional code
           and buffer space within the resident portion of the program.
           If a disk file had been used to save the video buffer, DOS
           function calls would have been required, increasing the
           possibility of program check during the memory test.

    3) The memory test should first attempt to find the failure using a
       read operation, so that the original failure remains undisturbed.
       If the read operation fails to produce the error, only then should
       write operations be used.  Furthermore, the failure should be
       located in a single pass through memory, if possible.  This method
       will provide the best odds of locating an intermittent failure.

             Memory test execution is slow, only because the test is
           thorough.