WATCHDOG timer handler, Version 1.0
Copyright 1988 by Ken Sykes.  All rights reserved.

This program may be used freely as long as the copyright notices are
preserved and it is not sold for profit.  The author makes no warranties,
expressed or implied, of the accuracy or fitness of this program.

DESCRIPTION
   This program takes advantage of timer channel 3, the watchdog timer,
to avoid cold boots after a system crash.  The watchdog monitors channel
0 (system timer) and decrements its counter if a system clock tick occurs
while IRQ 0 is active.  In other words, if the system timer interrupt is
not available to service the tick, the watchdog counter is decremented.
If the watchdog counter reaches 0, an NMI is triggered.
   WATCHDOG enables the watchdog timer and provides an NMI routine that
restores the machine stability to the point where the keyboard will be
serviced properly.  In particular, software interrupts are enabled and
the 8259A Mask register is set to enable keyboard interrupts.  Bus 
arbitration, which was turned off for the NMI, is resumed again.

This timer is available ONLY on PS/2 Models 50 and above.

USING WATCHDOG
    To install watchdog: watchdog
  To uninstall watchdog: watchdog u  (must be lowercase 'u')
  If the system hangs, press CTRL-ALT-DEL as always

KNOWN BUGS
  - Only a portion of the used memory is reclaimed during an uninstall
  - Once the NMI is triggered, the watchdog is disabled forever (?)
    Originally the watchdog was re-enabled on exit from the NMI, but
    system resets would not work properly.  The code as-is seems to
    break out of VERY tight loops and out of multiple areas of disabled
    interrupts.  I would welcome explanations of why this works (or doesn't
    work) from people who have used this timer.

RESTRICTIONS
  CodeView and Symdeb grab the NMI interrupt, thus knocking WATCHDOG out of
the picture.  Well almost.  If the system DOES hang, an NMI is still triggered
but it is the debugger's NMI routine that is activated.  Rebooting at this
point does not work.  This is due to the arbitration being turned off and the
watchdog timer still active.  Thus, it is a good idea to uninstall WATCHDOG
before using the debuggers.