RECALL                g.r.a.m.  Associates                 RECALL



         Purpose:  Recall permits the user to retrieve any one of up to 50
             unique DOS commands previously issued by the user.  Once
             retrieved, the command may be executed as is or modified by
             the user via the normal DOS line editing keys.

         Usage:  RECALL [-qb?]
                       -q  Suppresses the initial help screen when Recall
                           is loaded.
                       -b  Suppresses the loading and the end-of-buffer
                           bells.
                       -?  Produces a help screen without loading Recall.

         Operation:  F10         - recall the next oldest command.
                     Alt-F10     - recall the next newest command.
                     Shift-F10   - toggle the recall feature on and off.

         Note:  Attempts to recall beyond the first command issued (or the
             last command) are accompanied by a chirp (the end-of-buffer
             bell).  Recall will subsequently wrap around to the last
             (first) command.

         Examples:  Although the most meaningful examples will occur quite
             naturally with daily use, the following examples should help
             get things started.

             1) The goal is to get before and after printouts of the
             tabular data file mywealth.dat as produced by a BASIC program
             myprog.bas.  (It is assumed that the table requires the
             printer to be in 132 column mode for a readable printout and
             further that BASIC resets the printer.)

               Keystrokes        DOS screen               Comments
               ==========        ==========               ========
             1-Enter com-      A>dir my*.*                List files
             2- mands as       A>mode lpt1:132            Set printer
             3- shown after    A>copy mywealth.dat prn:   Print file
             4- DOS prompt.    A>basic myprog             Run program
             5-F10,            A>\
                   F10,F10     A>mode lpt1:132            Reset printer
             6-F10,            A>\
                   F10,F10     A>copy mywealth.dat prn:   Print new file

             2) Sometimes a rapid fire trigger finger will strike key F10
             too often, thus overrunning the DOS command.  In such a case
             the Alt-F10 combination may be used to return to the missed
             command.

               Keystrokes        DOS screen               Comments
               ==========        ==========               ========
                                 ...                      See example 1
             4-Enter as shown  A>basic myprog             Run program
             5-F10,            A>\
                   F10,F10,F10 A>dir my*.*                Oops!



                              RECALL V2.10   Page 1





         RECALL                g.r.a.m.  Associates                 RECALL


             6-Alt-F10         A>\
                               A>mode lpt1:132            Got it!
             7-F10,            A>\
                   F10,F10     A>copy mywealth.dat prn:   Print new file

         Caveats:
             - The DOS type ahead feature is disabled when using F10.
             - Recall will not work concurrently with FileCommand by IBM
             while it is attached to DOS.
             - Recall may fail if the total memory is changed to a non-4K
             multiple.
             - No known bugs.

         Technical:  The motivation for Recall was to provide a natural
             extension of the DOS F3 key which restored only the very last
             DOS command executed.  When first run, Recall attaches itself
             to DOS and chains itself onto the keyboard interrupt vector
             thus becoming poised to sense all F10, Alt-F10, Shift-F10 and
             other related keystrokes.  To prevent interference with other
             programs which use the function keys, Recall intercepts the
             DOS function calling mechanism and verifies that the user is
             at the DOS prompt level before processing any keystrokes.
             Moreover, Recall prevents multiple copies of itself from
             occupying memory by sensing its existence as an extension of
             DOS.  Recall reduces available memory by 8016 bytes.
                  Only the following versions of PC-DOS are currently
             supported: V1.1, V2.0, V2.1.  Support for any other IBM and
             compatible versions of DOS will correspond to interest and
             availability to the authors.
                  It is recommended that the loading of Recall be incor-
             porated into the boot-up procedure (autoexec.bat).


                              User Supported Software

                  If you have used this program and found it of value,
                  your contribution ($10 suggested) will be appreciated.
                  Regardless of whether you make a contribution, you are
                  encouraged to copy and share this program.  Users
                  sending in a contribution of $10 or more will be
                  entitled to a free update and notification of other
                  utilities as they become available.

                  Send all correspondence to:

                              G.R.A.M. Associates
                              User Supported Software
                              450 N. Jordan Street
                              Allentown, Pa.  18102








                              RECALL V2.10   Page 2



                                                                                                      RECALL V2.10   Page 2