September 12, 1986


SQZ6300 - - HOW TO FORMAT 20MB DISK TO 2K CLUSTERS

The  following  procedure  permits the formatting of a 20MB  hard
disk  running  on the AT&T 6300 to a cluster size of 2K, compared
to  the  present standard (MS-DOS 3.1) of 8K.  This  allows  much
more  efficient use of the available disk space, particularly for
small files.

    A. USING PC-DOS 3.1 (or later), perform the following:
       1. Load FDISK (i.e. from PC-DOS disk).
          a) Instruct  FDISK  to delete all DOS partitions on the
             hard disk.
          b) Create a new DOS partition.

       2. FROM PC-DOS, load FORMAT.

       3. Format  the  hard  disk with the  /S option  (i.e  type
          A:FORMAT C:/S).

    B. Transfer MS-DOS 3.1 COMMAND.COM back to the root directory
       of  the hard disk (it will work equally as well as the PC-
       DOS  version).  DO NOT destroy the hidden files already on
       the disk.

    C. At  this  point, the disk is ready to use.   However,  the
       AT&T  Clock  will not function.  To restore  normal  clock
       operation,  place  the files  TIMER.COM  and  SETCLOCK.EXE
       to  the  root  directory  and   execute  them  out  of  an
       AUTOEXECUTE.BAT file as follows:

                        TIMER
                        SETCLOCK/S

          Notes:  1. SETCLOCK.EXE  sets the hardware and software
                     clocks  from  the keyboard,  or (with the /S
                     option  simply transfers the contents of the
                     hardware clock to the software clock.
                  2. TIMER.COM  corrects a slight (3%) difference
                     between the clock frequencies of the IBM and
                     the 6300.