C A C H E
                          Documentation
                            07/23/84



     In  the effort to provide the  best internal  solutions  to
your hard disk needs,  we  now  offer  a software program to increase
hard disk performance.



DESCRIPTION

     CACHE  is a software program designed to increase  the  hard 
disk  operating  speed.   This speed increase is accomplished  by 
monitoring  all  disk accesses,  and keeping  the  most  recently 
accessed sectors in the ram memory allocated to the CACHE program.


     When  DOS requests access to a sector,  the CACHE ram memory 
is checked first to see if the desired sector is already present. 
If  so, the sector is returned to DOS without any  disk  accesses 
occuring. This greatly increases speed since ram access is faster 
than disk access.   If the desired sector is not present in CACHE 
ram,  it will then be read in to memory and placed into the CACHE 
ram and returned to DOS.   When this occurs,  the least  recently 
used  sector in CACHE ram is overwritten,  this insures that only 
the most recently used sectors will remain in the CACHE ram.  The 
more ram memory allocated, the faster the system will run.



INSTALLATION

     The  best  way to install the CACHE is to  place  the  CACHE 
command  in  your AUTOEXEC.BAT file so that it will be  installed 
every  time  you boot your system.   The CACHE  command  has  the 
following format:


               CACHE     [size] [-options]


     Where:

          [size] - specifies the amount of memory, in K bytes,
                   to allocate for the CACHE ram buffer.  The
                   size specified must be greater than or equal
                   to 8K.



          [-options] - specifies one of the following:

                    -a   reactivate the CACHE

                    -d   deactivate the CACHE

                    -s   display the current CACHE status

                    -u   update the unwritten buffered sectors
                         to disk.

                    -w   activate buffered write mode

                    -x   deactivate buffered write mode


OPTIONS

     The  -a  and -d options are used to activate and  deactivate 
the CACHE.   When the  CACHE is not  active all disk accesses are 
passed through without buffering anything in the CACHE ram, as if 
CACHE was not installed.


     The -s option will display the current status of the copy of 
CACHE  which is actually installed.   It will tell you  how  much 
memory  is allocated,  whether the CACHE is active or not active, 
and whether buffered write mode is active or not active.


     The  -w and -x options are used to activate  and  deactivate 
buffered  write mode.  Normally when DOS writes a sector to disk, 
it will be moved to the CACHE ram and written to the disk  before 
returning  to DOS,  which means CACHE does not increase the speed 
of disk writes.  If buffered write mode is active, and DOS writes 
a sector to disk, it will be moved to the CACHE ram and marked to 
be written to disk at a later time; so return to DOS is immediate 
without the delay of the physical disk write.  The buffered  disk 
sectors  will  be  written  to  disk (synced)  when  one  of  the 
following occurs:

          1. CACHE is deactivated.
          2. Buffered write mode is deactivated.
          3. CACHE -u  command is issued.


     The -u option is used to update the hard disk by writing any 
unwritten buffered sectors to disk.


     **WARNING**  Buffered write mode should only be used if  the 
system is running on  an uninteruptable power supply.  If for any 
reason the system loses power,  gets reset,  or is rebooted,  and 
buffered  write mode is active and the CACHE had not been updated 
your hard disk will be corrupted, which will require you to go to 
a backup.  When using the CACHE in buffered write mode, make sure 
you  issue the CACHE -u command before rebooting or powering  off 
the system.


     If  the  FORMAT command is issued to format  the  hard  disk 
while CACHE is active, CACHE will automatically deactivate.
 



EXAMPLES


     The  following  would  install  the CACHE with  a  256K  ram 
buffer:

               CACHE 256



     The following would display the status of the CACHE  already 
installed:

               CACHE -s



     The following would deactivate the version of CACHE  already 
installed:

               CACHE -d



     The following would install the CACHE with a 180K ram buffer 
and activate buffered write mode:

               CACHE -w 180



     The  following  would update the unwritten buffered  sectors 
onto disk (only needed if buffered write mode is active):

               CACHE -u



     The following would reactivate the cache and enable buffered 
write mode.

               CACHE -aw