This program was developed as an alternative to IBM'S "ADVANCED DIAGNOSTICS"
for the hard disk. Although you get more than a hard disk diagnostic with
IBM'S diagnostics, you pay $295 for the package. All I ask in return for
the FREE use of this diagnostic is that you do not change the copyright
nor charge for distribution of this program.

Any problems or suggestions should be forwarded to:

			   JIM BRACKING
			967 PINEWOOD DRIVE
			SAN JOSE, CA 95129
			  (408) 725-0628



PROGRAM FEATURES
----------------

This program is menu driven and in most cases should be self-explanatory. It
run on a IBM AT, PC or compatible computer.

The diagnostics are divided into two categories, destructive and non destructive
tests. These tests can be useful in installing a new disk, finding and
flagging bad data areas or testing the general working condition of your hard
disk and controller.


NON-DESTRUCTIVE TESTS
---------------------

In an IBM compatible hard disk bios the last cylinder is reserved for running
diagnostic tests on. This program uses that cylinder for diagnostic writes.

F1.......WRITE/READ/VERIFY TEST     This test verify's that read and write work
				    by writing one sector then reading it and
				    comparing it to the value it wrote.

F2.......SEEK TEST		    This test first verify's every cylinder
				    then exercises the read/write heads by
				    performing a crossing seek pattern.

F3.......HEAD SELECT		    This test selects one head on every
				    cylinder.

F4.......ECC TEST		    Most controllers have some form of onboard
				    error correction that writes four bytes of
				    ECC data with every data record. When the
				    data is read these four bytes of ECC are
				    used to determine the validity of the data
				    and make corrections for any incorrect
				    bits depending on the controller. This test
				    does a read long, modify's four bits and
				    write's the record back with a write long.
				    The next read should return the corrected
				    data.

F5.......RUN ALL TESTS		    This runs tests 1 through 4 and allows the
				    the user to loop up the tests.

F6.......PREPARE FOR RELOCATION     Moves the read/write heads to the landing
				    zone. The computer should be shut off after
				    executing this or the heads will move back
				    onto the data surface.

F7.......DEFECT SCAN		    Reads every sector the specified number of
				    times and reports the errors.


DESTRUCTIVE TESTS
-----------------

F8.......SURFACE ANALYSIS	    This test writes the worst case data
				    pattern (6DB6) on every sector and reads
				    it back three times. If any errors are
				    found they are reported and the track if
				    flagged.

F9.......FORMAT DISK		    This performs a physical format of the hard
				    disk and should not be confused with DOS
				    format. If you are formatting a disk for
				    the first time then you should specify "y"
				    to clear the defects, otherwise a quick
				    scan will be made to identify any flagged
				    tracks. After the format is done the tracks
				    that were flagged as bad will be flagged
				    again.

F10......FLAG DEFECTS		    Its a sad but true fact that most hard
				    come from the factory with some known
				    defects and some will be developed over
				    time. This routine is used to flag those
				    defects to prevent any data from being
				    written there.

A-F10....FORMAT TRACK		    The same as the format drive except it
				    only formats one track.



MISCELLANEOUS FUNCTIONS
-----------------------

A-F9.....TOGGLE PRINTER ON/OFF	    The printer can be used to log any errors.

A-F10....EXIT			    Return to DOS