HDPROTEK   -  Documentation         Version 1.0
Written By Craig Newlander
(C) Copyright @1988, By Comlink Data Systems of Chicago

HDPROTEK -> Hard Drive Protection

This program is Public Domain and may be freely distributed.

Use this program at your own risk.  I will not be responsible for
damages arising out of the use of, or your inability to use  this
program.   If  you have any questions concerning this program you
can reach me via US MAIL.

This program has been developed to protect  your  hard  drive  by
"VIRUS" or "TROJAN" type programs.

This  Program  disables  any  access  to  the  hard drive bios by
replacing the interrupt vector at interrupt 13h with the original
diskette  routine  (which  the fixed disk bios saves at interrupt
40H).  It  should   be   used  when  testing  new  programs, thus
providing  protection  from  intended damage of files on the Hard
Drive.

This program should not be run on machines without a hard  drive,
since  nothing  will  be  at interrupt 40H, and int 13H will then
contain garbage.

Before running this program it is  advisable  to  issue  the  DOS
command  "SET  COMSPEC=A:\COMMAND.COM"  to  ensure  that  DOS can
reload the command processor after the hard drive disappears.

To run this program simply  place  hdprotek.bas,  basic.com,  and
command.com   onto  a  diskette.   Then  issue  the  command  SET
COMPSEC=A:\COMMAND.COM.  Next Enter the command "BASIC HDPROTEK".
The  Hard   Drive  will  be  disabled.   You  might still see Dir
listings but you are only viewing the buffers.  This will go away
after a few accesses to the diskette drives.

Once  you  have  run  the program, any  access to  the hard drive
will cause a  "General Error Reading drive x" or similar message.
You  can  enable  the hard  drive by running the program a second
time.   This program creates a  file called "HDPROTEK.INT" in the
default  directory.  It  is important that  this file  be present
when attemping to enable the hard drive.  If this file is damaged
or erased you can only get the access back by re-booting.

This program is distributed in source  code  so  you  may  verify
yourself that it does what it is advertised.

Comlink  Data  Systems  -  PC Custom Programming and Consultants.
BBS phone number -> 312-267-4427 2400bps 24hr.