The programs in this file were written by Steve Gibson of
Gibson Research Corp  Box 6024  Irvine, Ca  92716

The programs will determine the hard disk performance of any IBM
compatable computer.  These programs have been tested and found to
be safe and NOT destroy data on any hard disk.  However since this
program is made available on BBS's, no guarantee is made if downloaded
from any board other than the Riverside Premium BBS 312-447-8175 where
I personally entered the code and tested the output.

If you obtain this program from any other source I would recommend that
you take normal precautions (BACKUPS).

The source code for creating the COM files is included and was compiled
under QuickBasic version

The programs included are;

 SPINTEST and SPINTIME

 SPINTEST determines exactly how many revolutions your hard disk
          currently requires for full track transfers.  Dos transfers
          a full track whenever programs or files larger than 9k are
          read or written... which is most of the time.  SPINTEST
          does NOT directly read your drive's interleave, but its
          interleaving performance can be easily inferred from
          SPINTEST's full track transfer revolution count.

SPINTEST  averages the time required for each of over two hundred full
          track reads in order to accurately determine the revolution
          count per read, then the number of revolutions required to
          read just one track and the controller's full-track data
          transfer rate are computed.  SPINTEST only READS data from your
          drive so data is never altered.

          Over two hundred track reads were used as a result of the
          inconsistent disk transfer behavior of AT&T's 6300 machines.
          These exhibit a maddening inconsistency in their ability
          to transfer disk data.  Sometimes they get the next sector
          and often not.  This means that a much looser than normal
          interleave generates the best overall throughput for AT&Ts.
          For this reason, and to guarantee correct results on any
          machines which might behave similary, SPINTEST performs
          many track reads and averages the results.

SPINTIME  Since SPINTEST measures track read time, it must assume a
          given ratio between elapsed time and disk rotation rate.
          Some weirdo clone computers have a clock which runs faster
          than normal when in TURBO (8mz) mode, and some lap computers
          have tiny hard disks spinning at strange speeds.  If these
          do not sound like your situation SPINTEST will deliver
          correct readings and you'll not need SPINTIME's confirming
          measurements.

          But if EITHER of these cases might be you SPINTIME will tell
          you for sure.  SPINTEST is only useable when SPINTIME gives st
          standard readings.  The single exception to this is for the
          AT&T 6300 and 6300 Plus machines.  Due to the overall
          problems they experience with disk transfers, SPINTIME may
          show a lower-than-3600 RPM reading.  For these machines
          this is acceptable.

          SPINTIME is interesting since it determines EXACTLY how fast
          your hard disk is really spinning.

RUN TIMES

         SPINTEST
           The time required to run this test will vary between
           approximately 14 seconds for a fast 2:1 interleave to
           98 seconds for an incorrectly interleaved 26-sector
           RLL encoded hard disk.  So simply type:  SPINTEST at the
           DOS prompt and wait a minute or two.  The results will
           be displayed on the screen.

         SPINTIME
           This program has two purposes:  To determine the speed of
           your system's clock, and to verify that your system's hard
           disk is spinning at close to the 3600 RPM standard.
           Your system's clock is checked by timing SPINTIME's exact
           execution time.  It should require EXACTLY 60 SECONDS to
           run, no matter what.  During that time it is busy watching
           your hard disk spin, counting every revolution.  After
           EXACTLY 60 seconds, it displays your drives exact RPM
           (within its measuring resolution).  If SPINTIME's total
           execution time is NOT EXACTLY 60 seconds or the displayed
           RPM is not close to 3600, SPINTEST's reported revolution
           count won't mean anything either.

           SPINTIME's real value is to assure you that SPINTEST is
           delivering worthwhile answers.

IMPORTANT NOTES

           Both programs assume and require DOS 2.0 or higher.  They
           operate on your FIRST (C) drive only.  It should not require
           any special CONFIG.SYS drivers for operation.
           The tests will also be more accurate if you do not have any
           memory resident programs active.  Many of these resident
           programs "steal" so much time from the computer that a
           delicate timing analysis could be upset.  Also turn off
           or remove any disk caching software.  Disk caching intercepts
           the disk reading performed by the programs and renders their
           measurements invalid.  By the way, disk caching program
           performance is significantly improved through proper
           disk interleaving.


My thanks to Steve Gibson for providing these programs.

As an additional note, Gibson Research has designed a quick and
painless software product which handles the entire chore of optimizing
and resetting a hard disk's sector interleave while leaving all
existing data in place.  The product will also perform several
other functions relating to assuring an MFM or RLL drive's data integrity.

The product is expected to be available for shipping within the next
two weeks for $29.  If you are interested in more information on
this new product or FlickerFree contact
Steve Gibson
Gibson Research Corp
Box 6024
Irvine, CA 92716

Be sure to mention you heard about it from the Riverside Premium BBS
in Riverside, IL  312-447-8175

May all your disks live longer and spin faster.   Spock