ANSI.SYS screen driver

        MS/PC-DOS 2  and  higher  allow you to install  software  "device 
        drivers"  when  you boot your computer.   These  are  essentially 
        extensions  of the operating system to handle specific pieces  of 
        hardware.   To run WSSINDEX,  most systems need to use the screen 
        driver  ANSI.SYS,  otherwise  the  control  sequences  which  are 
        supposed  to  select  colors,  position the cursor or  clear  the 
        screen will instead appear as characters on the screen.

        Installation of ANSI.SYS is simple:

        Check  your  boot disk with the DIR command to see if you have  a 
        file  called  CONFIG.SYS.    If  not,   use  your  favorite  word 
        processing program to create such a file,  and include in it  the 
        line
                  DEVICE=ANSI.SYS

        Either  upper or lower case is allowed,  but if you use an editor 
        such  as WordStar which can encode formatting information in  the 
        text,  be  sure  to  specify  non-document  mode.   If  you  TYPE 
        CONFIG.SYS, you shouldn't see any funny graphics characters.

        If you already have a CONFIG.SYS file,  simply add the above line 
        to it with a word processor, again in non-document mode. 

        Make  sure  that  the file ANSI.SYS is on your  boot  disk,  then 
        reboot your system.  Watch for any error messages during the boot 
        process.   The display should now be much more intelligible  when 
        you run WSSINDEX.

        Notes:

        1.  The  Dec  Rainbow and the Sanyo 555 (without the video  board 
        option)  don't  need ANSI.SYS because these functions  are  built 
        into the operating system.  There are probably other machines for 
        which  this is also true.   It is verrrrrry obvious if  you  lack 
        ANSI support.

        2.  ANSI.SYS  is not particularly fast at screen display.   There 
        are alternative commercial,  shareware and public domain programs 
        with names like FANSI.SYS,  NANSI.SYS,  which do a better job  on 
        IBM-PC compatibles.

        3.  I  have one user who complained that ANSI.SYS interferes with 
        some other applications software he uses.   This is unusual,  but 
        apparently not impossible.  The work-around is to have a separate 
        boot floppy disk for the configuration you use less frequently.

        Robert W. Babcock
        WSS Division of DDC
        4 Reeves Road
        Bdeford, MA  01730
        USA
        617-275-1183