Documentation for NARCCFG.EXE

   
                            Written by Gary Conway


                         Infinity Design Concepts, Inc


                              Copyright 1987,88









	IMPORTANT.	NARCCFG.EXE is NOT compatible with previous version(s)
			of NARC, that is version(s) prior to 1.1


		The main menu gives 7 options.

			0 - Exit NARCCFG.EXE (with save/abort option)
			1 - Customize Screen Colors for NARC.EXE
			2 - Customize Printer Strings for NARC.EXE
			3 - Restore All NARC defaults to those as released
			    in NARC.EXE
			4 - Toggle Sound Routines ON and OFF
			5 - Mouse Sensitivity
			6 - Video write method

NOTE: 	NARCCFG reads NARC.EXE and will show you the current configurations
	of all of the options. NARC.EXE -MUST- be in the same
	directory with NARCCFG.EXE and must be named NARC.EXE.

Exiting....

		When you choose the Exit option, you will have the
	opportunity to abort any changes that you may have made while
	running NARCCFG.EXE, or you may save them. Saving the changes
	causes NARC.EXE to be modified with whatever changes you have
	made and will reflect these modifications the next time NARC is
	run.


Customizing Colors....

		You will be shown a dummy NARC screen. The function keys
	are labeled on screen as to which colors they will change. The
	changes take place immediately on screen, so it is easy to see
	just what effect your changes will have. The ALT key in conjunction
	with any of the function keys will toggle high and low intensity.
	Hit the ENTER key when you are finished. The B and C keys are also
	used for determining the monitor type. The B key will force NARC
	to come up in black and white mode, regardless of the video adapter
	type that NARC discovers.

Printer Strings....

		There are three printer strings used in NARC.EXE. At print
	time, you have the option of sending any one of the three strings.
	You may enter up to 8 characters for each printer string. You can
	enter things like CTRL-P or the ESCape key. NARCCFG makes a distinction
	between upper and lower case on the printer strings, so make sure
	you use the shift key if necessary. The NULL character is enterd by
	the space bar, so if you only need to enter 2 characters for a string,
	NULL the remaining characters out. This will cause NARC to send your
	2 charcters and then 6 NULLs.

	NOTE: 	The strings are labelled as 10,12 and 17 cpi, but this is only
		for purposes of identification. You may use them for anything
		that you deem necessary in any order as long as you remember
		what you did.


Sound Toggle

		This option will toggle the sound routines in NARC on and off.
	

Mouse Sensitivity


		The mouse can be made more sensitive by decreasing the value
		in the table. This is done in NARCCFG with the function
		keys. The current value is displayed on the screen as well as
		the mouse text cursor. You can move the cursor around the
		screen with the mouse and simultaneously set the sensitivity
		and watch the effect. The smaller the number, the greater the
		sensitivity and the largest number permitted is 100. These
		numbers correspond to the sensitivity values shown in the
		Microsoft mouse manual and are set by NARC with function 15
		of the mouse driver. If no mouse driver is installed, NARCCFG
		will not allow access to this feature.


Video Write method

		This key is a toggle between DIRECT and BIOS.
		
	DIRECT (default) - This method is the fastest and causes NARC to draw
		 screens by writing directly to the video RAM buffer.
		
	BIOS - This method causes NARC to draw screens using the BIOS video
	       interrupts.
	       

EOF Narccfg.DOC