ZIP.DOC
                                   -------
                           Instructions for ZIP.COM
                     IBM PC Serial File Transfer Utility
                             Version 1.1 (04/88)

                               (c)1988 E. Meyer

      Requires:  100% IBM PC compatible computers;  MS/PCDOS 2.x or 3.x


     ZIP is a small, fast utility to transfer files between two IBM compatible 
computers over an ordinary serial cable connection.  This is most useful when 
the computers don't share a common disk format, as in the case of a desktop PC 
with 5" drives and a laptop (or PS/2) with only a 3" drive.  ZIP is easier to 
use, and over 6 times faster, than any ordinary telcom program.

              Telcom programs: modem       2400 bps      0.3 K/sec
              Telcom programs: cable      19200 bps      2.3 K/sec
        --->  ZIP: cable                 115200 bps     14.1 K/sec

     Most computer manufacturers offer additional disk drives or other 
hardware accessories to provide access to data on both 3" and 5" disks; but 
these can cost hundreds of dollars.  They can also make a laptop computer a 
lot less than portable.  Direct serial connection isn't quite as fast, but it 
does allow a data rate of 115,200 baud -- that's over 14K per second.

     There are commercial programs for this purpose (of which LapLink may be 
the best known).  I'm sure they work very well, and have many extra 
conveniences that ZIP lacks.  But even they are priced around $129, which is 
far more than I was willing to pay.  ZIP transfers files just as well, and is 
free.


                                  BASIC USE

     Obviously, you will need a copy of ZIP.COM on both computers.  (You can 
accomplish this using your serial cable, if both machines have telcom software 
with XMODEM protocol.)

     ZIP makes transferring a file as easy as copying it from one disk to 
another.  To transfer any MSDOS file, once the cable is properly connected to 
the COM1 ports, from any DOS prompt:

     (1) On the sending machine, type:        C>zip FILENAME
     (2) On the receiving machine, type:      C>zip
                                          or  C>zip DIRECTORY

(Don't try to hit RETURN at exactly the same time on both ends; this actually 
makes an initial handshaking error more likely.)

     "FILENAME" can be a single file, or a GROUP specified by wildcards 
and/or commas (see examples below).  Each name may include a directory.  Each 
file will appear, with the same name, on the receiving end.  During the 
transfer you should see a blinking asterisk.  When you see the message 
"Verified", you know that the received copy exactly matches the original.

     "DIRECTORY" may optionally be specified on the receiving end; otherwise, 
files are received in the current directory.  Note: the directory MUST end 
with either a colon ":" or a backslash "\", otherwise ZIP will think it's a 
file to SEND!  See examples below.

     ZIP can be aborted by pressing any key:
              (1) on either end, during initial handshaking
              (2) on sending end, during file transfer
                    (will abort once current file is finished)


                                   OPTIONS

     There is one option that you can specify (after all filename(s), if 
present) on either end, to determine which serial port is used:

     /2  = COM2.  Use the COM2 port instead of the default, COM1.


                                   EXAMPLES


C>zip                  receives files over COM1 into current directory

C>zip \my              sends file C:\MY over COM1

C>zip \my\             receives files over COM1 into directory C:\MY\

C>zip my.* /2          sends files C:MY.* over COM2

C>zip d: /2            receives files over COM2 into directory D:

C>zip gort,klaatu      sends files C:GORT, C:KLAATU over COM1



                              TECHNICAL DETAILS

     ZIP does full CRC checking on the received file.  Since it is designed 
for direct serial transfer at maximum hardware speed, ZIP is not compatible 
with any other software, including ordinary telcom programs.

     Be sure to use the SAME version of ZIP on both ends: the transfer 
protocol may have changed.  Otherwise, if you can't get ZIP to transfer files, 
your computer(s) or your cable are incompatible.

     ZIP is written entirely in assembly language; it will only work on fully 
IBM compatible computers.  I have tested it on 8088 PC clones with clock 
speeds of 4.77 to 8 MHz.  (Specifically, the 8250 SIO chip is manipulated 
directly, and the COM1 and COM2 port addresses must be 03F8 and 02F8.)

     Serial cables can be wired in many different ways.  See your manuals for 
the correct pinouts; the only three that should [?] matter are receive and 
transmit (RD,TD), which should be crossed, and signal ground (GND), which 
should be straight through.  The one I use was labeled as an "IBM AT adapter", 
and had female connectors on both ends (one DB9, one DB25).  Any cable that 
doesn't work by itself should with a null modem adapter.


                                ERROR MESSAGES

            <ERROR>  invalid command (probably illegal option).
    <OUT OF MEMORY>  less than 64K free RAM, or too many files.
       <FILE ERROR>  trouble reading or writing a disk file.
     <COMM FAILURE>  possible cable or compatibility trouble. (*)
        <CRC ERROR>  received file CRC did not match -- cable problem?
          <ABORTED>  you pressed a key.

(* - You may occasionally see this if handshaking fails; just try again.)


                                   HISTORY

ZIP 1.0 (04/88) - trial release.  Worked well on most systems, but had trouble 
                 on some fast AT's.
    1.1 (04/88) - improved transmission algorithm.  Batch transfers allowed 
                 using wildcards and/or commas.  Receive directory option.
                 Original file time/date preserved.


     ZIP and its documentation are (c)1988 E. Meyer, all rights reserved.  
They may be freely distributed, but not modified or sold for profit without 
my written consent.  The user takes full responsibility for any damages 
resulting from the use (or misuse) of this program.  Please report any 
problems encountered.

                 Eric Meyer
            427 N. Washington #4             CompuServe [74415,1305]
           Bloomington, IN  47401