* Documentation for DMP *
                  Memory resident printer driver/spooler.

                     Copyright (C) 1988 by T. McGuire.
                               Revision 1.31
                     Documentation updated 10 Jan. '88














































            TABLE OF CONTENTS

    Introduction.................................................... 1

    Release note - New with version 1.30............................ 1

    User supported software......................................... 2

    Contents of the DMP.ARC file.................................... 2

    General description............................................. 2

    File print utility - PF.COM..................................... 5

    Cautions........................................................ 5

    General examples - Quick Start.................................. 6

    Features and options............................................ 7

    Disk selection and 'Print-to-disk' functions.................... 7

    Printer selection............................................... 9

    Spooler control.................................................11

    Driver control / character conversions..........................13

    Use of DOS environment variable or command file.................20

    Command summary chart...........................................21






























                                      DMP rev. 1.30 documentation   page 1

            INTRODUCTION

            DMP is a general purpose printer controller program, including
       disk spooling capabilities.  The controller portion is designed to
       allow you to add some simple features to your printer and to allow
       a limited amount of emulation of one printer's features with
       another printer via command line options.

            DMP is a memory resident program which uses approximately 12K
       bytes of available memory on an IBM PC,XT,AT or close compatible.
       This program is not compatible with the DOS 'PRINT' utility, or
       with any other print spoolers/buffers which drive printer no. 1.
       It has been used with MS-DOS and PC-DOS versions 2.0 thru 3.1 and
       with numerous 'TSR' programs, with no compatibility problems except
       as noted.

            The ARC file also includes the utility "PF" for printing files
       from a disk without using the DOS 'COPY' command.  See cautions and
       description below.  The syntax for PF is:  PF filespec,filespec,...
       The filespecs use the DOS file and directory conventions.

            RELEASE NOTE - NEW WITH VERSION 1.31
       This version corrects a bug in the automatic parallel port startup
       from the previous version.

            Significant features that have been added to this revision are
       described in detail in the commands sections.  Three important new
       capabilities are a "Print-to-disk" option (see the /PF /OF and /AF
       commands), improved handling of serial port printers including XOn-
       XOff pacing, and programmable translation of escape sequences for
       printer emulation (see the /E... command).

            Other new features include the optional use of a DOS envir-
       onment variable and disk files for entering commands into DMP.
       This allows long commands for escape sequence conversion and other
       functions to be stored in the environment or in a separate disk
       file.

            Other changes include modification to the /B command for
       selection of a parallel printer.  This command is no longer
       required except in systems with more than one printer.  Also, a /Mx
       command has been added to allow adding a margin or indent of x
       characters to the left side of the page.

            NOTES on switching printers: As with earlier versions of DMP,
       the DOS 'MODE' command can not be used to switch between parallel
       and serial port printers once DMP has been installed.   Use the
       'DMP/B' or 'DMP/SC..' command to go to the parallel and serial port
       respectively.  The DOS 'MODE' command can be used to set serial
       port parameters if desired, but the 'DMP/SC..' command is the pre-
       ferred method. This is described in detail in the commands section.

            This version allows switching between the serial and parallel
       printers with data spooled or without.  It is recommended that you
       wait until a printer has finished printing all the data spooled for
       it, because some data may be lost during the switch.

            A logic error was fixed which prevented writing more than 99
       spool files to the disk.  Spool files will now be written with
       extensions up to .999, allowing a theoretical maximum of 4MB.




                                      DMP rev. 1.30 documentation   page 2

            USER SUPPORTED SOFTWARE

       This program is copyrighted material for private use.  It is not
       intended for commercial use.  Anyone desiring to use the program
       for commercial purposes or to resell it should contact the author
       at the address below for information.  No claims are made as to the
       program's suitability for any specific purpose.  The author
       disavows responsibility for any damages resulting from the use of
       this program.

            If you would like to continue to use this program after a
       reasonable evaluation period, please send a check or money order
       for $12.00 to the address below.  If you do not want to use the
       program, please erase it from your computer/disks or give your copy
       to someone else who may want to use it.  Making copies for others
       or placement on electronic bulletin boards is allowed and encour-
       aged, so long as the programs and documentation are transferred in
       their entirety with no modifications.

       Send payment and any inquiries to:

                   Terry McGuire
                   1127  12th Street #306
                   Santa Monica, CA 90403



        CONTENTS OF THE DMP.ARC FILE

        The downloadable file for DMP decompresses to three files:
            1.) DMP.DOC; this documentation.
            2.) DMP.COM; the memory-resident print spooler/driver.
            3.) PF.COM; 'Print Files' utility, described below.



        GENERAL DESCRIPTION

            This section provides fairly detailed information on how the
       DMP program works.  Read it if you are interested, or if you are
       having problems getting started, otherwise proceed to the next
       section on the 'PF' utility.  The commands are described in detail
       later.

            DMP provides numerous features and options as noted below.
       All options are controlled via command line switches, with the
       environment variable or a with separate command file.  Some options
       can only be set when the program is first loaded, but most can be
       changed by re-entering the command line with new options at any
       time.

            The program allows redirecting printer output to a serial
       port, COM1 or COM2 only, with options for bit rates and handshake
       signals as noted below.  It also allows redirecting output to a
       disk file.









                                      DMP rev. 1.30 documentation   page 3

            DMP is intended to be loaded with an autoexec.bat file,
       primarily because the commands can become complex if more than a
       few options are used, and the load command would be difficult to
       remember.  It can be loaded at any time, however, using a batch
       file, keyboard macro or typing it in.

            DMP sends confirmation messages for commands to DOS "standard
       output", usually the screen.  Once you have confidence that you
       have the commands you need, the output can be directed to 'NUL' to
       avoid cluttering the screen, e.g. DMP/B/M4 >NUL.  Error messages
       are sent to "stderr", so will show any problems even with the
       redirection.

            Use of the control character and escape sequence conversions,
       serial port redirection and several other options will almost
       certainly require a thorough understanding of the printer manual
       for the printer that is to be used.  Referring to that document at
       the same time as the command options given here should allow the
       program and printer to work together harmoniously, though the
       process may take some time.

            DMP only works with the 'primary' printer on a system,
       designated 'PRN' by DOS.  It can work with more than one printer on
       a system, one at a time, by redirecting output between parallel and
       serial ports.  The redirection can be done without rebooting.

            DMP functions by intercepting the BIOS software printer
       interrupt (17hex) and driving the parallel or serial port directly,
       or sending printer output to a disk file.  Calls to INT 17H which
       are for a printer other than the primary one are 'chained' to the
       previous vector.  It also intercepts the timer interrupt, calls the
       previous owner of the timer, then checks for any printer functions
       needed.  If the printer is redirected to a COM port, the hardware
       interrupt for that port is also used, and the use of the timer
       interrupt is reduced.  DMP also uses some DOS software interrupts
       for gaining access to DOS' disk read and write functions.

            The control character conversion option uses the program's PSP
       as a data table for the characters, since the PSP is not needed
       once the program has terminated.  The escape sequence conversions
       use a separate 512 byte buffer for the conversion strings.  The
       strings are sorted when they are entered, and compared using a
       binary search when being received.  This puts as much of the com-
       plexity as possible in the non-resident portion of the program.

            Of the 12K+ memory required for DMP, about 3.5K bytes is
       program code.  Buffers of 4K bytes each are used for input and
       output, and a 512 byte buffer is used for escape sequence con-
       version.  Printing files of less than 6-8K bytes will not require
       disk read/writes, therefore, but are still spooled.














                                      DMP rev. 1.30 documentation   page 4

            The spooler portion is a true spooler, not a buffer as many
       other printer programs.  It creates disk files with filenames
       $PSPOOL.nnn, where 'nnn' ranges from '000' to '999'.  The files are
       written as printer output is generated, then read and deleted when
       the information is printed.  The files are written on the disk
       drive designated on the command line when the program is first run.
       The spool files are written to the 'root' directory of the drive.
       Subdirectories on a hard disk can be used via the DOS 'SUBST' com-
       mand.  No filenames should be used on the system which match the
       program's format.  The files are not marked as 'hidden' or
       'system', so they will show up in directory listings made while the
       spooler is running.  If the system is stopped or rebooted while the
       spooler is running, extra files will be left on the designated
       drive.  This will not interfere with the operation of the spooler
       when it is reloaded, but the files should be deleted to free up the
       disk space.

            The "Print-to-disk" option uses the same mechanisms for
       writing to the disk as the spooler.  The main difference is that
       the output portion of the memory buffer is added to the available
       space used by DMP, as long as it is not needed for a printer. If
       the "Print-to-disk" function is enabled while there is data spooled
       to be printed, the spooled data will continue to print until it is
       finished or the spooler is aborted by command.  Any additional data
       that is sent from a running program or from DOS to the printer
       after "Print-to-disk" is started will go to the disk file.  Any
       character or escape sequence conversions that are in effect will
       show up in the disk file.

            The "Print-to-disk" option uses either a 4K byte data buffer,
       if data is still spooled for the printer, or between 4K and 8K for
       the buffer when no data is left for the printer.  The buffer is
       written to the disk file when it reaches 4K bytes in size, as soon
       as DOS is available for the disk write function.  If the buffer
       fills up (either 4K or 8K) and DOS is not ready, an error return is
       given to the program that is printing.  The buffer will also be
       written to the disk after a 10 second (approx.) timeout if nothing
       has been output to the printer.

            DMP works most efficiently when the spooler uses a RAMDISK,
       but it is compatible with any disk recognized by DOS.  A hard disk
       is convenient for large print files.  A floppy or any removable
       disk is NOT recommended, as removal of the diskette while the
       spooler is operating can cause the system to crash, and the I/O is
       very slow and will use noticeable portions of computer time while
       printing.


















                                      DMP rev. 1.30 documentation   page 5

       FILE PRINT UTILITY - PF

            The .ARC file includes PF.COM, for sending disk files directly
       to the printer.  This very simple utility may be used from the DOS
       prompt by entering PF followed by the names of the files to be
       printed.  This is useful for printing files output by word
       processors, compilers, data base programs, etc that are in 'ready
       to print' form.

            The PF program can also be used for later printing of DMP's
       own files that were generated by the "Print-to-disk" option. This
       may require some caution if control character or escape-sequence
       conversions were in effect at the time the file was generated.  It
       is a good idea to have any such conversions in effect when generat-
       ing the file or else when printing it, but not both.

            PF does no conversion itself, and may be used with or without
       DMP installed.  It's intent, however, is to spool data for printing
       with DMP, then allow the computer to be used for other purposes
       while the printing takes place.

            Please do not confuse this separate utility with the DMP
       command 'DMP/PF' for directing printer output to a disk file.

       CAUTIONS

            This version of the program does not handle critical disk
       errors.  It will function properly after a read or write error with
       spool files, but a DOS error resulting in the infamous 'Abort,
       Retry, Ignore' message may cause system failure, even if the
       message is from a disk drive other than the one with the spool
       files.

            Printing files by using the DOS 'TYPE' command with print
       screen turned on or the DOS 'COPY ...  PRN' command will prevent
       the spooler from writing to disk while the command is being exe-
       cuted.  The data will be buffered to the internal 8K memory only.
       If the files are shorter than this, or if you don't mind the wait,
       the program will function properly.

            Printing with 'TYPE' or 'COPY' while files are already spooled
       to the disk presents another problem.  There is no access to DOS
       for writing to the disk at this point, so DMP will signal DOS with
       a printer 'timeout' error.  DOS will signal you with a short
       message, followed by...(you guessed it) "Abort, Retry, Ignore?".
       Answer 'A' for abort, very soon.  Note that the DOS 'PRINT' program
       cannot deal with this situation either.

            Printing in this manner with the "Print-to-disk" option turned
       on has a better chance of success, since DMP has a variable size
       buffer in this case.  This allows a greater chance to gain access
       to the disk, but is still not a "bulletproof" solution.












                                      DMP rev. 1.30 documentation   page 6

       GENERAL EXAMPLES - QUICK START

            The only mandatory command line switch when the program is
       first loaded is '/D..' for selecting a disk drive for the spooler.
       If the printer is connected to any port other than the default
       parallel output, it must be redirected to another parallel port
       with the '/B' option, or to a serial port with the '/SC' option as
       described below.

            The examples below assume the disk configuration to be:
       floppy disk(s) as drives A:  and/or B:, hard disk as drive C:,
       VDISK or other ramdisk as drive D:.  Adjust the drive letters to
       match your system.

       Example 1.  BIOS default printer, text only, spool to ramdisk.

             Load spooler:  DMP/DD:

             Kill spooler output (e.g. paper jam) : DMP/SK
             Print files ABC.TXT and XYZ.TXT in directory \DOC on drive C:
                        PF C:\DOC\ABC.TXT C:\DOCS\XYZ.TXT
             Send printer output to file PRINTOUT.TXT in the current
                  directory: DMP/PFPRINTOUT.TXT
             Send output back to parallel printer: DMP/B
             Suspend spooler output : DMP/S- (Data continues spooling.)
             Restart spooler output : DMP/S+


       Example 2.  Parallel printer, text only, spool to hard disk,
             simulate form feeds with line feeds, expand tabs, skip
             perforation.

             Load spooler: DMP/DC:/F-/T+/V65

            Allow graphics printing temporary, i.e. don't change tab and
            form-feed characters: DMP/G+
            Re-enable character conversion features: DMP/G-


       Example 3. Parallel printer connected as LPT1:, text only, spool to
            ramdisk, send sequence 'Esc&k0S' to reset printer on startup.
            (You've checked the printer manual!)  Prevent character ^U
            from being sent to printer.

                Load spooler: DMP/DD:/B1/C27,38,107,48,83/X15-


       Example 4. Serial printer connected to COM1, text only, 1200bps,
            printer signal connected to DSR line, spool to hard disk.

            Load spooler: DMP/DC:/SC1R1200WDSR

            Printer output to disk file DATA.123 on drive A:, append
                output to existing file:  DMP/AFA:\DATA.123
            Change output to parallel printer and spool to ramdisk.  (No
                data spooled for printing.):  DMP/DD:/B
            Switch back to serial printer, leave spooling set to ramdisk:
                   DMP/SC1R1200WDSR






                                      DMP rev. 1.30 documentation   page 7

       FEATURES AND OPTIONS

            All options are controlled thru command line switches, the
       environment variable or a command file.  The commands and option
       selection is performed either when the program is first loaded, or
       by re-running it at any time.  The switches are always a right
       slash ('/') followed by a letter, followed by other information for
       the option chosen.  Commands in an environment variable are entered
       by the DOS 'SET' command, for example "SET DMP = /B". Any number of
       options may be entered each time the program is run, limited only
       by the length of the line.


            The commands are divided into four groups:

       1. Disk selection for spooler and "Print-to-disk".
       2. Printer selection.
       3. Spooler control.
       4. Driver control / character conversion.


        Descriptions of all commands follow, with syntax and examples.



    1. DISK SELECTION AND "PRINT-TO-DISK" FUNCTIONS.
       =============================================


     COMMAND FUNCTION: Select disk drive for spooler.
       THIS COMMAND IS MANDATORY WHEN INSTALLING THE SPOOLER.

        Default: NO drive selected.

        Syntax: DMP/Dx:
            'x'='A' thru last DOS recognized drive. The colon is required.

        Description: A disk drive must be selected when DMP is first
            installed, unless the spooler portion of the program is not
            installed. Refer to command '/S' below. The drive can be
            changed later, at any time when there are no spool files
            active. The command will work if there is data in the memory
            buffers, as long as nothing is spooled to the disk.

        Example: DMP/DD:  -Select drive D: for spooler.



     COMMAND FUNCTION: Read DMP commands from a disk file.

        Default: Commands are read from the environment or command line.

        Syntax: DMP/Rfilespec

        Description: Causes the disk file designated in 'filespec' to be
            opened and commands read from it as if the commands were
            entered after DMP on the DOS command line.  This command can
            only be specified on the command line.  See description in the
            "environment variable or command file" section below.





                                      DMP rev. 1.30 documentation   page 8

     COMMAND FUNCTION: Print to a disk file.

        Default: Print to selected printer.

        Syntax: DMP/PFfilespec or DMP/AFfilespec or DMP/OFfilespec

        Description:  The three command names stand for "Print File",
            "Append File" and "Overwrite File".  If the given file does
            not exist, all three will operate identically.  The file will
            be created and subsequent printer output will go to the file.

            If the file already exists, the commands operate as follows.
            The "/PF..." command will find the file, and ask if you want
            to append, overwrite or cancel the command.  The "/AF" and
            "/OF" commands will append or overwrite the file without
            asking. A confirmation message is displayed.

            This command allows only two possibilities for specifying the
            filename. The first is a filename only, with no drive or dir-
            ectory specifiers, like "OUTPUT.PTR".  This causes the file to
            be created (or appended to) in the drive/directory that is
            current when the DMP command is entered.  The second method is
            full path and filename, starting from the root directory of
            any DOS recognized drive, like "A:\TEXT\PRINTS\OUPUT1.DOC".
            Note that the backslash must be used to specify the root dir-
            ectory of a drive (unless it is the current directory).
            A:\DOC.TXT is correct. A:DOC.TXT is NOT correct and will
            generate an error message.

            The file that is being printed to does not have to be on the
            same disk that is used for the spool files while printing to
            the printer.

            This command is cancelled by the '/B' or '/SCx...' commands to
            direct output back to the serial or parallel printer. It may
            also be cancelled by '/PF-', '/AF-', or '/OF-'.  This will
            cause printer output to go back to the printer port that was
            in use before the Print-to-disk function was started.

            Please do not confuse this command with the separate utility
            'PF'.  This command is for sending printer data to a disk
            file.  The PF utility is for sending an existing file to the
            printer.

        Examples: DMP/PFC:\DOCS\PRINTOUT.TXT -Printer output goes to file
            "printout.txt" in directory "docs" on drive C until cancelled.

          DMP/OFPRTEXT -Printer output goes to file "prtext" in the
            current directory. If the file exists it is erased and re-
            written.

          DMP/B -If printer output had been set to a file, it is directed
            to the parallel port. The file is closed.











                                      DMP rev. 1.30 documentation   page 9

    2. PRINTER SELECTION.
       =================


     COMMAND FUNCTION: Set printer output to parallel port.

        Default: BIOS default printer.

        Syntax: DMP/B[n]    n=0,1 or 2 for parallel port number.

        Description: The function of this command has been changed in this
           revision of DMP. The default/startup state is now to use the
           BIOS default printer instead of parallel port #1.  Entering no
           '/B' switch or a '/B' switch without a number will result in
           the program checking for a printer port designation in the BIOS
           data area.  Once a parallel port is selected, the '/B' command
           with no number will cause output to go to the selected port.

           This may not function correctly on some of the less compatible
           "compatible" computers. If the program cannot find a useable
           printer address when first installed, it will install with no
           address, and inform you with an error message.  You may then
           re-enter a parallel port with this command.

            The ports are defined as:
            Port #0 - I/O addresses 378-37F hex - The one on the
                motherboard or on the 1st multifunction board (often).
            Port #1 - I/O addresses 3B8-3BF hex - The one on a mono or
                mono/graphics adaptor. The one on a multifunction board
                 (sometimes).
            Port #2 - I/O addresses 278-27F hex - The 2nd one on a multi-
                function or other option board.

            DMP cannot function with any parallel printers other than at
            these addresses.

            This command is also used to set the printer output back to
            the parallel port after it has been redirected to a serial
            port or to a disk file.  It can also be used to switch between
            two parallel printers.  Useful for systems with 2 printers,
            for switching back and forth without rebooting.



     COMMAND FUNCTION: "/SC..." command. Redirect printer output to serial
       port COM1 or COM2.  Set communication bit rate and select pacing.

        Defaults: Printer set to parallel port. Neither COM port is
            default; one of them must be specified when this command is
            entered.  There is no default bit rate when the serial port is
            selected; one should be specified, or the bit rate set with
            the DOS 'MODE' command before this DMP/ command is entered.
            The default pacing signal is 'CTS'.  Control via 'XOn/XOff' is
            always enabled, in case the printer uses it.

        Syntax: DMP/SCx[Ryyyy][Wabc]
            'x'='1' or '2' for COM1 or COM2.
            'yyyy'=bit rate. available values:
                300,600,1200,2400,4800,9600,19200,38400.
            'abc'='CTS', 'DCD', 'DSR', 'RI' for hardware handshake signal.




                                     DMP rev. 1.30 documentation   page 10

     /SC... command (cont.)

        Description: This is the redirect command for a serial printer.
           The command may be entered during or after installation of DMP.

            Note that the printer must NOT be redirected with the DOS
            'MODE' command or any other software.  Use the '/SC..' or '/B'
            commands if you want to switch between serial and parallel
            printers.

            The number after the '/SC' selects COM1 or COM2, and must be
            specified.

            The optional 'R' parameter sets the bit rate. Do not enter any
            '/' or '[' between the port select and 'R'. A bit rate may be
            selected from the above list, entered in numbers as shown.
            This parameter may be changed after the serial printer has
            been selected. If a bit rate is selected, other parameters for
            the serial port are set to 8 data bits, no parity, 2 stop
            bits. The alternative is to use the DOS 'MODE' command to
            select these parameters. It is recommended to use this DMP
            command, however, to ensure that the serial port is set
            properly before anything is printed. The printer should be set
            to 8N2 or 8N1, and the corresponding bit rate.

            The optional 'W' parameter selects the serial port input
            signal to be used as the printer 'busy' signal. The selected
            signal should be connected to the printer output signal for
            stopping serial input.  The signal designations and pin
            numbers for a 25-pin (PC/XT) and 9-pin (AT) connectors are as
            follows:

               Computer connector:      25pin       9pin
              CTS - Clear to send  -    pin 5       pin 8
              DCD - Carrier detect -    pin 8       pin 1
              DSR - Data set ready -    pin 6       pin 6
              RI  - Ring indicator -    pin 22      pin 9

            This version of DMP includes an additional feature in the
            pacing control to allow 'XOn/XOff' control of the output by
            the printer.  This function cannot be disabled. If the printer
            does not use it, this will have no effect.  If the printer
            does send 'XOff' characters to control output, a hardware
            pacing signal must still be selected as above.  The hardware
            signal should be disabled on the connector (either end) if it
            is desired to use only the 'XOn/ XOff' control.  If the output
            to the printer is stopped by 'XOff', it will restart when the
            printer sends an 'XOn' or if any other DMP command is entered
            from the DOS prompt.


        Examples: DMP/SC1R2400WCTS - Select COM1, 2400bps, 8data, no
                       parity, 2 stop bits, use CTS handshake.
                 DMP/SC2WDCD - Select COM2, use DCD handshake. Use other
                    parameters as is.









                                     DMP rev. 1.30 documentation   page 11

    3. SPOOLER CONTROL.
       ===============


     COMMAND FUNCTION: Do NOT install spooler portion of DMP. First time
                       program is run.

        Default: Spooler is installed.

        Syntax: DMP/S-  (During installation only.)

        Description: Installs only character processing functions. In this
            mode DMP will not drive the hardware directly. Useful for
            performing character conversion, tab expansion, automatic form
            feeds, etc when spooling is not needed. Spooler can NOT be
            added later without re-booting computer, and can NOT be
            'uninstalled' once it has been installed. It CAN be disabled
            and re-enabled after installation; refer to '/SB','/S+'
            commands below.

            Using this command will disallow the 'Print-to-disk' function.

        Example: DMP/S- -Driver program left resident without spooler.



     COMMAND FUNCTION: Stop spooler output to printer. After installation
            only, 2nd and subsequent times program is run.

        Default: Spooler output on.

        Syntax: DMP/S- (After installation only.)

        Description: Turns off output to printer. Spooler continues to
            function, generating printer output data to disk files if
            needed.  Output can be re-enabled from the point where it was
            stopped with '/S+' command.  Useful for spooling output for
            printing later, changing printer paper, etc.

            If printer output has been redirected to a disk file, this
            command affects only data which is still spooled for the
            printer, if any. Output continues to go to the disk file.

        Example: DMP/S- -Spooler output turned off temporarily.


     COMMAND FUNCTION: Restart spooler output after '/S-' or '/SB'.

        Default: Spooler output on.

        Syntax: DMP/S+

        Description: Turns on output to printer after it has been turned
            off with  '/S-', or bypassed with '/SB'. No effect if the
            output is already on.









                                     DMP rev. 1.30 documentation   page 12

     COMMAND FUNCTION: Cancel printing. Flush buffered printer data.

        Default: Normal spooler operation.

        Syntax: DMP/SK

        Description: Deletes any spool files from disk. Empties internal
            buffers.  Printing stops, but spooler operation continues
            normally after reset.  All data that was spooled to be printed
            is lost.  Useful for paper jam, printer malfunction, wrong
            setup, etc.

            If printer output has been set to a disk file, this command
            does not delete the disk file or stop the output.


     COMMAND FUNCTION: Bypass spooler function.

        Default: No bypass. Normal spooler operation.

        Syntax: DMP/SB

        Description: Bypass spooler operation for all subsequent printing.
            Keeps character conversion, tab expansion, auto form feeds,
            etc.  all operational.  Sends printer output thru BIOS after
            conversions, if any.  Any data that is stored for printing
            will resume at the point it stopped if '/S+' command is
            entered subsequently.  If printer output was directed to a
            disk file, it will stop going to the file until re-enabled by
            the '/S+' command.


































                                     DMP rev. 1.30 documentation   page 13

    4. DRIVER CONTROL / CHARACTER CONVERSIONS.
       ======================================

     COMMAND FUNCTION: Graphics, binary data printing ON/OFF.

        Default: Graphics/binary OFF. Normal driver/spooler operation.

        Syntax: DMP/G+ or DMP/G-

        Description: /G+ to turn on graphics printing has two effects on
            the internal operation of DMP:

            1. All character conversions are inhibited, including left
                margin setting, perforation skip, carriage return/line
                feed combinations, tab expansion, and any control
                character or escape sequence conversions entered with
                '/X...' or '/E...' commands.  The settings for all of
                these options are not changed, and will resume if the
                '/G-' command is entered.

            2. Output pacing of lines is disabled. Characters are sent to
                the parallel port as fast as possible, up to about 600 per
                second.  The character rate for a serial port printer is
                limited by the bps rate of the port itself. Both parallel
                and serial outputs are still limited by the printer
                attached.

            This command is useful to allow bit image graphics printing
            for dot-matrix or laser printers after some character
            conversion options have been selected.  The options can later
            be re-enabled with '/G-'.  Note that in the default, startup
            condition no character conversions are performed, so that
            printing graphics does not normally require this option.

            This command is also useful for speeding up output to the
            printer for graphics or any other type of printing. The faster
            printing may cause some slowdown in computer response, or
            possibly some lost characters on some printers when printing
            normal text. The only recommendation that can be given for
            this command is to experiment with your printer.






     CHARACTER STRINGS: The next 3 commands require entry of character
       strings for output or conversion. This is shown as: <char string>.
       A character string may be entered on the command line or in the
       environment variable or command file as either a quoted string,
       like: "Abc" or a series of decimal numbers like: 65,98,99.  If more
       than one of these is needed, separate them by commas. 5 examples of
       valid strings are:  "XYZ"  13,10  27,"W",65,66  "Test"  "abc",13,10











                                     DMP rev. 1.30 documentation   page 14

     COMMAND FUNCTION: Send character or control code string to printer.

        Default: None.

        Syntax: DMP/C<char string>
            See the description of character strings on page 13.

        Description: Sends characters directly to printer. Useful for
            resetting printer to desired state on startup, or for changing
            pitch, etc., especially from a batch file. Refer to printer
            manual for codes needed.

            This command sends characters to a printer only, not to a disk
            file.  If this command is entered the first time DMP is run,
            it must be preceded by a '/B' or '/SC..' on the command line
            or in the environment variable, so the program will know which
            printer to send characters to.

        Example: DMP/C27,"U"
            -Send 'Esc,U' to printer.



     COMMAND FUNCTION: Convert or inhibit an 'escape' sequence. Remove
            conversion or inhibit for a sequence.

        Default: No escape sequence conversions or inhibits.

        Syntax: DMP/E<char string> = <char string>    or
            DMP/E<char string>-    or   DMP/E<char string>+

            See the description of character strings on page 13.

            The first syntax causes the sequence on the left of the '=' to
            be replaced by the one on the right of the '=' before being
            sent to the printer.

            The '-' (minus) option inhibits the escape sequence from being
            sent to the printer.  The '+' (plus) option removes previous
            conversions or inhibits for this sequence.

        Description:  These commands allow conversion of control sequences
            beginning with the 'Escape' character (Ascii 27, Hex 1B).  If
            a number of these conversions are set up, the control seq-
            uences for one printer can be substituted for another.

            The limitations are as follows: A total of 64 sequences may be
            converted or inhibited at one time.  Each sequence may consist
            of up to 20 characters for both the input and output strings.
            (40 characters total.)  The total number of characters in
            all conversion sequences is limited to 512.

            Sequence conversion is not recursive.  The converted sequences
            are sent directly to the printer (or disk file) without pas-
            sing through the converter again.

            The escape character is implied in the command.  Do not
            include it after the '/E'.  The escape character is NOT
            implied in the 'to' sequence.  Escape sequences may be
            replaced by any other sequence.




                                     DMP rev. 1.30 documentation   page 15

            No escape sequence conversions take place in graphics '/G+'
            mode.

        Example:  DMP/E"W"=27,"&k9S" /E"&"=27,"&k0S"
           Convert the sequences 'EscW' and 'Esc&' to 'Esc&k9S' and
           'Esc&k0S'. This would convert the Diablo 630 bold on/off
           functions to the corresponding Epson MX-80 functions.
           (Those are trademarks of those 2 companies, and all that.)



     COMMAND FUNCTION: Convert or inhibit a control character. Remove
            inhibit from a control character.

        Default: No conversions. No characters inhibited.

        Syntax: DMP/Xnn=<char string>  or DMP/Xnn=-  or DMP/Xnn=+
            'nn'=decimal code for the character to be converted.

            See the description of character strings on page 13.

            'nn=-' inhibits this character from being sent to the printer.
            'nn=+' removes previous conversion or inhibit for this
                character.

        Description: Control characters can be converted to strings or
            blocked from being sent to the printer with these commands.
            The characters that can be converted or blocked are Ascii
            codes 0-31, except Tab(09), CR(13), LF(10), FF(12), and
            Escape(27).

            This function can be used for a limited amount of conversion
            from commands for one printer to commands for another, or to
            block printer commands from a word processor or other program
            that refuses to cooperate.

            Any conversions remain in effect when printer output is
            redirected between serial and parallel printers or to a disk
            file.  No conversions or character inhibits will take place in
            graphics '/G+' mode.

        Examples:  DMP/X15="x"  Convert ^O to lower case 'X'.
                   DMP/23=-     Prevent ^U from being sent to the printer.




     COMMAND FUNCTION: Set left margin.

        Default: Left margin is zero.

        Syntax: DMP/Mx  x is a decimal number from 0 to 99.

        Description:  This command allows a left margin or indent to be
            added to printouts. The number of spaces entered as 'x' will
            be added to each line.  DMP/M0 removes the margin.  No left
            margin is added in graphics '/G+' mode.

        Example: DMP/M8   -Add 8 spaces at the beginning of each line.





                                     DMP rev. 1.30 documentation   page 16

     COMMAND FUNCTION: Tab expansion function ON/OFF.

        Default: Expansion OFF. Tab stops at every 8 positions.

        Syntax: DMP/T+ or DMP/T-

        Description: /T+ enables tab expansion, /T- disables it. Any tab
            characters received will advance the print position to the
            next tab stop set.  Refer to the other '/T' commands below for
            setting tab stops. Tab expansion should be disabled if the
            printer includes tab stops and you want to use this feature.
            Since DOS and most word processors include tab expansion, this
            feature will not usually be needed.  It is useful when copying
            disk files which include tabs directly to the printer, or if
            you want to use non-standard tab stops.

        Note: No tab expansion will occur in graphics '/G+' mode.



     COMMAND FUNCTION: Reset tab stops to every 8 positions.

        Default: Tab stops at every 8 positions. Tab expansion OFF.

        Syntax: DMP/TR

        Description: Removes any tab stops set by other '/T' commands.
            Sets a tab stop at every 8 positions.



     COMMAND FUNCTION: Clear all tab stops.

        Default: Tabs reset to every 8 positions.

        Syntax: DMP/TC

        Description: Removes all tab stops. Useful for resetting tabs to a
            new format.



     COMMAND FUNCTION: Add or remove tab stops at column positions.

        Default: Tabs reset to every 8 positions.

        Syntax: DMP/Taa+,bb+,...  or DMP/Txx-,yy-,...
            'aa','bb',...=column numbers at which to add tab stops.
            'xx','yy',...=column numbers at which to clear tab stops.

        Description: Add(+) or remove(-) tab stops. The column numbers
            followed by '+' or '-' may be intermixed to set up a complete
            tab format. The program displays a representation of all tab
            stop settings when this command is entered, to allow
            verification.









                                     DMP rev. 1.30 documentation   page 17

        Example: DMP/TR/T+/T41-,43+,57-,64+,65-,69+,73-,75+,81-,82+
           -Resets tabs to every 8 columns, i.e. columns 9,17,25,...,
            enables tab expansion, then clears tab stops from columns 41,
            57, 65, 73, 81 and adds tab stops at columns 43, 64, 69, 75,
            82. Program responds:    "Tabs reset to every 8 columns.
                          Tab stops updated.
                          Tab stops:
            --------x-------x-------x-------x---------x-----x-------------
            --x----x-----x------x------x-------x-------x-------x-------x--
            -----."




     COMMAND FUNCTION: Inform DMP program whether printer has auto line-
                       feed.

        Default: Printer assumed NOT to have auto line feed.

        Syntax: DMP/A+ or DMP/A-

        Description: This option does not change DMP's character
            conversion functions, but allows the program to count the
            number of lines that the paper has advanced in order to
            generate the form feed function.  The program should always be
            properly set to match the printer's operation. If the printer
            does have automatic line feed, the preferable choice is to
            disable this function on the printer.  If it isn't or can't be
            disabled, add the /A+ command when DMP is installed. The '/A-'
            command resets to the default state. This command can be used
            in conjunction with the /L and /U commands (below) to force
            printed output to double or triple space. It can also cause a
            lot of paper to be wasted during experimentation.




     COMMAND FUNCTION: Instruct DMP program to send, or stop sending, line
            feed to printer after each carriage return character.

        Default: NO automatic line feeds sent.

        Syntax: DMP/L+ or DMP/L-

        Description: '/L+' causes line feeds to be added, '/L-' removes
            effect of '/L+'. This can be used to force double spacing or
            in conjunction with a print program which does not send line
            feeds, causing a "black bar" to be printed on one line. It is
            generally not needed.  See comments under '/A'.
            No line feeds will be added in graphics '/G+' mode.














                                     DMP rev. 1.30 documentation   page 18

     COMMAND FUNCTION: Allow or suppress line feeds after carriage
                       returns.

        Default: Allowed.

        Syntax: DMP/U+ or DMP/U-

        Description: This command refers to characters which are being
            sent from an application program to the printer. '/U-'
            inhibits line feeds after carriage returns; '/U+' reverts to
            default state. It can sometimes be used to force single-
            spacing when the program is printing double-spaced.  It can
            also be used together with /A and /L to force a consistent
            print format from a variety of programs which use different
            line spacings.
            Line feeds will not be inhibited in graphics '/G+' mode.




     COMMAND FUNCTION: Inform DMP program whether printer has form-feed
                capability.

        Default: Printer assumed to have form feed function.

        Syntax: DMP/F+ or DMP/F-

        Description: '/F+' (default state) tells DMP to pass form feed
        characters to the printer, and to use form feed characters when
        needed.  '/F-' causes the form feed function to be performed by
        adding line feeds to the end of the physical page length set by
        the '/P' option. The program should be set to match the printer.
        Form feed characters are not converted in graphics '/G+' mode.




     COMMAND FUNCTION: Force keyboard caps-lock ON, num-lock OFF.

        Default: None.

        Syntax: DMP/I

        Description: Forces locking keys on IBM compatible keyboard to the
            states shown. Does not change keyboard indicators. Useful in
            autoexec.bat file for setting startup state. No other locking
            key states may be set.

















                                     DMP rev. 1.30 documentation   page 19

     COMMAND FUNCTION: Set physical page length.

        Default: 66 lines per page.

        Syntax: DMP/Pnn
            'nn'=number of lines per page, 5 to 99.

        Description: This command informs DMP of the number of lines
            (printer line feeds) on a page. 66 lines corresponds to 6
            lines per inch, 11 inch paper. The program should be correctly
            informed if the page length is different. This number is used
            by the program for the form feed function and the 'skip
            perforation' function. See comments under the '/V' command
            below. The page length might be changed for graphics mode or
            an unusual print font.

            Entering this command with no numbers will cause the program
            to display the current setting. Entering this command at any
            time causes the program to be set to 'top of form', with
            nothing sent to the printer.





     COMMAND FUNCTION: Set text length - number of lines to print per
                       page.

        Default: 70 lines (no perforation skip function).

        Syntax: DMP/Vnn

        Description: This command is used in conjunction with '/P', above,
            to tell the program when to advance to the next page during
            continuous printing.  In the default state, the printer will
            not skip lines for the perforation, since the text length is
            set longer than the physical page length.  To enable this
            function, set the text length to one or more lines less than
            the page length with this command.

            Entering this command with no numbers will cause the program
            to display the current setting. Entering this command at any
            time causes the program to be set to 'top of form', with
            nothing sent to the printer.

            No perforation skip or automatic form feed function will take
            place when the driver is in graphics '/G+' mode, regardless of
            the settings for page and text length.

        Example: DMP/P84/V85
            -Set printer to 84 lines per page (14 inch paper). Disable
             'skip perforation' function.












                                     DMP rev. 1.30 documentation   page 20

    USE OF DOS ENVIRONMENT VARIABLE OR COMMAND FILE

        This version of DMP allows reading commands from an environment
    variable if desired.  The variable should be entered with the 'SET'
    command as: SET DMP = /options.  'options' can be any commands except
    the '/R..' command.  Any time DMP is run, it will read the environment
    and check for this variable.  If found, any commands will be executed
    if possible, with error messages generated if the command(s) are
    invalid.

        This function can be used to execute one or more commands any time
    the program is run.  It could be used, for example, to set the default
    printer to a parallel port other than the default BIOS printer, and
    make sure it stays there, or to send a reset command to the printer
    any time a DMP command is entered.

        The use of the environment variable is optional, and the program
    will execute command line selections whether the environment variable
    is used or not.

        This version also allows reading commands from a disk file if
    desired.  To read a command file, enter '/Rfilespec' as a DMP command
    during installation or later.  (This option may not be selected with
    the environment variable.)  The 'filespec' is a valid DOS disk file
    name, including drive and directory specifiers if desired.  Only one
    command file may be specified each time DMP is run.  Additional '/R'
    commands on a command line are ignored.

        The command file consists of commands from the lists in this
    document.  Each command must be preceded by the slash '/'.  Do NOT
    precede commands with 'DMP'.  Multiple commands may be entered on one
    line, but a single command may not be broken into two lines.

        When the DMP program is run, commands are interpreted in the
    following order:
        1.) Environment variable, if any.
        2.) All command line entries.
        3.) Command file, if any.

        This means that entries on the command line or in a file can be
    used to cancel those in an environment variable, if the entries are
    'cancellable'.  Sending a string of characters to the printer can not
    be cancelled;  setting the parallel printer for output is cancelled by
    setting a serial printer for output.




















                                     DMP rev. 1.30 documentation   page 21

    COMMAND SUMMARY CHART:

            Function                           Default       Select(/..)
        ------------------------------------------------------------------

        Spool to disk drive X. MUST be spec-     None           DX:
        ified when installing. Can be changed.

        When installing: Do NOT install spooler. Install        S-

        After installed: Spool output OFF (temp) ON             S-
          Spool output ON, after /S-.            ON             S+
          Cancel printing. Flush buffers/files.                 SK
          Bypass spooler. Pass chars to BIOS.                   SB

        During or after installation:
        Set printer output to parallel port #n.  BIOS           Bn
        Set default parallel port                               B
        Redirect spooler output to comm. x, bit  Parallel       SCxRyy
           rate yy, Wait for abc (CTS,DSR,DCD)   CTS            Wabc

        Direct printer output to a file:         Parallel       PFfile
            -Append to file if it exists                        AFfile
            -Overwrite file if it exists                        OFfile
        Read a command file                                     Rfile

        Graphics/binary mode printing ON,OFF.    OFF            G+,G-
        Send,No send LF to printer after CR.    *No send        L+,L-
        Allow,Suppress LF after CR from user.   *Allow          U+,U-

        Tab expansion ON,OFF                    *OFF            T+,T-
        Reset tabs to every 8 positions          Reset          TR
        Clear all tab stops                      8 spaces       TC
        Add tab stops at columns aa,bb,...       8 spaces       Taa+,bb+,
        Remove tab stops at aa,bb,...            "   "          Taa-,bb-,

        Set left margin.  nn=0 to 99             No margin      Mnn
        Printer does/doesn't auto LF on CR.      Doesn't        A+,A-
        Printer does/doesn't have form feed.    *Does           F+,F-
        Send char. string to printer                           C<char seq>

        Convert control char nn to string <char seq>
         up to 5 chars., 0 to 31, not Tab,CR,LF,FF,esc. *   Xnn=<char seq>
        Inhibit sending control char. nn                *       Xnn=-
        Remove inhibits/converts for char. nn           *       Xnn=+

        Convert escape sequence <seq 1>                 *     E<seq 1>=
            -replace with <seq 2>                               <seq 2>
            -remove conversions                         *     E<seq 1>+
            -inhibit sequence                           *     E<seq 1>-

        Force caps-lock ON, num-lock OFF.        None           I
        Set physical page length (paper length)  66 lines       Pnn
            nn=5 to 99
        Set text length for auto FF (skip perf)  70 lines       Vnn

        * DMP will not make data conversions for these options unless
          graphics mode is OFF.*