EPSON.COM      Written by:  Robert K. Ricketts
                                 P.O. Box 820984
                                 Houston TX, 77282-0984


     This program was written in the public domain.   Please feel free to copy
and share  this program with  whomever you choose.   The only  restriction  is
that it be done  without  consideration  or  remuneration.    If you find this
program useful,  a  modest  contribution  of  Five Dollars  would  be  greatly
appreciated.    Contributions such  as  these  keep the  public domain  wheels
rolling!

     EPSON is a program that allows you to send control bytes  and/or  text to
the printer.    There are two methods you can use.    One method allows you to
send  'canned'  control sequences to the printer by simply specifying a single
option  letter.    The other method  allows you to send  ANY  code sequence by
specifying a string of hex bytes.  You must specify a '!' if you want to enter
your own hex bytes.    When entering hex bytes,  you must specify both digits,
even if the value is F or less.  I.E.  '9' must be '09'.  Here is  an  example
of how to set double-strike elite print mode.

          EPSON F              ( using the pre-canned code )
    or    EPSON ! 1B 21 11     ( specifying the hex bytes )

     An example of a code that is not canned (and therefore must be entered in
hex) is the  'cancel skip over perforation'.   The command for this code would
be...

          EPSON ! 1B 4F

     If you use the  '!'  option,  you  can  also enter  text.    Text must be
enclosed in double quotes.     In fact, you do not have to enter a print code.
If need be,  you can enter only text.    The above example to cancel skip over
perforation could also be entered as...

          EPSON ! 1B "O"   ( 4F is hex for 'O' and therefore is equivalent )

     Please note  that if  you use  a canned code,  you can  only specify  the
letter that corresponds to the print mode desired.   No other code or text can
be entered.    If you do attempt  to specify  additional codes or text with an
option other than '!', the additional arguments will be ignored.  The selected
option will happen as if it were the only argument.   You can specify multiple
codes and/or text only when using the '!' option.    EPSON will also check the
argument  list  to ensure  that there  is not  illegal data.    Below are some
examples of good and bad EPSON calls.


  good    EPSON H             - Sets double-strike emphasized print mode.

  quasi   EPSON H "text"      - Not actually an error,  but  only  option  'H'
                                will happen.  "text" will be ignored.

  good    EPSON ! 1B 21 18    - Sets double-strike emphasized print mode.

  good    EPSON ! 1B 21 18 "Hello" 0D 0A   - Sets double-strike emphasized and
                                             prints "Hello".

  bad     EPSON ! 1B 21 1H "Hello"         - Illegal hex byte, '1H' not valid.
                                             Nothing will happen.

  good    EPSON ! 1B 21 18 "H" 1B 21 11 "ello" 0D 0A   - Prints the letter 'H'
                                in   double-strike  emphasized  mode  and  the
                                letters 'ello' in double-strike elite mode.

  bad     EPSON ! 1B 21 18 Hello 0D 0A     - Left off the quotes  for  'Hello'
                                             'Hello' will  be  interpreted  as
                                             hex bytes and  since  'hllo'  are
                                             not valid hex bytes,  the program
                                             will terminate and  nothing  will
                                             happen.


     Please note that  you should  include the  '0D 0A'  each time you want to
start a new line.  The '0D' is a carraige return and must be used to force the
printer to dump his internal buffer to paper.   If you do not specify carriage
returns, your data will stack up in the printer until  his  buffer  fills  up.
The line feed  '0A'  needs  to  be  present  to  advance  the  paper one line.
Omitting the line feed will cause the printer to overstrike.   Mind you,  this
is not necessarily a bad thing.   If you want the printer to overstrike, leave
off the '0A'.     The use of  '0D'  and/or  '0A'  is only a concern if you are
sending text to the printer (regardless wether or not you are sending codes).


     Since EPSON allows you to 'roll your own' using the  '!'  option, you can
send control codes to  ANY  printer connected to the  parallel  port that will
accept codes.   If there are several different codes using the "!" option that
you have developed for EPSON,   you can make batch files containing the actual
calls to EPSON.   I.E.  If you frequently wanted to print your name on the top
of a listing  in big letters,  you might make a  batch  file  in the following
manner...

          copy con: myname.bat
  1)      EPSON ! 0C
  2)      EPSON ! 1B 21 38 "Robert K. Ricketts" 0D 0A
  3)      EPSON ! 1B 21 18 "P.O. Box 820984" 0D 0A
  4)      EPSON ! "Houston TX, 77282-0984" 0D 0A
          (ctrl Z)

     The hex bytes do not have to be uppercase.  Each EPSON line is explained.
1) Sends  a  form  feed  to  the  printer.    2) Sets  enlarged  double-strike
emphasized print mode and prints my name.     3) Sets double-strike emphasized
print mode, and prints my address.  4) Prints my city and state using the last
print mode set.  Note that the printer will remain in what ever print mode was
last set until changed or powered off.

     Below is a partial  list of the  Epson  printer codes.   These were taken
from the FX-100 manual.   All of the listed codes will work on the  FX-80  and
many will work on the MX-80 and RX-80.  If your printer is another Epson model
or another brand of printer, you'll need to consult the manual for the control
sequences available.


     EPSON ! 1B 21 00   -   Normal
             1B 21 01   -   Elite
             1B 21 04   -   Condensed
             1B 21 08   -   Emphasized
             1B 21 10   -   Double-strike, Normal
             1B 21 11   -   Double-strike, Elite
             1B 21 14   -   Double-strike, Condensed
             1B 21 18   -   Double-strike, Emphasized
             1B 21 20   -   Enlarged, Normal
             1B 21 21   -   Enlarged, Elite
             1B 21 24   -   Enlarged, Condensed
             1B 21 28   -   Enlarged, Emphasized
             1B 21 30   -   Enlarged, Double-strike, Normal
             1B 21 31   -   Enlarged, Double-strike, Elite
             1B 21 34   -   Enlarged, Double-strike, Condensed
             1B 21 38   -   Enlarged, Double-strike, Emphasized

             1B 2D 31   -   Sets underline print mode.
             1B 2D 30   -   Cancels underline print mode.

             1B 30      -   Sets 1/8 inch line spacing.
             1B 31      -   Sets 7/72 inch line spacing.
             1B 32      -   Sets 1/6 inch line spacing.
             1B 33 nn   -   Sets nn/216 inch line spacing.
             1B 41 nn   -   Sets nn/72 inch line spacing.

             1B 38      -   Disables paper end signal.
             1B 39      -   Enables paper end signal.

             1B 43 nn   -   Sets form length by nn number of lines.
             1B 43 00 nn    - Sets form length setting to nn inches.

             1B 4E      -   Sets skip over perforation.
             1B 4F      -   Cancel skip over perforation

             1B 53 48   -   Selects superscript print mode.
             1B 53 49   -   Selects subscript print mode.
             1B 54      -   Cancel superscript/subscript print mode.


     Again, the above list is partial.   I included the codes you  would  most
likely need and use.  There are plenty more in the Epson (or whatever) printer
book.  If you have any comments, please write me.


                                               - RKR