TINYFONT  ver 1.0

                       Designed by:  Robert K. Ricketts

                              (c) Copyright 1987



                             Downloaded from:

                             PC Consultant
                             SYSOP:  Robert K. Ricketts
                             P.O. Box 42086
                             Houston, TX 77242-2086
                      Node 1 (713)270-7408
                      Node 2 (713)270-8129


          TinyFont is a downloadable 'Soft Font' for the Hewlett Packard
     Laser Jet Series II printer.  The font utilizes the 300 DPI mode of
     the printer so the resolution is pretty good - even at this very
     small size.  The font supports all the standard IBM characters,
     including control characters (happy face, playing card suits, etc.),
     all text characters, and everything above 128 (including all the line
     drawing characters).

          The vertical line spacing is twenty lines per inch and the pitch
     is twenty seven characters per inch.  At these settings, the type
     face is surprisingly easy to read.  All characters are fixed width so
     preparing column oriented text such as lists is very easy.

          TinyFont is great for making micro miniature address and phone
     number lists for carrying in your wallet.  Or anything else that is
     normally too large or cumbersome.  The standard courier font (default
     on Laser Jet II and almost all dot matrix printers) gives only 66
     characters per square inch.  TinyFont gives a remarkable 540
     characters per square inch - more than 700 percent higher density!
     The line printer internal font at 16.66 CPI pitch and 12 LPI gives,
     at best, 200 characters per square inch.

          Included in this ARC file are the following programs and files
     to help you use TinyFont.


          TINYFONT.DOC  - This file.
          TINYFONT.USF  - Actual binary downloadable font for printer.
          EPSON.COM     - Program to send commands to printer (Yes, it'll
                          work on the Laser Jet.  Please read EPSON.DOC
                          for more poop on this program.)
          EPSON.DOC     - Documentation for EPSON.COM.
          TINYDL.BAT    - Batch file for downloading TinyFont.
          TINYSET.BAT   - Batch file to select TinyFont for usage.
          COURIER.BAT   - Selects the internal Courier font (and
                          completely deselects TinyFont).




          TinyFont is super easy to load and use.  To download TinyFont
     to your printer, simply follow these steps:


          1.  Make sure all the files in this ARC file are in the default
              directory on your disk (.DOC files don't matter).

          2.  Make sure the printer is powered on, on line, and '00 READY'
              is displayed on the LCD panel.

          3.  Type:  'TINYDL' at the DOS prompt and hit enter.


          During the download process, both the ready LED and the form
     feed LED should be blinking.  The ready LED will probably blink a
     little faster.  When the ready LED stops blinking, the download
     process will be completed.


          To select and use TinyFont, issue the following command:


          TINYSET  <enter>


          Since there are several commands necessary to completely
     deselect TinyFont and all it's weird print parameters, I have
     included a batch file that will select the Courier internal font.
     The Courier internal font selection batch file is:


          COURIER  <enter>


          TinyFont, as does any font, utilizes a particular 'Symbol Set'.
     No other font may use this particular Symbol Set while TinyFont is
     loaded.  There are many possible Symbol Sets so duplicate values are
     not very likely.  Just for your information, TinyFont's Font
     Descriptor Symbol Set value is 64,050.  TinyFont's PCL Escape
     Sequence Value Field is 2,001 and the PCL Termination Character is
     'R'.  These values should be avoided when designing your own fonts.
     The font ID used for downloading and selecting TinyFont is 151.  This
     can be changed if necessary but unless there is an ID conflict with
     some other font, changing the font ID should not be done.

          Due to the very small size of this type face and the fact that
     the Laser Jet II has a fixed underline dot thickness of three, I do
     not recommend specifying an underline attribute while printing with
     this font.

          If you find any errors (bad bit patterns) with this font, please
     call my BBS and let me know.  As (and if) I discover any problems,
     I'll update the TinyFont library on my BBS.

          Thank you for choosing TinyFont.